## Slide 1: RF Principles and TM Mode Cavity
Erk Jensen
CERN BE/RF

## Slide 2: DC versus RF
DC accelerator
RF accelerator
potential

## Slide 3: Lorentz force
A charged particle moving with velocity through an electromagnetic field experiences a force .
The total energy of this particle is , the kinetic energy is .
The role of acceleration is to increase .
Change of (by differentiation):
Note: Only the electric field can change the particle energy!

## Slide 4: Maxwell’s equations (in vacuum)
Why not DC?
    DC (): , which is solved by
    Limit: If you want to gain 1 MeV, you need a potential of 1 MV!
Circular machine: DC acceleration impossible since
    With time-varying fields:
World’s highest energy Van-de-Graaff Generator on Daresbury Lab campus

## Slide 5: Maxwell’s equations in vacuum (contd.)
Source-free:
curl (rot, ) of 3rd equation and of 1st equation:
Using the vector identity and the 4th Maxwell equation, this yields:
i.e. the 4-dimensional Laplace equation.

## Slide 6: From waveguide to pillbox

## Slide 7: Homogeneous plane wave
Wave vector :
the direction of is the direction of propagation,
the length of is the phase shift per unit length.
behaves like a vector.
z
x
Ey
φ

## Slide 8: Wave length, phase velocity
The components of are related to the wavelength in the direction of that component as etc. , to the phase velocity as .
z
x
Ey

## Slide 9: Superposition of 2 homogeneous plane waves
+
=
Metallic walls may be inserted where without perturbing the fields. Note the standing wave in -direction!
This way one gets a hollow rectangular waveguide

## Slide 10: Rectangular waveguide
Fundamental (TE10 or H10) mode
in a standard rectangular waveguide.
Example 1: “S-band”: ... ,
Waveguide type WR284 (2.84” wide), dimensions: 72.14 mm x 34.04 mm.
cut-off: .
Example 2: “L-band” : ... ,
Waveguide type WR650 (6.5” wide), dimensions: 165.1 mm x 82.55 mm.
cut-off: .
Both these pictures correspond to operation at 1.5 .
electric field
magnetic field
power flow:
power flow
power flow

## Slide 11: Waveguide dispersion
What happens with different waveguide dimensions (different width a)?
1: a = 52 mm,
cutoff
2:
a = 72.14 mm,
3:
a = 144.3 mm,
1
2
3

## Slide 12: Phase velocity
1: a = 52 mm, f/fc = 1.04
f = 3 GHz
2:
a = 72.14 mm, f/fc = 1.44
3:
a = 144.3 mm, f/fc = 2.88
The phase velocity is the speed with which the crest or a zero-crossing travels in z-direction.
Note on the three animations on the right that, at constant f, it is .
Note that at , !
With , !
cutoff
1
2
3

## Slide 13: Summary waveguide dispersion and phase velocity:
In a general cylindrical waveguide:
for TE, for TM
E.g.: TE10-mode in a rectangular waveguide:
.
In a hollow waveguide: phase velocity , group velocity , .

## Slide 14: Rectangular waveguide modes
TE10
TE20
TE01
TE11
TM11
TE21
TM21
TE30
TE31
TM31
TE40
TE02
TE12
TM12
TE41
TM41
TE22
TM22
TE50
TE32
plotted: E-field

## Slide 15: Some more standard rectangular Waveguides
b
a
Waveguide name |  |  | Recommended frequency band of operation (GHz) | Cutoff frequency of lowest order mode (GHz) | Cutoff frequency of next mode (GHz) | Inner dimensions of waveguide opening (inch)
EIA | RCSC | IEC |  |  |  | 
WR2300 | WG0.0 | R3 | 0.32 — 0.45 | 0.257 | 0.513 | 23.0 × 11.5
WR1150 | WG3 | R8 | 0.63 — 0.97 | 0.513 | 1.026 | 11.50 × 5.75
WR340 | WG9A | R26 | 2.2 — 3.3 | 1.736 | 3.471 | 3.40 × 1.70
WR75 | WG17 | R120 | 10 — 15 | 7.869 | 15.737 | 0.75 × 0.375
WR10 | WG27 | R900 | 75 — 110 | 59.015 | 118.03 | 0.10 × 0.05
WR3 | WG32 | R2600 | 220 — 330 | 173.571 | 347.143 | 0.034 × 0.017
courtesy: Eric Montesinos/CERN
Chart: Peak Power vs Frequency
| 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800 | 850 | 900 | 950 | 1000
WR2300 | 526.6212 | 691.9711 | 780.7698 | 836.2189 | 873.7253
WR2100 | 505.359 | 603.6639 | 662.6881 | 701.8693 | 729.5056
WR1800 | 356.7648 | 426.8444 | 470.6129 | 500.5393 | 522.1536
WR1500 | 266.9728 | 302.4189 | 326.8145 | 344.6071 | 358.0966 | 368.6196
WR1150 | 156.0606 | 172.9928 | 185.53 | 195.1925 | 202.852 | 209.0547
WR975 | 107.9109 | 119.5368 | 128.3767 | 135.3407 | 140.9658 | 145.5965
WR2300
WR2100
WR1800
WR1500
WR1150
WR975

## Slide 16: Radial waves
Also radial waves may be interpreted as superposition of plane waves.
The superposition of an outward and an inward radial wave can result in the field of a round hollow waveguide.

## Slide 17: Round waveguide
f/fc = 1.44
TE11 – fundamental
TM01 – axial field
TE01 – low loss

## Slide 18: Circular waveguide modes
TE11
TM01
TE21
TE21
TE11
TE31
TE31
TE01
TM11
plotted: E-field

## Slide 19: General waveguide equations:
Transverse wave equation (membrane equation): .
 | TE (or H-) modes | TM (or E-) modes
Boundary condition: |  | 
longitudinal wave equations (transmission line equations): |  | 
Propagation constant: |  | 
Characteristic impedance: |  | 
Ortho-normal eigenvectors: |  | 
Transverse fields: |  | 
Longitudinal fields: |  | 
 | TE (or H-) modes | TM (or E-) modes
Boundary condition: |  | 
longitudinal wave equations (transmission line equations): |  | 
Propagation constant: |  | 
Characteristic impedance: |  | 
Ortho-normal eigenvectors: |  | 
Transverse fields: |  | 
Longitudinal fields: |  | 

## Slide 20: Special cases: rectangular and round waveguide
Rectangular waveguide: transverse eigenfunctions
Round waveguide: transverse eigenfunctions
where in both cases
TE (H-) modes: | 
TM (E-) modes: | 
TE (H-) modes: | 
TM (E-) modes: | 
TE (H-) modes: | 
TM (E-) modes: | 
TE (H-) modes: | 
TM (E-) modes: | 

## Slide 21: Waveguide perturbed by notches
“notches”
Reflections from notches lead to a superimposed standing wave pattern.
“Trapped mode”
Signal flow chart

## Slide 22: Short-circuited waveguide
TM010 (no axial dependence)
TM011
TM012

## Slide 23: Single WG mode between two shorts
short circuit
short circuit
Eigenvalue equation for field amplitude :
Non-vanishing solutions exist for :
With , this becomes .
Signal flow chart

## Slide 24: Simple pillbox
electric field (purely axial)
magnetic field (purely azimuthal)
(only 1/2 shown)
TM010-mode

## Slide 25: Pillbox cavity field (w/o beam tube)
The only non-vanishing field components :
h
Ø 2a

## Slide 26: Pillbox with beam pipe
electric field
magnetic field
(only 1/4 shown)
TM010-mode
One needs a hole for the beam pipe – circular waveguide below cutoff

## Slide 27: A more practical pillbox cavity
electric field
magnetic field
(only 1/4 shown)
TM010-mode
Round of sharp edges (to reduce field enhancement!)

## Slide 28: A (real) elliptical cavity
electric field
magnetic field
(only 1/4 shown)
TM010-mode

## Slide 29: Choice of frequency
Size:
  Linear dimensions scale as , volume as .
  amount of material, mass, stiffness, tolerances, …
  Outer radius of elliptical cavity .
Beam interaction:
  increases with – but also for HOMs!
  short bunches are easier with higher .
Technology:
  superconducting: BCS resistance .
  Power sources available?
  Max. accelerating voltage?

## Slide 30: Characterizing a cavity

## Slide 31: Acceleration voltage and
I define
The exponential factor accounts for the variation of the field while particles with velocity are traversing the cavity gap.
With this definition, is generally complex – this becomes important with more than one gap (cell).
For the time being we are only interested in .
The square of the acceleration voltage is proportional to the stored energy the proportionality constant defines the quantity called “R-upon-Q”:
Attention – different definitions are used in literature!
electric field

## Slide 32: Transit time factor
The transit time factor is the ratio of the acceleration voltage to the (non-physical) voltage a particle with infinite velocity would see:
The transit time factor of an ideal pillbox cavity (no axial field dependence) of height (gap length) is:
Field rotates by 360° during particle passage.

## Slide 33: Stored energy
The energy stored in the electric field is
The energy stored in the magnetic field is
Since and are out of phase, the stored energy continuously swaps from electric energy to magnetic energy.
On average, electric and magnetic energy must be equal.
In steady state, the Poynting vector describes this energy flux.
In steady state, the total energy stored (constant) is

## Slide 34: Stored energy and Poynting vector
electric field energy
Poynting vector
magnetic field energy

## Slide 35: Wall losses &
The losses are proportional to the stored energy .
The tangential on the surface is linked to a surface current (flowing in the skin depth ).
This surface current sees a surface resistance , resulting in a local power density flowing into the wall.
is related to skin depth as .
  Cu at has , leading to at 1 GHz, scaling with .
  Nb at has a typical at 1 GHz, scaling with .
The total wall losses result from .
The cavity (caused by wall losses) is defined as
Typical values:
  Cu at (normal-conducting): , improves at cryogenic by a factor .
  Nb at (superconducting):
No! Anomalous skin effect!
Only by a factor !

## Slide 36: Shunt impedance
The square of the acceleration voltage is proportional to the power loss .
The proportionality constant defines the “shunt impedance”
Attention, also here different definitions are used!
Traditionally, the shunt impedance is the quantity to optimize in order to minimize the power required for a given gap voltage.

## Slide 37: Geometric factor
With
and assuming an average surface resistance , one can introduce the “geometric factor” as
has dimension Ohm, depends only on the cavity geometry (as the name suggests) and typically is .
Note that (dimension , purely geometric)
is only used for SC cavities.

## Slide 38: Cavity resonator – equivalent circuit
Generator
Cavity
Z
: coupling factor
: shunt impedance
: R-upon-Q
Simplification: single mode
Beam

## Slide 39: Power coupling - Loaded
Note that the generator inner impedance also loads the cavity – for very large more than the cavity wall losses.
To calculate the loaded (), losses have to be added:
The coupling factor is the ratio .
With , the loaded can be written
For NC cavities, often is chosen (power amplifier matched to empty cavity); for SC cavities, .

## Slide 40: Resonance
While a high results in small wall losses, so less power is needed for the same voltage.
On the other hand the bandwidth becomes very narrow.
Note: a 1 GHz cavity with a of has a natural bandwidth of 0.1 Hz!
… to make this manageable, is chosen much smaller!
0

## Slide 41: Loss factor
Voltage induced by a single charge :
Cavity
Beam
V (induced)
Energy deposited by a single charge :
Impedance seen by the beam

## Slide 42: Summary: relations , and
acceleration voltage
𝑉_𝑎𝑐𝑐
acceleration voltage
wall losses
𝑃_𝑤𝑎𝑙𝑙
wall losses
Energy stored
𝑊
Energy stored
Attention – different definitions are used in literature !

## Slide 43: Beam loading
The beam current “loads” the cavity, in the equivalent circuit this appears as an impedance in parallel to the shunt impedance.
If the generator is matched to the unloaded cavity (), beam loading will (normally) cause the accelerating voltage to decrease.
The power absorbed by the beam is .
For high power transfer efficiency RF  beam, beam loading must be high!
For SC cavities (very large , the generator is typically matched to the beam impedance!
Variation in the beam current leads to transient beam loading, which requires special care!
Often the “impedance” the beam presents is strongly reactive – this leads to a detuning of the cavity.

## Slide 44: Multipactor
The words “multipactor”, “to multipact” and “multipacting” are artificially composed of “multiple” “impact”.
Multipactor describes a resonant RF phenomenon in vacuum:
  Consider a free electron in a simple cavity – it gets accelerated by the electric field towards the wall
  when it impacts the wall, secondary electrons will be emitted, described by the secondary emission yield (SEY)
  in certain impact energy ranges, more than one electron is emitted for one electron impacting! So the number of electrons can increase
  When the time for an electron from emission to impact takes exactly ½ of the RF period, resonance occurs – with the SEY>1, this leads to an avalanche increase of electrons, effectively taking all RF power at this field level, depleting the stored energy and limiting the field!
For this simple “2-point MP”, this resonance condition is reached at or . There exist other resonant bands.
courtesy: Sarah Aull/CERN

## Slide 45: Multipactor (contd.)
Unfortunately, good metallic conductors (Cu, Ag, Nb) all have SEY>1!
1-point MP occurs when the electron impact where they were emitted
Electron trajectories can be complex since both and influence them; computer simulations allow to determine the MP bands (barriers)
To reduce of suppress MP, a combination of the following may be considered:
  Use materials with low SEY
  Optimize the shape of your cavity ( elliptical cavity)
  Conditioning (surface altered by exposure to RF fields)
  Coating (Ti, TiN, NEG, C …)
  Clearing electrode (for a superimposed DC electric field)
  Rough surfaces

## Slide 46: Many gaps

## Slide 47: What do you gain with many gaps?
The of a single gap cavity is limited to some 100 Ω. Now consider to distribute the available power to identical cavities: each will receive , thus produce an accelerating voltage of . (Attention: phase important!) The total accelerating voltage thus increased, equivalent to a total equivalent shunt impedance of .

## Slide 48: Standing wave multicell cavity
Instead of distributing the power from the amplifier, one might as well couple the cavities, such that the power automatically distributes, or have a cavity with many gaps (e.g. drift tube linac).
Coupled cavity accelerating structure (side coupled)
The phase relation between gaps is important!

## Slide 49: Brillouin diagram; Travelling wave structure
synchronous
2p
speed of light line,
w = b /c
p
p/2
p
p/2
b L
0
0
p/2
p
2p/3

## Slide 50: The elliptical cavity
The elliptical shape was found as optimum compromise between
  maximum gradient ()
  suppression of multipactor
  mode purity
  machinability
Operated in -mode, i.e. cell length is exactly .
It has become de facto standard, used for ions and leptons! E.g.:
  ILC/X-FEL: 1.3 GHz, 9-cell cavity
  SNS (805 MHz)
  SPL/ESS (704 MHz)
  LHC (400 MHz)
At : , .
*): http://accelconf.web.cern.ch/AccelConf/SRF93/papers/srf93g01.pdf‎
D. Proch, 1993 *)

## Slide 51: Elliptical cavity – the de facto standard for SRF
FERMI 3.9 GHz
S-DALINAC 3 GHz
CEBAF 1.5 GHz
HEPL 1.3 GHz
TESLA/ILC 1.3 GHz
SNS ß=0.61,0.81, 0.805 GHz
HERA 0.5 GHz
KEK-B 0.5 GHz
CESR 0.5 GHz
LEP 0.352 GHz
cells
TRISTAN 0.5 GHz

## Slide 52: Practical RF parameters 1
Contour plot of
on the wall
on the wall
The ratio shows sensitivity of the shape to the field emission of electrons.
The ratio shows limit in Eacc due to the break-down of superconductivity (Nb ~190 mT).
Average accelerating gradient:
Contour plot of
courtesy: Jacek Sekutovicz/DESY

## Slide 53: Practical RF parameters 2
Both and are purely geometric parameters.
Like the shunt impedance , the product is a measure of the power loss for given acceleration voltage and surface resistance .
Minimize :
  operation at lower ,
  better surface cleanliness,
  lower residual resistance
Optimize geometry maximizing .
courtesy: Jacek Sekutovicz/DESY

## Slide 54: Single-cell versus multi-cell cavities
Advantages of single-cell cavities:
  It is easier to manage HOM damping
  There is no field flatness problem.
  Input coupler transfers less power
  They are easy for cleaning and preparation
Advantages of multi-cell cavities:
  much more acceleration per meter!
  better use of the power
  more cost-effective for most applications
courtesy: Jacek Sekutovicz/DESY

## Slide 55: Practical RF parameters 3
Cell-to-cell coupling will determine the width of the passbands in multi-cell cavities.
2p
p
p/2
p
p/2
b L
0
Brillouin diagram
courtesy: Jacek Sekutovicz/DESY

## Slide 56: Field flatness
Field amplitude variation from cell to cell in a multi-cell structure
Should be small for maximum acceleration.
Field flatness sensitivity factor for a structure made of cells:
  is related to the cell-to-cell coupling as and describes the sensitivity of the field flatness on the errors in individual cells.
courtesy: Jacek Sekutovicz/DESY

## Slide 57: Criteria for Cavity Design (1)
Here: Inner cells of multi-cell structures
Parameters for optimization:
  Fundamental mode: , , , , .
  Higher order modes: , .
The elliptical cavity design has distinct advantages:
  easy to clean (rinse)
  little susceptible to MP – can be conditioned …
Geometric parameters for optimization:
  iris ellipse half axes: , :
  iris aperture radius: ,
  equator ellipse half axes: ,
Problem: 7 parameters to optimize, only 5 to play with – some compromise has to be found!
courtesy: Jacek Sekutovicz/DESY

## Slide 58: Criteria for Cavity Design (2)
We see here that is a very “powerful” variable to trim the RF-parameters of a cavity.
Of course it has to fit the aperture required for the beam!
Criterion | RF parameter | Improves if | examples
high gradient operation |  |  | TESLA, CEBAF 12 GeV HG
low cryogenic losses |  |  | CEBAF LL
High | , |  | B-factory RHIC cooling LHeC
Criterion | RF parameter | Improves if | examples
high gradient operation |  |  | TESLA, CEBAF 12 GeV HG
low cryogenic losses |  |  | CEBAF LL
 |  |  | B-factory RHIC cooling LHeC
courtesy: Jacek Sekutovicz/DESY

## Slide 59: Effect of
ri = 40 mm ri = 20 mm
Ez (z) for small and big iris radius
Smaller allows to concentrate where it is needed for acceleration
courtesy: Jacek Sekutovicz/DESY

## Slide 60: Example: cell optimization at 1.5 GHz
A. Mosnier, E. Haebel, SRF Workshop 1991
courtesy: Jacek Sekutovicz/DESY

## Slide 61: Equator shape optimization
(and ) change when changing the equator shape.
courtesy: Jacek Sekutovicz/DESY

## Slide 62: Iris shape optimization
25 mm
20 mm
42 mm
42 mm
Both cells have the same: f, (R/Q) and ri
changes with the iris shape
courtesy: Jacek Sekutovicz/DESY

## Slide 63: Minimizing HOM excitation
HOMs loss factors ( , )
ri = 20mm
ri = 40mm
courtesy: Jacek Sekutovicz/DESY

## Slide 64: Cell-to-cell coupling
ri = 20mm
ri = 40mm
courtesy: Jacek Sekutovicz/DESY

## Slide 65: Scaling the frequency
fπ | [MHz] | 2600
R/Q | [Ω] | 57
r/q=(R/Q)/l | [Ω/m] | 2000
G | [Ω] | 271
fπ | [MHz] | 1300
R/Q | [Ω] | 57
r/q=(R/Q)/l | [Ω/m] | 1000
G | [Ω] | 271
x 2 =
courtesy: Jacek Sekutovicz/DESY

## Slide 66: Operating temperature
At the XFEL gradient, Qo is higher by 80% at 1.8 K
courtesy: Jacek Sekutovicz/DESY

## Slide 67: Historic evolution of inner cell geometry
ri | [mm] | 35 | 30 | 30
kcc | [%] | 1.9 | 1.56 | 1.52
Epeak/Eacc | - | 1.98 | 2.30 | 2.36
Bpeak/Eacc | [mT/(MV/m)] | 4.15 | 3.57 | 3.61
R/Q | [Ω] | 113.8 | 135 | 133.7
G | [Ω] | 271 | 284.3 | 284
R/Q*G | [Ω*Ω] | 30840 | 38380 | 37970
k┴ (σz=1 mm) | [V/pC/cm2] | 0.23 | 0.38 | 0.38
k║ (σz=1 mm) | [V/pC] | 1.46 | 1.75 | 1.72
Re-entrant optimized
Bpeak/Eacc
LL optimized
Bpeak/Eacc
TESLA optimized
Epeak/Eacc
1992
2002/04
2002/04
Example: ILC
courtesy: Jacek Sekutovicz/DESY

## Slide 68: Cavity optimization example
courtesy: Frank Marhauser/JLAB

## Slide 69: Higher order modes
IB
R3, Q3,w3
R2, Q2,w2
R1, Q1,w1
...
...
external dampers
n1
n3
n2

## Slide 70: Pillbox: 1st dipole mode
electric field
magnetic field
(only 1/4 shown)
TM110-mode

## Slide 71: Panofsky-Wenzel theorem
For particles moving virtually at , the integrated transverse force (kick) can be determined from the transverse variation of the integrated longitudinal force!
W.K.H. Panofsky, W.A. Wenzel: “Some Considerations Concerning the Transverse Deflection of Charged Particles in Radio-Frequency Fields”, RSI 27, 1957]
Pure TE modes: No net transverse force !
Transverse modes are characterized by
the transverse impedance in ω-domain
the transverse loss factor (kick factor) in t-domain !

## Slide 72: CERN/PS 80 MHz cavity (for LHC)
inductive (loop) coupling, low self-inductance

## Slide 73: Higher order modes
Example shown:
80 MHz cavity PS for LHC.
Color-coded:

## Slide 74: Higher order modes (measured spectrum)
without dampers
with dampers

## Slide 75: 7-cell 1.3 GHz structure for BERLinPro
Galek et al.: IPAC2013
Band diagram (top) and Q-factors (bottom)
Reminder:
0-mode -mode

## Slide 76: HOMs: Example 5-cell cavity
First passbands of HOMs typically dangerous
courtesy: Rama Calaga/CERN

## Slide 77: HOM dampers
Ferrite absorbers: broadband damper, room temperature
Waveguides: better suited for higher frequencies (size!)
Notch filters: narrow-band; target specific mode
Multi-cell cavities require broadband dampers
More tomorrow by Guillaume Devanz!
ferrite absorber
waveguides
notch filter
bandpass filter
double notch

## Slide 78: Tuners

## Slide 79: Small boundary perturbation
V
Perturbation calculation is used to understand the basics for cavity tuning – it is used to analyse the sensitivity to (small) surface geometry perturbations.
  This is relevant to understand the effect of fabrication tolerances.
  Intentional surface deformation or introduced obstacles can be used to tune the cavity.
The basic idea of the perturbation theory is use a known solution (in this case the unperturbed cavity) and assume that the deviation from it is only small. We just used this to calculate the losses (assuming would be that without losses).
The result of this calculation leads to a convenient expression for the (de)tuning:
V
ΔV
unperturbed:
perturbed:
Slater Theorem

## Slide 80: Lorentz force detuning
The presence of electromagnetic fields inside the cavity lead to a mechanical pressure on the cavity.
Radiation pressure:
Deformation of the cavity shape:
Frequency shift: ; typical:
This requires good stiffness – and the possibility to tune rapidly!

## Slide 81: Tuner principle
Slow tuners:
  compensate for mechanical tolerances,
  realized with stepper motor drives
Fast tuners:
  compensate Lorentz-force detuning and reactive beam loading
  realized with piezo crystal (lead zirconate titanate – PZT)
Tuning of SC cavities is often realized by deforming the cavity:
courtesy: Eiji Kako/KEK

## Slide 82: Blade tuner
Developed by INFN Milan
Azimuthal motion transferred to longitudinal strain
Zero backlash
CuBe threaded shaft used for a screw nut system
Stepping motor and gear combination driver
Two piezo actuators for fast action
All components in cold location
courtesy: Eiji Kako/KEK

## Slide 83: “Saclay” lever-arm tuner
Developed by DESY based on the Saclay design
Double lever system (leverage 1.25)
Cold stepping motor and gear combination
Screw nut system
Two piezo actuators for fast action in a preloaded frame
All components in cold location
courtesy: Eiji Kako/KEK

## Slide 84: Slide-jack tuner
Developed by KEK for STF cryomodule
Slide-jack mechanism
Single high voltage piezo actuator for fast action
Warm stepping motor for easy maintenacne
Access port for replacing piezo
courtesy: Eiji Kako/KEK

## Slide 85: FPC (Fundamental Power Coupler)

## Slide 86: Magnetic (loop) coupling
The magnetic field of the cavity main mode is intercepted by a coupling loop
The coupling can be adjusted by changing the size or the orientation of the loop.
Coupling:
coupling loop
courtesy: David Alesini/INFN

## Slide 87: Electric (antenna) coupling
The inner conductor of the coaxial feeder line ends in an antenna penetrating into the electric field of the cavity.
The coupling can be adjusted by varying the penetration.
Coupling
antenna
courtesy: David Alesini/INFN

## Slide 88: Fundamental Power Coupler – FPC
The Fundamental Power Coupler is the connecting part between the RF transmission line and the RF cavity
It is a specific piece of transmission line that also has to provide the cavity vacuum barrier.
FPCs are amongst the most critical parts of the RF cavity system in an accelerator!
A good RF design, a good mechanical design and a high quality fabrication are essential for an efficient and reliable operation.
More tomorrow by Guillaume Devanz!
LHC FPC
SPL FPC
HL-LHC FPC
courtesy: Eric Montesinos/CERN

## Slide 89: Cavity Fabrication techniques

## Slide 90: Materials
Selection criteria
  Electrical conductivity
  Secondary emission yield (SEY)
  mechanical stiffness/hardness (at cryogenic )
  thermal conductivity, thermal expansion
  machining & joining techniques
  vacuum tight, low outgassing rate
  creep resistance,
  magnetic permeability
  radiation hardness
  fatigue stress
  …
Important: specify what you need and what you can measure/control at reception!

## Slide 91: Niobium
Magnets use NbTi or Nb3Sn, SC Cavities use mainly Nb!
Pure Nb has a high critical magnetic field ()
Nb has a high transition temperature ().
It is chemically inert (surface covered by oxide layer)
It can be machined and deep-drawn
It is available as bulk and sheet material in any size, fabricated by forging and rolling
Large grain sizes (often favoured) obtained by e-beam melting
Instead of bulk or sheet Nb, Nb can also be coated (e.g. by sputtering) on Cu – CERN has built the LEP, LHC and HIE-Isolde cavities with this technique. Advantages: thermal stability, material cost, optimisation of possible; disadvantages: difficult technology to master, lower .
Nb ingot after EBM at Heraeus (D)

## Slide 92: Dielectrics
Aluminium oxide, AL2O3, aka Alumina, is often used in vacuum/RF windows and vacuum feed-throughs.
Isostatically pressed AL2O3 is used for leak-tightness (LEP power couplers, e.g.).
To reduce multipactor, it is often coated with titanium or titanium nitride (TiN).
Other window materials: Sapphire, BeO, quartz, diamond …)
Silicon carbide (SiC), C-loaded AlN have been effectively used as RF absorbers inside vacuum.
Different ferrites are used as absorbers and to use their variable magnetic permeability.
Coax transition through alumina window with traces of breakdown

## Slide 93: Fabrication of Nb sheets at
Nb ingot
Pressing
1st EB melting
2nd, 3rd … EB melting
Separate from base plate
Forging
Milling
Rolling
Polishing
Rolling
Cutting
Annealing
Levering
Chemical polishing
Inspections: (ICP-AES, Gas analysis, RRR, grain size, hardness tensile stress …)

## Slide 94: Other forming techniques
Forging, pressing, deep drawing, …
Spinning, planing, rolling, …
lapping, polishing, electropolishing, …
Electroforming, hydroforming, explosion forming
Powder metal techniques, additive manufacturing (3-D printing)
Sputtering
seamless cavity: e.g. back extrusion
back-extruded Nb tubes for E-XFEL
courtesy: Waldemar Singer/DESY

## Slide 95: Joining techniques
TIG welding
double joint: inner for vacuum,
out for mechanical stability
EB welding
Microstructure of the EB welding area grain size (50 ÷ 2000) μm

## Slide 96: Established cavity fabrication
Half cells are shaped by deep drawing.
Dumb bells are assemled by electron beam welding.
After proper cleaning eight dumb bells and two end group sections welded by electron beam together
Important: clean conditions on all steps
shape accuracy, preparation and EB welding
courtesy: Waldemar Singer/DESY

## Slide 97: Advances in SCRF Technology
Preparing for EP (inserting cathode)
Clean room assembly (JLAB)
Photos: Rongli Geng
C. Antoine: CAS SC 2013
Stay tuned for A. Romanenko’s lecture on Sat.!

## Slide 98: Thank you very much!