## Slide 1
Monte Carlo optimization of a next-generation ultracold-neutron source
Wolfgang Schreyer
for the TUCAN collaboration
2017-10-18, nEDM 2017, Harrison Hot Springs

## Slide 2
Design parameters
Optimization
  FLUKA
  MCNP
  PENTrack
Preliminary optimization results

## Slide 3: Design parameters
Spallation source
  Combination of neutron moderators
  Radiation shielding
Superfluid-helium converter
  Heating by γs, neutrons, β electrons
  Upscattering lifetime τup = 130K7s · T-7
Geometry of ultracold-neutron guides
Target 480 MeV p
He-II
(1K)
γ fast n

## Slide 4: Optimization
Starting geometry:
Best use of symmetry
Cylindrical aluminum vessels centered on target
Lead shielding
Beamline
Graphite
reflectors
D2O (300 K)
LD2 (20 K)
He-II
(1 K)
80 cm
Ø 80 cm
Light-water-cooled
Tungsten target
Ø 80 cm

## Slide 5: FLUKA
fluka.org (Free)
Monte Carlo simulation of particle transport in matter
Including multi-group transport of low-energy neutrons
Neutron-scattering models for many isotopes at 296K, some at 87K and 4K
Geometry as combination of basic shapes
Easy to use thanks to flair (geometry builder, plotter)
Can output particle flux in volume/over surface, production of radioactive nuclei, deposit of prompt and decay heat

## Slide 6: MCNP
mcnp.lanl.gov
Much more detailed nuclear-scattering data
Including many specialized neutron moderators
Combinatorial geometry, can be exported from flair
Detailed output of particle flux in volume/over surface, heat deposit, binned in energy, time, and direction
Text-only configuration

## Slide 7: Comparison FLUKA and MCNP
FLUKA has no scattering data for liquid deuterium at 20K
Good agreement between MCNP/FLUKA for free-gas model at 87K
Cold-neutron flux 10 times higher with 20K deuterium in MCNP

## Slide 8: Optimization with MCNP
Goal: maximize number of UCN available to experiment
Constraints:
  Cooling power at 1K: ~10W
  Amount of cold moderators (liquid deuterium!)
Simple model: maximize UCN production per heat P/Q
Detailed model: maximize P·τ with 1/τ = 1/τup(Q) + 1/ τwall + 1/ τβ

## Slide 9: Optimization with MCNP
Individually optimize
  Thicknesses of moderators
  Size of He-II bottle
  Target position
Iterate several times
Manage config-urations with git
Ca. 15min runtime for each configuration on ComputeCanada cluster (100,000 p)
Graphite He
LD2
D2O
Lead

## Slide 10: Optimization with MCNP
Lead layer above target
He-II
LD2
D2O
Lead

## Slide 11: Optimization with MCNP
D2O layer above target
He-II
LD2
D2O
Lead

## Slide 12: Optimization with MCNP
LD2 layer above target
He-II
LD2
D2O
Lead

## Slide 13: Optimization with MCNP
Radial LD2 layer
He-II
LD2
D2O
Lead

## Slide 14: Optimization with MCNP
Trade-off between D2O and LD2 layer above target
He-II
LD2
D2O
Lead

## Slide 15: Optimization with MCNP
Height and radius of He-II bottle
using improved model: P·τ with 1/τ = 1/τup(Q) + 1/ τwall + 1/ τβ

## Slide 16: Preliminary results
Radial LD2 layer more important than lower
Best He-II-bottle height 30-40 cm, radius 15-20 cm (for current cooling scheme)
Limited by amount of LD2!
For He-II height 30 cm, radius 15 cm, 40 μA beam:
  20.6 l He-II, 115 l LD2
  3.9·107 UCN/s
  7.9 W max. heat in He-II
  65 W max. heat in LD2
Best strategy to reduce LD2: reduce He-II size and go closer to target
16 cm
6 cm
15
7 cm 10
16 cm
13 cm
He-II
LD2
D2O
Lead

## Slide 17: PENTrack
Self-developed Monte Carlo simulation for UCN (+protons, electrons, comagnetometer atoms)
Interactions:
  Fermi-potential formalism, microroughness model
  Magnetic moment in strong magnetic fields
  Precession of spins in weak magnetic fields
  Fully relativistic equations of motion, BMT equation
Geometry directly imported from CAD, time-dependent (valves, etc.)
Magnetic/electric field maps imported from FEM
Open source: github.com/wschreyer/PENTrack.git
Description: 10.1016/j.nima.2017.03.036

## Slide 18: Optimization with PENTrack
Steve Sidhu & Patricia Gnyp:
Optimize geometry of UCN guides
Compare storage and extraction time for different bottle shapes

## Slide 19: Optimization with PENTrack

## Slide 20: Optimization with PENTrack
Tatsuya Kikawa:
Optimize vertical extraction height
Steady-state mode vs. batch mode

## Slide 21: Optimization with PENTrack
Tatsuya Kikawa:
Optimize vertical extraction height
Steady-state mode vs. batch mode

## Slide 22: Preliminary results
Vertical extraction of 50-100 cm seems best for nEDM experiment
Work in progress, many unknown parameters
  He-II temperature
  Wall lifetime

## Slide 23: Next steps
More realistic source
  UCN guides
  Heat exchanger, 3He
  Cryostat
  Shapes of pressure vessel
Optimize shielding
  Heat deposition in heat exchanger
  Activation of cryostat
3He heat exchanger
UCN guide
Shielding

## Slide 25: Delayed-heating model
Decay constant ~200 s
Assume 25% duty cycle 1 min beam, 3 min no beam
Use min./max. heat after 5 irradiations

## Slide 26: Detailed storage-time model
Detailed model: maximize P·τ with 1/τ = 1/τup(Q) + 1/ τwall + 1/ τβ
τup(Q) ~ Q-1.2 to Q-1.4