## Slide 1: Development a High Intensity Ultra-Cold Neutron Source using Superfluid Helium at TRIUMF
Shinsuke Kawasaki (KEK)
for the TRIUMF Japanese-Canadian UCN Collaboration

## Slide 2: outline
Ultra-Cold Neutron (UCN)
UCN production by super thermal method
  storage time
3He cryostat
UCN source at TRIUMF
  Vertical source <- was discussed by R. Matsumiya yesterday
  new UCN source
    with high cooling power
    cooling scheme
      temperature distribution
    UCN production figure of merit as a function temperature
Summary

## Slide 3: Ultra Cold Neutron (UCN)
Ultra Cold Neutron
Energy ～ 100 neV
Velocity ～ 5 m/s
Wave length ～ 50 nm
Interaction
Gravity 100 neV/m
Magnetic field 60 neV/T
Weak interaction
β-decay n → p + e
Strong interaction
Fermi potential 335 neV (58Ni)
  atom distance : ~ Å
  UCN feels average nuclear potential
UCN can be confine material bottle
→Use various experiments

## Slide 4: UCN production by super fluid Helium
Feature of our source
・spallation neutron
High neutron flux
  small distance between target and UCN production volume
・Super-fluid Helium converter
long storage lifetime
up-scattering by phonon
  τs = 600 s at THeII = 0.8 K
  τs = 36 s at THeII = 1.2 K
  1⁄ τs ∝ 𝑇7
UCN procution
spallation neutron
↓ D2O, LD2 Moderator (300K, 20K)
cold neutron ～meV
↓ Phonon scattering in He-II
Ultra cold neutron ～100neV

## Slide 5: UCN Storage Life Time
UCN Storage Life Time
τabs : absorption by 3He 3He/4He <10-11
τup-scat : phonon up-scattering ∝T-7
τwall : wall loss clean surface
τβ : β decay (886s)
UCN density
= Pτ (1 – exp(-t/τ))
P : UCN production rate ∝ cold neutron flux
τ : Storage time
t : proton irradiation time
large cold neutron flux
long τ
are important
UCN density during proton irradiation
UCN Storage Time measurement
at RCNP

## Slide 6: 3He cryostat
to keep He-II temp. 1.0K
decompressed Helium 3
3He vs 4He
  vapor pressure @ 0.8K
    3He: 9 Torr
    4He: 0.1 Torr
  cooling power
  @ 1.0 K with 10, 000 m3/hour pumping
    3He: 48 W
    4He: 1.1 W
  Cooling power depend on temperature
    larger vapor pressure in higher temperature
3He cooling
  evaporated 4He gas
  liquid He bath 4.2K
  1K pot (4He pumping) 1.4K
  3He pumping < 1.0K
Helium flow diagram

## Slide 7: UCN Source @ TRIUMF
Major Milestone
✓- 2016 proton beam line for UCN source(BL1U 500MeV, 40μA)
✓2016 commissioning proton beam line and cold neutron production
2017 UCN production by Vertical source (~ 1μA)
- 2020 High intensity UCN source (40μA)
Kicker
2015
2015 shutdown
2014 shutdown
2017 shutdown
Septum Magnet
Bender
BL1A
BL1U
W target
remote handling
Q Magnet
UCN Source
2016 shutdown

## Slide 8: Vertical UCN source
Vertical UCN source
  developed at RCNP
    THe-II : 0.8 K
    UCN life time: 81 sec
    UCN density: 9 UCN/cm3
      400 MeV × 1 μA = 0.4 kW
Y, Masuda et. al., Phys. Rev. Lett. 108, (2012), 134801
  move to TRIUMF
    modification for safety requirement
  2017 Jan. – Apr. install at Meson hall
  2017 Nov. UCN production

## Slide 9: new UCN source
proton beam power
0.4 kW at RCNP -> 20 kW at TRIUMF
A new helium cryostat which has high cooling power is necessary
Heat load on He-II depends on geometry
distance between target and He-II
cold moderator
gamma shield and so on
higher cold neutron flux cause higher heat load
ratio of this is constant in some region
Optimization is necessary

## Slide 10
5 – 9 times large cold neutron flux is achivable compared with ice D2O

## Slide 11: UCN Production Figure of Merit ideal case: 3He temperature is same as UCN production volume
UCN density ρ ∝ P x τ
  P : production rate
  ∝ cold neutron flux
  ∝ heat load
  = cooling power ( function of T)
  ∝ Vapor pressure * latent heat
  τ : UCN life time
    1/τ = 1/τβ + r*1/τupscat + 1/τwall
      τβ = 880s
      τupscat ∝ T-7
      1/τwall : ~100sec (depend on surface quality)
Figure of Merit (FOM) as a function of T
FOM = Cooling power x τ
a.u.

## Slide 12: In Reality
There is temperature difference between UCN production volume and 3He
  UCN lifetime
    temperature at UCN production volume
  cooling power
    3He temperature
The temperature difference is caused by following reason
  deposit heat at UCN production volume
  Heat transfer in He-II
  Kapitza conductance of heat exchanger

## Slide 13: Heat load on UCN production volume
Will be discussed by S. Wolfgang
deal with such a huge heat load around 1 K

## Slide 14: Heat transfer between heating point and cooling point
Heat transfer in He-II
  below 1 K, heat transfer is not good because of low fraction of normal fluid which convey heat (two fluid model)
Kapitza conductance of heat exchanger
  Conductance at the surface between liquid and solid is small at low temperature
3He pumping
heat deposit
Heat exchanger

## Slide 15: Superfluid Helium
 | Normal fluid | Superfluid
Viscosity | Ηn | ηs = 0
Entropy | Sn | Ss = 0
10.1103/Physics.3.5
Heat transport
Since superfluid has no entropy, heat is transported only by normal fluid.
Heat transport in low temperature (< 1K) become small because of small fraction of normal fluid
Two Fluid Model
Heat source
vn
vs
Ratio of super/normal component depends on temperature dependence.
fraction of normal mode become small in low temperature.

## Slide 16: Gorter-Mellink Equation
f(T)-1 : Heat transfer function of He-II based on Two fluid model

## Slide 17
Temperature difference in He-II
Chart: Temperature increase in He-II 10 W heat load
| 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2
Φ100 mm | 1.1967 | 1.1971 | 1.1994 | 1.2105 | 1.2453
Φ150 mm | 1.0442 | 1.0477 | 1.0662 | 1.1206 | 1.2053
Φ200 mm | 0.95194 | 0.96679 | 1.0187 | 1.1043 | 1.201
L = 1000mm
A : cross section of He-II
L : distance of heat transfer

## Slide 18: Kapitza Conductance
Kapitza conductance, hK(T) is a function of temperature.
There are several theory on Kapitza conductance.
  Phonon limit
    hK(T) ~ 4500 T3 [W/m2K]
      2 - 10 times larger than measured
  Khalatnikov theory
    hK(T) ~ 20 T3 [W/m2K]
      10 - 100 times smaller than measured
Experimental data strongly depends on surface quality
  plan to measure Kapitza conductance of material before fabricating a heat exchanger
Kapitza conductance
between Copper and He-II
Helium cryogenics, Steven W. Van Sciver
Phonon limit
  Khalatnikov theory
experimental
data

## Slide 19: Heat exchanger
Cu Heat exchanger should be plated by Ni
Kapitza conductance between Cu-Ni is large enough since junction is solid-solid
Kapitza conductance between Ni and He-II
hK Ni (T) = f*h_KK_Cu(T) f = 0.61
Kapitza conductance between Cu and 3He
hK(HeII) = ( 1.2 – 2.6 ) hK(3He)
ex) average quality of Cu, 10 W heat load
junction between He-II and Ni
  hK Ni (1.0K) = 244 [w/m2 K]
  ΔT He-II – Ni = 0.16 K
  T Ni = 0.84 K
junction between Cu and 3He
  hK Ni (0.84K) = 232 [w/m2 K]
  ΔT He-II – Ni = 0.09 K
  T 3He = 0.75 K
He-II
3He liq.

## Slide 20: Equilibrium temperature
Equilibrium temperature can be calculated as a function heat load.
example)
d = 150 mm, L = 1,000 mm
pumping speed 10,000 m3/hour
Heat load : 10 W case
Temperature distribution
  THe-II H : 1.06 K (τup-scat = 87 sec)
  THe-II L : 1.00 K
  TCu H : 0.84K
  TCu L : 0.83 K
  T3He : 0.75 K
  ΔT = 0.31 K
THe-II H
THe-II L
T3He
Cu Heat Exchanger

## Slide 21: FOM in real case
temperature increase between UCN production volume and 3He is take into account
L = 1000mm, d = 150 mm
FOM = Cooling power x τ
FOM (a.u.)
0.87
0.80
0.65
340
4.1
0.97
0.90
0.69
160
6.1
1.07
1.00
0.75
58
9.8
1.25
1.20
0.87
11
22
1.34
1.30
0.92
6
31
THe H
THe L
T3He
1.15
1.10
0.81
24
15
Temperature [K]
τup-scatt [s]
cooling power [W]

## Slide 22: Effect of He-II Volume ratio
Volume ratio of He-II and Vacuum is also important parameter.
Total lifetime is increase when volume ratio is small
UCN scattering with vapor He become serious when He-II temperature above 1.4 K

## Slide 23: He-II cryostat
A new He-II cryostat is been developing
  TRIUMF proton beam line BL1U
  500 MeV × 40 μA = 20 kW
  necessary cooling power is around 10 W at 1.0 K
  Heat conductance is important
    inside He-II
    Kapitza conductance between He-II/3He and heat exchanger
  FOM can be calculated as a function of temperature
  FOM = cooling power × UCN life time
  Optimum working temperature is around 1.0 – 1.2K

## Slide 24: Second UCN port : Y switch
Bend is necessary for radiation protection
  not to see target area directly
Y switch can be diverted UCN to another area.
  R&D for UCN guide, detector and so on
  open for user facility in future

## Slide 25: Summary
We will start UCN production with vertical UCN source comes from RCNP
  limit of proton beam power is ～0.5 kW due to small cooling power
High intensity UCN source is been developed
  proton beam power : 500 MeV * 40 μA = 20 kW
  new 3He cryostat with higher cooling power
    necessary cooling power : ~10 W at 1.0 K
  FOM can be calculated as a temperature
    optimum temperature is 1.0 – 1.2 K
  Final optimization is on going
    > 2.3×107UCN/sec.
    > 600 UCN/cc at EDM cell -> statistical error of 10-27 ecm / 100 MT day
  Plan to produce UCN from 2020