## Slide 1: The TUCAN next generation UCN source overview and some details
R. Picker

## Slide 2
Topics
UCN source key numbers
Source components and model
Schedule
Monte Carlo Optimization of UCN components
Gas handling systems, pumps and transfer line
Manpower:
C. Davis, B. Franke, C. Gibson, K. Hatanaka, T. Higuchi, S. Horn, S. Kawasaki, S. Imajo, T. Kikawa, A. Konaka, F. Kuchler, T. Lindner, Y. Makida, R. Mammei, C. Marshall, J.W. Martin, R. Matsumiya, K. Mishima, T. Okamura, R. Picker, D. Rompen, W. Schreyer, S. Sidhu, S. Vanbergen

## Slide 3
TUCAN UCN source recipe
using the prototype source as example
480 MeV protons on tungsten create spallation neutrons
lead, graphite, heavy water, (deuterium) moderate fast neutrons (MeV) to cold neutrons (meV)
4He at around 1 K converts 1 meV (9Å) neutrons to UCN
Extraction to experiments via material guides
300 K D2O
solid
D2O 10 K
4He <1 K
UCN
lead
graphite
graphite
tungsten
protons
1.2 m

## Slide 4
Vertical UCN source cryostat cooling scheme
from KEK/RCNP, Japan
Ryohei Matsumiya, Shinsuke Kawasaki
 Running nominally at 1 µA beam (as at RCNP).
3 cooling stages, heat exchanger to cool isopure 4He UCN converter
lHe bath cryostat (4.2 K)
4He pumping section (1.6 K)
3He pumping section (< 1.0 K)
Isopure 4He UCN converter cooled via heat exchanger
W. Schreyer, tomorrow

## Slide 5
TUCAN Next generation UCN source strategy
lead
tungsten
protons
UCN, vacuum valve
vacuum sep. foil
300 K
20 K
1.1 K
LHE
level
Similar basic layout with major improvements:
5
Parameter | Prototype source | Next gen source
Beam current | 1 μA | 40 μA (480 MeV)
Production volume | 8 L | 27 L
Cold moderator | sD2O | LD2
Production rate | 2x105 /s | 1.4-1.6x107/s (500 s-1cm-3)

## Slide 6
TUCAN Next generation UCN source strategy
lead
tungsten
protons
UCN, vacuum valve
vacuum sep. foil
300 K
20 K
1.1 K
LHE
level
Similar basic layout with major improvements:
6
Parameter | Prototype source | Next gen source
Beam current | 1 μA | 40 μA (480 MeV)
Production volume | 8 L | 27 L
Cold moderator | sD2O | LD2
Production rate | 2x105 /s | 1.4-1.6x107/s (500 s-1cm-3)
Cooling power | 0.3 W | 10 W
He-II temperature | 0.9 K | 1.1 – 1.15 K
Extraction | Vertical by 1.2 m | Near horizontal 0.3 m up
Vacuum separation | No foil | Warm vacuum sep foil + B field
Position of cryostat | On top of source | 2.5 m away

## Slide 7
Next generation UCN source basics
lead
tungsten
protons
UCN, vacuum valve
vacuum sep. foil
300 K
20 K
1.1 K
LHE
level
B4C liner
 2.5 m
(HEX)
|B|

## Slide 8
Main challenges and solutions
Large cold flux in UCN production volume  D2O, LD2 moderators, graphite reflector
Large thermal load from spallation source  lead shield plus geometry optimization
More material, more heat  near-spherical shape of UCN production volume
Large cooling power below 1 K  pumping on 3He (10000 m3/h  10 W)
Incompatibility of 3He with UCN  UCN friendly 3He-4He heat exchanger (flat surface inside)
3He very expensive  staged HEX approach and “cheap” 3He?
Kapitza resistance large at 1 K  large HEX surface (approx. 0.3 m2)
Cannot put cryostat right on top of target  UCN guide heat conduction channel (2.5 m long)
Low heat conductivity of He-II at 1 K  large UCN guide diameter (15 cm)
Freeze-out on cold vacuum separation foil  warm vacuum separation foil (inside B field)
Containment of liquid helium  (small) vertical rise in liquid filled UCN guide (23 cm)
Limited supply of liquid helium  design efficient cryostat
Large amount of deuterium required  inherent and/or redundant safety systems (safety approval)
Radiative heat input to SF LHE surface  testing UCN friendly radiation heat suppressors
C. Marshall
W. Schreyer
C. Marshall
W. Schreyer
S. Kawasaki
S. Kawasaki
S. Kawasaki
S. Kawasaki
RP
This presentation
S. Kawasaki, C. Gibson
Covered in presentations by
C. Marshall
https://doi.org/10.1016/j.nima.2020.163525
S. Kawasaki
S. Kawasaki
RP, W. Schreyer

## Slide 9
vacuum separation foil
UCN beam switcher
More detailed UCN source model
moderators,
tail section
LD2 cryostat
He cryostat
cryo connection box
9

## Slide 10
The source in the Meson hall
proton beamline 1U
proton beamline 1A
cryostat pit
target pit
pump pit
10

## Slide 11
Installations here have to happen while BL1A is offline (mainly shutdown).
Installations here can take place while BL1A is running.
Installations here can take place while UCN is running.
Top view
proton beamline 1U
proton beamline 1A
cryostat pit
target pit
pump pit
11
 10 m
BL1A shielding envelope
UCN shielding envelope

## Slide 12
Some estimates for relevant numbers
Mostly coming from MC (MCNP, PENTrack)
TUCAN source
(engineering stage)
Production 1.4-1.6 x 107 UCN/s
Source helium temp 1.03 K to 1.13 K
Cooling power 10 W (3He fridge)
Source storage lifetime 28 s
Figure of merit P = 4.5 x 108
Density in the source 3 x 103 UCN/cc
Total number in the source 3 x 108 UCN
Initial polarized density in 70 l EDM experiment 200 UCN/cc (> 10 m of guide)
Counted at the end of cycle 2 x 106

## Slide 13
Summer 2018
JSPS (Japan Society for the Promotion of Science) funding for the helium cryostat has been grantedat 152 MJPY.
Final decision to go for 3He cryostat (not 4He direct pumping).
Initial System Engineering Design (System Block Diagram, Top level Requirements, nEDM Experiment Requirements, He Cryostat Requirements, LD2 Subsystem Requirements, Initial Spec Sheetsgeneration)
Preliminary LD2 Safety Report Released
Initial release of UCN yield versus moderator and source design report
Released designs for UCN experiments in Fall 2018
Released schematics (P&IDs) for He-II Subsystem, LD2 Subsystem
Released initial design concept for biological shielding
Fall 2018
Tested first components for the new UCN source during 1-month of UCN beamtime at TRIUMF (UCN friendly vent port, UCN source valve, superconducting polarizer)
Performed UCN storage tests with a mock-up UCN production volume (NiP coating on aluminum) and determined that a bake out temperature of 100 C is sufficient.
Liquid deuterium system conceptual design received positive concept review from the safety authority Technical Safety BC.
Additional requirements documents released: He-II Subsystem, Simultaneous Spin Analyzer Subsystem
Some cryogenic calculations completed for He-Cryostat and LD2 Subsystem
Winter 2019
Additional requirements documents released: remaining source subsystems, nEDM Cell, UCN Guidance
Initial 3D concept of LD2 Subsystem
Initial stress calculations and 3D Model for the multi-layered source vessel containing LD2 and superfluid helium
Early orders for D2O
Spring 2019
Finished the bulk of UCN and cryogenics related calculations necessary to start detailed design.
Measurements at KEK confirm the Kapitza conductance at the 3He to 4He heat exchanger is in good agreement with our models.
Additional requirements documents released: Internal magnetometry
TRIUMF design review of biological shielding passed.
TRIUMF design review of He cryostat pumping system passed
Positive initial discussions with Technical Safety BC about LD2 system safety
Hemispherical production volume and moderator geometry chosen
Summer 2019
Target protect monitor (TPM) of BL1U commissioned
Detailed design of helium cryostat completed, start of production in Japan.
Confirm superleak tightness of a new designed helicoflex seal flange at KEK (it will be used for junction of the HEX1, which is the main heat exchanger, and the UCN guides.
Confirm superleak tightness of a junction of aluminum and stainless steel at KEK (it will be used for UCN guide upstream of the helium cryostat)
HEX7 test successfully completed at KEK (counterflow gas heat exchanger from room temperature to 10 K)
Fall 2019
UCN source storage valve upgrade tested successfully during UCN beamtime.
TRIUMF design review of He cryostat passed.
Important interfaces between He cryostat and remainder of He-II subsystem confirmed
UCN Y switch completed
Winter 2020
HEX5 test successfully completed at KEK (counterflow gas heat exchanger in the 1K pot pumping tube)
Recent Milestones
copied from https://ucn.triumf.ca/meetings-and-workshops/review-meetings/2020-02-eac-review-meeting/documentation-for-eac-review/New_UCN_Source_Status_2020-2019-12-20.pdf

## Slide 14
Mini Shutdown
Mini Shutdown
Main Shutdown
Main Shutdown
UCN source schedule
Calendar Year |  | 2020 |  |  |  |  |  |  |  |  | 2021 |  |  |  |  |  |  |  | 2022 |  |  | 
 |  | 1 |  |  | 4 |  | 7 |  | 10 |  | 1 |  | 4 |  | 7 |  | 10 |  | 1 |  | 4 | 
Vertical UCN source |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Shielding |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
He cryostat |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Moderators, tail section |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Cryo conn, LD2 cryost. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
He pumping system |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Services | LD2, 3He, nat He, Isopure handling system |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Slow control |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
UCN handling |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
BL1U |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
UCN?
Detailing
Construct (Torisha)
ship
uninstall
Inst
Construct, procure
prepare
moderator
region
KEK tests
Assemble
Construct, procure
Install
Detailing
Install LD2
Construct
Assemble
Install
Detailing
Construct
Assemble
Cryo testing
Plan
Procure
Assemble, connect, program
Detailing
Build, procure
Install
UCN
lift
Inst
lift
Inst
Maintenance, repairs, upgrade
Inst
to allow BL1
operation
to allow BL1U operation
Tender
Procure
Test
Install
Gray shaded systems are inside the biological shielding.
Beamspot calcs
beam
tests
Target cask detailing
Construct
Test
Inst
Inst Cryo Conn Box
including moderators
Concept
Uninstall?

## Slide 15
UCN source test plan
General remarks
Planned test campaigns
He cryostat components are tested pre-assembly at KEK (2019/2020)
Extensive cryo testing of all components planned for 2021
He cryostat can be cooled down without cooling LD2 system
Currently developing a more detailed installation and testing plan
LD2
LD2 handling system test with N2
LD2 cryostat cooldown
He cryostat
Cryo testing at KEK (no 3He)
1K pot pumping
3He pot pumping, probably with 4He first
HEX1 only test (if possible)
Connect tail section
Connect downstream UCN guide

## Slide 16
Optimizing the UCN handling from source to EDM
Starting point
Steps:
Well known statistical sensitivity formula
Naively one thinks you can only improve Ndet by improving the geometry using UCN MC simulations…
… but the energy spectrum also influences the optimal and more…
Perform three separate MC simulations (relevant durations)
  Simulate filling of EDM cells from UCN source (
  Simulate storage in EDM cells )
  Simulate emptying of EDM cells to detectors ()
Calculate for one cycle
  Inputs: T1, T2, detector efficiency etc
Calculate number of cycles needed for cm
Calculate required calendar days
  Inputs: a certain up time per day (16 hr), degaussing time, E field reversal etc
Then vary the four durations above to minimize the measurement time. (differential evolution algorithm from the SciPy library)
Goal: minimize the measurement time to reach a sensitivity cm
S. Sidhu, W. Schreyer, RP
next
slides
visibility polarization
free spin precession time
electric field
# of UCN detected

## Slide 17
(A) Filling Simulation
production volume
liquid helium
helium gas
HEX1
UCN valve
Al foil
detectors
temperature distribution
reference level for UCN energy
# UCN in EDM cell
# UCN in
EDM cell
top
bot
17
|B|
Color: UCN production time
Spawn UCN inside production volume at constant rate with UCN valve closed (Maxwellian tail spectrum)
Open UCN valve to start EDM cell filling, keep spawning UCN
Record UCN energy distribution in EDM cell every second
S. Sidhu
mean energy

## Slide 18
(B) Storage in cells
Spawn all UCN inside EDM cells at T=0 with a constant energy distribution
Store UCN with EDM cell valve closed for 300 s
Record energy distribution every second
# UCN in EDM cell
# UCN in EDM cell
top
bot
18
S. Sidhu
Not uniform:
energy distribution
weighed using (A)
and optimal timings
mean energy

## Slide 19
(C) Counting simulation
Spawn neutrons inside EDM cells at T=0 with constant energy distribution, EDM cell valve open and EDM switch connecting to detectors
Record energy distribution of neutrons collected in the detectors every second
# UCN detected
# UCN detected
top
bot
19
S. Sidhu
Starting:
energy distribution
weighed using (A) and (B)
and optimal timings
mean energy

## Slide 20
(C) Counting simulation
# UCN detected
# UCN detected
Spawn neutrons inside EDM cells at T=0 with constant energy distribution, EDM cell valve open and EDM switch connecting to detectors
Record energy distribution of neutrons collected in the detectors every second
top
bot

## Slide 21
Remarks on the general optimization results
Optimal timings
Accumulation time s
Fill time s
Storage time s
Counting time was s
Conclusions
These times are quite a bit longer than originally anticipated.
Transport timings are longer for lower energy neutrons. These have
  longer storage lifetime in EDM cells and
  a better collection efficiency.
This increases and
21
top
bot

## Slide 22
Parameters analyzed
shape of bottle
extraction out of bottle
guide diameter
gravity bend shape, height
vertical position of EDM cells
magnet bore shape
EDM feeders
EDM cell size
https://ucn.triumf.ca/meetings-and-workshops/review-meetings/2020-02-eac-review-meeting/documentation-for-eac-review/new-ucn-source/UCN_source_design_note.pdf
22

## Slide 23
Components not covered in other presentations
He gas systems
Initial P&ID released
More detailed P&ID in progress
Component spec’ing ongoing at the moment

## Slide 24
Components not covered in other presentations
Liquid helium transfer line
Helium pumping system
  43 m total length, ~4 m elevation drop
  Capacity ~100 L/hr
  Heat load as low as possible: <3 W, 4.2 L/hr LHe loss
  LN2 or return gas cooled shield
  Requesting support from TRIUMF’s cryogenics group
  RFP planned by mid 2020
Two systems required
  Natural helium (1K pot): 1.26 g/s at 5.4 Torr ($200k)
  Helium-3: 1.14 g/s at 2.38 Torr ($400k)
Ideally both systems use the same pump models.
Tender this spring
Starting with subset of pumps
He gas systems
Initial P&ID released
More detailed P&ID in progress
Component spec’ing ongoing at the moment

## Slide 25
Summary
We have solved nearly all major challenges posed by the TUCAN next generation source.
We are making good progress and have achieved major milestones.
We plan to install it in 2021 and perform first beam tests the same year.
This is highest priority of the TUCAN collaboration!
We have very challenging and demanding 2 years ahead of us to have many different components come together on time!
Main challenges, risks:
LD2 regulatory uncertainty
A lot of things have to click into place
Availability of TRIUMF support groups https://docs.google.com/spreadsheets/d/1UpaaIasmOP7XC00s2DEvn37fzRmK74w4TTxSC5PXwcs/edit?usp=sharing
Static heat input
Component failure

## Slide 26: Thank you Merci
Follow us @TRIUMFLab
www.triumf.ca

## Slide 27
Some relevant numbers (compared to inverse geometry source)
TUCAN source
(engineering stage)
Inverse geometry source
(conceptual stage)
Production 1.4-1.6 x 107 UCN/s
Source helium temp 1.03 K to 1.13 K
Cooling power 10 W (3He fridge)
Source storage lifetime 28 s
Figure of merit P = 4.5 x 108
Density in the source 3 x 103 UCN/cc
Total number in the source 3 x 108 UCN
Initial density in 70 l EDM expt 200 UCN/cc
Counted at the end of cycle 2 x 106
Production 1.8 x 109 UCN/s
Source helium temp 1.6 K
Cooling power 100 W (4He fridge)
Source storage lifetime 2 s
Figure of merit P = 3.6 x 109
Density in the source 5 x 104 UCN/cc
Total number in the source 6.5 x 109 UCN
Initial density in 100 l perfectly matched expt 10000 UCN/cc
https://arxiv.org/abs/1905.09459

## Slide 28: Meson hall He liquefier
Linde 1610
RSX compressor
1000l dewar
recovery compressors
He bag
liquefaction rate | 50 l/h
UCN needs 2017 | ca. 25 l/h
CMMS needs | Ca 15 l/h
Built 2012

## Slide 29
(C) Counting simulation
Spawn neutrons inside EDM cells at T=0 with constant energy distribution, EDM cell valve open and EDM switch connecting to detectors
Record energy distribution of neutrons collected in the detectors every second
S. Sidhu

## Slide 30
Simulation results summary
S. Sidhu

## Slide 31
EDM sensitivity
S. Sidhu

## Slide 32
Days to reach 10-27 ecm
S. Sidhu

## Slide 33
TUCAN UCN source pumping systems
Natural helium (1K pot): 1.26 g/s at 5.4 Torr
- well known pumping performance, low risk
- cost about 200 kCAD
Helium-3: 1.14 g/s at 2.38 Torr
- pumping performance only estimated
- minimize additional helium-3 for purges
- cost about 400 kCAD
- ideally both systems use the same pump models
Status
- discussion with three suppliers, 1-2 promising proposals
- TRIUMF conceptual design review in May 2019
- preparation of RFP ongoing
- approach to purchase minimal system first (possibly for Helium-3 only, use current pumps for Natural helium)
Example of proposed Helium-3 pumping system performance

## Slide 34
TUCAN UCN source liquid helium supply line
Natural helium supply
  liquefier production currently 50-55 L/hr
  Full, reliable operation requires upgrade of production rate and mother dewar capacity
Natural helium transfer line
  43 m total length, ~4 m elevation drop
  UCN source avg consumption 10W, 35% duty: 31 L/hr
  LHe supply line capacity ~100 L/hr
  Heat load <3 W, 4.2 L/hr loss (as low as possible)
  LN2 or return gas cooled
Status
  Request support from TRIUMF’s cryogenics group
  RFP planned by mid 2020
Proposed route of LHe transfer line
from liquefier to UCN source cryostat

## Slide 35
Inside shielding
35
Rendering issue,
disregard white tube

## Slide 36: Overarching Schedule
UCN services schedule (will go to appendix…)
Calendar Year |  |  | 2020 |  |  |  |  |  |  |  |  | 2021 |  |  |  |  |  |  |  | 2022 |  |  | 
 |  |  | 1 |  |  | 4 |  | 7 |  | 10 |  | 1 |  | 4 |  | 7 |  | 10 |  | 1 |  | 4 | 
Shielding |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Mod Pit Services |  | D2, D2O lines, controls, therm n det |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Cryo Pit Services |  | D2, H20, air, power, controls, roughing, He pump lines |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Cryo conn, LD2 cryost. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
He pumping system |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Services | LD2, 3He, nat He, Isopure handling system |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Slow control |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
UCN handling |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
BL1U |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Detailing
Inst
Construct, procure
Construct, procure
Install
Detailing
Install
Construct
Assemble
Assemble
Install
Detailing
Construct
Assemble
Cryo testing
Plan
Procure
Assemble, connect, program
Detailing
Build, procure
Install
UCN
lift
Inst
lift
Inst
Maintenance, repairs, upgrade
Inst
Tender
Procure
Test
Install
Gray shaded systems are inside the biological shielding.
Beamspot calcs
beam
tests
Target cask detailing
Construct
Test
Inst

## Slide 37
Shielding and pumps
Has to be installed
during shutdown
BL1A shielding line
37
 2.5 m
accessible while BL1A is running
4He
3He
Y switch
polarizer
valve
LD2
cryostat

## Slide 38
Converter cryostat: 3He pumping
Best cooling performance < 1 K
Proven technology
Own expertise
Pressure drop in pumping duct manageable.
Reasonable pumps required.
Uncertainty in surface and superfluid helium conductivity
These uncertainties have been studied and are being experimentally tested.
Main disadvantages of 4He direct pumping:
huge pumping power
pressure drop very critical
Technology choices for converter and cold moderator
Cold moderator: LD2
Well known (scattering kernels)
Among the best moderating performances
Liquid (no burping)
Explosive
Safety concept will be laid out. Volume < 150 liquid liters.
10 W
0.77 K
1.14 K
1.16 K
0.25 W static load, Kg=22, a=2.6, VanSciver
Cam Marshall
Shinsuke Kawasaki
Ryohei Matsumiya
Takahiro Okamura

## Slide 39
What is taken into account in the analytical model?
This is taken into account…
This is not… or not so well…
UCN production/heat input from MCNP simulations
Cryostat performance (pumps, pressure drop, HEX, heat conductivity)
Neutron storage lifetime in source (He liquid + vapor)
Phase space reduction due to wall Fermi potential and height differences
Dilution of neutron “gas”
Simple model of Ramsey cycle
Probable stable daily measurement period
Times for E field change, degaussing etc
Magnetic field of polarizer (it is in MC)
Transport is only modelled via loss per meter, bend, foil etc
Depolarization of UCN during transport (assuming 5% total)
Analytical model useful to study many more parameter options than possible in simulation.

## Slide 40
Heat exchanger sensitivity
Kapitza resistance parameter KG
3He Kapitza correction factor
okay above 25
okay below 3.5

## Slide 41
Heat exchanger sensitivity continued
Fin length
0.5 mm seems enough

## Slide 42
Heat exchanger sensitivity continued
HEX1 inner diameter
HEX 1 length
> 0.14 okay
> 500 mm okay

## Slide 43
Helium-3 pumping system
Pumping speed
Pressure drop in helium-3 pumping line
> 5000 m3/h should work
smallish effect

## Slide 44
Heat input and conduction
Static heat input
Model dependence
below 2.5 W is doable
both are acceptable,
but what if none fits?

## Slide 45
Heat conduction continued
UCN guide and heat conduction channel diameter
Length of the same
> 0.14 m works well
pretty mild effect

## Slide 46
General temperature dependence
Volume averaged isopure helium temperature
Model dependence
below 1.2 is fine,
above it hurts…
both are acceptable,
but what if none fits?

## Slide 47
General temperature dependence
Volume averaged isopure helium temperature
Model dependence
below 1.2 is fine,
above it hurts…
both are acceptable,
but what if none fits?

## Slide 48
nEDM parameter sensitivity
EDM cell radius
EDM cell height (E field kept at 13 kV/cm)
Large lever arm…
Above 200 kV reasonable?