## Slide 1: Isotope Production Activities at LBNL: The Tri-Lab Effort in Nuclear Data, and Novel Production Pathways for 225Ac
Andrew S. Voyles | 24 Aug 2022 | WTTC18
Notes: Emerging trends for next-generation (targeted & personalized) nuclear medicine:
  Targeted alpha therapy (5-10 MeV)
    40-80 μm range  single cell
  Targeted Auger therapy (20 eV – 1 keV)
    1 nm – 2 μm  cellular nucleus
  Theranostic medicine
    Simultaneous imaging and therapy

## Slide 2: The Nuclear Data Pipeline
ENDF/BV-11.1: Proton Reactions
(p,x) with Ep > 100 MeV
10 datasets
D.A. Brown, Nuclear Data Sheets, 148:1–142, 2018.
A.J. Koning, Nuclear Physics A, 744:15–76, 2004.
ENDF/BV-11.1: Neutron Reactions
User
Compilation (EXFOR)
24 000 datasets (46% for (n,x))
(p,x) reactions - 20%
4600 datasets (d,x) reactions 2000 datasets – 9%
Measure
Notes: And for the most part, we really don’t have a lot of answers to these experimental or modelling questions. Consider a version here of the nuclear data pipeline, and let’s see how the current proton reactions state fall into it. In the publishing and compilation steps, which is basically the body of existing experimental work, we see that there are 32 000 cross section datasets for all incident particle types. Of those, about a 20% subset are proton induced reactions, about out 6000 datasets. But of all those datasets, only 18 datasets guide our evaluation and modelling above 100 MeV, which the important range of our regional LINACS that I’ve discussed for isotope production.
And in terms of evaluation and recommended datasets across all energies, even from all those 6000 data sets, there are very few. And especially very few evaluated heavier target cases, which are the ones actually relevant to medical isotope production. So our basis of (p,x) in terms of experiment, evaluation, and modelling work is generally sparse. We certainly don’t know all that we should. And you can see our evaluation portion of the pipeline really lacks for protons versus neutron data, and the comparison is here.
In terms of neutrons reactions, we’ve done well to address some of these questions, still not necessarily at high energies though, but still for proton reactions we are really laid bare and clearly need improvement if we want to better our charged-particle isotope production capabilities.

## Slide 3: What If No Experimental Data Exist?
A.S. Voyles, EPJ A, 57 (2021) 94
H.L.O. Ekeberg, M.S. Thesis 2020
The good…
The bad…
The ugly…
Current nuclear data needs for applications Phys. Rev. Res. 4, 021001 (2022)
Notes: What about when there’s no data? Modeling codes must be used to predict XS, to design thick targets, or guide the design of a thin-target measurement. However, modeling efforts using default parameters often fail to exhibit modest predictive power (within ~20%).
Several trends:
Modeling is better where data have been measured previously, for strongly fed channels, and for reactions whose ejectiles don’t need to cross shell closures.
Common issues are: failure to model high-spin transfer reactions, or miss the shape (wrong compound peak, wrong amplitude)
3

## Slide 4: Isotope Production Research
A Tri-lab collaboration has been formed between LBNL, LANL, and BNL to measure (p,x) reactions relevant to isotope production from threshold to 200 MeV for primary isotopes of interest and their impurities.
LBNL 88-Inch Cyclotron Ep,max = 60 MeV
BNL BLIP Ep,max = 200 MeV
LANL IPF Ep,max = 100 MeV
The unique strength of this group is its access to the different irradiation facilities and expertise

## Slide 5: The Tri-Lab Effort in Nuclear Data
Not Pictured:
Eva Birnbaum (LANL)
Cathy Cutler (BNL)
Amanda Lewis (UCB)
Arjan Koning (IAEA)
Ellen O’Brien (LANL)
Meiring Nortier (LANL)
Andrew Voyles (UCB)
Jon Morrell (LANL)
Dmitri Medvedev (BNL)
Etienne Vermeulen (LANL)
Catherine Apgar (UCB)
Lee Bernstein (UCB/LBNL)
Jon Batchelder (UCB)
Michael Skulski (BNL)
Morgan Fox (UCB)
Special Guest: Laura McCann (TAMU)

## Slide 6: Stacked-Target Experimental Method
H+ Beam
Degraders Al, Cu
Monitor Foils Al, Ti, Cu, Fe, …
Foils of Interest
75As, 93Nb,…
A.S. Voyles et al., NIM B 429 (2018) & EPJ A 57:94 (2021) J.T. Morrell et al., EPJ A 56:13 (2020) M. B. Fox et al., PRC, 103(3):034601 (2021) & PRC 104, 064615 (2021)
Check out Curie! (and help improve it!) https://jtmorrell.github.io/curie/build/html/index.html

## Slide 7: 72Se and 68Ge Production
BNL
LANL
68Ga
PRC 104, 064615 (2021) J.Nuc.Med 57.12 (2016)
Arsenic route offers highest yield and purity for 72Se
LBNL
→ 68Ga
ε
t1/2 = 270.93 ± 0.13 d
t1/2 = 67.71 ± 0.09 m
t1/2 = 8.40 ± 0.08 d
t1/2 = 26.0 ± 0.1 h
72Se → 72As
ε
Notes: The data from TREND suggests that across all rele-
vant incident particle energies beyond reaction threshold,
the 75As(p,4n)72Se is the optimal production pathway
to the 72 Se/72 As generator system. The arsenic target
route offers an increase in yield of greater than an order
of magnitude versus the current methods, while still af-
fording radioisotopically pure production as best as pos-
sible. Specifically, no charged-particle production route
to the 72Se/72As generator system is uncontaminated
from 75−73Se co-production.
that 72As will be efficiently separated from the parent 72 75−73Se when needed, and that the co-produced Se will also follow the chemical separation [9, 11]. Additionally, the 75As(p,4n) pathway avoids any potential long-lived 74,73,71As contamination.

## Slide 8: Nuclear Data Contributions – Medical and Models
Our data adds direct value for isotope production
But we are also a nuclear data group
  And this is a large contribution of scarce data
  A valuable opportunity to study high-energy reaction modeling and evaluation
LBNL
BNL
LANL
How do we improve modeling for high-energy proton-induced reactions?
PRC 104, 064615 (2021)

## Slide 9: Impact Beyond “Better Fitting Lines”
The goal is not surface level improvements in
  The reflection of physics adjustments made and the process are vitally important pieces
This is the start to an evaluation approach and the comments we make are substantial because they immediately become a basis for these regimes
p
93Nb
94Mo
90Mo
n
n
n
p
93Nb
90Mo
n
Compound (10-16-18 s)
Pre-equilibrium (10-19-22 s)
93Nb
n
Exciton interactions
Increasing Energy/Nucleon
n
M. B. Fox et al., PRC, 103(3):034601, 2021
n
n

## Slide 10: This effort* seeks an improvement in the ability of reaction modeling to optimize radioisotope production
More data is needed to obtain the correct set of reaction parameters
But there are literally thousands of other parameters that can be adjusted!
*M. B. Fox et al., PRC, 103(3):034601, 2021 & PRC 104, 064615 (2021)

## Slide 11: What Happens if We Don’t Do the Right Thing?
M. Fox, PRC 103(3):034601, 2021
Consider 10 different models, with arbitrary choices of which simplistic or complex parameters are adjusted, to reproduce similar improvements over the default prediction...
Using the TALYS framework, what parameters might be chosen for adjustments?
  Level density: ldmodel, ctable, ptable (Compound)
  Optical Model: avadjust, rvadjust, w1adjust, v1adjust (Mostly Compound)
  E1 gamma-ray strength model: strength (Both)
  Pre-equilibrium: preeqmode, M2constant, M2shift, M2limit (Pre-Equilibrium)
Notes: And finally, with this all seemingly set and a true physical result taken out from it, we can see what happens if we don’t do this right thing. What if we don’t follow the procedure when making adjustments and what if we only look at one residual product channel instead of them multiple simultaneously, basically throwing that first puzzle piece step out the window.
Well, here’s the strongly fed 90Nb channel. If we were to just look at this, we can see that it’s possible to make a whole bunch of different sets of adjustments that reproduce/do better than the default. But which one is most correct, which one represents reality best. Well, if we are just looking at this one channel, we would say models 1,2,10. Am I actually improving predictive power from this, have I generated some sort of information to help me improve modelling and get out a correct solution. Questions you should ask if you’re making these type of adjustments. But as soon as you look at a neighbouring channel, you’ll find this approach is certainly not correct. Here models 1,2,10 perform extremely poorly.
Nevertheless, this type of single channel, arbitrary parameter adjustments is a norm in literature and it clearly leads to compensating errors. All of which can certainty be improved by the fitting approach I presented.

## Slide 12: What Happens if We Don’t Do the Right Thing?
Consider 10 different models, with arbitrary choices of which simplistic or complex parameters are adjusted, to reproduce similar improvements over the default prediction…
Using the TALYS framework, what parameters might be chosen for adjustments?
  Level density: ldmodel, ctable, ptable
  E1 gamma-ray strength model: strength
  Pre-equilibrium: preeqmode, M2constant, M2shift, M2limit
  Optical Model: avadjust, rvadjust, w1adjust, v1adjust
Models 1, 2, 10 perform best over default
Models 1, 2, 10 perform extremely poorly
Single-channel optimizations lead to non-unique, non-physical solutions!
M. Fox, PRC 103(3):034601, 2021
Notes: And finally, with this all seemingly set and a true physical result taken out from it, we can see what happens if we don’t do this right thing. What if we don’t follow the procedure when making adjustments and what if we only look at one residual product channel instead of them multiple simultaneously, basically throwing that first puzzle piece step out the window.
Well, here’s the strongly fed 90Nb channel. If we were to just look at this, we can see that it’s possible to make a whole bunch of different sets of adjustments that reproduce/do better than the default. But which one is most correct, which one represents reality best. Well, if we are just looking at this one channel, we would say models 1,2,10. Am I actually improving predictive power from this, have I generated some sort of information to help me improve modelling and get out a correct solution. Questions you should ask if you’re making these type of adjustments. But as soon as you look at a neighbouring channel, you’ll find this approach is certainly not correct. Here models 1,2,10 perform extremely poorly.
Nevertheless, this type of single channel, arbitrary parameter adjustments is a norm in literature and it clearly leads to compensating errors. All of which can certainty be improved by the fitting approach I presented.

## Slide 13: These results were used to develop a new data evaluation methodology for high-energy (p,x) reactions
Based in TALYS code
We established a collaboration with the TALYS lead developer, Dr. Arjan Koning (Head of the IAEA Nuclear Data Section)
Emphasis placed on pre-equilibrium parameter adjustments to match the strongest-fed channels
The modeling is validated via comparison to nonelastic, cumulative channels (same product formed by several exit channels)
Morgan Fox

## Slide 14: Evaluation Procedure applied to 93Nb(p,x), 139La(p,x)
Exciton model adjustments in this mass region have led to significant improvements in pre-equilibrium, with global improvements up to 40x
However, the base level density (ldmodel 4, Goriely HFB + Skyrme) needed to be changed (ldmodel 5, Hilaire HFB + Skyrme) for most Nb, Mo products
*M. B. Fox et al., PRC, 103(3):034601, 2021 & PRC 104, 064615 (2021)
All is not well in the state of Denmark w.r.t. level density!

## Slide 15: Level Density Adjustments in 75As(p,x)
*M. B. Fox et al., PRC, 103(3):034601, 2021 & PRC 104, 064615 (2021)
 ldmodel 4, Goriely HFB + Skyrme
 ldmodel 5, Hilaire HFB + Skyrme
All others  ldmodel 6, Temperature-Dependent HFB + Gogny
Like with Nb/La, we see a clear need to transition to a new level density model as we get far from target
  Effect is more prominent in As, as we produce isotopes further from stability
  More pronounced for (p,xn) channels
  This does NOT imply that one ldmodel is better than others – none work globally for high Ex!
This is a problem!
Notes: Unfortunately, TALYS’s implementation of the ECIS-06 code for optical model and CC calculations is unsuited for a pure vibrational coupling scheme for odd-Z nuclei, and the weakcoupling model has to be used in such cases. Moreover, the only odd-Z nucleus with any sort of vibrational deformation file in TALYS is 241Am, where vibrational collectivity is built on top of rotational character. Therefore, taking the 241Am deformation formatting as a guide, a weak vibrational band consisting of the 75As 9/2+ (303.9243 keV), 5/2+ (400.6583 keV), and 1/2+ (860.0 keV) levels was added to a second created coupling scheme including the prior discussed rotational band. In this suggested vibrational band, the 1/2+ level is dominated by transition to 5/2+, which then has an E2 transition to the 9/2+ of 76.4 (25) Weisskopf units [104]. The 9/2+ deexcitation is dominated by E3 decay to the ground state. This mixed rotational+vibrational coupling scheme was also added to TALYS.

## Slide 16: Limitations to Residual Product-Based Fitting
This approach can’t be used to fit to any products which are stable, lack observable decay gammas, or are too short-lived (< 10ish minutes)
  We need something beyond the stacked-foil technique!
*M. B. Fox et al., PRC, 103(3):034601, 2021 & PRC 104, 064615 (2021)
Isotope | Target | Beam | Measurement focus | Energy range | Site | Year
72Se, 68Ge | 75As | p | Primary: 72Se, 68Ge Impurities: 70,71,73,75Se, 66,67,69,71Ge | Up to 200 MeV | All | 1
202Pb | 205Tl | p,d | Primary: 202m,202gPb Impurities: 198-205Pb | Up to 200 MeV | All | 2
202Pb | 203Tl | p,d | Primary: 202m,202gPb Impurities: 198-203Pb | Up to 200 MeV | All | 3
119Te, 117mSn | natSb | p,d | Primary: 119m,119gTe, 117mSn Impurities: 116-118,121m/g,123mTe, 113,119m,121m/gSn | Up to 200 MeV | All | 4
134Ce | natLa | p,d | Primary: 134Ce Impurities: 132,133,133,137,139Ce | Extend to 200 MeV | LANL, BNL | 4
Nuclear reaction | Energy range | Site | Year
natTi(p,x)48V | Extend to 200 MeV | All | 2
natNb(p,4n)90Mo | Up to 200 MeV | BNL | Out years
Isotope Production
Flux Monitoring
Stay tuned!
Catherine Apgar
Michael Skulski
Preliminary
Preliminary

## Slide 17: And Now, For Something Completely Different…
Notes: Production of clean 225Ra beta precursor allows for milking of radiopure 225Ac

## Slide 18: How to (not) Make 225Ac
232Th(p,x)
TRIUMF
BLIP @ BNL
IPF @ LANSCE
α
α
β-
What about neutrons?
226Ra(p,2n)
226Ra(γ,n)
227Ac Long-Term Dose: R.J. Abergel, et al., J. Med. Imag. Rad. Sci. 50.4 (2019): S93.
Notes: Production of clean 225Ra beta precursor allows for milking of radiopure 225Ac

## Slide 19: What About Neutrons?
HFIR
1014-15 neutrons/cm2/s
Fast fission spectrum
(Low energy)
M.A. Mosby, NIMB 381 29-31 (2016).
K.P. Harrig, NIMA 877 359–366 (2018).
LANSCE - IPF
107 neutrons/cm2/s/µA
5 < En (MeV) < 100
(Low flux)
IPF – 230 µA•h
D-breakup (Au → Be)
1010-12 neutrons/cm2/s/µA
5 < En (MeV) < 30
DD / DT Generator
107-9 neutrons/cm2/s
2.7 / 14.1 MeV
(Low current)
Jon Engle
Li(p,n) QMN
104-6 neutrons/cm2/s
0 < En (MeV) < 60
(Low flux)

## Slide 20: Deuteron Breakup
Beryllium
d
n
n
n
n
θ
d
d
d
Deuteron has no bound excited states
  Excitation / stripping causes the deuteron to breakup into constituent proton + neutron
  ~5-10% of deuterons are converted into neutrons
  Conservation produces a highly (θ≈10°) forward-focused “blowtorch” of neutrons
  Be breakup target gives highest n-yield, and doesn’t activate
  Tunable En, negligible target heating
J.P. Meulders, P. Leleux, P. C. Macq & C. Pirart
Phys. Med. Biol. 20, #. 2, 235-243, (1975)
J.T. Morrell PhD Thesis (2021) & PRC (Submitted, 2022)
Jon Morrell

## Slide 21: The High Energy Incident Flux for Emerging Radionuclides Target: HEIFER
1 mg = 1 mCi 226Ra
target at atmosphere
In vacuum: 6mm Be
breakup target
33 MeV d+ beam, 1cm OD
J.T. Morrell PhD Thesis (2021) & PRC (Submitted, 2022)
Patent US20220199276A1
WO2020210147A1
EP3953949A1

## Slide 22: Alpha and gamma-ray spectra taken at LBNL
Radiochemical Ac/Ra separation at 14 days post-EOB
  Dissolve down 1 mg Ra target in 3M HNO3
  Precondition 2 mL Eichrom DGA resin column with 5 bed volumes 3M HNO3
  Load column with Ra/Ac solution at 0.8 mL/min
  Wash column with 2 bed volumes 3M HNO3
  Strip Ac from column with 5 bed volumes 0.1 M HCl at 0.8 mL/min
  Rinse column with 5 bed volumes DI water
Activities and separation efficiency quantified via LSC, HPGe, α-spec
Separation protocol still under refinement
Rebecca Abergel
Patent US20220199276A1
WO2020210147A1
EP3953949A1
 | Eichrom DGA | Eichrom DGA (Aliquot 1) | Bio-Rad AG50 (Aliquot 2)
225Ac Recovery | 60% (0.84 µCi) | 37% (0.143 µCi) | 44% (0.168 µCi)
226Ra Breakthrough | 4.3 ∙ 10-3 % (35.1 nCi) | 2.6 ∙ 10-3 % (12.8 nCi) | 3.5 % (17.7 µCi)
Ac/Ra Separation Factor | 13900 | 14500 | 12.7
J.T. Morrell PhD Thesis (2021)

## Slide 23: Production of 225Ac at the LBNL 88” Cyclotron
Initial Results
Production rate: 2.1 mCi/mAh/g226Ra
Subsequent milking would produce more
2-month count period on HPGe shows:
No fission fragments identified in recovered 225Ac
No detectable activity of 227Ac (227Ac MDA: approx. 218 Bq (5.9 nCi) or <0.4% radio-impurity)
Next Steps:
Pre-clean 226Ra sample to remove 228Th
Use different deuteron energies to optimize yield
Optimize chemical separation procedure
Chemical Separation
Pre-clean (remove 228Th)
Irradiation
227Ac separation (7 hour)
225Ac in-growth (10-15 day)
225Ac separation (multiple?)
226Ra recovery
Patent US20220199276A1
WO2020210147A1
EP3953949A1
J.T. Morrell PhD Thesis (2021)

## Slide 24: D-breakup neutron production is most effective on thick targets
Assumptions: 40 MeV D and e beams; 25 kW beam power; cylindrical target
Note: No fission products observed at either deuteron energy
226Ra(g,n) (40 MeV e- Brehm)
226Ra(n,2n) (40 MeV D-breakup)
232Th(p,x) TTY (<200 MeV)
226Ra Cross Sections
We benchmarked these numbers at 33 and 40 MeV using a 1 mg 226Ra sample
24
J.T. Morrell PhD Thesis (2021) & PRC (Submitted, 2022)
Patent US20220199276A1
WO2020210147A1
EP3953949A1

## Slide 25: Simultaneous production using Deuteron Breakup neutrons
Assumptions: 40 MeV D and e beams; 25 kW beam power; cylindrical target
Difference in production attributable to cross section differences
67Cu
47Sc
25
J.T. Morrell PhD Thesis (2021) & PRC (Submitted, 2022)
Patent US20220199276A1
WO2020210147A1
EP3953949A1

## Slide 26: Takeaways + Questions for YOU!
Nuclear Data
  When measuring cross sections / yields for isotope production, please report all products you observe!
  Question: Where do you see issues in modeling cross sections / yields?
225Ac Production
  Currently designing a 20kW production target!
  Question: how to benchmark thermal modeling?
Cross-Cutting
  The Nuclear Data community is currently organizing 5-10 year priority plans, and Isotope Production is one of the top priorities for applications
26
What data needs do you have for quantifying issues / uncertainties / covariances in Isotope Production?
Email: ASVoyles@lbl.gov

## Slide 27: Thank you for your attention!
This research was supported by the U.S. Department of Energy Isotope Program, managed by the Office of Science for Isotope R&D and Production, carried out under Lawrence Berkeley National Laboratory (Contract No. DE-AC02-05CH11231), Los Alamos National Laboratory (Contract No. 89233218CNA000001), and Brookhaven National Laboratory (Contract No. DEAC02-98CH10886).
Andrew S. Voyles1, Rebecca J. Abergel1,2, Catherine E. Apgar1, Jon C. Batchelder1, Lee A. Bernstein1,2, Eva R. Birnbaum3, Cathy S. Cutler4, Morgan B. Fox1, Arjan Koning5, Amanda M. Lewis1, Dmitri Medvedev4, Jon T. Morrell3, F. Meiring Nortier3, Ellen O’Brien3, Michael A. Skulski4, and Etienne Vermeulen3
1 University of California-Berkeley Dept. of Nuclear Engineering
2 Lawrence Berkeley National Laboratory
3 Los Alamos National Laboratory
4 Brookhaven National Laboratory
5 International Atomic Energy Agency
27
https://nucleardata.berkeley.edu/