## Slide 1: Machine Detector Interface & Collimation System
27th Oct. 2021
EIC Accelerator Partnership Workshop
M. Valette, A. Drees, G. Robert-Demolaize
With contributions from:
J. Bellon, A. Blednyk, C. Hetzel, S. Seletskiy

## Slide 2: Introduction - Machine Detector Interface
The EIC will feature powerful beams
-10x the stored energy of RHIC
-2x SuperKEK-B target stored energy with 1/2 the bunches
Collimators accomplish 2 main missions
-Beam cleaning to reduce radiation &
backgrounds form lost particles
-Machine protection from
accidental beam loses
(CCs, kickers, instabilities, …)
Constraints
-Impedance budget
-Beam lifetime
-$ budget

## Slide 3: Context
-The e- bunches will be very dense (0.5 mm2) and melt metals in case of normal impact.
-The p+ beam will have similar parameters as the post-LIU SPS.
Other complexes have reported issues limiting performance:
-SuperKEK-B experienced instabilities causing collimator damage and limiting beam currents.
-HL-LHC will switch to coated collimators (MoGr) to reduce impedance.
Assuming SKEKB-like tails

## Slide 4: Electron ring
IR2 - Horizontal
IR4 – Vertical & Momentum
Focus on the 10 GeV case with the most stored energy.
Planned in IR2 & 4 :
-2-sided prim. + 2 sec. for cleaning and flexibility with phase advances and optics
+injection shielding in IR2
(+masks in IR6 & 8)
IR12 - Injection protection

## Slide 5: Electron ring (2)
Collimation hierarchy :
-Imposed by squeezed optics in the IRs
-Retraction from prim. -> sec. -> app. based on orbit stability
-Arc is tighter than experiment in the horizontal plane
-Masks upstream of IRs will avoid losses into the focusing quads showering to the detectors
secondary
Arc
Exp. magnets
primary
secondary
Exp. magnets
Exp. detector
primary
IR2
secondary
secondary
Horizontal
Vertical
13σ
14σ
45σ
14σ
48σ
23σ
28σ
70σ
28σ
63σ
Exp. detector
e- beam
IR4
Arc
Masks

## Slide 6: Optics considerations
Phase advances :
-key to protect against kicker failures
-important to ensure cleaning efficiency from the secondaries
-optics will have to be monitored to ensure protection/cleaning
Orbit stability, beta beating, errors, …, will affect collimations hierarchy by increasing retraction margins.
We are following developments at KEK-B closely to learn from their experience.
Inj. Abs.
Prim.
Q1eF
Kickers
Q1eR
Prim.
Experiment
Sec.
Sec.
0°
180°
90°
270°
Sec.
Sec.

## Slide 7: Hadron ring
Different constraints:
-Different loss behavior for protons/ions
-Cold ring requires good cleaning efficiency in the arcs
-More flexibility on the optics
We can benefit from RHIC and LHC experience.
Planned in IR12 :
-issues with other users due to radiation
-switchyard doubles the second secondary
Momentum collimators are planned for the sector 11 dummy.
Courtesy G. Robert-Demolaize

## Slide 8: Summary
IR12 e Injection absorbers
IR4 e Vertical Collimation
IR2 e Horizontal collimation
(and potential abort)
IR4 e momentum collimation
p Injection protection
(note: not actual inj. location)
Electron : 5-7 collimators
Hadrons : 5-7 collimators
+absorbers and masks
Sector 11 p momentum collimation (‘dummy’)
Sector 12 p primaries
and secondaries
 | LER | HER | RHIC (Yellow) | ESR | HSR
1 sided | 0 | 16 | 3 | 1 | 1
2 sided | 11 | 4 | 0 | 7 | 7
Total | 22 | 24 | 3 | 15 | 15
Comparison table

## Slide 9: Mechanical Design
Electrons :
  The tips would be made of coated Carbon and 30-90 cm long.
  With 1:10 tapering to standard apertures (impedance), the collimators would be 90-120 cm long without RF fingers and bellows.
Hadrons :
  The collimators would have similar lengths with longer jaw and less tapering
Designs courtesy of Vacuum taskforce, see C. Hetzel’s talk from this morning.

## Slide 10: Conclusion & Outlook
Upcoming simulation studies :
-ANSYS : to study heat extraction from SR and short lifetimes.
-FLUKA : to investigate particle deflection, energy deposition and potential damage/activation. Will allow confirming jaw length and materials/coatings.
-SixTrack : Tracking and cleaning efficiency simulations will confirm the number and location of collimators.
Integration of collimators into their respective IRs must be consolidated to ensure fitting geometry and cohabitation with other instruments. Work has already started for IR12.
Opportunities for collaboration :
-Collimator / Kicker / Dump design
-Tracking / Background simulations
-Coatings, surface processing, …..

## Slide 11: Thank you for your attention !
Questions ?

## Slide 12: Locations of interest : momentum
Goal : large ηx
figure of merit ηx.W/σx.ncoll > 1.
IR4
FOM = 1 !
Upstream of IR6
A bit crowded
Masks between the two experiments

## Slide 13: Summary table
5/10 GeV
18 GeV
Collimator | s (m) | near | up/downstream | beta_x (m) | beta_y (m) | D_x (m) | half-gap (sigmas) | half-gap (mm) | target punch through | tip length (m) | material | phase advance | Full open (sigmas) | half-gap (mm) | Stroke
Primary H | 2483.0993 | Q11 @1 | downstream | 23.87 | 16.80 | 0.00 | 13.06 | 9.02 | 0.01 | 0.27 | C (coated) | 0 | 20 | 13.82 | 4.80
Secondary H | 2504.3607 | Q9 @1 | downstream | 49.49 | 22.41 | 0.00 | 14.31 | 14.24 | 0.00001 | 0.81 | C (coated) | 60.84309 | 20 | 19.90 | 5.66
Secondary H | 2526.9222 | Q7 @1 | upstream | 52.30 | 24.86 | 0.00 | 14.31 | 14.63 | 0.00001 | 0.81 | C (coated) | 95.42692 | 20 | 20.45 | 5.82
Primary V | 1842.4243 | Q10 @11 | downstream | 25.22 | 52.20 | -0.35 | 23.31 | 5.83 | 0.01 | 0.27 | C (coated) | 0 | 40 | 10.01 | 4.18
Secondary V | 1864.5826 | Q8 @11 | upstream | 15.50 | 57.35 | -0.03 | 28.41 | 7.45 | 0.00001 | 0.81 | C (coated) | 36.29843 | 40 | 10.49 | 3.04
Secondary V | 1909.7409 | Q4 @11 | upstream | 20.25 | 56.97 | 0.08 | 28.41 | 7.43 | 0.00001 | 0.81 | C (coated) | 114.8636 | 40 | 10.46 | 3.03
Injection absorber (V) | 1954.771 | Q9 @12 | upstream | 46.62 | 11.54 | -0.69 | 38.00 | 36.69 | 0.0005 | 0.54 | C | NA |  |  | 
Momentum (H) | 3299.5 | Q15/16 @4 | middle | 21.36 | 35.70 | 0.70 | 12.87 | 8.41 | 0.000001 | 0.45 | Al (coated ?) | NA |  |  | 
Collimator | s (m) | near | up/downstream | beta_x (m) | beta_y (m) | D_x (m) | half-gap (sigmas) | half-gap (mm) | target punch through | tip length (m) | material | phase advance | Full open (sigmas) | half-gap (mm) | Stroke
Primary H | 2483.1 | Q11 @1 | downstream | 23.87 | 16.80 | 0.00 | 11.94 | 9.04 | 0.01 | 0.27 | C (coated) | 0 | 20 | 15.14 | 6.10
Secondary H | 2504.4 | Q9 @1 | downstream | 49.49 | 22.41 | 0.00 | 13.06 | 14.24 | 0.00001 | 0.81 | C (coated) | 60.84309 | 20 | 21.80 | 7.56
Secondary H | 2526.9 | Q7 @1 | upstream | 52.30 | 24.86 | 0.00 | 13.06 | 14.63 | 0.00001 | 0.81 | C (coated) | 95.42692 | 20 | 22.41 | 7.77
Primary V | 1842.4 | Q10 @11 | downstream | 25.22 | 52.20 | -0.35 | 18.12 | 5.85 | 0.01 | 0.27 | C (coated) | 0 | 40 | 12.92 | 7.07
Secondary V | 1864.6 | Q8 @11 | upstream | 15.50 | 57.35 | -0.03 | 22.01 | 7.45 | 0.00001 | 0.81 | C (coated) | 36.29843 | 40 | 13.55 | 6.09
Secondary V | 1909.8 | Q4 @11 | upstream | 22.28 | 58.77 | -0.04 | 22.01 | 7.55 | 0.00001 | 0.81 | C (coated) | 138.1612 | 40 | 13.71 | 6.17
Injection absorber (V) | 1954.8 | Q9 @12 | upstream | 46.62 | 11.54 | -0.69 | 35.00 | 37.02 | 0.0005 | 0.54 | C | NA |  |  | 
Momentum (H) | 3299.5 | Q15/16 @4 | middle | 18.75 | 55.06 | 0.52 | 9.28 | 6.22 | 0.000001 | 0.45 | Al (coated ?) | NA |  |  | 
https://brookhavenlab-my.sharepoint.com/:x:/g/personal/mvalette_bnl_gov/EXwLNtgLRe1GhWV1DpmBLVEBynh3Z3woU0xyS-i1dE6cBg?e=BDWudO
Link to live version