## Slide 1
Design and hardware for handling SR in light sources
Seunghwan Shin (PAL) on behalf of PLS-II accelerator division
EIC Accelerator Partnership Workshop (2021. 10. 28)
October 28, 2021

## Slide 2
Introduction
Handling SR
Damage protection
BPM position stabilization.
2
Contents
EIC Accelerator Partnership Workshop (2021. 10. 28)

## Slide 3
3
Average brightness (photons / sec / mm2 / mrad2 / 0.1 % bandwidth)
106
108
1010
1012
1014
1016
1018
1020
1022
1024
1026
1028
Candle
Sun
1st GSR
2nd GSR
3rd GSR
4th GSR
XFEL-SASE
XFEL-O
3rd GSR ALS
4th GSR ALSU
The progression of x-ray source
EIC Accelerator Partnership Workshop (2021. 10. 28)

## Slide 4
4
Smaller emittance and MBA
Maximum radiation damping
- High field bending magnets? => increase of quantum excitation too - Damping wiggler in small dispersion => requires much space
Minimum quantum excitation
- Minimize dispersion at radiation locations => many short bends to limit dispersion => highest radiation at lowest dispersion (longitudinal gradient bend for this)
D. Robin (ALS)
Equilibrium
emittance
in storage ring
A. Streun (PSI)
EIC Accelerator Partnership Workshop (2021. 10. 28)

## Slide 5
Ongoing 4GSR projects
5
Classical MBA, HMBA, Variations
R. Bartolini (PETRA-IV) @ 7th DLSR workshop
EIC Accelerator Partnership Workshop (2021. 10. 28)

## Slide 6
Korea-4GSR project
6
EIC Accelerator Partnership Workshop (2021. 10. 28)
Korea-4GSR - Preliminary study by PAL: 2017 ~ 2019. - CDR project: 2020. - Project stat: 2021. 7 ~ - Budget: 1 B $
Parameter | Units | PLS-II | Korean 4GSR
Electron energy | GeV | 3 | 4
Horiz. Emittance | pm | 5800 | 58 (RB: 39 )
Vert. Emittance | pm | ~ 58 | ~ 5.8 (RB: 39 )
Bunch length (rms) | ps | 20 | 13 (50 with HC)
Circumference | m | 280 | 800
Harmonic # |  | 470 | 1332
RF frequency | MHz | 500 | 500
Beam stability @ ID (x/y) |  | < 4 / 2 | < 2.5 / 0.45
Injection mode |  | Top-up | Top-up
Parameter | Units | PLS-II | Korean 4GSR
Electron energy | GeV | 3 | 4
Horiz. Emittance | pm | 5800 | 58 (RB: 39 )
Vert. Emittance | pm | ~ 58 | ~ 5.8 (RB: 39 )
Bunch length (rms) | ps | 20 | 13 (50 with HC)
Circumference | m | 280 | 800
Harmonic # |  | 470 | 1332
RF frequency | MHz | 500 | 500
Beam stability @ ID (x/y) |  | < 4 / 2 | < 2.5 / 0.45
Injection mode |  | Top-up | Top-up

## Slide 7
ID beam port
Bending magnet beam port
Vacuum system in Korea-4GSR
7
EIC Accelerator Partnership Workshop (2021. 10. 28)
Characteristics - Required average vacuum pressure is low 10-9 mbar (CO equivalent). - PSD gas is pumped by distributed pill-type NEGs and lumped sputter ion pumps. - 5° inclined side chamber wall absorbs SR photon beams. - Thermo-mechanical analysis results show that both aluminum and copper alloy are suitable for the SR vacuum chamber material. - Booster ring vacuum chambers are made of 1 mm-thick stainless steel and pumped with lumped sputter ion pumps.
Lumped vacuum pumps (SIP)
RF-bellows
BPM
Layout of an arc section
Cross section of the SR vacuum chamber
Vacuum chambers of an arc-section

## Slide 8
Overview of SR issues
8
EIC Accelerator Partnership Workshop (2021. 10. 28)
Vacuum system should accommodate:
New generation light source: “High current & low emittance”
T. Ha (PAL) @ HBSLS workshop

## Slide 9
SR heat load (Synrad+)
9
EIC Accelerator Partnership Workshop (2021. 10. 28)
e-
[Power (W/cm2)]
A
A
B
B
SR power
- from C-bend (line AA): ― incident, ―absorbed
- from LGB2 (line BB): ― incident, ―absorbed
0.6 W/mm2 (center bend)
 Tmax = 62℃
0.07 W/mm2 (LGB2)
 Tmax = 30℃
Aluminum chamber

## Slide 10
Handle higher SR power (1)
10
EIC Accelerator Partnership Workshop (2021. 10. 28)
B
B
OFHC Copper - Commonly used for photon absorption (easily available). - Excellent thermal conductivity. - Very low outgassing rate. - Need bi-metal joint with stainless steel flange (brazing, EBW, …) - Softened after exposure to high temperature for brazing.
Glidcop - Good thermal conductivity & high strength. - Resistance to thermal softening. - UHV compatible. - Widely used for high-heat-load vacuum components. - Difficult to optimize brazing condition. - Limited supplier (cost, delivery)
T. Ha (PAL) @ HBSLS workshop
“Glidcop absorbers at NSLS-II”
“Glidcop absorbers at ALBA”

## Slide 11
Cold forged OFHC Copper - Excellent thermal conductivity. - Easily available. - E-beam weld to prevent softening from brazing. (shorter exposure to high temperature than brazing)
CuCrZr - Good thermal conductivity. - UHV compatible. - Conflat flange integrated to absorber. - Widely available.
Handle higher SR power (2)
11
EIC Accelerator Partnership Workshop (2021. 10. 28)
B
B
T. Ha (PAL) @ HBSLS workshop
“Cold forged OFHC
absorber at PLS-II”
EBW (Cu-SST)
EBW (Cu-Cu)
“CuCrZr flange at NSLS-II”
“CuCrZr absorber at TPS”

## Slide 12
Foil damage in IVUs at PLS-II
12
EIC Accelerator Partnership Workshop (2021. 10. 28)
B
B
Abnormal pressure change before beam dump

## Slide 13
Improvements of IVU
13
EIC Accelerator Partnership Workshop (2021. 10. 28)
B
B
Hardware - Removed all side clamps - Increased the thickness of the Cu/Ni foil from 50/20 μm to 50/50 μm.
Orbit control - Apply a fast beam orbit interlock: 200 ms => 1 ms.
Heat load reduction: Bunch length increase - RF gap voltage reduction by Ext. Q adjustment. - 3rd harmonic cavity discussion but not applied. - Bunch pattern: 400 -> 430 (temporary) but 300 + 1 (12 mA) confirmed later.

## Slide 14
RF-shielding failures
14
EIC Accelerator Partnership Workshop (2021. 10. 28)
B
B
PLS-II
PEP-II
NSLS-II
SOLEIL

## Slide 15
Designs for robust RF-shielding
15
EIC Accelerator Partnership Workshop (2021. 10. 28)
SuperKEK
NSLS-II
Wide thick fingers
Comb type
RF-shielding
Mo-type flange
Sliding fingers
ESRF EBS
Gate valve with wide fingers

## Slide 16
BPM position stability
16
EIC Accelerator Partnership Workshop (2021. 10. 28)
B
B
Effect of BPM displacement to photon beam stability - Orbit feedback system intends that the electron beam pass through the center of the BPMs - Position of BPM could be changed by ground motion, thermal load change, etc., then the electron beam orbit can be changed. - Beam dump  Δtemperature  Δe-BPM position  Δphoton beam position.
New design of BPM chamber & support - Balance in thermal expansion. - Enhanced cooling.
Existing
design
Improved
design

## Slide 17
Improvement of Δ BPM position
17
EIC Accelerator Partnership Workshop (2021. 10. 28)
B
B
Improvement of new BPM chamber & support - (a) Reduction of BPM displacement: 25 μm -> 5 μm. - (b) Fast recovery after beam abort & restoration: 3 h -> 1 h.
(a)
(b)

## Slide 18
18
Summary
Introduction - New era of synchrotron radiation: fourth-generation storage ring. - Should handle SR heat load, protect damage from SR, and realize BPM position stabilization.
Handling SR - More options in material choice rather than Glidcop.
Damage protection - Need fast orbit interlock (< 1 ms) to prevent damage in IVU. - Various shielding mechanisms are studied.
Need high mechanical stability (1 μm) - Water cooling is very effective. - Need careful design of BPM support.
EIC Accelerator Partnership Workshop (2021. 10. 28)

## Slide 19
We sincerely thank all those who joined in this presentation.
EIC Accelerator Partnership Workshop (2021. 10. 28)