## Slide 1: Vacuum system of SuperKEKB interaction region
Kyo Shibata
(on behalf of SuperKEK Vacuum Group)
2021.10.27
TRIUMF 2021 EIC Accelerator Partnership Workshop
ESR vacuum system session
Inter-University Research Institute Corporation High Energy Accelerator Research Organization (KEK)
大学共同利用機関法人 高エネルギー加速器研究機構 (KEK)

## Slide 2
Contents
Almost all presentation materials were provided by
K. Kanazawa(SuperKEKB), S. Tanaka(Belle) and K. Gadow(DESY).
Overview
IP pipe
QCS pipes
RVC
Summary
IP: interaction point
QCS : final focusing superconducting magnets system
RVC : remote vacuum connection

## Slide 3
1. Overview

## Slide 4
SuperKEKB interaction region
SuperKEKB Interaction Region (IR)
IP pipe (Be)
QCS-R
QCS-L
(Final focusing superconducting magnets in the left system to IP)
(Final focusing superconducting magnets in the right system to IP)
QCS
Final focusing superconducting magnet system
RVC
IP pipe
RVC
Remote vacuum connection
Photo by DESY
Positron beam (4 GeV)
Electron beam (7 GeV)
SuperKEKB
Positron beam (4 GeV)
Electron beam (7 GeV)
QCS cryostat
Belle II detector

## Slide 5
Configuration inside Belle II detector
RVC
RVC
QCS-R cryostat
QCS-L cryostat
IP pipe
BPM-bellows chamber
IP pipe assembled with VerteX Detector (VXD)
VXD

## Slide 6
Installation procedure of IR beam pipes
1.1 Assembling IP pipe and VXD
1.2 Installing BPM-bellows chambers into both sides
of IP pipe
1.3 Installing IP pipe assembled with VXD into Belle II
2.1 Installing QCS beam pipes into QCS cryostat
2.2 Inserting QCS on movable platform into Belle II
3.1 Connecting IP pipe and QCS pipes by RVC
3.2 Installing magnets and beam pipes outside
movable platform

## Slide 7
2. IP pipe

## Slide 8
IP pipe
IP part
Crotch part
Central IP part is made of Be and crotch parts are made of Ta.
Ti is used to connect Be and Ta.
Only taper parts are exposed to direct SR from last bend.
Taper/Ridge
Ridge
Au plated (10 m)
Cu plated (10 m)
Cu plated (10 m)
Paraffin cooled
Water cooled
Water cooled
Be
Ti
Ti
Ta
Ta
Positron beam
Electron beam
Taper/Ridge

## Slide 9
Synchrotron radiation and Trapped mode
Be
Au coat (1020 m)
Positron beam
Electron beam
20
10
Taper/Ridge
Taper : to reduce the number of photons entering into the central part
Ridges : to keep the direction of scattered photons away from Be pipe
Ridges are omitted to avoid complex machining.
This part is slightly bent downward (in this drawing) to avoid direct SR hit on Be pipe.
No trapped mode at the central part
Electro-magnetic field (HOM) due to the crotch :
300 W
HOM due to the taper and the ridge :
50 W
300 W
100 W

## Slide 10
Central part of IP pipe
Outer tube
The central straight part consists of inner and outer tubes.
Paraffin runs between tubes for cooling.
Connection between tubes is done by Ti-Ti EBW.
Connection between IP part and crotch part is done by Ta-Ta EBW.
Be
Ti
Ti
Be
Ti
Ti
Be-Ti Brazing
Be-Ti Brazing
Ti-Ti EBW
Ta
Ta
Inner tube
Ta-Ti by HIP
Ta-Ti by HIP
(HIP : Hot Isostatic Pressing)
Ti-Ti EBW
Ta-Ta EBW
Ta-Ta EBW
Outer Be : 0.4 mm thick
Inner Be : 0.6 mm thick
Gap : 1 mm

## Slide 11
Installation of IP pipe into Belle II
1.1 Assembling IP pipe and VXD
1.2 Installing BPM-bellows chambers into both sides of IP pipe
1.3 Installing IP pipe into Belle II
Bellows with finger-type RF shield
BPM

## Slide 12
Installation of IP pipe into Belle II
1.1 Assembling IP pipe and VXD
1.2 Installing BPM-bellows chambers into both sides of IP pipe
1.3 Installing IP pipe into Belle II

## Slide 13
Installation of IP pipe into Belle II
IP pipe alignment
  IP-pipe_VXD assembly is mounted on CDC.
  Location of IP-pipe_VXD assembly is determined by CDC positioning pins.
  Position of CDC positioning pips are measured by laser tracker before installation of IP-pipe_VXD assembly.
  Pin holes of IP-pipe_VXD assembly are positioned so that the IP pipe can be installed in the proper position for the accelerator.
  Position of VXD is estimated from particle track data.
1.1 Assembling IP pipe and VXD
1.2 Installing BPM-bellows chambers into both sides of IP pipe
1.3 Installing IP pipe into Belle II
IP-pipe_VXD assembly installed into CDC (mock-up)

## Slide 14
3. QCS pipes

## Slide 15
Beam pipes for QCS
Beam pipe
Helium vessel
QC2LE
QC2LP
QC1LP
QC1LE
BPM
Bellows with O-ring seal
O-ring seal between beam pipes and cryostat
QCS-L cryostat
Beam pipes are fixed to QCS cryostat.
They are made of stainless steel with a 4 mm thick wall.
They have water cooling channels on both sides.
Inner surface is coated with Cu (+ TiN only for positron ring).
Movable platform

## Slide 16
IR pressure distribution
IP pipe and QCS beam pipes have no pump.
Pressure at IP is estimated to be about one order higher than that at the end of the cryostat.
Thanks to J. Carter (ANL), M. Ady, R. Kersevan, and P. Chiggiato (CERN)
No vacuum pumps in this region.

## Slide 17
QCSR beam pipe installation
Installation procedure :
  Set beam pipe
  Attach BPM and leak check
  Connect BPM cable
  Leak check of the cryostat
super insulator
Fiberglass (G10) spacer
QCS beam pipe
Beam pipe is inserted using a special tool.
Service window on QCSR cryostat is used to manually guide the beam pipe and to attach BPM.
Service window
BPM
Photo by Y. Arimoto

## Slide 18
QCSL beam pipe installation
Photo by Y. Arimoto
BPM
Since QCSL cryostat has no service windows, the cryostat is disassembled for beam pipe installation.

## Slide 19
4. RVC

## Slide 20
Remote vacuum connection (RVC)
QCS is inserted into Belle II by movable platform and connected to IP pipe.
There is no space for vacuum sealing work by hands.
RVC is a mechanism introduced by Belle group to connect QCS beam pipes to IP pipe (BPM-bellows chambers) by a remote manipulation.
RVC was designed and produced by DESY.
Photo by DESY
RVC on QCSR head
RVC on QCSL head
Remote manipulation wheel

## Slide 21
How RVC works
Drawing by K. Gadow
Single lock flange with a retainer is attached to two bellows units.
BPM-bellows w/o lock flange
BPM-bellows w/ lock flange
QCS is inserted into Belle II.

## Slide 22
How RVC works
Drawing by K. Gadow
These components (red+blue) rotate to catch the lock flange.
Protruding claws of the lock flange are caught by RVC.

## Slide 23
How RVC works
Drawing by K. Gadow
Cylinder for dry N2 (about 50 bar)
These parts are connected to the piston in the cylinder, and shift to press the bellows flange to the cryostat.
As a result, vacuum sealing between IP pipe (BPM bellows chamber) and QCS pipe is completed.
High pressure N2 gas is introduced into this volume.

## Slide 24
How RVC works
This large light blue screw nut turns to lock the mechanism.
Drawing by K. Gadow
Completed!!

## Slide 25
IR exterior appearance
Finally concreate radiation shields cover accelerator components.

## Slide 26
5. Summary

## Slide 27
Summary
IP pipe;
  IP pipe consists of Be (center), Ti and Ta (crotch) parts.
  Central Be pipe is not exposed to direct SR.
  Crotch part has taper and ridge structures to reduce the number of photons entering into the central part.
  IP pipe is assembled with VXD and installed into Belle II.
QCS pipes;
  SUS pipes are fixed to QCS cryostat and inserted into Belle II by QCS movable platform.
  QCS pipes have no pump
  Pressure at IP is estimated to be about one order higher than that at the end of the cryostat.
RVC;
  RVC is a mechanism introduced by Belle group to connect QCS pipes to IP pipe by a remote manipulation.
  RVC was designed and produced by DESY.

## Slide 28: Fin.
Inter-University Research Institute Corporation High Energy Accelerator Research Organization (KEK)
大学共同利用機関法人 高エネルギー加速器研究機構 (KEK)
Thank you for your attention.

## Slide 29
Backup