## Slide 1: TRIUMF e-Linac RF Issues ERW2022
Yanyun Ma

## Slide 2
Outline
  300kV RF modulated thermionic Gun
    650MHz
  SRF cryomodules performance
    Field emission
    RF stability
  High power RF system
    Klystron and Waveguide system
    KPS
  Discussion
In future

## Slide 3
Outline
  300kV RF modulated thermionic Gun
    650MHz
  SRF cryomodules performance
    Field emission
    RF stability
  High power RF system
    Klystron and Waveguide system
    KPS
  Discussion
In future

## Slide 4
E-Gun
650MHz RF modulation bunches the beam at the grid
  RF tuned by matching circuit
  No feedback for RF regulation
  The tuner works for pre-tuning only
Matching circuit
  Position sensitivity is too high
    Drive the tuner through 1m rod
    The beam tuning range is only about 0.4mm
    Beam current is too sensitive to position
  Movable RF contact (fingerstock)
    fragile
Notes: TEL2341

## Slide 5
Proposal for e-gun tuner
DCCT
ACCT
Proposal for e-gun tuner control
The ACCT is just after E-gun.
The ACCT signal could be used for feedback control.
A pneumatic tuner mechanism is proposed to improve tuning control.

## Slide 6
Outline
  300kV RF modulated thermionic Gun
    650MHz
  SRF cryomodules performance
    Field emission
    RF stability
  High power RF system
    Klystron and Waveguide system
    KPS
  Discussion
In future

## Slide 7
Cryomodules
Box cryomodule with a top-loading cold mass;
  One/two nine-cell 1.3GHz cavity
  Two/four 50kW power couplers
  HOM coaxial dampers
4K/2K heat exchanger unit with JT valve on board;
Scissor tuner with warm motor;
LN2 cooled thermal shield;
4K intercepts cooled by syphon circuit from 4K tank;
2 layers mu-metal shield
WPM alignment system
ICM 2K static load is 5.0W
ACM1 2K static load is 10.9W

## Slide 8: EINJ field emission and pulse conditioning
EINJ Q0 deterioration due to operational mistake during venting and pumping
  Vented EINJ RF space in 15 minutes in 2016.
  10 Torr pressure step during pumping in 2017
    a pressure step between 716Torr to 708Torr (cavity was lower side).
Could not run @ 10MV/m
Could run @ 10MV/m with strong x-ray after pulse conditioning
Notes: We have to move einj offline for Vecc cryomodule(ICM2) commissioning

## Slide 9: EINJ field emission and pulse conditioning
Continue pulse conditioning
  During pulse conditioning, we use a beam loss monitor to measure the x-ray
  Run CW after pulse conditioning to check the progress
Moderate pulse conditioning
  11MV/m~ 13MV/m 15ms~20ms LLRF self-excited pulse, 1~10Hz
High gradient pulse conditioning
  Signal generator, 3ms, up to 16~16.3MV/m
  sometimes it becomes worse
Moderate pulse conditioning is more efficient
Stuck and hard to improve
10MV/m
Notes: Continue pulse conditioning

## Slide 10
Field emission controlled by high power pulse conditioning
    Improved after conditioning
    Strong field emission at 10MV/m
Refurbished the EINJ cavity in clean room and restored the performance
    We found the pickup antenna and flange burned
    Might be burned by field emission electrons
Refurbish EINJ during 2020-2021 shutdown

## Slide 11: Slow venting and Pumping
During the 2020-2021 shutdown, we installed a venting/pumping system on CMs
  control pressure changing rate through MFC(mass flow controller);
  A new PG has been installed to monitor the pressure.
Venting takes 7 hours for EINJ
  With Max. 120 sccm(standard cubic centimeter per minute) flow rate
Slow pumped EINJ 5 days(3 days+ weekends) – too slow
  Need a bigger MFC for pumping line or a bypass pumping line

## Slide 12
EACA 1st cavity Q0 deterioration during warming up /cooldown
After 2018 cooldown, 1st CAV Q0 was about 6e9@10MV/m
  Moderate pulse conditioning, push Q0 to 9.4e9@10MV/m
After 2020 cooldown, 1st CAV Q0 was 4e9@10MV/m
  was pushed to 8.6e9@10MV/m and 7.27e9@11MV/m.
  Quench at 14.57MV/m with 3ms pulse and Q0 drop to 5.2e9@10MV/m
  After moderate pulse conditioning and CW operation, Q0 recovered to 8e9@10MV/m
    During day-to-day 20MV CW operation, EACA vacuum kept improving from 1e-9Torr to 5e-10Torr
Notes: 20200824data

## Slide 13
Reprocessed EACA in 2018
Both of EACA cavities show Q0 deterioration with time
  extra cryogenic load and x-ray limit the gradient
EACA Cavities performance by year

## Slide 14: EACA RF Stability
Amp
Power Divider
Vector Sum
Tuner Loop 2
Tuner Loop 1
Cavity 1
Cavity 2
Att
C1~0
C2~0
A
EACA cavities are driven by a single klystron in Vector Sum
Under certain conditions, individual cavity voltages can oscillate in counterphase causing an instability in the beam energy
  The instability is driven by coupling between cavity mechanical vibrations and `the Lorentz force
  Mitigation: 1. reduce microphonics 2. appropriate choice of detuning parameters
Vsum
V1
V2
V1
V2
LLRF compensation and mitigation of two cavity instability. Ramona LEEWE ,TTC2019,Vancouver

## Slide 15
Beam energy Stability without beam loading
After Microphonics suppression, Piezo installation and LLRF watchdog upgrade, we could run EACA smoothly
Relative fluctuation of the beam energy measured at a dispersive location over a period of time of > 30 min. FWHM= 0.09%.
37 hours of uninterrupted operation of EACA at 20MV vector sum
RF stability demonstration

## Slide 16: 30MeV/ 10kW
Pulse profile after EINJ
Pulse profile on EHD dump
Adaptive feed-forward (ILC-- Iterative Learning Feedforward Controller) compensation when running in pulsed mode
  There are energy fluctuations in a single pulse (microphonics?) and between pulses (current stability?)
  The beam energy stability is 0.4%

## Slide 17
EACA 20MV vector sum
100Hz harmonics
  Manual FF has stronger harmonics
  ILC could suppress the harmonics
  Need to study the correlation between the beam loading and feed forward compensation
Notes: 20210120 data

## Slide 18
Outline
  300kV RF modulated thermionic Gun
    650MHz
  SRF cryomodules performance
    Field emission
    RF stability
  High power RF system
    Klystron and Waveguide system
    KPS
  Discussion
In future

## Slide 19: Klystron
Klystron and waveguide distribution system
  CPI VKL 7967A
    1.3 GHz, 300 kW, CW Klystron with 58% efficiency, 6 MHz bandwidth.
  During operation, we had few water related problem
    Flow meter failure
    Klystron RF window cooling channel clogged
      The channel section is 1mm*1inch
      Found some rubber seal materials
    Water contaminated the high voltage isolation oil
      Huge Water leak in collector cooling circuit (INLET) of Klystron 1; rubber gasket is broken due to high pressure of hot water from pump.
      The water went to oil tank through the gaps
      The Klystron isolation ceramic burn during HV test
      Replaced the oil, seal the gaps and protect klystron with plastic film

## Slide 20: Waveguide distribution system
Waveguide Damper material melt (Polyurethane)
  Applied too much stress on waveguides during damper installation;
    The alignment changed, and there was an RF leak on the power divider flange
    The temperature was up to 100C with about 19kW RF power
    The damper melted and went into the waveguide
  removed the damper and cleaned the flanges.
  Re-aligned the waveguides.
Few water leaks event for phase shifter, power divider
Klystron Power Supply (KPS )
  3/96 high voltage modules failure
    two of them broken during a campus power bump
  Maintenance on filament power supply, magnet power supply, flow meter, fan controller, etc.,
  Connect 12.5kV AC to KPS causes a power fluctuation (Electromagnetic Compatibility)
    It happens at ‘standby’ stage, the high voltage is still off
    Trip Cyclotron magnet power supplies
    Contactor failure on high voltage modules
      Upgrade the module FPGA code

## Slide 21: Discussion
A new E-gun RF matching circuit tuner is under development and we plan to add feedback control with an ACCT signal.
SRF cryomodules had been refurbished in the last few years.
The cavities show Q0 deterioration with time
  Causes extra cryogenic load and x-ray.
  Slow venting and pumping system has been implanted.
  We use 11~13MV/m moderate pulse conditioning to reduce field emission.
  Periodic Helium conditioning might be helpful( procedure? And parameters?)
The beam energy stability in pulsed mode is 0.4%
  This should improve after better beam intensity control

## Slide 23: 31MeV Beam to EHD
EINJ--- was 8.5MeV(after refurbish EINJ could output 10MeV beam)
EACA---22.5MeV
EINJ was limited by strong x-ray and EACA JT valve fully open

## Slide 24: Pulse conditioning for VECC cryomodule
During ICM2 commissioning, we used 11~12MV/m, 5~15ms, 1~10Hz pulse conditioned cavity
1-week moderate pulse conditioning
VECC cryomodule is a twin sister of EINJ