## Slide 1
TRIUMF Science Week 2022, July 18-22, 2022, Vancouver (BC), Canada
MYRRHA
Accelerator Driven Systems; the path towards sustainable Nuclear Energy
Hamid AÏT ABDERRAHIM
DDG SCK CEN, Director of MYRRHA
SCK CEN, Boeretang 200, B-2400 Mol, Belgium
haitabde@sckcen.be or myrrha@sckcen.be

## Slide 2: Accelerator Driven System: intrinsic safety
To keep the reactor operating we need CW proton beam with very high reliability
Notes: video vertragen

## Slide 3: Fission generates high level radioactive waste
U235
n
Pu
Np
Am
Cm
Actinides
Minor Actinides
Neutron
Uranium
Fission
Fuel
U238
n
n
n
U235
U238
Plutonium
Neptunium
Americium
Curium
Source: SCK•CEN MYRRHA Project Team
FP
FP
After 4,5 years the spent nuclear fuel contains:
  94,7% of resources we can recycle (U+Pu)
  5,1% of nuclear waste with low radiotoxicity (FP’s)
  0,2% of high radiotoxicity nuclear waste
1 ton of nuclear fuel used 4,5 year in commercial PWR reactor produces electricity for 100,000 Belgian families per year (3500 kWh/y per family)


## Slide 4: Partitioning & Transmutation
vs
Just like for classical household waste we need sorting and then valorizing through recycling
Partitioning
  Separate the ingredients of the spent fuel in “similar” categories we can treat in a similar way
Transmutation
  Use intense neutron field to transmute isotopes into others, less “nasty” and producing energy (circular economy)

## Slide 5: Possible Fuel Cycles for High Level Waste treatment
1 ton UO2 used fuel (50 GWd/t)
93,5 % U
1,2 % Pu
0,2 % MAs
Vitrified with FPs
(in 2)
Transmuted is ADS
(in 3)
~5,1 % FPs
1- Once Through
No Reprocessing
Spent fuel considered as HLW to go in Geological Disposal
Presently adopted in USA, SE, FIN
Decision for industrial Geol. Disp. construction taken in SE & FIN not yet in USA
Radiotoxicity of HLW for more than 300,000 y
Industrial scale

## Slide 6: Possible Fuel Cycles for High Level Waste treatment
1 ton UO2 used fuel (50 GWd/t)
93,5 % U
1,2 % Pu
0,2 % MAs
Vitrified with FPs
(in 2)
~5,1 % FPs
1- Once Through
No Reprocessing
2- Todays Recycling
PUREX
All 1 ton spent fuel considered as HLW to go in Geological Disposal
Presently adopted in USA, SE, FIN
Decision for industrial Geol. Disp. construction taken in SE & FIN not yet in USA
Burden of HLW for more than 300,000 y
Industrial scale
Industrial scale
U + Pu recycled in PWRs or BWRs
No recycling of MOX fuels
FPs + MAs vitrified and to go to Geolo. Disp.
Presently adopted in FR, JP, …
No formal decision for industrial Geol. Disp. yet
Radiotoxicity of HLW for more than 10,000 y

## Slide 7: Possible Fuel Cycles for High Level Waste treatment
1 ton UO2 used fuel (50 GWd/t)
93,5 % U
1,2 % Pu
0,2 % MAs
Vitrified with FPs
(in 2)
Transmuted is ADS
(in 3)
~5,1 % FPs
1- Once Through
No Reprocessing
2- Todays Recycling
PUREX
3- Advanced Recycling (P&T)
All 1 ton spent fuel considered as HLW to go in Geological Disposal
Presently adopted in USA, SE, FIN
Decision for industrial Geol. Disp. construction taken in SE & FIN not yet in USA
Burden of HLW for more than 300,000 y
Industrial scale
Industrial scale
R&D level
U + Pu recycled in PWRs or BWRs
No recycling of MOX fuels
FPs + MAs vitrified and to go to Geolo. Disp.
Presently adopted in FR, JP, …
No formal decision for industrial Geol. Disp. yet
Burden of HLW for more than 10,000 y
U + Pu recycled in PWR or FR
MAs in ADS
MA are turned in FPs to go to Geolo. Disp. In specific packaging
Presently R&D programme (FR, JP, BE, DE, EU, CN, ROK, USA)
Radiotoxicity of HLW for ~300 y

## Slide 8
Natural Uranium
1
Spent
Nuclear
Fuel
1000
300 years
+10,000 years
+300,000 years
Todays Recycling
PUREX
Once through
no reprocessing
Radiotoxicity
Advance Recycling (P&T)

## Slide 9: European Strategy for P&T (2005) with objective of possible industrialisation from 2040
EU P&T Strategy 2005: “The implementation of P&T of a large part of the high-level nuclear wastes in Europe needs the demonstration of its feasibility at an “engineering” level. The respective R&D activities could be arranged in four “building blocks”:
Source: European Commission Strategy Paper on Partitioning & Transmutation (2005)
P&T building blocks |  | Description | Name & Location
 | Partitioning | Demonstrate capability to process a sizable amount of spent fuel from commercial Light Water Reactors to separate plutonium, uranium and minor actinides | Atalante (FR)
 | Fuel production | Demonstrate the capability to fabricate at a semi-industrial level the dedicated fuel needed to load in a dedicated transmuter | JRC-ITU (EU)
 | Transmutation | Design and construct one or more dedicated transmuters | MYRRHA (BE) ASTRID (FR)
 | MA Fuel Partitioning | Specific installation to process fuel unloaded from transmuter Not necessarily the same as type to process original spent fuel unloaded from commercial power plants | 
The European Commission contributes to the 4 building blocks and fosters the national programmes towards this strategy for demonstration at engineering level.
1
2
3
4

## Slide 10: Technology Readiness Level (TRL)
Advanced partitioning = “sorting of the waste” beyond classical PUREX
  TRL = 7 ~ 8
Fabrication of dedicated transmutation fuel (loaded with Minor Actinides)
  TRL = 3 ~ 4
Pre-Industrial sized transmuter demonstration (MYRRHA)
  TRL (FR = 9, ADS = 4 ~ 5 after building MYRRHA  9)
Advanced reprocessing of transmuter fuel (≠ from 1, Pyroreprocessing as the most promising)
TRL = 3
Advanced fuel technological aspects: transportation, cooling, and handling
TRL = 3 ~ 4
NSC Task Force on Demonstration of Fuel Cycle Closure including Partitioning and Transmutation (P&T) for Industrial Readiness by 2050 (TF-FCPT) with experts from Belgium, France, Japan, Russia, UK, US and EC

## Slide 11: Three options for Minor Actinide (MA) transmutation
Core safety parameters limit the amount of MA that can be loaded in the critical core for transmutation, leading to transmutation rates of:
  FR = 2 to 4 kg/TWh
  ADS = 35 kg/TWh (based on a 400 MWth EFIT design)
 ADS performs the best
FR
heterogeneous
FR homogeneous
ADS
Driver fuel
Blanket with MA
Fuel with MA
Blanket
Fuel with MA

## Slide 12
Europe should go for a regional approach (see PATEROS, ARCAS)
Countries with different nuclear energy policies to collaborate together
  Countries willing to continue Nuclear Energy
  Countries willing to develop fast reactor systems
  Countries in nuclear phase out, interested in Partitioning &Transmutation (P&T)
Source: [TBD]
Shared & efficient solution for Minor Actinides management
EU case with 144 power reactors using EFIT 400 MWth
15 EFIT * 400 MWth = 6000 MWth
For all EU HLW treatment
Doel (BE) = 9000 MWth
Tihange (BE) = 9000 MWth
Gravelines (FR) = 17118 MWth
Zaporizhzhya (UA) = 18000 MWth
Bruce (CND) = 18702 MWth
Kashiwazaki-Kariwa = 23895 MWth

## Slide 13: Transport issues of MA-Fuels FR vs ADS
Reprocessing &
Fuel Fabrication
FR
FR
FR
FR
FR
FR
FR
FR
FR
Transmutation in Fast Reactors
Large number of FRs needed
Many transport of MA-Fuels on the roads
Transmutation in ADS
Small units in small number  Single site
Few or no transport of MA Fuel on the roads
Reprocessing &
Fuel Fabrication
ADS
ADS
ADS
ADS
no or limited “on-the-road” transport

## Slide 14: Even with completely different national NE policies European solution for HLW works with ADS
FP6 PATEROS project: Scenario 1 objective: elimination of A’s spent fuel by 2100
A = Countries Phasing Out, B = Countries Continuing
Advantages for A
ADS shared with B
ADS burn A’s Pu& MA
Smaller Fu-Cycle units & shared
Advantages for B
ADS shared with B
ADS burn B’s MA
A’s uses B’s Pu (part) as resource in FR
FR fleet not contam with MA’s
Smaller Fu-Cycle units & shared

## Slide 15: National context evolution (3) 2015 -> Today (National Program on waste management)
In 2014 the national policy for the management of spent fuel from commercial nuclear power plants is the safe storage of spent fuel followed by its reprocessing & disposal or direct disposal
2017: Prospective study on the strategies for the management of Belgian nuclear spent fuel
6 different strategies are assessed:
    Direct disposal
    Classical reprocessing of full inventory & disposal
    Partial reprocessing
    Advanced separation (P&C)
    Partitioning & Transmutation (P&T)
    Additional research

## Slide 16: Belgian geological repository: impact on gallery length (km)

## Slide 17: Belgian geological repository: impact on footprint (km²)

## Slide 18
 Transmutation demonstration
 ADS at pre-industrial scale
 Flexible irradiation facility
600 MeV
Linear accelerator
100 MeV
Phase 1
Phase 2
Phase 3
Sub-Critical Reactor
Pb-Bi Cooled
MYRRHA: Accelerator Driven System
Notes: What is MYRRHA
What offers

## Slide 19
MYRRHA’s Application Portfolio
Radio-isotopes
Fundamental research
Multipurpose
hYbrid
Research
Reactor for
High-tech
Applications
Fusion
SNF*/ Waste
*SNF = Spent Nuclear Fuel
Mat.& Fuel GEN IV
Support to
SMR LFR
Notes: What is MYRRHA
What offers

## Slide 20
Phase 1 – 100 MeV
+ Proton Target Facility
Phase 2 – 600 MeV
Source: SCK CEN MYRRHA Project Team
MYRRHA’s phased implementation strategy
Phase 3 – Reactor
UNDER CONSTRUCTION
MYRRHA phase 1 = MINERVA
(see next presentation by Adrian FABICH
Notes: OK

## Slide 21: MINERVA implementation by 2026
Overall architecture frozen, main internal floor plan decisions taken
PTF design close to level of ACC, FPF catching up

## Slide 22
NF ACC
Outline Basic Design phase
  3D data model
    determines minimum level of detail (LOD 100) of all SSC
    links ‘all’ information
    tool for integration of SSC

## Slide 23
NF PTF
Conceptual Design phase
  3D data model
    minimum LOD 100, higher level reached
    primary systems included
Strong & Fruitful collaboration between TRIUMF and SCK CEN for the development of ARIEL and ISOL@MYRRHA

## Slide 24: SC single spoke cavities & cryo module
Prototyping progressing at collaboration partner IJCLab (FR)
Production of pre-series single spoke cavity parts
is ongoing at RI (DE)

## Slide 25
Injector test stand established at CRC (LLN-BE)
SCK CEN operates an injector test-stand consisting of:
ECR ion source
LEBT
  2 solenoids
  Alison scanner, Faraday cup,…
  Fast beam chopper
RFQ
  4 rod design
  Powered by up to 160 kW RF solid state amplifiers
  176.1 MHz
2 quarter wave rebunching RF-cavities
In fall, a emittance meter and a bunch shape monitor will be added
Target beam current/cycling achieved
RFQ commissioned with >95% transmission
Beam energy confirmed after the RFQ by ToF

## Slide 26
MYRRHA Reactor: implementation in 2036
Objectives = transmutation + radioisotopes + fusion material r&d + Fission technology platform

## Slide 27
MYRRHA reactor Highlights

## Slide 28: MYRRHA reactor primary design Rev. 1.8, frozen end 2020
Integrated Pool-type concept with LBE coolant
Fuel assemblies: hexagonal bundles of cylindrical wire-spaced fuel pins (MOX fuel 30wt.% Pu)
4x heat exchangers: double-walled with leak detection; water/steam on secondary side
2x primary pumps: vertical shaft mixed-flow design
Bottom core loading: single in-vessel fuel handling machine (IVFHM)
Safety vessel integrated into the primary vessel

## Slide 29: MYRRHA Core design for multipurpose R&D : Subcritical core layout
fuel assembly (78)
control rods (3)
experiments (6)
thermal islands (3)
reflector (42)
beam tube + spallation target
Source: L. Fiorito, 2019
Notes: This is the layout selected for the subcritical core revision 1.8
It contains 78 hexagonal FAs (in white) with 30% MOX fuel
6 experiments for material irradiation are loaded close to the spallation target in correspondence of the multifunctional channels where the neutron flues are the highest
3 thermal islands for Mo-99 production, farther from the center to not disrupt the flux, but close enough to have enough neutrons

## Slide 30: MYRRHA: World Class Technology complex to serve HLM SMR development
LiLiPuTTeR-II
HELIOS 3
HLM Lab
MEXICO
CRAFT
LIMETS 3
RHAPTER
COMPLOT
ESCAPE
Ultrasonic Lab
GUINEVERE
Material development & testing
Lead-Bismuth Chemistry & Conditioning
Component testing & Thermal Hydraulics
Instrumentation & Visualisation
Lead Zero Power Reactor

## Slide 31: Belgian Government decision of 7 September 2018 Confirmed on 23 July 2021 (+ creation of MYRRHA NPO)
Decision to build MYRRHA as large new research infrastructure in Mol, Belgium
Belgium allocates € 558 m for 2019-2038
  2019-2026: construction of MINERVA (linac 100 MeV + PTF & FTS)
  2019-2026: design, R&D and licensing for Phases 2 (extended linac 600 MeV) & 3 (reactor)
  2027-2038: MINERVA operations (linac 100 MeV)
Establishment of international non-profit organisation
MYRRHA AISBL/IVZW
Decided 23.07.2021
Created 17.09.2021
Government support for establishing MYRRHA partnerships
  Belgium appoints tutorship ministers to promote and negotiate international partnerships
Source: Belgian minister of Energy, Environment & Sustainable Development

## Slide 32: How to participate in MYRRHA

## Slide 33: MYRRHA AISBL/IVZW official from 16 December 2021

## Slide 34
MYRRHA AISBL: separate legal entity needed to find external partners/investors
Responsability:
  SCK CEN
  Design & build MINERVA
  Conduct R&D for phases 2 ACC-600 & 3 MYRRHA Reactor
  Obtain licenses for Phase 1 and later on for Phases 2 & 3
  Being the nuclear operator of MYRRHA/MINERVA
  MYRRHA AISBL
  Establish the MYRRHA International Consortium
  Guarding the overall scope of MYRRHA programme
MYRRHA
MYRRHA
International nonprofit
organisation
ANS
MDB
Notes: Spreker: Hamid Aït Abderrahim
En nog een organisatiewijziging: MYRRHA
  Aparte rechtsstructuur: ‘internationale vereniging zonder winstoogmerk’
  Blijvende ondersteuning van SCK CEN
  de belangstelling van buitenlandse partners voor een instap in het project stimuleren / internationale investeerders samenbrengen

## Slide 35: MYRRHA AISBL/IVZW: Membership
Member categories :
  Founding members : Belgian State and SCK CEN
  Contributing members open for :
    Countries
    National Research Organisations, industries of a country
    International Institutions or Associations
Rights & Obligations
  Contribution in-cash or in-kind to become contributing member
  from 40 M€ contribution :
    1 Director in the Board of Directors (overall maximum of 4)
    1 Voting right in the General Assembly per 40 M€ contribution
  Annual membership fee <100 k€ on proposal of BoD (right of nomination of a representative in the International Scientific and Technical Advisory Board (ISTAB)

## Slide 36: Conclusions
2018
Positive decision
Ground breaking Q2-2023
Belgium sends a strong signal about its ambitions:
Maintaining a high level of know-how in the nuclear field
Becoming an international pole of attraction for young talents in nuclear applications
Convert innovations into solutions for societal challenges (nuclear waste, nuclear medicine, sustainability)
Encourage and welcome international cooperation and partnership

## Slide 37
Copyright © 2022 – SCK CEN
PLEASE NOTE!
This presentation contains data, information and formats for dedicated use ONLY and may not be copied, distributed or cited without the explicit permission of the SCK CEN.
If this has been obtained, please reference it as a “personal communication. By courtesy of SCK CEN”.
SCK CEN
Belgian Nuclear Research Centre
Stichting van Openbaar Nut
Fondation d'Utilité Publique
Foundation of Public Utility
Registered Office: Avenue Herrmann-Debrouxlaan 40 – B-1160 BRUSSELS
Operational Office: Boeretang 200 – B-2400 MOL