## Slide 1: Progress towards a measurement of the neutron electric dipole moment using a world-leading ultracold-neutron source at TRIUMF
Wolfgang Schreyer on behalf of the TUCAN collaboration
TRIUMF Science Week 2022

## Slide 2: Neutron Electric Dipole Moment violates CP symmetry
Violates T & CP symmetry  may explain matter-antimatter asymmetry
Test of beyond-Standard Model theories
Can be detected by measuring precession frequency in electric + magnetic field
T
Figures by D. Ries https://www.youtube.com/watch?v=QBKPQFUdDB0

## Slide 3: Ramsey’s method
“Separated oscillatory fields”
Figures by D. Ries https://www.youtube.com/watch?v=QBKPQFUdDB0

## Slide 4: Ultracold neutrons are the ideal tool for nEDM searches



Totally reflected by many materials
(Fe: 209 neV, Ni: 245 neV)
Interact with magnetic
field (60.3 neV/T)
Convert cold neutrons to ultracold through phonon-scattering
1 meV  100 neV
Influenced by gravity (103 neV/m)

## Slide 5: A great way to annoy theorists
dn < 1.8 x 10-26 ecm (90% C.L.) C. Abel et al., Phys. Rev. Lett. 124, 081803 (2020)
Many groups pursuing ~ 10-27 ecm measurement as next step
2020
2030
PSI
TUCAN, others
SNS
Adapted from https://en.wikipedia.org/wiki/Neutron_electric_dipole_moment
New UCN source
technology

## Slide 6: Goals of the TUCAN collaboration
Search for nEDM at 10-27 ecm sensitivity
Build the world’s strongest UCN source
Provide a second UCN delivery port as a user facility

## Slide 7: A unique spallation-driven UCN source using superfluid helium
(480 MeV cyclotron)
(300 K)
(20 K)
(MeV)
(neV)
tungsten
He-II (1.1 K)
phonon
UCN-production cross section in superfluid helium
Cold neutron
(meV)

## Slide 8: Neutron spallation source
Fast kicker magnet to share proton beam with CMMS
10.1016/j.nima.2019.01.074
10.1103/PhysRevAccelBeams.22.102401

## Slide 9: Prototype source (decommissioned 2020)
Pumping ducts
UCN guides
UCN detectors
Pumps
Spallation target
3He Cryostat
D2O (20 K)
4He (0.9 K)
UCN valve
Helped us learn a lot during three runs (2017 – 2019):
Potential performance bottlenecks, clogging issues
Tested UCN guides (polishing, NiP coatings), valves, polarizers & detectors
S. Ahmed et al., Phys. Rev. C 99, 025503 (2019)
0
1
m

## Slide 10: Performance of prototype source
S. Ahmed et al., Phys. Rev. C 99, 025503 (2019)
UCN lifetime in He-II strongly dependent on temperature  need low temperature, high cooling power
PRELIMINARY

## Slide 11: TUCAN source
B4C-filled panels
Graphite
D2O
LD2
He-II
Target
Steel shielding
Steel
shielding
To nEDM
To 2nd port
Concrete shielding
Concrete shielding
3He cryostat
LD2 cryostat
3He-4He heat exchanger
Supercond. polarizer
40x proton-beam current
Optimized moderator geometry
Liquid deuterium moderator
4x He-II production volume
40x cooling power (10 W @ 1.1 K)
800x UCN-production rate (1.5x107)
W. Schreyer et al, Nucl. Instrum. Meth. Phys. Res. A 927, 101-108 (2019)
0
1
m

## Slide 12: Superfluid-helium converter vessel
Machined, thin-walled Al domes to minimize neutron absorption and heat load
UCN-reflective NiP coating: Measured UCN storage lifetime at LANL in 2021  higher loss rate than expected, but acceptable
Superfluid-tight: Undergoing extensive leak checking
He-II vessel
LANL UCN source
UCN valve

## Slide 13: Moderator vessels
Machined, thin-walled Al domes to minimize neutron absorption
Withstand potential D2 explosion pressures
Machining finished, preparing to start complicated assembly
D2O
LD2
He-II
0.8 m

## Slide 14: Cooling power: 10 W at 1K
3He fridge built & tested in Japan, shipped to TRIUMF in 2021
Pumps arrived 2021
Undergoing acceptance tests
3He pumping
4He pumping
UCN
3He pumping
3He-4He heat exchanger designs

## Slide 15: Lots of infrastructure
33 m-long liquid-helium transfer line
Large pumps to cool cryostat
Power
Cooling water
PLC
Pumping ducts
Piping for four different gas systems

## Slide 16: Radiation shielding
2021:
Reconfigured radiation shielding, foundation for moderator & cryostat installation
Original shielding
Removing prototype source
Reconfiguration
Service installation
Covering up

## Slide 17: TUCAN EDM
Magnetically shielded room with sliding door
UCN switch
Spin analyzer, & detector x 4
Dual (top/bottom) measurement cells &
Hg comagnetometer
Self shielded B0 coil
(box cos theta)
Polarized UCN
3.5m

## Slide 18: Magnetic shielding
Shielded room installation starting this month
Internal coils nearing construction
0.75m
3.5m
Prototype shield

## Slide 19: Magnetometry
Operating 5 optical Cs magnetometers & 5 more on order
Hg comagnetometer prototype achieved 10s free precession, 1 pT resolution Goal: 10 fT

## Slide 20: Precession cell
Recently tested at J-PARC UCN source: Prototype cell & valve, polarizers, detectors
HV discharge testing of electrodes, insulators, coatings, comag gases

## Slide 21: Outlook
Q3 2022:
Cryostat installation
Start shielded room installation
Q4 2022:
First cryostat test
Q1 2023:
Moderator installation
Complete radiation shielding
Q2 2023:
Full cryostat commissioning
Shielded room installation complete
Q4 2023:
First UCN production
Goals
Search for the neutron electric dipole moment with a sensitivity of 10-27 ecm
Build the world’s strongest ultracold-neutron source
Provide a UCN port for other users

## Slide 22
2022 virtual collaboration meeting
Thank you