## Slide 1: UCN handling for UCN source and EDM experiment
R. Picker
Picture: 3He gas panel

## Slide 2
UCN handling components for the source
UCN production volume
(bottle)
1.2 K
UCN guide bottle to HEX
HEX to thermal
transition guide
Thermal transition guide
UCN valve
SC
polarizer
Warm bore guide with
vacuum separation foil
Y switch
2nd port
EDM port
shielding
RT guides
HEX
Pressure bypass
UCN source cryo guides
Burst disk guide
Pump out port
UCN source RT
guides
Polarized RT
guides
Vacuum tight valve

## Slide 3
UCN handling components for the source
EDM switch
Spin flipper
EDM-y guide
EDM guides
EDM cell insulator
EDM ground electrode
EDM HV electrode
SSA
6Li detector
polarizer
polarizer
SSA guide
from EDM port
EDM cell valve

## Slide 4
Requirements
General UCN guide requirements
Wall Fermi potential: 212 neV (NiP) or higher (NiP coating) (except for EDM cell)
Smooth inner surfaces (mirror finish surface, very few scratches allowed, will we do acceptance test on the surfaces?)
  In the simulation we assumed 3% diffuse reflection - how does this correlate with any measured surface roughness…?
Vacuum level inside guides better than 10-6 mbar
UCN source cryo guides
Temperature range: 0.8 K to 450 K
Superfluid tight (Helicoflex delta seals?)
Wall Fermi potential: 212 neV (NiP) or higher (NiP coating)
All requirements are recursive.

## Slide 5
Requirements and questions?
UCN production volume (bottle)
Bottle to HEX guide
Base material shall have low beam heating and low neutron absorption (Al or better AlBeMet or Be)
Inside surface shall be smooth (better for baking)
Metal sealed flange to HEX to bottle guide
Size: ca 340 mm diameter, ca 490 mm long (from moderator optimization)
Superinsulation necessary on outside? (cryogen relief calcs will inform)
Heaters necessary around bottle?
Base material should have low beam heating and low neutron absorption (Al)
Inside surface shall be smooth (better for baking)
diameter: 150 mm? (see Steve’s presentation)
Length: ??
Superinsulation necessary on outside? (cryogen relief calcs will inform)
Heaters on the outside
Extraction height from bottle (see Steve’s presentation)
Owners: CM (mechanical), SK, RM (coating), RP (AlBeMet)
Owners: CM (mechanical), RM (coating)

## Slide 6
Requirements
HEX
HEX to thermal transition guide
Base material should provide best conductivity (OHFC copper, which grade?)
Inner diameter: 150 mm?
Length: 600 mm?
Can the HEX be baked?
Contains liquid helium surface
Diameter shall neck down to reduce film flow above liquid surface (Which diameter? Need PENTrack sims and film-flow heat-input estimation)
Film burner required? Knive edge required?
Elevation gain? (PENTrack simulations…) Height of liquid level? (Pressure head calcs…)
Pump-out port and burst disk shall be located along its length
Thermal anchors are necessary to reduce heat input into superfluid
Thermal radiation should be minimized through its design
Thermal transition guide must have low thermal conductivity (either thin walled stainless or titanium?)
Owners: SK
Owners: CM (mechanical), RM (coating), ? (film flow suppression), ? (thermal anchors)

## Slide 7
Requirements
Burst disk
Pump-out port
Required since there is a vacuum tight valve downstream and the guides contain a cryogen
Diameter required (relief calcs…)
Current vertical source design good enough? (Fall 2018 experiments!)
Required to pump the UCN source guides out well to achieve long UCN storage lifetimes
Required opening? (How to determine?)
Similar design as horizontal source?
Owners: CM
Owners: CM?, SK?

## Slide 8
Requirements
Source UCN vacuum valve
SCM warm bore guide, vacuum separation
Stores UCN in source during irradiation so that they don’t have to pass through foil which lowers storage lifetime.
Needs to be vacuum tight in case of problems with the window or when pumping out downstream section of UCN guides.
Shall facilitate a good storage lifetime in closed and good transmission in open position.
Body shall have pumping port to facilite pumping of UCN guide at least while in motion.
VAT valve with spreadable protection ring good enough? (Fall 2018 experiments!)
Above valve has CF flanges, adapters to UCN guide are necessary
Can we make it better?
With current SCM, guide diameter probably restricted to 85 mm with warm bore. (Fall 2018 experiments!)
Guide downstream of foil shall be polarization conserving.
SCM guide incl. foil shall be exchangeable without lifting shielding blocks.
Foil and foil mount have to be vacuum tight (leak rate < 10-7 mbar l/s)
Foil shall withstand 100 mbar? pressure difference?
Fermi potential lower than 54 neV (Al or better)
Need pressure equalisation line with pressure activated valve to avoid foil failure.
UCN valve
SC
polarizer
Owners: FK?, RP?
Owners: WS, KH?

## Slide 9
UCN source Requirements
Y-switch
Polarized RT source guides
Horizontal two way switch for EDM and 2nd port.
Shall be compact enough to minimize shielding cavity.
Needs to be service free. (100 000 cycles?)
Good transmission (>80%), virtually no leakage (<0.1%?)
Opening angle < 30O
Needs to be polarization conserving.
Possibility to pump guides through switch housing.
Polarization conserving!
2nd port should have a vacuum tight UCN valve, since switch cannot be UCN tight.
Is NiP on SS good enough? How about NiP on Al?
How about EDM port?
Diameter?
Owners: RP
Owners: RM?

## Slide 10
EDM Requirements
General EDM guide requirements
Smooth surface very important due to their length!
Shall be polarization conserving. Less than 10% loss of polarization to EDM cell, less than 5% loss of polarization from EDM cell to SSA.
Diameter upstream and downstream of Y?
Need to be non-magnetic, at least inside MSR. (How to measure? What’s the criterion?)

## Slide 11
EDM Requirements
Spin flipper
EDM Y guide
Needs non-conducting UCN guide. (NiMo on glass from Movatec? Torsten’s company?)
Spin-flip efficiency > 95%? Or higher? (Fall 2018 experiments!)
Could incorporate diameter change. (PENTrack simulation needed).
Split guides horizontally?
Spin flipper
Owners: SHR?, BJ?
Owners: RM?

## Slide 12
EDM Requirements
EDM switch
SSA
Three way switch: source to EDM, source to detector, EDM to detector.
Polarization conserving!
Transition speed? 2 s?
Pumping position?
Shall have end switches
Spin flip efficiency > 95% (99%?)
Analysing power > 90% (95%?)
Detection efficiency (just Li6 detector) > 90%
Rate capability: 100 kHz? (2.5 x 106 UCN detected after Ramsey cycle)
SSA
6Li detector
polarizer
polarizer
SSA guide
Owners: RP, CM
Owners: BJ, SHR

## Slide 13
EDM Requirements
EDM cell valve (see Sean’s presentation)
EDM cell electrodes and insulator
(see Florian’s presentation)
Good transmission > 95%
Vacuum tight (leak rate < 10-6 mbar l/s?)
Low UCN loss during storage (storage lifetime in EDM cell > 120 s)
Totally non-magnetic (How to measure? What is the criterion?)
Transition time < 2 s?
High voltage compatibility. (12 kV/cm)
Cavity created by valve in EDM electrode shall be small (< 5 mm)
Reliability: > 100000 cycles
Shall have end switches
Abrasion free movement
HV compatible
Non-magnetic
Fermi potential should be bigger than 170 neV (dPS)
Openings for gas inlet, UCN valve in electrode
UV transparent windows for comag lasers (ca 250 nm) and photo detection (850 nm?)
Owners: SV, RP
Owners: FK, RP

## Slide 14
EDM sensitivity intro & parameters
Sensitivity formula
Visibility
α: visibility – 62%
E: electric field strength – 12kV/cm
tRamsey: free spin precession time – 124 s
N: UCN detected – ca 106
α0: polarization at beginning of Ramsey cycle – 95%
twait: time before Ramsey cycle starts – 2 s
tpulse: π/2 flip duration – 2 s
T1: longitudinal depolarization time – 1000 s
T2: transverse depolarization time – 500 s
Storage lifetime in EDM cells – 120 s
16 h of useable average time on beam days
Size of each EDM cell r = 18 cm, h = 16 cm
Time to reach 10-27 ecm: roughly 400 beam days

## Slide 15
Two streams to estimate sensitivity
Analytical
Simulation
UCN storage in source lifetime in source calculated via different contributing ’s
Transport efficiency caclulated via some loss parameters
PENTrack MC simulation from UCN creation in source to closing of EDM cell door
See Steve’s presentation

## Slide 16
What is taken into account in the analytical model?
This is taken into account…
This is not… or not so well…
UCN production/heat input from MCNP simulations
Cryostat performance (pumps, pressure drop, HEX, heat conductivity)
Neutron storage lifetime in source (He liquid + vapor)
Phase space reduction due to wall Fermi potential and height differences
Dilution of neutron “gas”
Simple model of Ramsey cycle
Probable stable daily measurement period
Times for E field change, degaussing etc
Magnetic field of polarizer (it is in MC)
Transport is only modelled via loss per meter, bend, foil etc
Depolarization of UCN during transport (assuming 5% total)
Any systematic effects  nEDM CDR
https://ucn.triumf.ca/resources/proposals/ucn-cdr-2018/EDMsensitivity2018CDRv12.xlsm
Analytical model useful to study many more parameter options than possible in simulation.

## Slide 17
Robustness and mitigations (I)
Kapitza resistance parameter KG
3He Kapitza correction factor
We need KG to be above 20.
Not so critical…
The analytical model is adjusted to fit the simulation and then parameters are varied.

## Slide 18
Robustness and mitigations (II)
Pumping speed
4He temperature (3He cryostat)
3He pump performance requirement is relaxed
Need < 1.2 K
The wiggles are Excel rounding errors…

## Slide 19
Robustness and mitigations (III)
UCN source wall storage lifetime
EDM cell size
Above 40 s is fine.
Source contamination less critical.
Decided against exchangeable UCN bottle.
Risk mitigation strategy in case of lower production

## Slide 20
Robustness and mitigations (II)
Irradiation time (batch mode)
UCN storage time (observation time)
Optimum times can be predicted this way…

## Slide 21
Height of EDM cell
Extraction height out of prod. vol.
Height of upward kink
Fermi potentials (lHe, NiP, dPS) are taken into account
Starting spectrum
x
… can be optimized with this simple analytical model.
1
2
2
1

## Slide 22: Thank you for your attention.

## Slide 23
Influence on production volume temperature (I)
Kapitza Kg
3He Kapitza correction factor a

## Slide 24
Influence on production volume temperature (II)
Correction factor for Ni
Pumping speed

## Slide 25
Influence on production volume temperature (III)
Heat input
Pumping speed

## Slide 26
Parameters used