## Slide 1: Implicit Particle-in-Cell Development for Bounded Plasmas
Nicolas Savard1,2, G. Fubiani3, R. Baartman1, M. Dehnel2
1TRIUMF, 2D-PACE, 3CNRS

## Slide 2: Ion Source Modeling
Ion sources development experimentally focused
Particle-in-Cell has large computational cost at high electron densities - > Impractical!
Implicit Particle-in-Cell scheme claims more than 1000x speedup in high density cases
Can we get speedup that would make implicit practical for engineering?

## Slide 3: Particle-in-Cell Method: Explicit
Simple implementation
Need resolution on order of debye length and plasma frequency: Δx < λDe, Δt < 1/ωp
Disobeying above requirements leads to numerical instabilities!
Makes high plasma density (~ 1018 m-3) simulations for ion sources impractical
Interpolation of particle charge on grid
Solve for fields on grid
Interpolation of fields on particles
Solve for particle motion
Δt
Explicit example:

## Slide 4
Solve Ek+1 given vk+1, xk+1 for particles
Solve vk+1, xk+1 for particles given Ek+1
Implicit Example:
tk+1 = tk + Δt
Fields dependent on future particle phase space and vice versa: non-linear!
Implicit scheme is unconditionally stable and energy conserving
Allows Δx > λDe, Δt > 1/ωp which can offset additional computation
Claims of large speedups!
Particle-in-Cell Method: Implicit
Convergence?
Solved!
Yes
No

## Slide 5
1D energy-and-charge conserving scheme (Chen 2011)
Uses discrete curvilinear mapping to rectangular grid (Chacon 2013)
Programming kept as similar as possible with explicit scheme
Run + average results over 22 us
This Work
Field Eq:
Picard Iteration:
Convergence:

## Slide 6
Benchmark Model: Emmert et.al. 1980
φ
x = 0
x = L
Symmetry Boundary
wall
φwall
1D Ion kinetic equation
Ion source term flux-Maxwellian
Boltzmann electrons
Neumann/symmetric boundary
Metal plate

## Slide 7
Benchmark Match
Te = 5 eV, Ti = 1 eV, <ne> = 2.5 x 1016 m-3, L = 0.05 m
Explicit: Δx = 0.5 λDe (952 nodes), Δt = 0.2/ωp
Implicit: 64 nodes, last cell Δx = λDe, Δt = 2/ωp
Run + averaged over 22 us

## Slide 8
Implicit vs Explicit Timing
Equivalent but large PPC for low # nodes with implicit -> Speedup!
  Not fair as using more particles than necessary in explicit
If field solver dominates particle mover, then implicit will be faster for larger L/ λDe
  Using conjugate gradient solver leads unfair
  multi-grid methods can lead to roughly linear scaling with # nodes
Use Thomas algorithm as best-case O(n) solver
∆xexp
∆ximp
Implicit example
Explicit example
3 PPC

## Slide 9
Changing Number-Simulation-Particles (NSP)
Δx = 0.15 λDe, Δt = 0.05/ωp explicit PIC used as reference for absolute value residual
Other explicit (blue) at Δx = 0.5 λDe, Δt = 0.2/ωp
Implicit needs less particles for accuracy in bulk, but sheath suffers

## Slide 10
Timing for varied NSP
Extra iterations costly for same amount of NSP
Can reduce particles for speedup, but explicit can also be reduced
But… limit to how much particles can be reduced, eventually field dominated
For engineering purposes, 10% accuracy is ok!

## Slide 11
Low-macroparticle Resolution 1018 m-3
128 PPC, Δx = 0.5 λDe, Δt = 0.2/ωp explicit PIC used as reference for residual
Use 32 nodes for implicit, cell at wall has Δx = λDe
8.6x faster for similar accuracy, goes up with density as expected!
12x faster when relaxing convergence criterion

## Slide 12
Future Work
2D bounded plasma: does # macro-particles in volume needed scale with dimensions? How does particle pusher scale with density using multigrid in higher dimensions for fixed # CPUs? Picard iterations necessary for particles lead to slowdown?
Linear interpolation: slower particle mover, but lower macroparticle # needed?
Pre-conditioned Jacobian-Free Newton-Krylov?
1D self-consistent discharge: implicit numerical stability offer greater advantage over explicit?

## Slide 13
References
G. Emmert et.al., “Electric sheath and presheath in a collisionless, finite ion temperature plasma”, Phys. of Fluids 1980
R. Procassini et.al., “A fully kinetic, self consistent particle simulation model of the collisionless plasma-sheath region”, Phys. of Fluids, 1989
G. Chen et.al., “An energy-and-charge-conserving, implicit, electrostatic particle-in-cell algorithm”, J. Comp. Phys., 2011
L. Chacon et.al., “A charge-and-energy-conserving implicit, electrostatic particle-in-cell algorithm on mapped computational meshes”, J. Comp. Phys., 2013
S. Mattei et.al., “A fully-implicit Particle-in-Cell Monte Carlo Collision code for the simulation of inductively coupled plasmas”, J. Comp. Phys., 2017
D. Eremin et.al., “An energy-and-charge-conserving electrostatic implicit particle-in-cell algorithm for simulations of collisional bounded plasmas”, J. Comp. Phys., 2022
G. Chen et.al., “An implicit, conservative and asymptotic-preserving electrostatic particle-in-cell algorithm for arbitrarily magnetized plasmas in uniform magnetic fields”, J. Comp. Phys., 2023