## Slide 1: Intense proton beam production with Compact Ion Sources - ALISES ion sources family developed at CEA Saclay
Olivier TUSKE
Université Paris-Saclay – CEA – Irfu
ICIS 2023 September 18, Victoria, BC, CANADA

## Slide 2: OUTLINE
ECR Ion Sources for light ions production
Intense Beam Problematic
ALISES Ion Source family
Conclusion

## Slide 3: « Typical » LINAC ENVIRONNEMENT IPHI Accelerator 100 mA Proton @3 MeV
Ion Production
and
Electrostatic Acceleration
Transport
and
Beam characterization
SILHI source
9mm
H+ 100 mA
@95 keV
LEBT with diagnostics
Low Energy Beam Transport line
IPHI : Injecteur Proton Haute Intensité (Saclay, France)
SPIRAL2 : Système de Production d’Ions RAdioactifs en Ligne de 2eme génération (Caen, France)
FAIR : Facility for Anti-proton and Ion Research at GSI (Darmstadt, Germany)
IFMIF : International Fusion Materials Irradiation Facility (ITER Broader Approach, Rokkasho, Japan)

## Slide 4: Intense Light Ion ECR Source
High Voltage 95 kV
ECR Heating Process
(Electron Cyclotron Resonance)
Plasma
Ion Source
Diagnostics
LEBT
Size, angle, position and proportion:
EMU; Wires Profiler/Camera; Wien filter
Pentode extraction system
Ground
-3 kV
65 kV
H+ H2+ H3+
D+ D2+ D3+
HF microwave
Magnetic field
Current : Faraday Cup - ACCT / DCCT
Ion Production
and
Electrostatic Acceleration
Transport
and
Beam characterization
H2 / D2
injection
Magnetron
generator
2,45 GHz

## Slide 5: Intense Beam Problematic at Low Energy
Need for a « good / stable » Ion Source
Intensity, energy and emittance value
Reproducibility over time
Reliability (high MTBF)
Easy maintenance (low MTTR)
Context : Injection into RFQ
Pair of SOLENOIDS to control size and angle of beam
PROBLEMATIC: Emittance growth along LEBT
if Space Charge Compensation is perturbed by
  ► Electric field aberrations
  ► Magnetic & Fringe field
  ► Strong focalization while beam transport
Simple solutions:
► Space charge compensation must be effective as soon as possible
► Solenoid length reduction
► Transport beam smoothly
“ The shorter, the better”
RFQ
Notes: What do we call a good or stable ion source ?
The source must fulfill the project requested value for extracted current, energy and emittance.
Naturally those measurements must be reproducible in time
The ion source must be reliable, so that meantime between failure must be the highest
And must have easy maintenance with the shortest the mean time to repair
Our context is to inject the beam into the RFQ so we must control the size and angle of the beam: this is done with a pair of solenoid in the LEBT
The intense beam interacts with the residual gas in the LEBT, it ionize the gas and free electrons are produced. Those electrons remain trapped by the transverse potential of the beam and so reduce the space charge of the beam. We called the process the Space charge compensation
There will be emittance growth in the LEBT if this space charge compensation process is perturbed
This perturbation is effectif if electric field is applied, but even with magnetic field, where the electron motion is diverted
Strong focalization and a cross over introduce an huge electric field that destroy this compensation
So the simple solution to reduce as much as possible this emittance growth is to leave the SCC to be effective as soon as possible
Reduce the Solenoid length
And transport the beam smoothly
In other word : the shorter LEBT, the better

## Slide 6: Emittance growth along LEBT
RFQ entrance
Extraction Hole
Z0
SOLENOID
High voltage
HV platform
IFMIF source
D+ 160 mA
@95 keV

## Slide 7: ALISES : Advanced Light Ion Source Extraction System
Request
► A compact extraction system
to reduce the LEBT length and to reduce Emittance growth along LEBT
► A smaller & cheaper Ion Source
By modifing internal plasma chamber dimensions
Plasma chamber length / internal diameter
Microwave Injection
► An easily maintenable Ion Source
Less people required
Less stress
Reduced maintenance time (MTTR)
Interest
Need

## Slide 8: Proof of Concept - Idea n°1 A compact extraction system
20 cm
Reduction
Z0
ALISES v1
SILHI
Z0
The ALISES concept : Reversed structure
► Put the insulating structure before beam extraction
► ECR resonance obtained with fringe field of a solenoid at ground potential at the beginning of LEBT
► Extraction system is simplified, except for the puller

## Slide 9: Proof of Concept - Idea n°2 A smaller & cheaper Ion Source
RF Injection study
Adjustable gaps
Injection side can be shifted to modify plasma chamber length
Installation of a tube to modify the internal diameter of plasma chamber

## Slide 10: ALISES v1: built with SILHI’ spare parts
ALISES
is not really small
Patent FR 2969371 -2010
Commissioning started
on BETSI in 2012
Notes: On BETSI, we had only a 50kV high voltage power supply and for a start we were really confident that is will be high enough.
So at first we tested the ECR process, without high voltage: as the magnetron was turned on the pink color of the plasma was visible : proving that Hydrogen was ionized with 500 watt of µwave and a reasonable Hydrogen flux.
As the high voltage and the magnetic field was set simultaneously on, the power supply voltage dropped down with a maximum current flow. This behavior was systematic and occurs even without sparks. We suggested that it could be a Penning discharge occurring inside the accelerating column.

## Slide 11: PENNING DISCHARGES 1/3 ExB = shutdown of High Voltage Power Supplies
PHD Thesis : S. Nyckees
Areas where B and E field are not collinear :
► Electrons are accelerated and trapped
► Hit on biased electrodes leading to the shutdown of source HV PS
OPERA Code simulation

## Slide 12: PENNING DISCHARGES 2/3 Simulations Validation with Experiment
Experimental measurements
Simulation validation

## Slide 13: PENNING DISCHARGES 3/3 How to get rid of them !
Fill up the empty spaces under vacuum
► With 5 ceramic parts in the insulating structure
► With glass tube around electrode gaps
Biased up to 23 kV
► 2 months of tests
► Plasma chamber parameters modifications

## Slide 14: Plasma chamber length “Reductio ad Absurdum”
Pressure = 10-3mbar
H+
neutralized
lost
Tiny volume : few H2 molecules for H+ creation
There must be an optimum somewhere between infinite and short plasma chamber length !
First measurements:
@17 kV in pulsed mode
Maximum extracted current for L = 95 mm
Infinite length
No particles
extracted
Few or no
particles extracted
Notes: I need your help ti imagine an very long plasma chamber…

## Slide 15: Plasma Chamber Diameter
Magnetron @2.45 GHz
► TE10 mode rectangular
► TE11 mode in cylindrical
Plasma chamber :
► plasma> 71 mm
Ion Source operating only in Pulsed mode
Plasma Chamber  95 mm
45 mm and 30 mm
Plasma ignition as long as resonant zone is near cavity entrance
EVANESCENT WAVE ?

## Slide 16: Towards ALISES v2
From three to only one smaller insulating structure
Insulator in contact with plasma chamber and wave guide (source body)
Keep the ALISES 1 coil
ALISES v1
ALISES v2
ALISES family roadmap :
LEBT Reduction
Compactness
Easy Maintenance
SILHI performances

## Slide 17: ALISES v2 : Assembly and tests in 2015
Assembly
Leak Tests
HV tests
Alignment & cabling
Installed on BETSI

## Slide 18: ALISES v2 : First beam in 2015
Patent FR 1556871 -2015
Standard plasma chamber length : 100 mm
Standard plasma chamber diameter :  90 mm
Extraction aperture :  6 mm
Electrical insulator in ceramic :  200 mm
Usual settings for the 87.5 mT at plasma chamber entrance
► Icoils = 181 A
No sparks & no Penning discharges !!
Pulsed beam 50% duty cycle @1Hz
Total extracted current = 18mA @35kV

## Slide 19: ALISES v2 : while optimization, unexpected…
IALISES COIL= 108 A
BEST RESULT:
PHF = 980 W, H2 gaz injection = 1.65 sccm
35 mA @ 50 kV, Puller = 22 kV, CW mode
Is It still an ECR Heating?
181A
108A

## Slide 20: ALISES v2 Investigation On Magnetic Field Profile
Magnetic configuration optimization
3 possible working modes :
► Initial ALISES source coil only : Icoil = 181 A
► SILHI-type coil only : Icoil = 115 A
► Tuning with both SILHI-type and ALISES source coils
SILHI-type coil

## Slide 21: Using SILHI type + ALISES type Coils
ISILHI COIL= 104 A
Pulsed Mode
BEST RESULT : PHF = 700 W, @50 kV
Pulsed H2 gas injection = 1.95 sccm Iext = 40.7 mA
CW mode H2 gas injection = 2.10 sccm Iext = 48.5 mA
LEBT BEAM DUMP in CW ► Ibeam dump = 26 mA

## Slide 22: ALISES v2 Plasma Chamber Radial Reduction
Plasma chamber reduction still works!

## Slide 23: ALISES v2 for other Projects
FAIR Project
EMU Debugging
4D Emittance-meter R&D
Irradiation tests of scintillators
Hydrogen beam 35 mA @40 kV extracted from ALISES, 17 mA H+ at the end of BETSI LEBT on beam stop prototype for S3
SPIRAL2 Project
Thermal stress of new beam stop prototype for S3 spectrometer experiment
Emittance measurements with a new Allison scanner for FAIR proton linac injector

## Slide 24: Towards ALISES v3
ALISES v2
ALISES v3
Extraction system simplified
Plasma chamber diameter reduced
Insulator diameter reduced
One Silhi-type Coil
ALISES family roadmap :
LEBT Reduction
Compactness
Easy Maintenance
SILHI performances

## Slide 25: ALISES v3
Compact Ion Source :
► Internal diameter : Ø45 mm
► Aperture hole : Ø6 mm
► Electrical insulator in Ceramic : Ø175 mm
► No platform, the ion source is plugged directly onto the beam line
TROPICS
BETSI
P.25
Tested on the TROPICS test bench in sept-2019
(Test, Research and Optimization for Production of Ions with Compact Sources)
---
Installed on BETSI in 2020

## Slide 26: ALISES v3, Long runs for stability in 2022
Source in pulsed mode, current on beam dump :
► 140 hours (6 days) ~25 mA @ 37 kV
► 85 hours (3,5 days) ~21 mA @ 40 kV

## Slide 27: ALISES v3, Emittance measurements campaign in 2022
P.27
Constant settings :
► Gas : 1,3 sccm
► Frequency : 10 Hz – 10 ms
► HF Power : 600 W

## Slide 28: ALISES v3, toward 100 kV
Initial design adapted for 50 kV :
GAP #1 Plasma ► Puller 20 kV
GAP #2 Puller ► Ground 30 kV
Initial Design
Second Design
Ceramic Second Design (2022) :
was made to increase the path length on ceramic surface between electrodes
Bias voltage increased slowly to 95 kV :
GAP #1 Plasma ► Puller 30 kV
GAP #2 Puller ► Ground 65 kV
Poster session : DUBOIS Augustin, n°71
But for higher extraction voltage, ceramic length between electrode under vacuum were not adapted at all.
 “carbonized” path inside the ceramic in GAP #2
BEST RESULT in early 2023 : PHF = 800 W
Pulsed 40% – 41 mA @ 70 kV
CW – 50 mA @ 76 kV

## Slide 29: ALISES family objectives
P.29
ALISES v3
ALISES family roadmap :
LEBT Reduction
Compactness
Easy Maintenance
SILHI performances
Next Compact Design
► Gas injection system simplified
► Different materials for
plasma chamber & ceramics
► Plasma chamber diameter at 80 mm

## Slide 30: SUMMARY ALISES SOURCES at SACLAY
v2-2015
Ø6
Pulsed – 40.7 mA @ 50 kV
CW – 48.5 mA @ 50 kV
First plasma Nov. 2018 on TROPICS
Installation 2020 on BETSI
v3-2018
95 kV CW mode
Ø9 – 130 mA
Ø6 – 60 mA
1995
v1-2012
Ø6
Pulsed – 21 mA@ 23 kV
ALISES v1
► LEBT reduction
► Penning discharges
► Plasma Chamber size reduction tests
ALISES v3
► Compact source
► Long runs and Beam qualification with EMU up to 65 kV
►Second design of insulator to reach 100 kV
ALISES v2 et v2 mod
► Electrical insulator in single ceramic
► Plasma Chamber size reduction validation
► Some unexplained results
Ø6
Pulsed – 41 mA @ 70 kV
CW – 50 mA @ 76 kV
P.30
We are really close to SILHI performances
Work in Progress!

## Slide 31: Thank you for your attention
Olivier TUSKE – olivier.tuske@cea.fr
Université Paris-Saclay – CEA – Irfu