## Slide 1: X-ray Diagnostics of ECR Ion Sources
Richard Racz
Institute for Nuclear Research (Atomki)
Debrecen, Hungary

## Slide 2: Outlook
What is diagnostics?
Why the diagnostics is needed?
Type of diagnostics?
How the X-ray photons are generated?
Detection of X-ray photons
Soft X-ray diagnostics
Hard X-ray diagnostics
Soft X-ray imaging
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23

## Slide 3: What is diagnostics?
Diagnostics: tests/methods are used to obtain a diagnosis
Diagnosis: recognising a condition, or disease from the signs and symptoms
Signs and symptoms are revealing unnormal operation
So the role of the diagnostics:
To obtain signs and symptoms to control
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23

## Slide 4: Why is it needed?
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23
“we must cultivate our garden.”
The aim: to collect the fruits
For fruits we need healthy tree crowns
For healthy crowns we need regular lifecycle
We should know the indicators of the regular or more efficient lifecycle
To obtain indicators we need diagnostics methods
Once we have indicator we can further improve the crops
Voltaire:
ICIS 2015, New York, USA, Dr. Atsushi Kitagawa:

## Slide 5: ECR diagnostics
The plasma
The heart of the ECR Ion Source
The beam parameters (brightness, emittance, etc.) directly linked to the plasma conditions
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23

## Slide 6: How to obtain information about the plasma
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23
Difficulties to have an access to the plasma

## Slide 7: Type of diagnostics
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23
Local
Langmuir-probes
Intrusive method
Plasma parameters can be derived
Interpretation of the measured curves are difficult
Many type of probes: cylindrical, emissive, probe
Mainly used in semiconductor technique (rf plasmas)

## Slide 8: Type of diagnostics
near
soft
X-ray
hard
far
mid
near
far
10-3eV
10-2eV
10-1eV
1 eV
10 eV
100 eV
103 eV
104 eV
105 eV
106 eV
1 mm
100 µm
100 nm
1 µm
10 nm
1 nm
1 Å
0.1 Å
0.01 Å
10 µm
Visible light
Infrared
UV
RF
Global
Plasma emits EMW
The energy of the photons are corresponding to the different plasma processes
high energy plasma electrons gyro-motion
molecular motion
atom-atom interaction
Or
ion, atom – low energy (cold) electron
warm electron to atom and ion
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23
mainly plasma chamber wall and hot electron interaction
Electrons with this energy are effective for the ionization!

## Slide 9: Processes that prone to X-ray emission
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23
Electron impact:
An+ + e-  A*(n+1) +2e-
A*(n+1)+  A(n+1)+ + hv
Charge exchange:
An+ + B  A*(n+1) + B+
A*(n+1)+  A(n+1)+ + hv
Recombination:
An+ + e-  A*(n-1) + hv
The emitted photon has characteristic energy. Those emissions are isotropic.
Bremsstrahlung:
Electrons are decelerated by the Coulomb interaction 
Continuous spectra from zero to energy of impacting electrons.
Anisotropic.

## Slide 10: Detectors
The incoming photons generate charges
Number of the charges is proportional with the photon energy
Different detectors for different energy domains
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23

## Slide 11: Possible detector arrangement
X-ray
detector
AM
FC
Lead collimation
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23
Collimation by high Z materials

## Slide 12: Methods and its applications
Soft X-ray detection and interpretation of the obtained data
Results obtained by this techniques
K-alpha diagnostics
Results, obtained by this techniques
Hard X-ray detection and interpretation of the obtained data
Results obtained by this techniques
Soft X-ray imaging
Results obtained by this techniques

## Slide 13: Typical spectra in soft X-ray ranges (SDD)
Chart: Energy (eV)
Plasma Bremsstrahlung
Argon K-beta
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23
Using the Kramer’s formula and assuming Maxwellian distribution of the warm electron domain:
In log plot, the inverse slope of the fitted BS gives the spectral temperature
Intersection of the fitted BS with the vertical axis gives a value proportional with the electron density
e.g. in Gumberidze et al. Rev. Sci. Instrum. 81, 033303 2010

## Slide 14: An example: frequency tuning
Mascali et al, REVIEW OF SCIENTIFIC INSTRUMENTS 87, 02A510 (2016)
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23
Strong collimation to measure just the plasma emissions

## Slide 15: K-alpha diagnostics, inner shell ionization rate
C Hombourger: J. Phys. B: At. Mol. Opt. Phys. 31 (1998) 3693–3702.
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23
The K-alpha emission rate from plasma can be used to determine the absolute inner shell ionization.
Why to measure?:
Easy to simulate and easy to measure: code validation
Estimation of EEDF:
R. Friedlin et al Rev. Sci. Instrum. 67, 1261–1263 (1996)

## Slide 16: As an example:response to tuning parameter
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23
M. Sakildien et al. Nuclear Inst. and Methods in Physics Research, A 900 (2018) 40–52

## Slide 17: Typical hard X-ray spectra
Again the Kramer’s formula:
To obtain spectral temperature
!
Up to 1 MeV
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23

## Slide 18: Some example / power dependence
J. Benitez et al IEEE Transactions on Plasma Science 45, 1746 (2017).
VENUS
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23

## Slide 19: Some example: Bmin / BECR dependence
J B Li et al, Plasma Phys. Control. Fusion 62 (2020) 095015
VENUS
SECRAL
J. Benitez et al IEEE Transactions on Plasma Science 45, 1746 (2017).
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23

## Slide 20: Some example: anisotropy
B. S. Bhaskar et al, Plasma Physics and Controlled Fusion 63, 095010 (2021).
14 GHz AECR at Jyvaskyla University
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23

## Slide 21: X-ray imaging in soft X-ray region
Object
Pinhole
Image
For visible light imaging used from the 11th century
The ’simplest’ method for imaging
No lens
Infinite depth of field
Perspective view
The best way for X-ray imaging
X-ray
Plasma
~ 100 um pinhole
X-ray CCD
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23

## Slide 22: X-ray imaging
w
W ~ several 100 um
Since ddet*λ<<w  no diffraction effect
Resolution is in the range of w if do << ddet
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23
S. Biri JINST 16 (2021) P03003

## Slide 23: X-ray imaging (spectrally integrated)
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 2 | 0 | 0 | 0 | 0
2 | 0 | 0 | 0 | 0 | 2 | 0 | 0
0 | 2 | 0 | 2 | 0 | 2 | 0 | 0
0 | 2 | 0 | 2 | 0 | 0 | 0 | 0
0 | 0 | 2 | 2 | 0 | 0 | 0 | 0
2 | 0 | 2 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 2 | 0 | 2 | 0
0 | 2 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 3 | 0 | 0 | 0 | 0
3 | 0 | 0 | 0 | 0 | 3 | 0 | 0
0 | 3 | 0 | 3 | 0 | 3 | 0 | 0
0 | 3 | 0 | 3 | 0 | 0 | 0 | 0
0 | 0 | 3 | 3 | 0 | 0 | 0 | 0
3 | 0 | 3 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 3 | 0 | 3 | 0
0 | 3 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 4 | 0 | 0 | 0 | 0
4 | 0 | 0 | 0 | 0 | 4 | 0 | 0
0 | 4 | 0 | 4 | 0 | 4 | 0 | 0
0 | 4 | 0 | 4 | 0 | 0 | 0 | 0
0 | 0 | 4 | 4 | 0 | 0 | 0 | 0
4 | 0 | 4 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 4 | 0 | 4 | 0
0 | 4 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 5 | 0 | 0 | 0 | 0
5 | 0 | 0 | 0 | 0 | 5 | 0 | 0
0 | 5 | 0 | 5 | 0 | 5 | 0 | 0
0 | 5 | 0 | 5 | 0 | 0 | 0 | 0
0 | 0 | 5 | 5 | 0 | 0 | 0 | 0
5 | 0 | 5 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 5 | 0 | 5 | 0
0 | 5 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 6 | 0 | 0 | 0 | 0
6 | 0 | 0 | 0 | 0 | 6 | 0 | 0
0 | 6 | 0 | 6 | 0 | 6 | 0 | 0
0 | 6 | 0 | 6 | 0 | 0 | 0 | 0
0 | 0 | 6 | 6 | 0 | 0 | 0 | 0
6 | 0 | 6 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 6 | 0 | 6 | 0
0 | 6 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 7 | 0 | 0 | 0 | 0
7 | 0 | 0 | 0 | 0 | 7 | 0 | 0
0 | 7 | 0 | 7 | 0 |  | 0 | 0
0 | 7 | 0 | 7 | 0 | 0 | 0 | 0
0 | 0 | 7 | 7 | 0 | 0 | 0 | 0
7 | 0 | 7 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 7 | 0 | 7 | 0
0 | 7 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 8 | 0 | 0 | 0 | 0
8 | 0 | 0 | 0 | 0 | 8 | 0 | 0
0 | 8 | 0 | 8 | 0 | 0 | 0 | 0
0 | 8 | 0 | 8 | 0 | 0 | 0 | 0
0 | 0 | 8 | 8 | 0 | 0 | 0 | 0
8 | 0 | 8 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 8 | 0 | 8 | 0
0 | 8 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 9 | 0 | 0 | 0 | 0
9 | 0 | 0 | 0 | 0 | 9 | 0 | 0
0 | 9 | 0 | 9 | 0 | 9 | 0 | 0
0 | 9 | 0 | 9 | 0 | 0 | 0 | 0
0 | 0 | 9 | 9 | 0 | 0 | 0 | 0
9 | 0 | 9 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 9 | 0 | 9 | 0
0 | 9 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 10 | 0 | 0 | 0 | 0
10 | 0 | 0 | 0 | 0 | 9 | 0 | 0
0 | 10 | 0 | 10 | 0 | 10 | 0 | 0
0 | 10 | 0 | 10 | 0 | 0 | 0 | 0
0 | 0 | 10 | 10 | 0 | 0 | 0 | 0
10 | 0 | 10 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 10 | 0 | 10 | 0
0 | 10 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 11 | 0 | 0 | 0 | 0
11 | 0 | 0 | 0 | 0 | 11 | 0 | 0
0 | 11 | 0 | 11 | 0 | 11 | 0 | 0
0 | 11 | 0 | 11 | 0 | 0 | 0 | 0
0 | 0 | 11 | 11 | 0 | 0 | 0 | 0
11 | 0 | 11 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 11 | 0 | 11 | 0
0 | 11 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 17 | 0 | 0 | 0 | 0
42 | 0 | 0 | 0 | 0 | 73 | 0 | 0
0 | 50 | 0 | 40 | 0 | 30 | 0 | 0
0 | 72 | 0 | 11 | 0 | 0 | 0 | 0
0 | 0 | 56 | 47 | 0 | 0 | 0 | 0
17 | 0 | 60 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 43 | 0 | 72 | 0
0 | 50 | 0 | 0 | 0 | 0 | 0 | 0
Long exposure time: several 10 s, to avoid the blooming of the CCD
One frame for one image
Individual pixels can be loaded by many X-ray photons  no spectral information
Spectrally integrated but spatially resolved structural information
Acquisition
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23

## Slide 24: X-ray imaging (photon counting mode)
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 17 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 25 | 0 | 0
0 | 47 | 0 | 25 | 0 | 1 | 0 | 0
0 | 9 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 30 | 20 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
Short exposure time (ms)
Thousands of frames for one image
Individual pixels as a single photon detector
Spectrally and spatially resolved information
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23

## Slide 25: Spectrally integrated images
Injection plate
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23
We can measure the energy content
Counts ~ Sum [ni * Ei]
Argon plasma
D. Mascali et al 2022 Plasma Phys. Control. Fusion 64 035020

## Slide 26: Some example
Frequency tuning
Strong effect of the rf frequency on the plasma images especially in the near axis region
The total counts measured at the near axis regions
Plasma images in the near axis region becomes emptier at each reduction step (horizontal profiles)
Plasma is expanding and is shifting toward the plasma chamber wall
This shift can be explained by the radial expand of the resonant surface
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23
Axial B-field tuning
R. Racz et alPlasma Sources Sci. Technol. 26 (2017) 075011 (14pp)

## Slide 27: Photon counted images
Low energy electrons lose mainly axially
Spatial distribution of the argon plasma; dense in magnetic gap position
High energy electrons lose mainly radially
Selecting only the pixels of the frames which are loaded by the photons having energy correspond to:
‚Low’ energy E < 2 keV
Argon K-alpha line 2 keV < E < 4 keV
‚High’ energy E > 4 keV
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23
R. Racz et al Plasma Sources Sci. Technol. 26 (2017) 075011 (14pp)
D. Mascali et al Rev. Sci. Instrum. 87, 02A510 (2016)
Low power

## Slide 28: Photon counting at high power operation
High power
Read out noise: shutter and /or algorithm
HDR X-ray photography
Richard Racz, X-ray Diagnostics of ECR Ion Sources, 22.09.2023, ICIS’23
E. Naselli et al 2022 JINST 17 C01009
E. Naselli et al Condens. Matter 2022, 7, 5
Important component of PANDORA diagnostics
E. Naselli’s talk yesterday
Calculation of density distribution
B. Mishra et al PHYSICS OF PLASMAS 28 : 10 Paper: 102509 (2021)

## Slide 29: Thank You for Your attention
For more information and references: