## Slide 1: ALPHA-g & HAICU Antimatter science at TRIUMF
Science Week 2023
Chukman So
Notes: Name
Applied physicist
Belong to ALPHA, international collaboration with a major TRIUMF and Canadian contribution
I want to tell you a bit about our work, which is the study of antimatter

## Slide 2: Antimatter science
Fundamental symmetries
ALPHA at Cern’s AD
  First trapping in 2010 - Nature 468, 673 (2010)
  1S-2S - Nature 557, 71–75 (2018)
  1S-2P - Nature 561, 211-215 (2018)
  Hyperfine - Nature 548, 66–69 (2017)
  Lamb shift - Nature 578, 375–380 (2020)
  Charge neutrality - Nature Communications 5, 3955 (2014)
Next: gravity
  More exotic than a feather!
Notes: By comparing antimatter and its normal matter counterpart, we can better understand how the universe come to be dominated by…
Also one way to investigate fundamental CPT symmetry, and to explore physics beyond…
ALPHA specialises in antihydrogen, the antimatter version of hydrogen, which is…
We have had great success…
Next experiment is an analogue of the classic classroom experiment…
Probe the nature of gravity as well as particle physics

## Slide 3: The ALPHA-g experiment

## Slide 8: The ALPHA-g experiment
Penning trap
  Catching and cooling plasmas
  Mixing to create antihydrogen
Magnetic trap
  Trapping anti-atoms
  Release for gravity
Detector
  Determine the behaviour of antihydrogen
  Rejecting anything else

## Slide 9: Magnetic minimum trap
|B|
vertical
octupole
mirror
mirror
Anti-atoms attracted to minimum in |B|
Radial confinement: octupole
Vertical confinement: mirror coils
g
horizontal

## Slide 10: Gravity measurement
horizontal
|B|
vertical
octupole
mirror
mirror
Mirror coils slowly turned off
Observe antiatom escape, up or down
g

## Slide 11: Gravity measurement

## Slide 12: Gravity measurement
Uncompensated trap favours “down”
Balanced escape require stronger bottom coil
Determine gravity by horizontal offset of the curve

## Slide 13: Challenges
Trapping antihydrogen
  O(1011) decrease in energy
  Method developed and refined in ALPHA and ALPHA-2
Precise field control
  O(10-5) control in trap field

## Slide 14
Inner
magnets
3 m

## Slide 15: Inner magnet geometry
Centre: Precision measurement
Bottom: Stronger trap
Top: reflected copy
Why the complicated trap?

## Slide 16: 1. Persistent field
Induced field in superconductor
  Current loops induced in response to field changes
  History-dependent
Mitigation:
  Weak magnets
  Thin, numerous NbTi filaments
  Symmetrise magnetic history
  Neighbouring strong trap for initial trapping

## Slide 17: 2. Wire placement
Octupole winding
  Wire-laying precisely controlled, but nothing is perfect
  Field error most severe near end turns
  Measurement regions avoid these regions
  Long + short octupole minimises number of end turns near the precision region

## Slide 18: 2. Wire placement
Coil winding
  Each layer is macro-photographed and analysed to locate turns

## Slide 19: 3. Separated DoF
Energetic escape requires hitting pin hole with all energy allocated to z
Slow (x,y) and z energies mixing
Anti-atoms mostly escape off-axis, at much later time
Must tailor on- and off-axis fields
bottom coil
top coil

## Slide 20: 3. Separated DoF
A coil’s field is saddle-shaped

## Slide 21: 3. Separated DoF
Two coils at different currents cannot form equal barriers for all r
Even messier picture with octupole contribution
Correctors implemented to improve trap bias uniformity across r
gravity gradient
Main mirror coil
Corrector coil
Corrector octupole

## Slide 22: 4. Current supply
Extremely fine current control on barrier coils
  Common mode: 70 A to ~0 A, no specific precision requirement
  Difference: ~ 0.1 A, precise to ~1 mA
Two completely separate PS: 10 ppm
One bulk current supply and one “tickle” supply: 10000 ppm
Two currents measured by DCCT and fed back to power supplies PID control

## Slide 23: 5. Background solenoid uniformity
Affects gravity measurement due to field gradient
As-built
  ~20 G non-uniformity
With outer shims
  ~4 G non-uniformity
  Compensate by adjusting mirror coil currents
Possible future inner shims
  ~0.02 G non-uniformity
  Reduced coil adjustment

## Slide 24: Performing a first measurement

## Slide 25: An “up-down” measurement
Using only the bottom set of magnets
Pro
  Deeper trap, more statistics
  Fewer magnet elements needed
Con
  Less accurate field – more persistence effect, no correctors
  Cannot use the long octupole
Aiming to resolve the direction of gravity on antihydrogen

## Slide 26: Magnetometry
Persistence effect is inevitable
Measure field and adjust current, to maintain trap bias throughout release ramp
ECR
  Measures cyclotron frequency in Penning trap
  Slow measurement process
Magnetron counting
  Measures the phase of ExB drift of Penning trap plasmas
  Fast measurement
  Less accurate than ECR
Able to control relative trap bias to ~0.1 Gauss

## Slide 27: Field model
Magnetometry results are integrated into a 3D field model
O(1 Gauss) precision, much better around the saddle points
Particle pusher uses field to evolve anti-atoms through the entire experimental sequence
  Obtain the expected escape bias as a function of gravitational acceleration
  Field model is critical as antiatoms escape off-axis
Wire model field, from currents we provide
Exponentially saturating component
from magnetron results
Residual to account for ECR
Field we
don’t control

## Slide 28: Experiment progress
In 2022: performed experimental release at 13 trap biases
Results being analysed and compared to simulation

## Slide 29: Future precision
Using the proper precision region
Steepness of escape balance curve closely affects sensitivity
Long ramp = more chance anti-atoms can escape on-time, higher sensitivity
Down side:
  Long window = more cosmics
  Depends on our ability to reject cosmics
Other factors like current noise and anti-atom temperature

## Slide 30: HAICU

## Slide 31: Interferometer
Raman interferometer:
  Weighing atoms without field
  Coherent interrogation during free-fall
  10-2 vs 10-14 precision
Requires extremely slow atoms
  Beyond Doppler laser cooling with magnetic compression
Special magnetic trap with a “neck”
  Bitter magnet trap
  Bitter magnet trap with a neck
  Superconducting trap with a much stronger neck

## Slide 32: Bitter magnet development
Water-cooled, normally conducting
350 A, 5 kW test coil
Test of fabrication and assembly technique

## Slide 33: Magnetic trap prototype
High power density winding
  1800 A, 80 kW quadrupole
  350 A, 10 kW mirror coils
  0.2 T trap depth on a 0.3 T background
  10 L/s cooling water
Axial and perpendicular optical access for laser cooling
In final design stage
Experiment located in meson hall extension
Uses hydrogen atom as proxy
Aiming for commissioning by end of 2023

## Slide 34: The big picture
ALPHA-g design and construction: a decade-long effort
  Magnet
  Detector
  Current control
  Beamline
  Cryostat
  Vacuum system
  Penning trap
  Sequencer
  Laser and optics
  Microwave
  Diagnostic stations
First physics in 2022
Moving towards 1% precision
Planning for an interferometer