## Slide 1: Recent results from the mass spectrometer EMMA at TRIUMF
Louis Wagner
Postdoc for DRAGON and EMMA at TRIUMF
2023 TRIUMF Science Week Jul. 31st, 2023
Vancouver, B.C. Canada
Notes: 6 minutes radiative capture
12 minutes for recoil separators
12 minutes for science highlights

## Slide 2: TRIUMF

## Slide 3
TRIUMF ISAC Facility
EMMA
The Isotope Separator and Accelerator (ISAC) facility at TRIUMF provides a wide variety of intense beams of exotic nuclei produced using the ISOL method
Beams reaccelerated through 35 MHz RFQ with A/q<30
105 MHz variable energy DTL (3 ≤ A/q ≤ 6)
Energies between 0.15 MeV/u & 1.8 MeV/u
Low-energy regime well suited for reaction studies for novae & X-ray bursts
ISAC-II SC-LINAC max. beam energies 6.5 – 16.5 MeV/u suited for transfer reactions on heavy ions

## Slide 4: Recoil Mass Spectrometer EMMA

## Slide 5
The Electro-Magnetic Mass Analyzer (EMMA)
PGAC
Ion Chamber
Angular Acceptance: ± 3.6° | Energy Acceptance: ±15% | m/q acceptance = ±3.3% | Rigidity limit: ~7q MeV
PGAC spectrum from Fusion Evap test run:
IC PID plot from 17O experiment:
Ion-implanted Silicon
[1] B. Davids, M. Williams, et al., NIMA 930, 191-195 (2019).
.

## Slide 6
Beam suppression in EMMA
Suppression Slits
Magnetic Dipole
Need to use EMMA’s slit systems to improve beam suppression.
Suppression factor of slits alone was measured ~5 x104 with no cuts on the data
Together with gate on Time-of-Flight total suppression up to ~1010 can be achieved
Focal plane slits

## Slide 7: TIGRESS γ-detection array
12 Clover detectors with 8 centered at 90° and 4 at 135°
segmented outer contacts for improved Doppler correction for spectroscopy after in-beam reactions
4 crystals in a common cryostat
BGO Compton suppressor shields, reconfigurable in situ

## Slide 8
Studying the weak r-process with EMMA+TIGRESS
Slide from Matthew Williams
How to make a target from an inert gas?
Typical options include gas targets and implanted foils
Advances in materials science provides new options: Magnetron-sputtered silicon thin-films formed in a helium plasma environment.
(α,n) reactions on isotopes of Kr, Rb and Sr are identified as particularly important for determining weak r-process abundance signatures.
Currently there is a lack of (α,n) cross-section data in this mass region, so all predictions rely on statistical model calculations, which carry large uncertainties (> x10).
High He density
Homogeneous distribution.
Content stable in storage and in beam.
Compact with no expensive infrastructure.
[1] J. Bliss et al., Phys. Rev. C 101, 055807 (2020).
[2] V. Godinho et al., ACS Omega 1,1229– 1238 (2016)
Helium
Nano-pockets

## Slide 9
Measurement of 86Kr(α,n)89Sr
Two measurements were performed of 86Kr(α,n)89Sr at 265 and 240 MeV bombarding energies
In both measurements a gold degrader foil was used, since the recoils would otherwise be too energetic to bend.
November 2021: Si:He targets were self-supported with a 2μm Gold degrader mounted ~10 cm downstream.
  Pro: little influence of degrader on γ-ray background (coulex).
  Con: recoil angles entering EMMA not constrained to region where EMMA’s acceptances are known ()
August 2022: Si:He targets were deposited directly onto a 4μm gold degrader foil.
  Pro: can use 3° aperture to define maximum recoil angle entering EMMA.
  Con: Introduces γ-ray background from coulex (not an issue for this particular experiment) also potential for Doppler broadening of some lines of interest (not yet confirmed).
Chart: Beam Transmission vs Energy Tune
| 102.4 | 92.2 | 107.5 | 112.6 | 117.8 | 110
 | 0.098765 | 0.06275 | 0.10244 | 0.11096 | 0.09935 | 0.11514
Transmission through EMMA was measured for different energy tunes and charge states to find optimum settings. Compare attenuated beam rate on scintillator vs focal plane.
Beam normalisation & target content measured via 2 SSB detectors
Slide from Matthew Williams

## Slide 10
Stable beam test measurement: 86Kr(α,n)89Sr
Slide from Matthew Williams
EMMA was tuned to A=89 (q=19+) 89.7 MeV recoils
See clear peak in the timing signal between EMMA and TIGRESS events.
The timing peak is also correlated with a well-focused A=89 (q=19+) peak seen in the focal plane X-position (dispersive direction).
Able to pick-out clear 89Sr γ-rays in coincidence with EMMA events gated on the PGAC spectrum. Can now use these γ-ray yields to constrain statistical model calculations.
Measurements were successful with stable beam & targets clearly performed well!

## Slide 11
Measurement of 83Rb84Sr
Slide from Matthew Williams
G. Lotay, S. Gillespie, M. Williams, et al., Phys. Rev. Lett. 127, 112701
Large background from 83Sr contamination in the beam, which scatters onto EMMA’s entrance aperture → obscures the timing peak!
Plotting γ-ray energy vs the correlation time reveals signal of high energy γ-rays at the expected correlation time.
Gating around the correlation peak reveals the transition from the first 2+ to ground state transition in 84Sr. (16 events above background)
11

## Slide 12
First measurement of a p-process reaction with a radioactive beam
Slide from Matthew Williams
Partial cross-section is converted to the full reaction cross section using γ-cascade models (included in the SMARAGD code), which predict 71 10% of (p,γ) reactions result in a 2+ → 0+(g.s.) decay.
Total cross sections are approximately 4x smaller than predicted by Hauser-Feshbach models
G. Lotay, S. Gillespie, M. Williams, et al., Phys. Rev. Lett. 127, 112701 (2021).
M. Williams, et al., Phys. Rev. C 107, 035803 (2023).
Statistical modeling by T. Rauscher

## Slide 13
Astrophysical impact of 83Rb84Sr measurement
Investigated for both Type II and Type Ia supernovae explosions
Slide from Matthew Williams
Astrophysical modeling by N. Nishimura
15 CCSNe = +30 %
25 CCSNe = +12 %
Type 1a SNe = +32 %
M. Williams, et al., Phys. Rev. C 107, 035803 (2023).
Lower 83Rb84Sr cross-section leads to less efficient destruction of the 84Sr p-nucleus in supernovae, raising its production factor.
The total uncertainty in 84Sr production is reduced by a factor of 2 from previous sensitivity study.
Uncertainties represent the combined effect of all reaction rates variations – not just 83Rb84Sr.
Abundance enhancement not sufficient to explain enhanced 84Sr seen in Allende Meteorite but could relieve tension – full GCE simulations required!

## Slide 14
New target chamber SHARC-II for EMMA & TIGRESS
Louis Wagner
Upgrade of SHARC target chamber to connect it to EMMA
Designed by C. Diget et al., J. Instrum. 6, P02005 (2011)
6 DSSSD detectors to cover angular range of: 10° − 28° ∼ 100° − 140° 146° − 172°

## Slide 15
Test of new target chamber SHARC-II with EMMA & TIGRESS
Louis Wagner
M. HAGEN, U. JANETZKI and K.-H. MAIER Nuclear Physics A152 (1970) 404--418
Tested with 36Ar 7+ beam impinging on 3 MeV/u on CD2 target 300µg/cm²
Simultaneous measurement of 36Ar(d,p)37Ar and 36Ar(d,n)37K
Different gate conditions reveal (d,p) and (d,n) reactions

## Slide 16: SUMMARY / OUTLOOK
Transfer reactions critical for many astrophysical processes/sites but very challenging to measure
Recoil mass spectrometer very specific device to solve issue (primarily for RIB)
Techniques well developed for all conditions: low cross section, beam contaminants
Recoil Separation needed to making pioneering measurements, i.e. first direct measurements of p-process reaction with radioactive beam
Can contribute to precision measurements of stable reactions as well, complementary to normal kinematics
Upcoming EMMA experiment in August: 86Kr(α,n)89Sr and 94Sr(α,n)97Zr (Part III) for weak r-process
SHARC-II chamber allows transfer reaction measurement with full information on reaction products (light particle, gamma & recoil)
Decay station for studying recoil decay will be assembled over the next year

## Slide 17: Thank you Merci
Follow us @TRIUMFLab
www.triumf.ca
My thanks to Barry Davids (TRIUMF) & Matthew Williams (Uni of Surry) for slides and to all my collaborators at EMMA & TIGRESS!

## Slide 18: Backup Slides

## Slide 19
Maximum possible recoil angle when Eg is maximized for Eg = Q+Ec.m.
AND emission perpendicular to beam axis (qγ=p/2)
qg
q’3
Recoil Separator Goes Here!
Inverse Kinematics

## Slide 20: The Challenge
In inverse kinematics we have:
– Beam that did not interact
– Recoil with, in average, the same momentum as the beam
– Recoil with an momentum/energy distribution
– Recoil with an angular opening that is larger than that of the beam
– Beam and recoil with various charge states
Difficult to detect the recoils right after the target
Recoil separators are devices which separate nuclear reaction products (recoils) leaving a target from the unreacted beam particles.

## Slide 21: Inverse Kinematics
Necessity due to not being able to make short-lived radioactive targets
Detect recoiling product nucleus: forward focused, 100% efficiency
Becomes problem of separating rare reaction products from abundant beam
  zero-degree electromagnetic separator
Additional advantages:
  Target either H2 or He: usually gaseous  windowless (jet,extended), purified etc…
  Still detect gamma rays (tag)
  Particle ID on reaction products
T3*’ = T1’ – E
http://skisickness.com/2020/02/kinematics/

## Slide 22: Angular distribution of recoils
For absolute cross section, full transmission of the selected charge state is needed
Example from FMA to study 13C(p,γ)14N and 18O(p,γ)19F and 18F(p,γ)19Ne but limited in transmission