## Slide 1
Lorenzo Fortunato
Univ. Padova & INFN
Italy
Reviving Nuclear Fusion Reaction Cycles in Solido
An old idea is reappraised:
Nuclear fusion cycles
Fusion -in solido- and not -in plasma-
New data and modern computational techniques
We obtain high yields and energy output
Might represent an alternative route to fusion
NEW: after introducing Bethe-Block energy loss, the stopping power quenches the secondary reaction!
NEW: the net outcome is still worth investigating
14th International Conference on Nucleus-Nucleus Collisions
Aug 2024 - Whistler, Canada

## Slide 2
Collaborators
Lorenzo FORTUNATO – Prof. Univ. Padova and INFN-Sez. Padova
Andres Felipe LOPEZ LOAIZA – M.Sc. Thesis Univ. Padova 2023
Giulio ALBERTIN – B.SC. Thesis Univ. Padova 2022
Enrico Fragiacomo – INFN Trieste – GEANT simulations
Idea
We have found a series of papers and lab reports that have almost gone forgotten amid cold-war era documents and might as well be lost.
We studied the problem from a modern perspective, including new ideas, new tools and new data, finding out that the topic deserves more attantion that it has received.
It might significantly impact fusion energy research.

## Slide 3
History-1
1950 Ulrich Jetter publishes a paper in which, in connection with warfare uses of nuclear energy, he introduces a fusion cycle
U. Jetter , Physikalische Blätter - Mai 1950 - Die sogenannte Superbombe
With the idea of igniting nuclear reactions with a small amount of initial neutron plus the emitted neutrons from the secondary reactions.
The calculations are simple energy estimates and do not contain any cross-section or dynamical information.

## Slide 4
History-2
1956 Richard F. Post (Livermore, USA) takes into account also the proton cycle and has a better control over reaction dynamics, but the considered reaction are still in plasma
R.F.Post, Rev. Mod. Phys. 28 (1956) 338
The first reaction has a Coulomb barrier that makes it less probable than the neutron induced one.

## Slide 5
History-3
J. Rand McNally Jr. (Oak Ridge, USA) in a series of published and unpublished papers and lab-reports (covering 1972-1988) that have been released only after the cold-war era, exhamines all the cycles and attempts a dynamical reaction calculation, including losses and other effects, aiming at controlling the main parameters of a plasma containing 6LiD fuel and other alternative fuels.

## Slide 6
History-4
Albert G. Fisher patented in Germany and in USA a device called FISCATRON that is based on a sudden electric discharge that should initiate a micro thermonuclear explosion that then propagates into a solid 6LiDT fuel pellet, burning it as if it was a chemical reaction.
The closest idea to ours is that of “wet-wood burners" of Dawson, Furth and Tenney : the burning of a “nuclear controlled fire" might happen in a small irradiated portion of a larger fuel material in solido.

## Slide 7
Fusion cycles : Jetter + Post and coupling reaction
Jetter cycle
Post cycle
Coulomb barrier here!
The two cycles can be coupled through the endothermic neutron-induced deuteron breakup reaction.
More effective at intermediate-high energy

## Slide 8
Cross-section data – digging the databases
The cross-section data for the neutron-induced reactions grows at low energy, this means you can extract a lot of energy without putting to much energy into neutron motion!

## Slide 9
Reaction calculations - taming of a little monster
We have written and set up a code that calculates the fulll reaction dynamics, solving a system of coupled first order differential equations, taking into account the abundancies Yi and the reaction rates with Non-thermal energy distributions (most of the fragments come out from binary reactions splitting the Q-value energy according to the mass proportions).
Reactions
forming i
Reactions
consuming i
Decays to and from

## Slide 10
Typical results of our calculations (at some 0.24 MeV neutron injection energy)
Time scale for complete burnout can be extracted from graph

## Slide 11
Specific Power – these reactions would produce a huge energy output
Q-value
Density
in solido
>> plasma
Integrated 1300 GJ for a mole of material (assuming it is completely burnt)

## Slide 12
Now seriously… -dE/dx  -dE/dt
When fast chaged particles travel through matter, they loose energy by ionising the material they travel in, before igniting the secondary reactions.
This can be modeled with the Bethe-Bloch formula:
NOTE: Bethe-Bloch Stopping power as it appears on Krane's book and Segré's book. Check Seltzer & Bergen. (High Z correction of Barkas and Bloch, not implemented, not valid below min validity)
dE/dx
dE/dt
At these energies, ranges are of the order of a few tens of m

## Slide 13
New system of differential equations (stiffer than before)
Neutron deceleration (by impact) not yet implemented, thought to be minor
System of equations much larger and non-linear
Works reasonably in a certain range of neutron intensities (lucky)
Typical nuclear burning time for a mole of crystal is about
The MonsteR grows horribly !

## Slide 14
Specific Power –new results including energy loss by ionization
Should still be advantageous if compared with chemical burning of CH4 fuel!
It leads mainly to alpha particles !
Take this parameter more or less as a burning efficiency.

## Slide 15
Summary and outlook
TO DO LIST:
Another 80 reactions or so can be implemented, but they have small cross-sections and often data on reactions involving tritium are very scarce
Find people interested in trying some experimental setup
DONE:
We have demonstrated that these reactions deserve further attention:
  Exoenergetic with high specific power!
  burn cheap and abundant fuel
  sub-critical , no explosions!
  self-terminating, quickly after dropping the source of neutrons
  radiologically quite safe, as the main outcome is 4He (some neutrons) , no harmful radiations!
  no dependence on tritium economy
  still worth burning this fuel with neutrons, even after taking into account energy losses due to Bethe-Bloch stopping power
CONCLUSION:
Why nobody puts this crystals into a calorimeter and fires neutrons in ?

## Slide 16
Back up slides – GEANT range simulations
– Courtesy of Enrico Fragiacomo (Trieste)
GEANT simulations (statistical) confirm the range calculated by integration of the Bethe-Bloch formula.