## Slide 1: #133 Photon-to-Digital Converter for Large Scale Noble Liquid Detectors and Neutron Imaging
Olivier Lepage1,2 , Tommy Rossignol1,2, Nicolas Roy1,2, Frédéric Vachon1,2, Keven Deslandes1,2, Arnaud Samson1,2, Lorenzo Fabris3, Jean‑François Pratte1,2 and Serge A. Charlebois1,2
1 Université de Sherbrooke, Department of Electrical and Computer Engineering, Sherbrooke, Québec, Canada
2 Interdisciplinary Institute for Technological Innovation, Sherbrooke, Québec, Canada
3 Oak Ridge National Laboratory, Oak Ridge, United States
61st Winter Nuclear & Particle Physics Conference
February 15th to 18th 2024

## Slide 2
Large Scale Noble Liquid Experiments
Neutrinoless double beta decay and dark matter search
4.6 m2 of detectors
200 W max.
Large Scale Noble Liquid Experiments and Neutron Imaging
[1] nEXO Collaboration et al, 2018
Neutron imaging
Large pixelated sensitive area
Portability (compact and low-power)
30 cm
30 cm
ORNL Portable Pixelated Fast-Neutron Imaging Panel [2]

## Slide 3
Large Scale Noble Liquid Experiments
Neutrinoless double beta decay and dark matter search
4.6 m2 of detectors
200 W max.
Large Scale Noble Liquid Experiments and Neutron Imaging
[1] nEXO Collaboration et al, 2018
Neutron imaging
Large pixelated sensitive area
Portability (compact and low-power)
Need : Large area, low-power and good timing precision photon counting system.
30 cm
30 cm
ORNL Portable Pixelated Fast-Neutron Imaging Panel [2]

## Slide 4: Digital Solution: 3DPDC + Tile controller
PCB
Notes: Our solution
3D integration (detector top and electronic bot)
Maximize photosensitive (why?)
Tile controller: interfacing and communication
Transition: Lets talk about how the detector work

## Slide 5: Digital Solution: 3DPDC + Tile controller
PCB
Notes: Our solution
3D integration (detector top and electronic bot)
Maximize photosensitive (why?)
Tile controller: interfacing and communication
Transition: Lets talk about how the detector work

## Slide 6: Digital Solution: 3DPDC + Tile controller
PCB
Notes: Our solution
3D integration (detector top and electronic bot)
Maximize photosensitive (why?)
Tile controller: interfacing and communication
Transition: Lets talk about how the detector work

## Slide 7: Digital Solution: 3DPDC + Tile controller
Notes: Our solution
3D integration (detector top and electronic bot)
Maximize photosensitive (why?)
Tile controller: interfacing and communication
Transition: Lets talk about how the detector work

## Slide 8: Single photon avalanche diode (SPAD)
1
2
3
SPAD cross-section
Schematic circuit
SPAD I-V curve
Quench
Hold-off
Recharge
(20-60 V)
Notes: PN junction with trenches
Schema: We bias the diode
CS: high electric field
Photon hit -> avalanche -> high current
To not burn the diode -> Quench the circuit, put the voltage under breakdown voltage
Hold off to let the carriers finish the avalanche
Recharge the spad and ready to detect photon
All this process means that the response of the spad is binary

## Slide 9: Single photon avalanche diode (SPAD)
1
1
2
3
SPAD cross-section
Schematic circuit
SPAD I-V curve
Quench
Hold-off
Recharge
(20-60 V)
Notes: PN junction with trenches
Schema: We bias the diode
CS: high electric field
Photon hit -> avalanche -> high current
To not burn the diode -> Quench the circuit, put the voltage under breakdown voltage
Hold off to let the carriers finish the avalanche
Recharge the spad and ready to detect photon
All this process means that the response of the spad is binary

## Slide 10: Single photon avalanche diode (SPAD)
1
1
2
2
3
SPAD cross-section
Schematic circuit
SPAD I-V curve
Quench
Hold-off
Recharge
(20-60 V)
Notes: PN junction with trenches
Schema: We bias the diode
CS: high electric field
Photon hit -> avalanche -> high current
To not burn the diode -> Quench the circuit, put the voltage under breakdown voltage
Hold off to let the carriers finish the avalanche
Recharge the spad and ready to detect photon
All this process means that the response of the spad is binary

## Slide 11: Single photon avalanche diode (SPAD)
1
3
1
2
2
3
SPAD cross-section
Schematic circuit
SPAD I-V curve
Quench
Hold-off
Recharge
(20-60 V)
Notes: PN junction with trenches
Schema: We bias the diode
CS: high electric field
Photon hit -> avalanche -> high current
To not burn the diode -> Quench the circuit, put the voltage under breakdown voltage
Hold off to let the carriers finish the avalanche
Recharge the spad and ready to detect photon
All this process means that the response of the spad is binary

## Slide 12: Single photon avalanche diode (SPAD)
1
3
1
2
2
3
SPAD cross-section
Schematic circuit
SPAD I-V curve
Quench
Hold-off
Recharge
Response of the SPAD is binary
(20-60 V)
Notes: PN junction with trenches
Schema: We bias the diode
CS: high electric field
Photon hit -> avalanche -> high current
To not burn the diode -> Quench the circuit, put the voltage under breakdown voltage
Hold off to let the carriers finish the avalanche
Recharge the spad and ready to detect photon
All this process means that the response of the spad is binary

## Slide 13: Analog SiPM VS Digital SiPM
HV
Amplifier, Shaper,…
ADC
Analog current sum
SiPM capacitance → electronic noise
Response of the SPAD is binary
Quench
Quench
Digital Signal Processing
HV
The amplifier transforms charge into voltage and then BACK to digital.
Individual SPAD readout, no D/A+A/D conversion. Everything stays digital.
Analog SiPM
Photon to Digital Converter (aka Digital SiPM)
SPAD
SPAD
SiPM : Silicon Photo Multiplier
Notes: Usually, we use SiPM as detector
They are array of spad in parallel
Compare to analog system SiPM -> we stay digital
Our system use quench on each individual spad
Since Spad response is binary, send a binary value directly to the processor
EVERYTHING STAYS DIGITAL
Next -> architecture of our system: the PDC

## Slide 14: Photon-to-Digital Converter: Architecture
×64 PDCs/Controller
Notes: Architecture:
All spads have their own QC
If not integrated -> 2D SPAD for testing without 3d integration
Next -> PDC output

## Slide 15: Photon-to-Digital Converter: Architecture
×64 PDCs/Controller
3D SPAD
  4096 SPAD
  3D pads
  HV at the anode
CMOS readout pads
  3D pads (X 4096)
  Individual quenching circuit for each SPAD
2D CMOS SPAD
  64 SPAD on CMOS readout
  Individually quenched
Quenching circuit
Read the SPAD from the cathode
Send the flag
Hold-off et recharge the SPAD
Notes: Describe each output:
Flag: Fastest - if one or more trigger, the flag is sent
DS: Do a sum of the spad triggered at a moment in time. Memory of 128 acquisitions
AM: Like SiPM -> Current proportionnal to spad triggered (for test)
Controller: Start acquisition based on flag received
TDC for timing measurements
Receive data + do post-processing
Communication with computer

## Slide 16: Photon-to-Digital Converter: Architecture
×64 PDCs/Controller
3D SPAD
  4096 SPAD
  3D pads
  HV at the anode
CMOS readout pads
  3D pads (X 4096)
  Individual quenching circuit for each SPAD
2D CMOS SPAD
  64 SPAD on CMOS readout
  Individually quenched
Quenching circuit
Read the SPAD from the cathode
Send the flag
Hold-off et recharge the SPAD
Notes: Describe each output:
Flag: Fastest - if one or more trigger, the flag is sent
DS: Do a sum of the spad triggered at a moment in time. Memory of 128 acquisitions
AM: Like SiPM -> Current proportionnal to spad triggered (for test)
Controller: Start acquisition based on flag received
TDC for timing measurements
Receive data + do post-processing
Communication with computer

## Slide 17: Photon-to-Digital Converter: Architecture
×64 PDCs/Controller
3D SPAD
  4096 SPAD
  3D pads
  HV at the anode
CMOS readout pads
  3D pads (X 4096)
  Individual quenching circuit for each SPAD
2D CMOS SPAD
  64 SPAD on CMOS readout
  Individually quenched
Quenching circuit
Read the SPAD from the cathode
Send the flag
Hold-off et recharge the SPAD
Notes: Describe each output:
Flag: Fastest - if one or more trigger, the flag is sent
DS: Do a sum of the spad triggered at a moment in time. Memory of 128 acquisitions
AM: Like SiPM -> Current proportionnal to spad triggered (for test)
Controller: Start acquisition based on flag received
TDC for timing measurements
Receive data + do post-processing
Communication with computer

## Slide 18: Photon-to-Digital Converter: Architecture
×64 PDCs/Controller
3D SPAD
  4096 SPAD
  3D pads
  HV at the anode
CMOS readout pads
  3D pads (X 4096)
  Individual quenching circuit for each SPAD
2D CMOS SPAD
  64 SPAD on CMOS readout
  Individually quenched
Quenching circuit
Read the SPAD from the cathode
Send the flag
Hold-off et recharge the SPAD
Notes: Describe each output:
Flag: Fastest - if one or more trigger, the flag is sent
DS: Do a sum of the spad triggered at a moment in time. Memory of 128 acquisitions
AM: Like SiPM -> Current proportionnal to spad triggered (for test)
Controller: Start acquisition based on flag received
TDC for timing measurements
Receive data + do post-processing
Communication with computer

## Slide 19: Photon-to-Digital Converter: Architecture
×64 PDCs/Controller
Flag output
  Pulsed output (adjustable from few ns to tens of ns).
  From an OR-tree.
  Timing jitter better than 100 ps RMS.
Digital Sum
  Digital count of triggered SPADs inside a bin (dynamic range of 4096 photons).
  Adjustable bin width from 10 ns up to µs.
  Internal FIFO of 128 bins.
Analog Monitor
  Current proportional to triggered SPADs.
Controller (1 for 64 PDCs)
Start PDC acquisition, based on the number of flag received to discriminate dark count.
Bank of TDCs for timing measurements on flags.
Receives data from PDCs and includes post-processing.
Communicate with an external computer.
Notes: Describe each output:
Flag: Fastest - if one or more trigger, the flag is sent
DS: Do a sum of the spad triggered at a moment in time. Memory of 128 acquisitions
AM: Like SiPM -> Current proportionnal to spad triggered (for test)
Controller: Start acquisition based on flag received
TDC for timing measurements
Receive data + do post-processing
Communication with computer

## Slide 20: Photon-to-Digital Converter: Architecture
×64 PDCs/Controller
Flag output
  Pulsed output (adjustable from few ns to tens of ns).
  From an OR-tree.
  Timing jitter better than 100 ps RMS.
Digital Sum
  Digital count of triggered SPADs inside a bin (dynamic range of 4096 photons).
  Adjustable bin width from 10 ns up to µs.
  Internal FIFO of 128 bins.
Analog Monitor
  Current proportional to triggered SPADs.
Controller (1 for 64 PDCs)
Start PDC acquisition, based on the number of flag received to discriminate dark count.
Bank of TDCs for timing measurements on flags.
Receives data from PDCs and includes post-processing.
Communicate with an external computer.
Notes: Describe each output:
Flag: Fastest - if one or more trigger, the flag is sent
DS: Do a sum of the spad triggered at a moment in time. Memory of 128 acquisitions
AM: Like SiPM -> Current proportionnal to spad triggered (for test)
Controller: Start acquisition based on flag received
TDC for timing measurements
Receive data + do post-processing
Communication with computer

## Slide 21: Photon-to-Digital Converter: Architecture
×64 PDCs/Controller
Flag output
  Pulsed output (adjustable from few ns to tens of ns).
  From an OR-tree.
  Timing jitter better than 100 ps RMS.
Digital Sum
  Digital count of triggered SPADs inside a bin (dynamic range of 4096 photons).
  Adjustable bin width from 10 ns up to µs.
  Internal FIFO of 128 bins.
Analog Monitor
  Current proportional to triggered SPADs.
Controller (1 for 64 PDCs)
Start PDC acquisition, based on the number of flag received to discriminate dark count.
Bank of TDCs for timing measurements on flags.
Receives data from PDCs and includes post-processing.
Communicate with an external computer.
Notes: Describe each output:
Flag: Fastest - if one or more trigger, the flag is sent
DS: Do a sum of the spad triggered at a moment in time. Memory of 128 acquisitions
AM: Like SiPM -> Current proportionnal to spad triggered (for test)
Controller: Start acquisition based on flag received
TDC for timing measurements
Receive data + do post-processing
Communication with computer

## Slide 22: Photon-to-Digital Converter: Architecture
×64 PDCs/Controller
Flag output
  Pulsed output (adjustable from few ns to tens of ns).
  From an OR-tree.
  Timing jitter better than 100 ps RMS.
Digital Sum
  Digital count of triggered SPADs inside a bin (dynamic range of 4096 photons).
  Adjustable bin width from 10 ns up to µs.
  Internal FIFO of 128 bins.
Analog Monitor
  Current proportional to triggered SPADs.
Controller (1 for 64 PDCs)
Start PDC acquisition, based on the number of flag received to discriminate dark count.
Bank of TDCs for timing measurements on flags.
Receives data from PDCs and includes post-processing.
Communicate with an external computer.
Notes: Describe each output:
Flag: Fastest - if one or more trigger, the flag is sent
DS: Do a sum of the spad triggered at a moment in time. Memory of 128 acquisitions
AM: Like SiPM -> Current proportionnal to spad triggered (for test)
Controller: Start acquisition based on flag received
TDC for timing measurements
Receive data + do post-processing
Communication with computer

## Slide 23: Pdc: Fabricated CMOS READOUT
5.3 mm
5.85 mm
64x 2D CMOS SPADs
64×64 quench circuits ready for 3D integration
IO pads ESD protected
Key Specifications
TSMC 180 nm BCD CMOS process.
78 µm SPAD-to-SPAD pitch for a 5X5 mm active area
Every SPAD is controlled individually.
  Noisy/defective SPADs can be disabled.
Dynamic range of 0 to 4096 photons.
PDC CMOS READOUT
Notes: 3 main sections
Compare to SiPM, we can disabled noisy SPAD
We remove « screamers »

## Slide 24: 2×2 Photodetection Module
2×2 PDCs
50 mm
50 mm
Top
Bottom

## Slide 25: 2×2 Photodetection Module with LED Testing
Current in the LED to trigger the SPADs
  Driven by a waveform generator
Analog Monitor
  Amplitude proportional to the number of SPADs triggered
Digital Sum Acquisition
  Based on a 100 MHz readout clock
  Generated by the FPGA (Tile Controller)
1010101010
Using embedded CMOS test SPADs of the PDC
Notes: LED that emits small amount of photons
AM: similar to SiPM
DS: adjust bin width

## Slide 26: 2×2 Photodetection Module with LED Testing
Current in the LED to trigger the SPADs
  Driven by a waveform generator
Analog Monitor
  Amplitude proportional to the number of SPADs triggered
Digital Sum Acquisition
  Based on a 100 MHz readout clock
  Generated by the FPGA (Tile Controller)
1010101010
Using embedded CMOS test SPADs of the PDC
Notes: LED that emits small amount of photons
AM: similar to SiPM
DS: adjust bin width

## Slide 27: 2×2 Photodetection Module with LED Testing
Current in the LED to trigger the SPADs
  Driven by a waveform generator
Analog Monitor
  Amplitude proportional to the number of SPADs triggered
Digital Sum Acquisition
  Based on a 100 MHz readout clock
  Generated by the FPGA (Tile Controller)
1010101010
Using embedded CMOS test SPADs of the PDC
Notes: LED that emits small amount of photons
AM: similar to SiPM
DS: adjust bin width

## Slide 28: 2×2 Photodetection Module with LED Testing
Current in the LED to trigger the SPADs
  Driven by a waveform generator
Analog Monitor
  Amplitude proportional to the number of SPADs triggered
Digital Sum Acquisition
  Based on a 100 MHz readout clock
  Generated by the FPGA (Tile Controller)
1010101010
Using embedded CMOS test SPADs of the PDC
Notes: LED that emits small amount of photons
AM: similar to SiPM
DS: adjust bin width

## Slide 29: Wafer run of the PDC
200 mm wafer of PDCs
Notes: 2X2 and 8X8 require a lot of work: PCB, dicing, wirebonding, etc.
For 3D integration wafer to wafer
Wafer contain a lot of device (600 device)
So we need a testing platform

## Slide 30: Test Bench for wafer-level measurement
Probe station with probe card attach to it
Notes: Use a probe station

## Slide 31: Test Bench for wafer-level measurement
Dedicated probe card
Active probe card with FPGA
Passive probe card
Probe station with probe card attach to it
Needles of the probe card
Notes: Use a probe station

## Slide 32: Test Bench for wafer-level measurement
Automated movement for wafer-level measurement (over 600 PDC)
Movement of the chuck in relation to the wafer
Notes: Utilisez les images

## Slide 33: Test Bench for wafer-level measurement
Automated movement for wafer-level measurement (over 600 PDC)
Movement of the chuck in relation to the wafer
Notes: Utilisez les images

## Slide 34: Test Bench for wafer-level measurement
Wafer topology
Automated movement for wafer-level measurement (over 600 PDC)
Movement of the chuck in relation to the wafer
Adjusting the height of contact according to wafer topology
Notes: Utilisez les images

## Slide 35: Conclusion
Photon-to-Digital Converters keep the information digital all along the acquisition chain.
FPGA-based tile controller gives a lot of flexibility to implement multiple features.
  Flag-based acquisition, dark count mitigation, pulse shape discrimination, and so on.
Tile Controller ASIC in development to replace the FPGA boards.
Wafer level measurement will accelerate the testing of multiple PDC for larger system integration.
Notes: Wafer to be use on larger panel

## Slide 36: Conclusion
Photon-to-Digital Converters keep the information digital all along the acquisition chain.
FPGA-based tile controller gives a lot of flexibility to implement multiple features.
  Flag-based acquisition, dark count mitigation, pulse shape discrimination, and so on.
Tile Controller ASIC in development to replace the FPGA boards.
Wafer level measurement will accelerate the testing of multiple PDC for larger system integration.
Notes: Wafer to be use on larger panel

## Slide 37: Conclusion
Photon-to-Digital Converters keep the information digital all along the acquisition chain.
FPGA-based tile controller gives a lot of flexibility to implement multiple features.
  Flag-based acquisition, dark count mitigation, pulse shape discrimination, and so on.
Tile Controller ASIC in development to replace the FPGA boards.
Wafer level measurement will accelerate the testing of multiple PDC for larger system integration.
Notes: Wafer to be use on larger panel

## Slide 38: Conclusion
Photon-to-Digital Converters keep the information digital all along the acquisition chain.
FPGA-based tile controller gives a lot of flexibility to implement multiple features.
  Flag-based acquisition, dark count mitigation, pulse shape discrimination, and so on.
Tile Controller ASIC in development to replace the FPGA boards.
Wafer level measurement will accelerate the testing of multiple PDC for larger system integration.
Notes: Wafer to be use on larger panel

## Slide 39: Conclusion
Photon-to-Digital Converters keep the information digital all along the acquisition chain.
FPGA-based tile controller gives a lot of flexibility to implement multiple features.
  Flag-based acquisition, dark count mitigation, pulse shape discrimination, and so on.
Tile Controller ASIC in development to replace the FPGA boards.
Wafer level measurement will accelerate the testing of multiple PDC for larger system integration.
Notes: Wafer to be use on larger panel

## Slide 40: A team’s work
Université de Sherbrooke
Jean-François Pratte
Serge Charlebois
Artur Turala
Catherine Pepin
Frédéric Nolet
Frédéric Vachon
Gabriel Lessard
Guillaume Théberge-Dupuis
Jeanne Morehead
Jérémy Chenard
Jérôme Deshaies
Keven Deslandes
Nicolas Roy
Philippe Arsenault
Philippe Martel-Dion
Raffaele Aaron Giampaolo
Robin Scarpellini
Samuel Parent
Sean Prentice
Simon Carrier
Tommy Rossignol
Olivier Lepage
Yves-Alexandre Beebe
Teledyne Dasla
ORNL
Lorenzo Fabris
Paul A. Hausladen
Samuel Parent
Claude Jean (CEO)
Stephane Martel
René Martel
Robert Groulx
Maxime Côté
This material is based upon work supported by the U.S. Department of Energy, National Nuclear Security Administration, Defense Nuclear Non-Proliferation Research and Development Office, and by the U.S. Department of Energy, Office of Science, High Energy Physics, under contract number DE-AC05-00OR22725.

## Slide 41: References
[1] nEXO Collaboration et al, “Nexo Pre-Conceptual Design Report,” arXiv.org, 13-Aug-2018. [Online]. Available: https://arxiv.org/abs/1805.11142.
[1] M. R. Heath et al., “Development of a Portable Pixelated Fast-Neutron Imaging Panel”, DOI:10.1109/TNS.2021.3136344.
Notes: Wafer to be use on larger panel

## Slide 42: BACKUP

## Slide 43: Test Bench for wafer-level measurement
Probe station
Probe station
Fully automatic chuck enabling scripts for multiple measurement on a wafer
Program to adapt for the wafer topology
Probe card
Can act as the interface between the PDC and the controller (FPGA)
Wafer topology
Probe card on the station

## Slide 44: Portable API-Based neutron Radiography
PDC panel array of 42 modules of 8 x 8 PDC
400-500 nm peak pixelated plastic scintillators
11E+6 SPADs over 30 x 30 cm2
40W PDC power consumption
  10 ns binning for 3k events/s/PDC,
  128 bins/event (1280 ns range/event)
Simulated timing distribution PDC of 25 ps RMS
~30 cm
~30 cm
Top side
Bottom side

## Slide 45: Digital Solution: Towards a 3D Integration
8 inch CMOS wafer
Reticle of 4×4 dies
Alignment die for 3D bonding
PDC CMOS readout
8 inch to 6 inch coring down
3D Bonding @ Teledyne DALSA (TDSI)
6 inch
SPAD wafer
6 inch
CMOS wafer
*SPAD process & 3D bonding process completed @ TDSI

## Slide 46: 8×8 Photodetection Module
8×8 PCB tile prototype​
8×8 PDCs
74 mm
94 mm
Top
Bottom

## Slide 47: Next Step: FPGA board to a Tile controller
FPGA-based Controller
45 mm
57 mm
ASIC-based Controller
Top side
Bottom side

## Slide 48: Toward 3d-PDC
150 mm SPAD wafer
200 mm PDC wafer

## Slide 49: Test Bench for wafer-level measurement
Probe station
Semi-automatic movement for wafer-level measurement (over 600 PDC)
Wafer topology interpolation
Wafer topology
Movement of the chuck in relation to the wafer
Notes: Utilisez les images

## Slide 50: Test Bench for wafer-level measurement
Laptop with Python scripts
Probe card on a probe station
Needles of the probe card (Microscope view)
Dedicated probe card
Active probe card with FPGA
Passive probe card
Notes: Use a probe station