## Slide 1: Extended HAICU Meeting
UBC Development
Takamasa Momose – Project Lead, Colin Noort – Mechanical Research Engineer
Tony Mittertreiner – Systems Engineer, Reza Akbari – Engineering Technician

## Slide 2: 2. Decelerators
How it Works: Anti-Helmholtz Coils
    Current is sent through one trap.
    Small coil has 8 windings (4 x 2)
    Large coil has 16 windings (4 x 4)
    Results in asymmetric field with minimum.
    Particles feel additional fictitious force in moving frame of reference  negative slope potential superimposed on quadrupole potential created by coils.

## Slide 3: 2. Decelerators
How it Works: Moving Trap
Design: Apply 5 – 250 μsec π pulse current (~ 600A) to an anti-Helmholtz coil at different timings.
Current Pulses
Anti-Helmholtz Coils
Trap Motion
H Atoms

## Slide 4: 2. Decelerators
Design Overview
    1st Decelerator section has ~370 Anti-Helmholtz coils:
      12.7 mm ID.
      24 AWG wire.
      6.5 mm trap-to-trap spacing.
    2nd Decelerator section has ~100 Anti-Helmholtz coils:
      10 mm ID.
      26 AWG wire.
      5 mm trap-to-trap spacing.
    Beamline runs along coil central axis and is connected to t-slot extrusion to ensure linearity.
    Coils are connected to electronics through set of bus bars.

## Slide 5: 2. Decelerators
Design Overview

## Slide 6: 2. Decelerators
Design Overview

## Slide 7: 3. Benders
Role: Separate seed gases (H2, He and/or Ne) from H atoms
Requirement:
    Bend 45 degrees at 350 m/s
Design:
    Halbach array hexapole using permanent magnets
Status:
    The same design has been used by our collaborators (Oxford).
    Field simulations have been done for the H atom bender.
    Design of bender is complete. Parts are currently being manufactured.
    January, 2024 we will test bending of CH3 radicals at UBC.
Bender 1
Role: Send 121 nm cooling pulses through the bender to the trap
Requirement:
    Bend 45 degrees at 20-50 m/s
Design:
    Quadrupole electromagnetic bender
Status:
    A quadrupole electromagnetic bender has been previously built and tested at UBC on CH3 decelerator.
    Chukman, Tony, and Colin are working collaboratively to develop the bender.
Bender 2

## Slide 8: 3.1. Permanent Magnet Halbach Array Bender
How it Works: Operating Principle
    Blocks precursor and carrier gases while acting as a low-pass velocity filter
    Maximum guidable beam velocity in a curved guide: , where R is the bend radius, and dB(r)/dr is the magnetic field gradient in transverse direction.

## Slide 9: 3.1. Permanent Magnet Halbach Array Bender
Design Overview: Magnet Selection in COMSOL

## Slide 10: 3.1. Permanent Magnet Halbach Array Bender
Design Overview: 3D Model with Precise Geometry

## Slide 11: 3.1. Permanent Magnet Halbach Array Bender
Design Overview: Assembled Magnet Clamp

## Slide 12: 3.2. Electromagnetic Bender
How it Works: Operating Principle
    Electric current sent through conductors. Current produces field which interacts with low field-seeking particles. Guides and focuses beam.
    Quadrupole, hexapole, and octupole configurations were all simulated at 2000 A
    Quadrupole was selected due to superior focusing
    Maximum guidable beam velocity in a curved guide:

## Slide 13: 3.2. Electromagnetic Bender
Design Overview (In Progress): Chukman’s 8-Wire Design
  Specifications:
    Channel is 6.4 mm wide
    Wire is a uniform 1.5 mm diameter copper conductor
    Current = 1616
    Winding Resistance = 0.00964 Ohm
    Self Inductance = 0.6436 uH

## Slide 14: Click to edit Master title style

## Slide 15: 2. Decelerators
Technical Challenges
    Amount of parts which need manufacturing will require dedicated attention in the coming months. 370 coils need to be wound and electrically connected to PCBs.
    All coils will need to be diligently checked before and after manufacturing for defects.
    MECH shop at UBC needs to make 96 bus bars and 50 coil housings, which will take time, work on this is in progress.
    Once all coils are connected to electronics through busbars, their connections will need to be checked, this will be done through a waveform oscilloscope program developed by Tony.

## Slide 16: 2. Decelerators
Timeline: Expected Completion Dates
    Build frame Completed
    Build adjustment system for aligning beamline Completed
    Manufacture and assemble busbar system February, 2024
    Manufacture and assemble coils, coil housings, and PCBs February, 2024
    Connect coils to busbars, and busbars to tune boxes March, 2024
Timeline: Milestones for Q1 and Beyond
    Finish manufacturing busbars, coils, and coil housings Q1
    Finish assembling decelerator sections Q1
    Connect all electronics to decelerator coils Q1
    Troubleshoot and optimize decelerator operation Q2

## Slide 17: 3.1. Permanent Magnet Halbach Array Bender
Technical Challenges
    Permanent magnet Halbach array bender has not been made at UBC before, and so there will likely be some minor troubleshooting throughout development.
    Magnets must be very precisely located so manufacturing requires a high degree of accuracy with very tight tolerances.
    Magnetic fields are not alterable, therefore the velocity of incoming beam will need to be tuned close to the expected incoming beam velocity the bender was designed for.

## Slide 18: 3.1. Permanent Magnet Halbach Array Bender
Timeline: Expected Completion Dates
    Complete 3D model and drawings for shop January. 2024
    Order and receive magnets from external company January, 2024
    Manufacture all bender box components February, 2024
    Assemble magnets inside of bender box February, 2024
    Connect bender to 1st decelerator section and obtain good signal March, 2024
Timeline: Milestones for Q1 and Beyond
    Finish manufacturing Q1
    Finish assembly Q1
    Finish testing and optimization Q1

## Slide 19: 3.2. Electromagnetic Bender
Technical Challenges
    Results of previous EM bender tests were not conclusive. Operating principle has yet to be proven with significant success rate.
    EM benders are very difficult to manufacture due to the curved nature of the conductor channels in the bender. May require multiple manufacturing iterations.
    Change to 8 wire configuration will require more complicated wiring procedure which could cause issues.
    Need to coordinate closely with Chukman and Sarah since they will be developing a flapper that will interface with our EM bender.

## Slide 20: 3.2. Electromagnetic Bender
Timeline: Expected Completion Dates
    Finalize the design of the EM bender February, 2024
    Manufacture EM bender components March, 2024
    Assemble and test the performance of the EM bender March, 2024
Timeline: Milestones for Q1 and Beyond
    Finalize Design Q1
    Manufacture and Assemble Q1
    Test Q1