## Slide 1: Overall schematic

## Slide 3: Magnetic trap, continuum model
Non-integer turns
No limit on copper sheet gauges
Non-integer number of coolant holes
v19 to v20: re-scaling some parameters

## Slide 4: Optimisation using simplex search

## Slide 7: Limiting induced voltage
Depends on the Sorensen
Right: 0.3 V induced voltage, assumes constant voltage from the Sorensen, no attempt to correct current deviation

## Slide 8: Discretising the continuum model
Imperfect match due to limited copper sheet gauges and integer number of turns
  Quadrupole: 0.040” copper, 0.003” Kapton, 18 turns
  Gate coil: 0.016” copper x 2, 0.003” Kapton, 4+40 turns
  Booster coil: 0.012” copper x 2, 0.003” Kapton, 1+6 turns
Still able to retain most of the trap depth
Issue: Booster coil is more power-dense than the gate coil, but both share the same coolant hole pattern
In the process of fixing this, re-running optimisation

## Slide 11: Coolant hole placing
Bernoulli equation with frictional loss:
  Input: a 1/16" diameter, 166.8332 mm long coolant hole subject to 30 psi of pressure difference
  Output: flow speed = 8.027 m/s
Turbulent flow simulation:
  Input: a 1/16" diameter, 166.8332 mm long coolant hole, inlet temperature of 30 degC, wall temperature of 50 degC along a 106.8332 mm section
  Output: power removed = 380.6025 W
Comsol 2D electrical + thermal sim
  Input: 6 coolant holes per 45 degrees, each coolant hole removes 380.6025 W / 2.5 = 152.241 W (safety factor of 2.5), 9 V / 44 turns / 8 sectors voltage difference applied across the simulation domain
  Output: 369.388 A current per 0.032" thickness, which is higher than the required 360 A.