## Slide 1: Fast-Closing Shutter for Particle Decelerator
Motivation: Improve the vacuum quality in the HAICU trap by preventing gas from off-gassing in the decelerator from entering
Design: A spring actuated fast-closing (<10 ms) shutter at the bender before the trap to be triggered after particles pass through the bender
Shutter design, installed at the last bender

## Slide 2: Fast-Closing Shutter for Particle Decelerator
Valve Motion: Resetting
1
2
3
Closed Valve
Valve Resetting, 1-way door opened
Valve Reset, ready to open

## Slide 3: Fast-Closing Shutter for Particle Decelerator
Valve Motion: Opening & Closing
4
5
6
Valve Opening
Valve Opened (70° max. rotation)
Valve closed rapidly by spring tension

## Slide 4: Fast-Closing Shutter for Particle Decelerator
Shutter Details:
3D Printed SS316 Parts
Viton Dampener
PEEK Bushings at Rotating Parts
Installed Shutter

## Slide 5: Fast-Closing Shutter for Particle Decelerator
Actuator Details:
One-Way Door, Tensioned Closed
PEEK Bushing
Shutter Pin-Path through the actuator

## Slide 6: Fast-Closing Shutter for Particle Decelerator
Design Considerations
  Many space constraints – off-the-shelf fast-closing valves are not suitable
  FEA & hand calculations to validate shutter strength
  Designed for UHV
    UHV Compatible Materials (SS316, Viton, PEEK)
    PEEK Bushings to prevent cold-welding of moving parts
    No closed volumes
Next Steps:
  Order 3D printed metal parts for benching testing
Shutter FEA Results, 50 N