## Slide 1
ARIEL Target Development
ARIEL Town Hall Meeting
January 11, 2017
Alexander Gottberg Department Head, Targets and Ion Sources

## Slide 2: ARIEL + ISAC: A RIB Factory
Thick targets, 500 MeV separation online
Production facility, 0.153 – 1.8 MeV/u
Post-Acceleration ≤16 MeV/u 2500 RIB h/y
Increased reliability, efficiency, flexibility, additional RIB species, 3000 RIB h/y
TRIUMF RIB Factory 2023
TISOL
1988
ISAC I
1995
ISAC II
2005
ISAC Upgrade
2018
CANREB
2020
ARIEL
2022
HRS, EBIS charge state booster, Nier-spectrometer, increased beam purity
2 additional target stations, independent e-driver, medical isotope production
9000 RIB h/y, 3 simultaneous beams, increased development capabilities, pure n-rich beams, extended beamtimes
→ Bob Laxdal: Operational model and ramp-up
→ Eric Guetre: ARIEL schedule

## Slide 3: ISAC Radioisotope Beams Since 1998
target materials:
UCx
UO2
ThO
Nb
Ta
TaC
NiO
ZrC
TiC
SiC
ion sources:
surface
resonant lasers
FEBIAD
IG-LIS

## Slide 4: An Independent Driver for TRIUMF’s Rare Isotope Program
500 MeV x 10 µA protons [1/s]
50 MeV x 10 mA electrons [1/s]
production intensity from 238UCx
Pure n-rich products from photofission

## Slide 5: An Independent Driver for TRIUMF’s Rare Isotope Program
cross sections
50 MeV x 10 mA electrons [1/s]
production intensity from 238UCx
Pure n-rich products from photofission
Production cross section greatly reduced in comparison to high-energy hadrons

## Slide 6: An Independent Driver for TRIUMF’s Rare Isotope Program
500 MeV x 10 µA protons [1/s]
50 MeV x 10 mA electrons [1/s]
production intensity from 238UCx
Pure n-rich products from photofission
Production cross section greatly reduced in comparison to high-energy hadrons

## Slide 7: An Independent Driver for TRIUMF’s Rare Isotope Program
50 MeV x 10 mA electrons [1/s]
production intensity from 238UCx
Pure n-rich products from photofission
Production cross section greatly reduced in comparison to high-energy hadrons
How much electron beam energy?
How much electron beam power?
  … for a competitive RIB program
TRIUMF’s new superconducting e-linac

## Slide 8: e-Induced Radioisotope Production Principles
electrons
UCx / BeO
50 MeV electron range ≈ 10 mm → direct target irradiation leads to:
inhomogeneous heat profile
overheating for Pe > 3 kW
→ use of high-Z e-to-γ converter

## Slide 9: ARIEL Production at Various Electron Energies
→ Ee = 35 MeV
Postpone resource-intense implementation of 50 MeV electron beam capabilities.

## Slide 10: Electron Beam Power
Electron Fluence [1/cm2]
Photon Fluence [1/cm2]
1· 1018
1· 1017
1· 1016
1· 1015
1· 1014
1· 1018
1· 1016
1· 1014
1· 1012
1· 1010
6 cm
1· 1018
1· 1017
1· 1016
1· 1015
1· 1014
W converter 4.6 mm
10 mm Al
attenuator
blocking residual primaries
1· 1018
1· 1016
1· 1014
1· 1012
1· 1010
1· 1018
1· 1016
1· 1014
1· 1012
1· 1010
1· 1018
1· 1017
1· 1016
1· 1015
1· 1014
UCx target 80 mm
ARIEL, 50 MeV, 10 mA, 500 kW

## Slide 11: Electron Beam Power
Electron Fluence [1/cm2]
Photon Fluence [1/cm2]
1· 1018
1· 1017
1· 1016
1· 1015
1· 1014
1· 1018
1· 1016
1· 1014
1· 1012
1· 1010
6 cm
1· 1018
1· 1017
1· 1016
1· 1015
1· 1014
W converter 4.6 mm
10 mm Al
attenuator
blocking residual primaries
1· 1018
1· 1016
1· 1014
1· 1012
1· 1010
1· 1018
1· 1016
1· 1014
1· 1012
1· 1010
1· 1018
1· 1017
1· 1016
1· 1015
1· 1014
UCx target 80 mm
ARIEL, 50 MeV, 10 mA, 500 kW
1· 103
1· 102
1· 101
1· 100
1· 10-1
1· 10-2
Power Deposition [kW/cm3]
power deposition:
200 kW in converter
80 kW in target container
ISAC is currently the facility with the highest power in an ISOL target (≈ 8 kW) world-wide.
No cooing technology available beyond that without significant RIB intensity losses!

## Slide 12: Design Study: Towards 500 kW
Heat gradients
Increased assembly vulnerability
Longer effusion times for less volatile species
Additional interlock systems
electron beam power from 100 kW to 500 kW → ≤2-fold increase in exotic radioisotope yields For comparison: x5 is a typical reach of any target / ion source development.
≤
!
20 kW per target container
windowless liquid metal converter
electron beam multi-spot scanning
multiple horizontal target containers
common transfer line
target + transfer line heating challenging
ion source
multiple transfer lines
→ Pe ≤ 100 kW
Postpone resource-intense implementation of 500 kW converter and target capabilities.

## Slide 13: Development of Requirements and Concepts
Process and design development driven by:
Operational model
Schedule and budget
Maximum RIB intensity, diversity, purity, reliability
Development flexibility
Choosing state-of-the art technology and applying lessens learnt in ISAC and other facilities
Ee = 35 MeV (saturation of fission rate)
Pe ≤ 100 kW (no technology for efficient use of higher power available, shielding designed for 500 kW)
mechanical part of target exchange in ≤ 24 h → target exchange in station not in hot cell, maximum fraction of process load in main control room
pre-conditioned hermetic target vessel and target acceptance stand (TISA) to approach 95% target assembly reliability (from top level requirement)
…

## Slide 14: Towards a > 2 kW ARIEL Electron-to-Gamma Converter
Solid Trench-Type Converter
high-Z primary converter layer
effective thickness: 0.5 S0
vertical UCx container
vertically scanned electron beam
minimize distance converter-target
limit target thickness
Full primary electron absorption:
→ beam power limit for solid converter: 30 - 100 kW (subject to tests)
→ 15% of beam power deposited in target → beam power limit for target ≈ 80 kW
water cooling
e-
8 x 45 mm
Al cooling body
5 cm
high-Z primary converter
transfer line
vertical 50 cm3 BaO / UCx target
50 kW e-beam power, 35 MeV
generation of bremsstrahlung in high-Z layer
stopping all primaries in low-Z material
Al cooling body with water cooling

## Slide 15: Towards a > 2 kW ARIEL Electron-to-Gamma Converter
γ-ray window
50 mm
target container 2000 °C
primary converter layer (Au) ~300 °C
water-cooled converter backing (Al) ~60 °C
e-beam 50 kW, 35 MeV
8 x 45 mm2
ARIEL electron-to-γ converter, γ-ray window, target geometry
→ converter materials irradiation test stand at e-linac to simulate AETE power density (material bond qualifications ongoing)
300 keV e-gun
300 keV diagnostics
converter test stand

## Slide 16: Target / Ion Source / Converter Concept
Making use of novel technology (Al welding techniques, sealing materials, etc.)
≈50 kW electron-to-gamma converter
γ-window separating electron and RIB beamlines
Full offline conditionability
Life time approximately 5 weeks
Target design allowing for proton / electron module compatibility
Flexibility for ion source and transfer line design
Compatible target vessel waste strategy developed
Preparing for 30 target units per year (target material synthesis, assembly production, waste management)
trench-type converter
target material container
ion source
water-cooled high current feedthrough
converter-to-e beamline vacuum interface
primary vacuum
flexible Ta sheet connectors
γ-ray window
gate valve
target-to-RIB vacuum interface

## Slide 17: ARIEL Target Station / Target Hall
module storage
remote-controlled crane (existing)
hot cell facility
target exchange point
spent targets
protons
electrons
AETE
APTW
drivers beam tunnel (existing)
Hall with two floor levels (existing)
RIB
RIB
Direct target exchange process (target remote connections at target station without moving target module to hot cell)
Modular design of components in high-radiation fields
Target station (gas and vacuum management, module interfaces)
Target pit (shielding, support / alignment structure, main services voids)
Hot cell, RIB modules, electron delivery line
ASTM

## Slide 18: ARIEL Target Station / Target Hall
Target module
1st RIB transport module
Target access
shield plug
Converter module
Electron diagnostics module
secondary confinement gas enclosure (vacuum at ISAC)
high-voltage feedthrough
Modules that allow for hot-cell based maintenance and repair
Direct target exchange in target station in ≤ 24 h
Hermetic and disposable target vessel
Converter on target vessel (start-up), on converter module (later)
Secondary confinement volume in air
Symbiotic medical target behind target
3.2 m
hermetic target vessel
AETE / APTW compatible TIS front end
target remote coupling table
hermetic target vessel
isolation valve
remote vacuum disconnect
remote vacuum disconnect
60 kV insulation
HV feedthrough
2nd RIB transport module
3rd RIB transport module
4th RIB transport module

## Slide 19: FLUKA Production Map from 35 MeV Electrons
ARIEL Current Concept Design In-Target Production Yields [10 kW-1·s-1]
In-target production rates [10 kW-1 ∙ s-1]:
from BeO:
8Li: 5∙1010
from UCx:
78Ni: 1∙105
98Kr: 8∙107
100Rb: 1∙108
98Sr: 5∙109
132Sn: 5∙108
146Xe: 2∙107
144Ba: 5∙109
150Cs: 4∙105
in agreement with initial project description
Neutron Number
In-Target Production Rate in Current Concept [(10kW s)-1]

## Slide 20: Preliminary: Expected Yields from AETE in Low Energy Stations
ARIEL 35 MeV, 10 kW, concept geometry [s-1]
ISAC 500 MeV, 10 µA [s-1]
From BeO at 50 kW electron beam power:
8Li expected yield: 5∙107 s-1 (assuming 0.2% extraction, 10% ionization)
From UCx at 50 kW electron beam power: Overall fission rate: ~1∙1012 s-1
ARIEL RIB yield predictions available for experiment planning

## Slide 21: Preliminary: Expected Yields from AETE in Low Energy Stations
From BeO at 50 kW electron beam power:
8Li expected yield: 5∙107 s-1 (assuming 0.2% extraction, 10% ionization)
From UCx at 50 kW electron beam power: Overall fission rate: ~1∙1012 s-1
AETE will provide:
Pure n-rich fission fragments
Additional beamtime with modern, reliable driver
Chances for long-duration beam time
High integrated yields for specific isotopes
Development capability
APTW will provide:
Access to all ISAC spallation targets
Hermetic target vessel → new target materials
Additional development flexibility for new ion sources and transfer line technologies
ARIEL 35 MeV, 10 kW, concept geometry [s-1]
ISAC 500 MeV, 10 µA [s-1]
134Sn
134Sn
ARIEL RIB yield predictions available for experiment planning

## Slide 22: RIB Development
ISAC is currently ≈1.8-fold overbooked
with ARIEL the output of RIB shall triple (from ~2800 h/a to over 9000 h/a)
→ ARIEL will offer new RIB perspectives in alignment with high international backload on RIB delivery (targets with flexible technology for optimized and reliable isotope yields, quick turn-over, purity, isotope availability)
Areas of target, ion source, converter development:
New target nuclides (Be, Ca, La, W, Pb, Bi)
Nanostructured porous target materials (SiC, TiC, UCx, LaC2)
Molecular beams for extraction of non-volatile species
New ion sources (TRILIS + FEBIAD, various work function SIS)
New transfer lines (quartz, cold, variable temperature)
High-power electron-to-γ converter
Proton-to-neutron converter
ARIEL will allow for:
More online development time (4 target stations, faster target turn-over, 2 yield stations, 2 independent drivers)
Additional development capabilities (pulsed driver beam, hermetic target vessel, additional development space for ion sources and transfer lines)
Conditions: sufficient resources, experts that are not occupied with operation / repair / maintenance, sufficient online development time
ISAC yields since 1998

## Slide 24: Upcoming Challenges
Target module refurbishment
Target laboratories restructuring
ARIEL development / construction
Target production ramp-up
→ Proactive approach :
Target material and target assembly production schedule with sufficient reserve
Sustainable target module refurbishment program
One additional target module in circulation
Upscaling production methodology (UCx production currently ~ 6 weeks)
Systematic approach towards targets assembly reliability
Utilizing additional ARIEL infrastructure (laboratories, material ovens, manpower)
less “firefighting”

## Slide 25: TRIUMF – A High-Power Target Laboratory
ARIEL (since 2010)
2 target stations under construction
35 MeV: 100 kW electrons
500 MeV: 50 kW protons
TRIUMF (since 1968)
550 MeV, 150 kW cyclotron
50 MeV, 500 kW e-linac
>6000 proton h annually to:
ISOL production (50 kW protons,100 kW electrons)
µ and π production (60 kW)
medical isotopes (50 kW)
cold neutrons (20 kW)
proton therapy (50 W)
ISAC (since 1995)
2 target stations
500 MeV, 50 kW protons
Post-Acc. RIB:
1.8 MeV/u &
≤16 MeV/u
→ RIB power: 1 pW to 100 nW

## Slide 26: ISAC Target Assembly
target oven
ionizer tube
cooling-water supply
diffusion bonded Ta fins → radiative cooling of up to 13 kW
→ 50 kW proton irradiation
target oven heating terminals
ionizer heating terminals
heat shield (cover hidden)
multi-pin (diagnostics, ion source, etc.)
target container ~2000 °C
(Ø 20 mm, 60 cm3)
extraction electrode
hot cell telemanipulator grips
heat shield