## Slide 1: Mass Measurements of the Heaviest Elements with the SHIPTrap Mass Spectrometer @GSI
Francesca Giacoppo
GSI Darmstadt
Helmholtz-Institut Mainz
20th International Conference on Electromagnetic Isotope Separators and Related Topics, EMISXX - Oct. 19 -24, 2025 Whistler, Canada

## Slide 2: PTMS for SHE
What is the structure of SHEs?
...Stability due to shell effects
 accurate binding energies!
≈ 1/s ≈ 1/day ≈ 1/week
EMISXX - 21.10.2025

## Slide 3: Are superheavies made in the r-process?
What is the heaviest element
that can be synthetized in a lab?
...and in the stars?
≈ 1/s ≈ 1/day ≈ 1/week
O. R. Smits et al, Nature Rewiew P. 6 86 (2024)
S. A. Giuliani et al, RMP 91, 011001 (2019)
EMISXX - 21.10.2025

## Slide 4: Mapping nuclear shell effects with direct mass measurements
High-precision mass spectrometry of the SHEs allow to...
  ... map and study nuclear shell effects
  ... provide anchor points to fix alpha decay chains
  ... benchmark theoretical models
  … investigate isomeric states
E. Minaya Ramirez et al, Science 337 1207 (2012)
O. Kaleja et al, PRC 106, 054325 (2022)
EMISXX - 21.10.2025

## Slide 5: Mapping nuclear shell effects with direct mass measurements
TASCA 21 @GSI, 22 June 2021
254No
55s
270Ds
0.1ms
262Sg
6.9ms
266Hs
2.3ms
258Rf
13ms
α
α
α
α
Z = 102
Z = 104
Z = 106
Z = 108
Z = 110
270Ds mass can now be fixed with about 40 keV uncertainty
SHIPTRAP PI-ICR
SHIPTRAP TOF-ICR
Connected isotopes
M. Dworschak et al, PRC 81 (2010)
O. Kaleja et al, PRC 106, 054325 (2022)
High-precision mass spectrometry of the SHEs allow to...
  ... map and study nuclear shell effects
  ... provide anchor points to fix alpha decay chains
  ... benchmark theoretical models
  … investigate isomeric states
EMISXX - 21.10.2025

## Slide 6: PTMS for SHE: Where we started and where we are
50 ions in 4 days
𝝳m/m = 3E-7
256Lr2+
M. Block et al., Nature 463, 785 (2010)
M. Dworschak et al., PRC 81, 064312 (2010)
E. Minaya Ramirez et al., Science 337, 1183 (2012)
O. Kaleja et al., PRC106, 054325 (2022)
Until 2012 up to masses of
252-255No and 255,256Lr
with δm/m ~ 10-7 to 10-8
2021
SHIPTRAP
SHIPTRAP @GSI
TRIGATRAP @ Mainz
MR-TOF @Riken
2018
EMISXX - 21.10.2025

## Slide 7: The SHIPTRAP setup
EMISXX - 21.10.2025

## Slide 8: Ion storage in a Penning Trap
133Cs+
???
radioactive
Low ion rate = long measurements
Challenges:
Reduced drift of the magnetic field  Two/three steps temperature stabilization
of the magnet bore
                (temperature fluctuations reduced to ~ 10mV)
Reduced drift of the trapping voltage  More stable power supplies for MT temperature-controlled cabinet (dV < 1 mV)
Reference
Ion of interest
Time
Ion of interest
Reference ion
Important: (systematics) → choice of reference!
DPG SAMOP 2024 – 11.03.2024
EMISXX - 21.10.2025

## Slide 9: Phase Imaging Ion-Cyclotron Resonance method PI-ICR
S. Eliseev et al., Phys. Rev. Lett. 110, 082501 (2013)
S. Eliseev et al., Appl. Phys. B114, 107 (2014)
Determination of the
spatial distribution
Radial excitation
Radial excitation followed by
a phase accumulation time
Φ
Gain in Precision ≈ 4.5
Gain in resolving power ≈ 40
P. Filianin et al, Phys. Lett. B 758 407-411 (2016)
EMISXX - 21.10.2025

## Slide 10: Beamtime June-July 2018: 255mLr
255mLr
E*≈30 keV
T1/2≈2.5 s
Cyclotron Phase
O. Kaleja et al., PRC 106, 054325 (2022)
A. Chantillon et al., Eur. Phys. J. A 30 (2006) 397
F. Hessberger et al., Phys. At. Nucl. 70 (2007) 1445
S. Antalic et al., Eur. Phys. J. A 38 (2008) 219
Resolving power ≈
11 000 000 !!!
PRELIMINARY
EMISXX - 21.10.2025

## Slide 11: Beamtime April-June 2021
F.-P. Heßberger et al, Z. Phys. A 359 415 (1997)
K. Hauschild et al, Eur. Phys. J. A 58 6 (2022)
257gRf2+
257mRf2+
PRELIMINARY
center
Mass measurements of heavy nuclides with SHIPTRAP @GSI in 2021/24: 257Rf (Z=104) & 258Db (Z=105)
257Rf : supreme mass resolving power of SHIPTRAP up to 11,000,000 allows resolving low-lying nuclear isomers (resolution at the keV-level for excitation energy!)
258Db : first measurements with only 5 detected ions in total and rates down to ≈ 0.00002/s
15 events in 15 hours
~1200 ms Acc. time
EMISXX - 21.10.2025

## Slide 12: 241Cf has an isomer!
241mCf2+
241Cf2+
PRELIMINARY
200 ms
Acc. time
19 events in 8 hours
~200 ms Acc. time
EMISXX - 21.10.2025

## Slide 13: Summary
Thanks to the technical and methodical improvements achieved at SHIPTRAP in the last years we had extended our investigations towards more exotic nuclides with higher Z.
Implementation of the Cryogenic buffer-gas cell Boosted overall efficiency of about a factor of 10 compared to 2010
Development of a new measurement method, the PI-ICR technique Confirmed PI-ICR high mass resolving power for radioactive nuclides at the lowest production yields
Successful direct measurements of the first superheavy
257Rf (σ=15 nb) and its low-lying isomeric state!
EMISXX - 21.10.2025

## Slide 14: Low 258Db incoming rate: efficiency drop?
TASCA 21 @GSI, 22 June 2021
SHIP
The cryocell entrance
window got thicker with time!
258Db(1)
T1/2=4.4 s
(5+, 10-)
51 keV
258Db(2)
T1/2=2.17 s
(0-)
0 keV
254mLr
254gLr
M. Vostinar et al., EPJA 55, 17 (2019)
P. Schury et al., RIKEN AP Rep. 55, 7 (2022)
Outlook: Hunting 258Db
Exp. February 2024 X
Exp. May 2025 X
EMISXX - 21.10.2025

## Slide 15
TASCA 21 @GSI, 22 June 2021
Outlook: What’s next?
New Off-line Branch for SHIPTrap: recoil source buffer-gas cell + compact buncher
          53% Extraction efficiency
          in first tests with 225Ac source
EMISXX - 21.10.2025

## Slide 16
TASCA 21 @GSI, 22 June 2021
Outlook: What’s next?
New Off-line Branch for SHIPTrap: recoil source buffer-gas cell + compact buncher
          53%
EMISXX - 21.10.2025

## Slide 17
TASCA 21 @GSI, 22 June 2021
SHIP
Outlook: What’s next?
New Buncher for SHIPTrap  Cryogenic! (Ongoing)
Design of a new Penning-trap system  more efficient purification and PI-ICR in cryogenic environment (Starting Soon)
                (We are looking for a PhD student!)
EMISXX - 21.10.2025

## Slide 18: SHIPTRAP collaborators
B. Anđelić, L. Arcila Gonzalez, K. van Beek, J. Berrocal Sanchez, A. Brizard, L. Blaauw, K. Blaum,
M. Block, J. Cipagauta Mora, P. Chauveau, S. Chenmarev, P. Chhetri, C. E. Düllmann, M. Eibach, J. Even, P. Filianin, M. Gutierrez Torres, B. Hartigan, F. P. Hessberger,
N. Kalantar-Nayestanaki, O. Kaleja, T. Kieck, J. van de Laar, M. Laatiaoui, S. Lohse,
E. Minaya Ramirez, A. Mistry, S. Morard, E. Morin, Y. Nechiporenko, D. Neidheer,
S. Nothhelfer, Y. Novikov, J. Patel, S. Raeder, E. Rickert, D. Rodriguez,
L. Schweikhard, P. G. Thirolf, J. Warbinek, A. Yakushev
EMISXX - 21.10.2025

## Slide 19
TASCA 21 @GSI, 22 June 2021
Thank you for your attention!
EMISXX - 21.10.2025

## Slide 20
TASCA 21 @GSI, 22 June 2021
EMISXX - 21.10.2025

## Slide 21: Ion storage in a Penning Trap
n-
n+
nz
axial motion
cyclotron motion
magnetron motion
trajectory
axial motion
EMISXX - 21.10.2025