## Slide 1
Present and future mass measurement methods
of the Rare-RI Ring
A. Yano (Univ. of Tsukuba / RIKEN)
for the Rare-RI Ring collaboration

## Slide 2
Outline
Introduction
- Principle of isochronous mass spectrometry
- The Rare-RI Ring facility@RIBF
- Achieved isochronism & mass precision
Recent upgrades
- Injection to the Rare-RI Ring
- Extraction from the Rare-RI Ring
- Future mass measurements in the Rare-RI Ring
Summay & Outlook

## Slide 3
Principle of mass measurements
Isochronous mass spectrometry (IMS)
Isochronism: constant revolution time ()
for the reference particles
Orbit length () ⇔ Magnetic rigidity ()
<
Reference particles
Target particles

## Slide 4
Principle of mass measurements
where
Revolution times,
Velocity,
Magnetic rigidity
or
correction method
correction method
Isochronous mass spectrometry (IMS)
Isochronism: constant revolution time ()
for the reference particles
Orbit length () ⇔ Magnetic rigidity ()
<
Reference particles
Target particles

## Slide 5
F3
F5
S0
Injection beamline
Kicker
magnet
F2
Trigger signal
R3
BigRIPS
OEDO-SHARAQ
The Rare-RI Ring (R3) facility
Combined with a powerful
in-flight separator, BigRIPS
Individual injection method
S. Naimi et al., EPJA 59-90 (2023)
PID plot@F2-F3
Circumference
60.35 m
Max. Bρ
6.4 Tm
Momentum acceptance
dp/p=1%
Measurement
time
<1 ms
Injection
acceptance of R3
A. Ozawa et al., PTEP2012 03C009 (2012)
Y. Yamaguchi et al., NIM-B317 629-635 (2013)

## Slide 6
701100
701200
701500
701600
701300
701400
Stored time [ns]
-0.5
-0.3
0.0
-0.2
-0.1
-0.4
0.1
0.2
0.3
0.4
0.5
dp/p [%]
Achieved isochronism & mass precision
78Ge (isochronous reference)
Isochronism: ~5.4x10-6
D. Nagae et al., PRC110, 014310 (2024)
75Cu
79As
78Ga
76Zn
δ(m/q) 2.7x10-5 1.1x10-5
75Cu
correction
correction
-
-4.010-5
-2.010-5
0.0100
2.010-5
4.010-5
δm ~740 keV ~290 keV

## Slide 7
Recent upgrades
(i) Injection to R3
(ii) Extraction from R3
(iii) Future mass measurements

## Slide 8
(i) Injection to R3
00
F3
Injection
line
R3
Low injection efficiency to R3
±18 mm
Vertical shift
Y : -2.0 mm
Y’: -2.7 mrad
Geometrical acceptance
Vertical steering magnets

## Slide 9
00
F3
Injection
line
R3
Vertical shift
Y : -2.0 mm
Y’: -2.7 mrad
Geometrical acceptance
ST1
 | ST1 | ST2
Magnetic flux density | 0.056 T | 0.067 T
Current | 19 A | 17 A
Size | 370430300 mm | 310360250 mm
Pole gap | 170 mm | 125 mm
Weight | 180 kg | 110 kg
 | ST1 | ST2
Magnetic flux density | 0.056 T | 0.067 T
Current | 19 A | 17 A
Size |  | 
Pole gap | 170 mm | 125 mm
Weight | 180 kg | 110 kg
±18 mm
Vertical steering magnets
(i) Injection to R3
Low injection efficiency to R3

## Slide 10
Kicker magnet
Y [mm]
0
50
-50
-7.4 mm
w/o ST
Y’ [mrad]
0
10
-10
-1.8 mrad
w/o ST
Deflection angle
ST1: -1.5 mrad
ST2: +1.7 mrad
Y [mm]
-20
-10
0
10
20
-10
0
10
20
Y’ [mrad]
124Xe ~155 MeV/u@R3
Y and Y’ at the kicker magnet
Y: -2.0 mm
Y’: -2.8 mrad
Vertical beam profile@F3
Commissioning results
(i) Injection to R3

## Slide 11
Y [mm]
0.4 mm
w/ ST
0
50
-50
-7.4 mm
w/o ST
Y’ [mrad]
0
10
-10
-0.5 mrad
w/ ST
-1.8 mrad
w/o ST
Y and Y’ at the kicker magnet
Deflection angle
ST1: -1.5 mrad
ST2: +1.7 mrad
Vertical mismatch
was corrected
Injection x2
Extraction x3.5
Kicker magnet
Commissioning results
Y [mm]
-20
-10
0
10
20
-10
0
10
20
Y’ [mrad]
124Xe ~155 MeV/u@R3
Y: -2.0 mm
Y’: -2.8 mrad
Vertical beam profile@F3
(i) Injection to R3

## Slide 12
(ii) Extraction from R3
Beam motion inside R3
Y. Abe et al., NIM-A1072,170083 (2023)
78Ge, 4.8508 Tm (175 MeV/u)
0.9 ppm standard deviation
Still large gap between RMD-4 and ELC
 Beam motion inside R3
Transmission relative to F3
0.1
1
10
100
F3
S0
ILC1
ILC2
RMD-4
ELC
x10
S. Naimi et al., EPJA 59-90 (2023)
Beam tracking simulation with By
3D magnetic field
Runge-Kutta method
Isochronism evaluation
Stored

## Slide 13
(ii) Extraction from R3
Vertical beam motion
Main coils
Trim coils for isochronous magnetic field
Calculate 3D magnetic field using Opera 2023
Parameterize the magnetic field as a function of the beam position
78Ge
4.8508 Tm (175 MeV/u)
After 6 revolutions
ppm-order isochronism region
Simulated isochronous conditions of dp/p=0 particles

## Slide 14
(iii) Future mass measurements
Schottky-based IMS
Present (detectors upstream R3)
Velocity : TOF (F3-S0)
: Position@F5
Future (detectors installed in R3)
Velocity : Revolution time
: Position@R3
Whole measurements will be completed inside R3
Better transmission of high-Z beams

## Slide 15
(iii) Future mass measurements
Present (detectors upstream R3)
Velocity : TOF (F3-S0)
: Position@F5
Future (detectors installed in R3)
Velocity : Revolution time
: Position@R3
Schottky-based IMS
Electric or magnetic field is induced
Non-destructive
Schottky detectors
Fast detection
F. Suzaki et al.,
RIKEN APR49,179 (2016)
T. Yamaguchi et al.,
RIKEN APR58
124Xe54+ (155 MeV/u) was detected <10 ms!
Whole measurements will be completed inside R3
Compact Schottky
for velocity measurements
Better transmission of high-Z beams

## Slide 16
Reference cavity
Elliptical cavity
Position-sensitive
Courtesy by G. Hudson-Chang
(iii) Future mass measurements
Schottky Cavity Doublet (SCD)
Schottky Cavity Doublet (SCD)
for measurements
Signal sensitivity of the elliptical cavity
D. Dmytriiev et al., NIM-B463, 320-323 (2020)

## Slide 17
Reference cavity
Elliptical cavity
Position-sensitive
Courtesy by G. Hudson-Chang
(iii) Future mass measurements
Schottky Cavity Doublet (SCD)
Schottky Cavity Doublet (SCD)
for measurements
Signal sensitivity of the elliptical cavity
D. Dmytriiev et al., NIM-B463, 320-323 (2020)
Positional dependence
Signal height (elliptical cavity / reference cavity)
The beam position inside R3

## Slide 18
Reference cavity
Elliptical cavity
Position-sensitive
Courtesy by G. Hudson-Chang
(iii) Future mass measurements
Schottky Cavity Doublet (SCD)
Schottky Cavity Doublet (SCD)
for measurements
Sep. 2024
Shipped from Germany

## Slide 19
Summary & Outlook
The Rare-RI Ring facility: A unique storage ring optimized for IMS
Outlook:
Test of Schottky Cavity Doublet
Mass measurements:
n-rich side / high-z region with 238U
p-rich side with 124Xe
Isomer beam filter: Poster #128
T1/2 < ~20 ms
High-Z
Some recent upgrades:
Injection to the Rare-RI Ring
- The vertical beam trajectory correction  The vertical steering magnets
- The Injection (x2) and the extraction (x3.5) was improved
Extraction from the Rare-RI Ring
- Injected beam is not fully extracted  Beam motion
- The beam tracking simulation with 3D magnetic field
Future mass measurements
- Schottky-based IMS
- Compact Schottky & Schottky Cavity Doublet

## Slide 20
Summary & Outlook
The Rare-RI Ring facility: A unique storage ring optimized for IMS
28
28
50
Outlook:
Test of Schottky Cavity Doublet
Mass measurements:
n-rich side / high-z region with 238U
p-rich side with 124Xe
Isomer beam filter: Poster #128
Some recent upgrades:
Injection to the Rare-RI Ring
- The vertical beam trajectory correction  The vertical steering magnets
- The Injection (x2) and the extraction (x3.5) was improved
Extraction from the Rare-RI Ring
- Injected beam is not fully extracted  Beam motion
- The beam tracking simulation with 3D magnetic field
Future mass measurements
- Schottky-based IMS
- Compact Schottky & Schottky Cavity Doublet

## Slide 21
Thank you for your listening!
M. S. Sanjari1, A. Ozawa2, Y. Yamaguchi3, T. Ohnishi3, Y. Abe3, G. Hudson-Chang3,4,
D. Nagae5, T. Yamaguchi5, N. Chandratakumar3,4, N. Imai6, Y. Kikuchi5, N. Kitamura6, R. Kojima6,
J. Li6, T. Moriguchi2, S. Nishizawa5, F. Suzaki7, K. Takiura5, N. Tomioka5, R. Tuchiya6, M. Wakasugi8,
K. Watanabe5, R. Yokoyama6, and H. Zhang2
1 - GSI, 2 – University of Tsukuba, 3 – RIKEN, 4 – University of Surrey, 5 – Saitama University,
6 – The university of Tokyo, 7 – JAEA, 8 – Kyoto University

## Slide 23
(i) Injection to R3
Low injection efficiency to R3
Vertical
steering
magnets
ST1: -0.7 mrad
ST2: +1.0 mrad
Correct
the vertical
beam trajectory
R3
100@F3
10@Injection
1@ELC
00
F3
Injection
line
R3
Y: -2.0 mm, Y’: -2.7 mrad

## Slide 24
Design of the vertical steering magnets
ST1
 | ST1 | ST2
Magnetic flux density | 0.056 T | 0.067 T
Current | 19 A | 17 A
Size | 370430300 mm | 310360250 mm
Pole gap | 170 mm | 125 mm
Weight | 180 kg | 110 kg
 | ST1 | ST2
Magnetic flux density | 0.056 T | 0.067 T
Current | 19 A | 17 A
Size |  | 
Pole gap | 170 mm | 125 mm
Weight | 180 kg | 110 kg
ST1
ST2
Concidered beam conditions
Max. Bρ 6.4 Tm
Position deviation < |3| mm
Angle deviation < |6.5| mrad
 Required BL product : ~0.0192 Tm
Geometrical requirements
Aperture of the beam pipe
ST1 : 150 mm
ST2 : 110 mm
Max. pole length
ST1 : 300 mm
ST2 : 250 mm

## Slide 25
Schottky Cavity Doublet (SCD)
Sep. 2024
Shipped from GSI
Beam
Elliptical cavity
Reference cavity
Installed at the 2nd
straight section
F.G.
Signal

## Slide 26
Mass measurements in R3 vs other techniques
RIKEN APR56, S1-S5 (2023)
75Cu
Advantages of R3
Short measurement time
Δm ~few 100 keV
T1/2 < ~20 ms

## Slide 27
How to prepare 3D magnetic field in the simulation
Main coils
Trim coils
X
Y
Z
Total B = Bmain + Btrims
w/ Trim coils
1915 A
Y=Z=0 mm
Z-direction: 5-order enge function
Parameterized By distribution
of the main coils
X-position [mm]
0
-50
-100
-150
50
100
150
200
-200
-12000
-11000
-10000
-9000
-8000
1915 A
Y=Z=0 mm
Y-magnetic field flux [G]

## Slide 28
How to prepare 3D magnetic field in the simulation
Main coils
Trim coils
X
Y
Z
200 A
0
-50
-100
-150
-200
50
100
150
200
X-position [mm]
Y-magnetic field flux [G]
-60
-40
20
0
-20
40
60
Y=Z=0 mm
Parameterized By distribution
of the trim coils
w/ Trim coils
Total B = Bmain + Btrims

## Slide 29
How to prepare 3D magnetic field in the simulation
Main coils
Trim coils
X
Y
Z
Total B = Bmain + Btrims
w/ Trim coils
X-position [mm]
Y-magnetic field flux [G]
Parameterized
By_main + By_trims distribution
Y=Z=0 mm
-20 mm≦Y≦20 mm in 1 mm steps
 Spline interpolation

## Slide 30
Specifications of the Schottky detectors
Res. freq. | ~500 MHz
Q-factor | ~7000
Rsh | ~3 MΩ
Res. freq. |  | 
Q-factor | ~3000 | ~2300
Rsh | ~420 kΩ | -
~230 MHz