## Slide 1: Ion source development for TATTOOS: the new large-scale radionuclide production infrastructure at PSI
IMPACT/TATTOOS
Maryam Mostamand
EMIS 2025, 22 Oct 2025

## Slide 2
IMPACT-TATTOOS/PSI
P+
100 μA, 590 MeV
α- therapy
β- therapy
Auger therapy
SPECT
PET
TATTOOS

## Slide 3
181Ta(p,10p + 23 n)149Tb
Radiopharmaceutical
manufacture
149Tb: A flowchart based on ISOLDE/PSI collaboration

## Slide 4: Introduction: Target & Front end
  Reusable target
  ISOLDE-like target (sealed target)
  Very high throughput (10’s of μA beams)
  Beam quality
    Energy spread
    Emittance
    Focal point
    Separations
Energy spread
emittance
Extraction system

## Slide 5: Extraction system
ISAC
ISOLDE
The production target at ISAC, P. Bricault, et. al. American Institute of Physics (2001).
Schematic layout of a standard ISOLDE target-ion source unit, E. Bouquerel, et al. Thesis (2009)
Plasma electrode
Lens
(extraction electrode)
Ground electrode
Movable ground electrode
Fixed electrodes
HV
HV

## Slide 6: Simulation representation (COMSOL)
Target
Ion source
Extraction electrode
(grounded)
Laser beam
Two separate particle seeding methods have been generated for laser ionization and surface ionization.
Laser ionization seeding is within the ionizer volume and ions hitting the ionizer wall, will be removed from the remaining computations.
Surface ionization seeding only occurs on the surface of the ionizer walls. ions hitting on the wall, reset their energy and bounce back as thermal re-emissions.
Ionization processes are not considered, only transport considerations.
Plasma effect and space charge effect are not included in the simulations.
Axis-symmetry (r-z plane).
Laser beam

## Slide 7: 1. ISOLDE-like extraction
Surface only
laser only
Surface & laser ions
4ϵrms = 5.8 ± 0.3 mm-mrad
d= 60 mm

## Slide 8: 1. ISOLDE-like extraction
25 % outside 10 eV
d= 60 mm

## Slide 9
Energy spread is large in this design
The opening angle of the screen is important:
The field inside the ionizer tube changes.
The angle helps with the focusing of the beam while varying ground electrode distance with respect to the ionizer (d) doesn’t have significant impact on the beam collimation.
ISOLDE-like extraction- discussion
Acceleration region inside the ionizer
Acceleration region
Ɵ

## Slide 10: 2. ISAC-like extraction
lens
Plasma electrode
Ground electrode
Surface only
Laser only
Surface & laser ions
4ϵrms = 4.1 ± 0.2 mm-mrad

## Slide 11: 2. ISAC-like extraction
lens
Plasma electrode
Ground electrode
2 % outside 10 eV

## Slide 12
Changing G electrode distance (d) with fixed lens voltage:
Slight change in energy spread and beam focusing, No change in emittance.
Fixed G electrode with lens voltage variation:
Higher bias voltages result in larger E_spread, Emittance; slight change in beam focusing, however beam will have tails for higher bias voltages. Optimal is between 1-2kV.
Plasma electrode angle variations:
Slight change in beam focusing, smaller angle result in larger emittance and E_spread due to larger field penetration. Optimal is around 60 – 75 degrees.
2. ISAC-like extraction- observations
d

## Slide 13: 3. ISAC-like extraction without lens
By increasing distance of G electrode, emittance and energy spread becomes smaller (comparable to the ISAC design), while the ion beam is well collimated. Optimal is 90 mm.

## Slide 14: Energy spread
2 % outside 10 eV
d = 60 mm
d = 100 mm
25 % outside 10 eV
d = 70 mm
6 % outside 10 eV
Extraction with 2 electrodes
Extraction with 1 electrode

## Slide 15: Conclusions
Laser ionization has larger energy spread and smaller emittance.
Surface ionization has larger emittance and smaller energy spread.
The shape and opening diameter of the closest electrode/plate to the ionizer tube is what defines the field shape inside the ionizer and consequently changing the beam quality.
Having a gradual extraction such as adding an extra electrode between the ionizer and ground electrode can smooth the field inside the ionizer and improve the energy spread significantly.
This additional electrode also keeps the energy spread and emittance consistently small while the beam collimation can be adjusted by the ground electrode.

## Slide 16: Thank you for your attention!
Thanks to all the TATTOOS team members and the external advisors!

## Slide 17: Back up slides

## Slide 18
Gap: 60 mm
Gap: 100 mm
ISOLDE
Laser ionization

## Slide 19
ISOLDE-gap 100mm
Laser ionization
ISAC_lens 2 kV

## Slide 20
ISAC-lens: 2kV, Plasma angle: 60,
G electrode distance (d): variable
d=30 mm
d=60 mm
d=90 mm
d=80 mm
d=70 mm
4.0 +/- 0.2
4.0 +/- 0.2
4.0 +/- 0.2
4.0 +/- 0.2
4.0 +/- 0.2
452+645=1097
d

## Slide 21
ISAC-lens: 2kV, Plasma angle: 90,
G electrode distance (d): variable
d=30 mm
d=60 mm
d=90 mm
3.7 +/- 0.2
1077

## Slide 22
No lens- plasma angle: 60,
G electrode distance (d): variable
d=10 mm
d=30 mm
d=60 mm
d=70 mm
d=90 mm
4rms: 10.5 +/-0.6
4rms: 7.0 +/-0.4
4rms: 4.8 +/-0.3
4rms: 4.3+/-0.3
4rms: 4.0 +/-0.2
Adding extra extraction lens helps with keeping the emittance and energy spread small while moving the G electrode!
1076
1107

## Slide 23
Ionizer radius: 2 mm, no lens, d=90mm, plasma angle: 75o, plasma r= 1.5 mm
4rms = 5.8 +/- 0.3
Lens: 2kV, d=70mm
4rms = 5.7 +/- 0.3
1516
1529

## Slide 24
4rms = 6.0 +/- 0.3
4rms = 5.7 +/- 0.3
Ionizer radius: 2mm, lens: 2kV, d=80mm, plasma angle: 75o , plasma r= 1.8 mm
plasma r= 1.5 mm
1553
1543

## Slide 25
gap: 30 mm
gap: 60 mm
gap: 100 mm
gap: 30 mm
gap: 30 mm
gap: 60 mm
gap: 60 mm
gap: 100 mm
gap: 100 mm
15°
60°
75°

## Slide 26
ISOLDE (measurements)