## Slide 1: High-precision mass measurements with TITAN Multi-Reflection Time-of-Flight (MR-TOF) Mass Spectrometry
Pavithra Weligampola | EMIS 2025 | TRIUMF and University of Manitoba
1

## Slide 2
https://people.physics.anu.edu.au/~ecs103/chart/
Precision in mass measurements away from stability is crucial for our understanding of nuclear structure and astrophysical studies
dm/m = 10-7
Halos and skins
dm/m = 10-5 – 10-6
Nuclear shell structure
dm/m < 10-6 – 10-7
Nucleosynthesis via the r-process
And we need high-precision mass measurement tools !

## Slide 3: TITAN facility at TRIUMF can perform such measurements
TRIUMF’s Ion Trap for Atomic and Nuclear science (TITAN)
EBIT Charge breeder
Penning trap mass spec.
RFQ
Cooler & buncher
Isobar Mass
Separator
Low-energy
beam transport
TITAN
ISOL Target
≤100uA,
500 MeV
protons from cyclotron
MR-TOF

## Slide 4
  The mass is determined by its time-of-flight (TOF).
  Mass resolving power (R)

## Slide 5
C. Jesch et al., Hyperfine Interact. 235 (2015) 97, M. Yavor et al., Int. J. Mass Spec. 381 (2015) 1-9 ,T. Dickel et al., J. ASMS 28 (2017) 1079
TITAN MR-TOF achieves high performance to meet its science objectives.
  High resolving power 600,000
  High dynamic range 104 -108
  Mass accuracy 10-7
  Published sensitivity 0.006 pps*
Resolved low-lying isomers
Bonus: complementary to ISAC Yield Stn.
High performance largely due to re-trapping
TOF Analyzer
MagneTOF Detector
Trap section
Transfer RFQ
Cooled and bunched RIB
RF switchyard
Thermal ion source

## Slide 6: Beam purification with mass-selective re-trapping
How it’s done:
  Inject ions into TOF analyzer and separate in time
  Dynamical re-capture/trap ions of interest back into the injection trap
  Re-cool ions of interest
  Re-inject into the TOF analyzer and make mass measurement
104-108 suppression of isobaric background ions
Purification for
  MR-TOF itself
  downstream traps
Analyzer mirror 1
Injection trap

## Slide 7
Contaminants dominate the spectra (Attenuated beam)
Increased isotope of interest while suppressing Contaminants
(Unattenuated beam)

## Slide 8
Mass measurements with
TITAN MRTOF up to fall 2024

## Slide 9: TITAN has developed 3 methods to determine half-lives with the atomic mass in the MR-TOF.

## Slide 10: 1. Half-lives via variation of storage time in injection trap
Half-lives ~50ms
I. Mukul JPCS (2020); C. Walls, PhD thesis, U. Manitoba 2025
100Rb
100Rb+
Storage time (ms)
Storage time (ms)
R. Silwal et al., Phys. Lett. B. 833 (2022) 137288
I. Mukul et al., J. Phys: Conf. Ser. 1643 (2020) 012057
Counts
Counts
https://www.nndc.bnl.gov/nudat3/
https://www.nndc.bnl.gov/nudat3/
t1/2 lit = 1.16 s
t1/2 lit = 15.13 min
t1/2 exp = 23 (12) ms, t1/2 lit = 28 ms
t1/2 exp = 50 ±5 ms, t1/2 lit = 52 ms

## Slide 11: 2. Half-Lives with Beta Tagging
Half-lives ~ 10ms - 50ms, decided by the MRTOF cycle time
Low ion rate/ Ion-by-ion decay tagging
~50% detection efficiency
C. Walls, PhD thesis, U. Manitoba 2025
Red : T ½ Exp
Dotted : : T ½ lit
54K+
Mass (A/Q)
Decay time (s)
Probability Density
Counts
Detector
Injection trap

## Slide 12: 3. Half-lives with a high purity source
Beta decay rate (cps)
Mass (A/Q)
Half-lives 30s to several minutes
Re-trapping to reduce isobaric contaminants
Contamination checked with mass spectrometry
C. Walls, PhD thesis, U. Manitoba 2025
T1/2
= 2.45 min
180Yb+
180Lu+
Counts
Time (s)

## Slide 13: Switching gears to The Science

## Slide 14
First mass measurements of n-rich 136-138Sn isotopic chain to examine nuclear shell evolution and r-process nucleosynthesis.
Experiment setup
Protons: 480MeV, 50 μA
Target : p-to-n UCx
Ion source: TRILIS
138Sn yield: 0.08 pps
MR-TOF res. power: 450k
Re-trapping on
Precision ≤ 29 keV
Lasers ON
Lasers Blocked
138Sn
Sn: A. Mollaebrahimi et al., Physical Review Letters 134 (2025). p-to-n target: L. Egoriti, PhD thesis, UBC 2023
Publication: A. Mollaebrahimi et al., Physical Review Letters 134 (2025)
t ~ 2.2 hours
t ~ 0.5 hours

## Slide 15
A. Mollaebrahimi et al., Physical Review Letters 134 (2025).
S2n and ab- initio theory flatter than extrapolated AME
Empirical shell gap Δ2n
  Strong peak at N=82 as expected
  Flat trend in Sn lower than neighbors
Flatter trend in S2n beyond N = 82 has implications for nucleosynthesis.

## Slide 16
Our mass measurements
  TITAN mass uncertainty : too small to contribute to abundance uncertainty.
  Predict a lower abundance of A=135 compared to A=137 in the calculated scenario
A. Mollaebrahimi et al., Physical Review Letters 134 (2025).
R-process Abundance Calculations

## Slide 17
Summary:
  TITAN MR-TOF provides high-precision mass measurements of radioactive isotopes far from stability for nuclear structure & astrophysical studies.
  The addition of simultaneous half-life measurements has been used for isotope identification purposes and science
  Measurement of n-rich Sn up to 138Sn
Outlook:
  TITAN prepares for the ARIEL era with triple the RIB capacity
  Upcoming upgrades to improve precision and performance of the MR-TOF
    Laser ablation ion source (LAS) to add more calibrants and enable off-line science
    Active thermal stabilization of mirror electrode power supplies for higher resolving power
  Outstanding experiments require coupling the MR-TOF with downstream ion traps from Penning-trap mass spec and in-trap spectroscopy
Notes: Next slide TITAN group thank