## Slide 1: The low energy storage ring CRYRING@ESR operational experience and beams available for experiments
F. Herfurth, Z. Andelkovic, S. Fedotova, W. Geithner, N. Kehl, C. Krantz, M. Lestinsky, S. Trotsenko, G. Vorobyev
GSI Helmholtz Center for Heavy Ion Research GmbH, Darmstadt, Germany

## Slide 2: Collaborators and Support Team
ESR
Accelerator Physics
System Design
GSI/FAIR Expert Groups
External Partners TU Darmstadt
HIJ Jena Stockholm University Krakow University
KVI Groningen
IKF Frankfurt
Decelerator Experiments
SPARC Det.
Atomic Physics
Ion Sources
UNILAC RF
Ring RF
Magnets
Vacuum
Power Suppl.
Beam Diagns.
Controls
Transport&Installation
Beam Cooling
Mechanical Design/Integration
Decelerators
(DEC)
Accelerator Operations
SPARC
APPA
collaboration
BMBFTR (Ministry)
„Verbundforschung“
DEC @ GSI
Z. Andelkovic, S. Fedotova, W. Geithner, FH, N. Kehl, N. Kotovskiy, J. Ködel, D. Racano, S. Rausch, N. Stallkamp, S. Trotsenko, G. Vorobjev, D. Zisis
HITRAP
Facility
Engineering
Construction
Notes: Nice example of cowork between GSI – FAIR – Research – Accelerator – Collaborations and external Partners

## Slide 3
Precision Experiments
- Ion traps ( <eV/u)
- Optical traps (<meV/u)
- Storage Rings (100s keV/u)
Exotic (rare) Ions
- radioactive
- (heavy) highly charged (HCI)
- antiprotons
MeV/u
100 MeV/u
GeV/u
Heavy element’s
fragments / HCI
(and p̅)

## Slide 4
ECR
S-EBIT
SIS
Stripper
400 MeV/u
UNILAC
FRS
ESR
4 MeV/u
HITRAP
4 K
10 MeV/u
CRYRING
4 MeV/u … 100 keV/u
400 MeV/u
HITRAP – in development / partially operational
Linear Decelerator and Ion Trap as a source for heavy, HCI at keV .. 0 eV energies
up to 106 of ions alike U91+, Bi82+ …
constructed 2003 .. 2007 with some refurbished parts
online operating time about two 10-day periods p.a.
CRYRING@ESR – in regular operation
Low energy storage ring for heavy, HCI at 0.1 .. 10 MeV/u
includes a local injector for lighter, lower charged ions
built in Sweden in the 1990s, recommissioned at GSI 2016+
Operation within GSI beamtime periods
Slow, Heavy, Highly-Charged Ions at GSI/FAIR

## Slide 5
Ionsources
UNILAC
HITRAP
SIS18
Fragment-
separator
ESR
CRYRING@ESR
HESR,
PANDA
SIS100
Collector-Ring
Super-FRS,
Antiproton
target
CBM
image created by W. Geithner
Slow, Heavy, Highly-Charged Ions @ GSI/FAIR

## Slide 6: The low energy storage ring CRYRING@ESR
Introduction
CRYRING@ESR
  Key layout and Electron Cooling
  Opportunities for experiments using examples
In case you are interested how HITRAP is doing .. two slides
Summary

## Slide 7: CRYRING@ESR
Max. rigidity 1.44 Tm
  15 MeV/u U92+
  96 MeV/u protons
Min. rigidity ~ 0.054 Tm
  Actual limit given by beam life time
UHV … 10-11 mbar

## Slide 8
Beams available in CRYRING@ESR
ions from GSI Accelerator Chain and ESR
  transfer efficiency (stored to stored) ~ 50%!
    I.e. 1e6 ions at 10 MeV/u in ESR = 5e5 ions in YR
  example: up to 2·106 U91+ or 8·106 Au75+ in YR
ions from local injector
  intensity limited by ion source and physics
  independence allows for high flexibility
constant development of ions from local source (mostly 10 GHz ECR)
  in 2023/24 Li, S, W
  in 2024/25 F
local injector | GSI complex (from ESR)
H2+, D+ | Ar18+
C+, 7Li+, O6+, Ne2,3,7+, 24,25Mg+ | Pb78+, Au78+, U91+
S3+, 6Li1+,2+,3+, F6+, W?+ | 
Up to 50%
ESR
CRYRING@ESR

## Slide 9
Beams available in CRYRING@ESR
ions from GSI Accelerator Chain and ESR
  transfer efficiency (stored to stored) ~ 50%!
    I.e. 1e6 ions at 10 MeV/u in ESR = 5e5 ions in YR
  example: up to 2·106 U91+ or 8·106 Au75+ in YR
ions from local injector
  intensity limited by ion source and physics
  independence allows for high flexibility
constant development of ions from local source (mostly 10 GHz ECR)
  in 2023/24 Li, S, W
  in 2024/25 F
local injector | GSI complex (from ESR)
H2+, D+ | Ar18+
C+, 7Li+, O6+, Ne2,3,7+, 24,25Mg+ | Pb78+, Au78+, U91+
S3+, 6Li1+,2+,3+, F6+, W?+ | 
Work on improvements : Genetic Opt.
[1] S. Appel, W. Geithner, et al.: “Optimization of heavy-ion synchrotrons using nature-inspired algorithms and machine learning”,
13th Int. Computational Accelerator Physics Conf., doi:10.18429/JACoW-ICAP2018-SAPAF02

## Slide 10: Electron Cooling ESR - CRYRING
Data and graphics courtesy of C. Krantz

## Slide 11: Electron Cooling ESR - CRYRING
Data and graphics courtesy of C. Krantz, M. Lestinsky

## Slide 12: X-Ray Spectroscopy of U90+
U90+ ions
stopped by particle detector
Coincidence
condition
· U91+ beam
13 MeV/u
· Duty cycle
40 sec.
· 5∙106 ions
maXs
180°
maXs
0°
e- beam
30 mA
Radiative recombination followed by photon emission
U91+ ions
First (!) identification of Ka components in a high-Z system
Transition energies in agreement with bound-state QED
Uncertainty dominated by counting statistics
G. Weber, T. Stöhlker, et al.

## Slide 13: Section YR09: targets
First transversal electron target – commissioned C. Brandau et al.
Gas jet target – lots of improvements:
  Pumping
  Controls and DAQ
  Shutter for jet
  Hydrogen gas safety
N. Petridis, A. Biniskos et al.
Photo: C. Brandau
Electron target
Gasjet target
CARME
coordination of user activites: M. Lestinsky

## Slide 14: Section YR09: targets
First transversal electron target – commissioned C. Brandau et al.
Gas jet target – lots of improvements:
  Pumping
  Controls and DAQ
  Shutter for jet
  Hydrogen gas safety
N. Petridis, A. Biniskos et al.
Photo: C. Brandau
Electron target
Gasjet target
CARME
coordination of user activites: M. Lestinsky
Gas | Density (cm-2)
H2 | 2x1014
He | 6x1011
Kr | 2x1012
Xe | 6x1012
N2 | 6x1011

## Slide 15
Target effect on beam is well under control
Injection at 300 keV/u
Cooling
Deceleration to 92 keV/u
Cooling
Section YR09: gas jet target and ion beam
Electron Beam only 0.5 mA@50eV
Horizontal Beam Profile as time goes by
w/o gasjet
w gasjet

## Slide 16: Nuclear Reactions at very low energy
Big Bang Nucleosynthesis: D(D,p)3H
5∙108 locally produced D+ ions, E ≥ 90 keV/u, f = 300 kHz
detection with Double-sided Silicon Strip Detectors (CARME)
Jordan Marsh, Carlo Bruno et al. (CARME)

## Slide 17: Section YR07: Laser Spectroscopy & Extraction
Laser Spectroscopy of Mg+ and Li+
Extraction and Raman spectroscopy of Au75+, 4.8 MeV/u for swift HCI – surface interactions
Lowest possible energy: HCI 0.8 MeV/u, LCI 90 keV/u
K. Mohr, PhD Thesis, TU Darmstadt 2022

## Slide 18: Beamtime Schedule 2025
2021-25 ca. 5 months of beam for experiments, going towards 200 days per year from 2028 onwards
CRYRING@ESR beam is granted by G-PAC when ESR beam
intensity goals and beam quality well under control
New proposals welcome! Especially for local operation.
5 ⋅ 107
4⋅108
5 ⋅ 106
1⋅107
5 ⋅ 107
2⋅107
3 ⋅ 106
8⋅106
5 ⋅ 107
8⋅106
2 ⋅ 106
1.4⋅106
requested in proposal
achieved intensity
HITRAP 197Au79+
Easter break

## Slide 19: Low energy, exotic ion beams – Highly charged and heavy Low energy storage ring CRYRING@ESR and HITRAP
CRYRING@ESR
    in operation = delivers cooled beam to Experiments
    with heavy, exotic and highly charged ions produced at GSI (via ESR)
    with local injector : light ions but more beam time available
    Exceptionally well controlled beam (cooling, energy, position)
    Opportunity for exciting experiments
      e.g. at astrophysical energies (100s of keV/u down to several 10 keV/u)
HITRAP
    electron cooling of highly-charged ions demonstrated (offline)
    Capture of Heavy, Highly-Charged ions in a Penning trap!
    First User Experiment Q1/2025: surface implantation of Au79+ @6 keV/u!
    On-Line e-cooling still to be done. Charge state population and energy spread investigation to come.

## Slide 20: HITRAP facility - overview
from ESR
4MeV/u
Buncher
IH
RFQ
Cooling trap
Experimental stations
~10m
500keV/u
6keV/u
~eV/q
Platform
Cave
Optical Clocks with HCI, e.g. Micke, Leopold, King et al., Nature 578 (2020)
HCI interaction with surfaces, e.g. Wilhelm et al., PRL 119 (2017)
g-Factor of Ar13+, e.g. I. Arapoglou, A. Egl, M. Höcker et al., PRL 122 (2019)
EBIT

## Slide 21: First Experiment with decelerated HCI
Beam to Trap
Irradiation of solid state surface with Au79+ ions at only 6 keV/u
18 ± 3 keV/q
10-10 mbar
A. Niggas et al., G-22-00057: Nanostructuring of monolayer graphene by highly charged ions
6 keV/u only!

## Slide 22: Electron cooling!
Coulomb
interaction
0 V
6 kV
- 600 V
4 keV/q
< eV
: HCI
: electron
0 V
6 kV
- 600 V
4 keV/q
: HCI
First electron cooling of highly charged ions!!
Simon Rausch, Max Horst, Nils Stallkamp, Zoran Andelkovic, Sergiy Trotsenko et al.
Ar18+