## Slide 1: Overview of ISOL Facilities EMIS XX 2025 Whistler, Canada
João Pedro Ramos
Monday, 20 Oct 2025
(RIB Production techniques given yesterday at the lecture)

## Slide 2: ISOL Isotope Separation
Energetic particles
+/- 15V
1000 A
+/- 15 V
2400 A
Ion Source
Particle
Transfer line
4. Ionization
3. Effusion
2. Diffusion
1. Production
– Cross section [mb]
– Proton flux [cm-2]
– Nr of exposed atoms [dim]
– Efficiency [%]
5. Mass Separation
6. Transport
Extraction optics
Mass separator
Target unit
OnLine
Extraction electrode
up to 2300 °C
20 cm
Target heating by current and/or beam
<60 kV
0 V
(on target)
(on converter)
From the lecture yesterday…

## Slide 3: Efficiency is key!
1 proton on target
~1 isotope created
(order of magnitude)
~0.5 mol
~1023 atoms
Target (U/Th)
~6 pmol/s
~1012 atom/s
1 µA p+
All production
(6x1012)
~0.2 fmol/s
~108 atom/s
RIB of interest
~0.2 amol/s
~105 atom/s
(to extract!!)
pico – 10-12
femto – 10-15
atto – 10-18
Full stadium has now:
1016 – 10 quadrillion grains of sand
Sand:
8 – 15 billion grains per m3
Typical football stadium. Inner volume ~ 1 million m3
Let’s fill it with sand!
Now we need hope that 1 specific grain of sand gets out of the stadium by heating it up to 2000°C!
(corresponds to an isotope with an in-target production of ~107 /s=16 amol/s)

## Slide 4: ISOL Facilities Worldwide
ISOLDE
CERN
1.4 – 1.7 GeV p Geneva (CH)
ALTO-LEB
IPN Orsay
50 MeV e→ Orsay (FR)
ISAC, ARIEL
TRIUMF
490 MeV p, 30 MeV e→ Vancouver (CA)
TRIGA Reactor
UNI Mainz
n (1.1×1011 n/(cm2 s)
Mainz (DE)
IGISOL
UNI-JYFL
30 MeV p, 14 MeV d,
HI < 130 MeV/u Jyväskylä (FI)
LERIB
iThemba LABS
70 MeV p Cape Town (ZA)
SPES
INFN-LNL
40 MeV p
Legnaro (IT)
ISOL RAON
IBS
70 MeV p
Daejeon (KR)
CARIBU
Argonne National Lab
252Cf sf Lemont (US)
Spiral, SPIRAL-II
GANIL
HI <95 MeV/u ,40 MeV d, 33 MeV p, 14.5 MeV/u HI
Caen (FR)
IRIS
PNPI
1 GeV p
St. Petersburg (RU)
ISOL@MYRRHA
SCK CEN
100 MeV p
Mol (BE)
TATTOOS
PSI
590 MeV p Villigen (CH)
ANURIB
VECC
50 MeV e→ New Town in Kolkata (IN)
MEDICIS
CERN
1.4 GeV p and
external sources
Geneva (CH)
RISIKO
UNI Mainz
External sources
Mainz (DE)
BRIF
CIAE
100 MeV p Beijing (CN)
Operational
Future
Offline RIB (operational)
Legend:
p+ High energy
p+ Low energy
e→
Gas catcher
Heavy ion
IRIN-PIK reactor
PNPI
n (3×1013 n/(cm2 s)
St. Petersburg (RU)
BISOL-CARIF reactor
CIAE
n (8 × 1014 n/(cm2 s)
Beijing (CN)
Reactor

## Slide 5: High Energy Proton Facilities
ISOLDE
CERN
1.4 – 1.7 GeV p Geneva (CH)
ISAC, ARIEL
TRIUMF
490 MeV p, 30 MeV e→ Vancouver (CA)
IRIS
PNPI
1 GeV p
St. Petersburg (RU)
TATTOOS
PSI
590 MeV p Villigen (CH)
Operational
Future
Offline RIB (operational)
Legend:
p+ High energy
p+ Low energy
e→
Gas catcher
Heavy ion
Reactor

## Slide 6: ISOLDE at CERN
ISOLDE
CERN
1.4 – 1.7 GeV p Geneva (CH)
Operational
Future
Offline RIB (operational)
Legend:
p+ High energy
p+ Low energy
e→
Gas catcher
Heavy ion
Reactor
Contributions
Invited (Wed 8h30): M. Au – Molecular beams
Talk (Thu 4:30 PM): W. Wojtaczka – TbF beams for medical applications

## Slide 7: Facility
GPS
General Purpose Separator
HRS
High Resolution Separator
High Energy RIB
Target area
MEDICIS
(later)
Radioactive laboratory Class A
Low energy RIB
Extension: nano actinide lab
Protons (1.4 – 1.7 GeV)
High energy RIBs (up to 10 MeV/u – A/q=4.5)
Low energy RIBs (up to 60 keV)
Will enter long shutdown (CERN wide upgrades) for 3 years
Pulsed protons (1.2 s)
1.4 – 1.7 GeV
3.3x1013 protons per pulse
75 chemical elements
>1000 beams
>30 targets, 5 transfer lines, >5 ion sources

## Slide 8: Facility
GPS
General Purpose Separator
HRS
High Resolution Separator
High Energy RIB
Target area
MEDICIS
Radioactive laboratory Class A
Low energy RIB
Extension: nano actinide lab
Beam dump replacement
Study started in 2020
Will last 2 years from 2026
4 interconnected gloveboxes (air) to contain nanopowders
Lab being commissioned to start nanoUCx production
During shutdown, focus to upscale nanoUCx
Upgrade proton beam lines to allow 1.4 to 2.0 GeV p+
New magnets to be designed and produced
Beam dumps already account for 2.0 GeV upgrade
RILIS Laboratory situated in a very crowded area
Required to be close to GPS and HRS separator zones
RILIS laser cabin to be extended
Slide Material Courtesy of J. Vollaire, E. Siesling and S. Stegemann

## Slide 9: ISAC at TRIUMF
ISAC, ARIEL
TRIUMF
490 MeV p, 30 MeV e→ Vancouver (CA)
Operational
Future
Offline RIB (operational)
Legend:
p+ High energy
p+ Low energy
e→
Gas catcher
Heavy ion
Reactor
Contributions
Invited (Thu 1:30 PM): O. Hassan – Beam line tunning with Bayesian Optimization
Talk (Mon 11:20 PM): C. Babcock – ISAC reliability increase
Poster (Tue 6:00 PM): C. Babkock – upgrades to TIS HV operation
Poster (Tue 6:00 PM): D. Neilson– ISAC Test stand
Poster (Tue 6:00 PM): S. Ghosh– Thermal investigations target materials
Poster (Tue 6:00 PM): M. Cervantes – TaC coated Ta

## Slide 10: ISAC at TRIUMF
Water-cooled heat
shields
target materials:
UCx
UO2
ThO
Nb
Ta
TaC
NiO
ZrC
TiC
SiC
target container ~2000 °C
(Ø 20 mm, 60 cm3)
ion sources:
surface
resonant lasers
FEBIAD
IG-LIS
500 MeV protons
Target ion source service connections
Slide Material Courtesy of A. Gottberg, C. Babcock
Remote handling: G. Minor et al. DOI: 10.1016/j.net.2020.09.024
up to 100µA
>700 isotopes extracted
Modular system!

## Slide 11: TATTOOS at PSI
TATTOOS
PSI
590 MeV p Villigen (CH)
Operational
Future
Offline RIB (operational)
Legend:
p+ High energy
p+ Low energy
e→
Gas catcher
Heavy ion
Reactor
Contributions
Talk (Mon 11:20 PM): S. Warren – TATTOOS facility talk
Talk (Wed 9:00 AM): M. Mostamand – Ion source development at TATTOOS
Poster (Tue 6:00 PM): D. Regianni – TATTOOS beam line and target design

## Slide 12: TATTOOS at PSI
Collections
Class – A LAB
Proton beam
Service Cells
Systems & services
Access control port
Secondary ion beam line
60T crane
Target station and front end
Modular systems inspired in TRIUMF
Chemical quantities of isotopes
100 uA [p+] 590 MeV driver beam
m/dm ~ 3000
RIB into Hot Cell
Slide Material Courtesy of S. Warren

## Slide 13: Heavy ion facilities GANIL
Spiral, SPIRAL-II
GANIL
HI <95 MeV/u ,40 MeV d, 33 MeV p, 14.5 MeV/u HI
Caen (FR)
Operational
Future
Offline RIB (operational)
Legend:
p+ High energy
p+ Low energy
e→
Gas catcher
Heavy ion
Reactor
Contributions
Invited (Fri 10:30 PM): P. Jardin – Fusion evaporation target TULIP
Talk (Mon 2:00 PM): S. Hurier – Novel fragmentation targets for SPIRAL1
Poster (Tue 6:00 PM): E. Le Villain – New RIBs of Fe, Ni, Co at SPIRAL1
13

## Slide 14
Operating since 2001
58 primary beams from 12C (2e13pps, 95MeV/u, 3kW) to 238U (5e9pps, 24MeV/u, 5W)
Targets:
  Fragmentation target: Graphite target (so far), studies on expand this
  Fusion-evaporation targets: new TULIP concept with a thin target
3 ion sources: MonoNaKe (surface ion source with a graphite ionizer), NANOGAN (ECR), FEBIAD + TULIP’s surface source
34 elements from He to Cs over 100 isotopes identified, including over 60 at more than 1e5pps.
Mass separation in the SPIRAL1 LEB : 2 dipoles magnets with a resolving power of a few 100. Low energy beams will typically be sent to the DESIR hall, which is equipped with a HRS with a measured resolving power of 20000-25000.
Post-acceleration possible with the CIME cyclotron from 2MeV/u, up to 25MeV/u for Q/A=1/2.
GANIL – SPIRAL 1
Slide Material Courtesy of P. Chauveau

## Slide 15: e→ Facilities
ALTO-LEB
IPN Orsay
50 MeV e→ Orsay (FR)
ISAC, ARIEL
TRIUMF
490 MeV p, 30 MeV e→ Vancouver (CA)
ANURIB
VECC
50 MeV e→ New Town in Kolkata (IN)
Operational
Future
Offline RIB (operational)
Legend:
p+ High energy
p+ Low energy
e→
Gas catcher
Heavy ion

## Slide 16: ALTO-LEB at IJCLab
ALTO-LEB
IPN Orsay
50 MeV e→ Orsay (FR)
Operational
Future
Offline RIB (operational)
Legend:
p+ High energy
p+ Low energy
e→
Gas catcher
Heavy ion

## Slide 17: ALTO-LEB in IJCLab
Target-ion source vault
Mass separator
(magnet dipole) Δm/m = 1500
RIB
e-
e-
UCx targets (~25g, ~60 pellets)
Ionizer tube
Extraction electrode
https://alto.ijclab.in2p3.fr/en/facility/alto-leb/production/
50 MeV electrons, >10 µA, internal conversion in the UCx target
March 2012 : Operating licence from nuclear safety regulator, based on ISOLDE concept
First operational RIB facility based on photo-fission
 populating the GDR of 238U(~1011 f/s)
New frontend commissioned in October 2022
Robot for TISS tested in Summer 2024
Slide courtesy of E. Minaya

## Slide 18: ARIEL at TRIUMF
ISAC, ARIEL
TRIUMF
490 MeV p, 30 MeV e→ Vancouver (CA)
Operational
Future
Offline RIB (operational)
Legend:
p+ High energy
p+ Low energy
e→
Gas catcher
Heavy ion
Contributions
Invited (Mon 1:30 PM): L. Egoriti – ARIEL overview
Talk (Fri 9:00 AM): J. Lassen – TRILIS upgrade for ARIEL
Talk (Tue 4:50 PM): R. Baartman – ARIEL high resolution separator
Talk (Fri 9:00 AM): F. Maldonado – R&D opportunities at ARIEL
Poster (Tue 6:00 PM): N. Noori – ARIEL Hermetic target vessel
Poster (Tue 6:00 PM): R. Schick-Martin – ARIEL HRS diagnostics
Poster (Tue 6:00 PM): M. Cervantes – ARIEL Target material labs
Poster (Tue 6:00 PM): M. Hartmann – post acceleration beamline CANREB

## Slide 19: ARIEL at TRIUMF
Addition of two ISOL target stations to TRIUMF
  e -> station, 30 MeV electron, 10 mA
  p+ station, 490 MeV up to 100 µA
Beam switchyard capable of delivering up to three simultaneous RIB to users
Flexible Target and Ion Source Assembly based on ISOLDE one
AETE HTV
100 kW electrons @ 30 MeV
APTW HTV
50 kW protons @ 500 MeV
Slide material courtesy of E. Egoriti and A. Gottberg

## Slide 20: Low Proton Energy Facilities
SPES
INFN-LNL
40 MeV p
Legnaro (IT)
ISOL RAON
IBS
70 MeV p
Daejeon (KR)
ISOL@MYRRHA
SCK CEN
100 MeV p
Mol (BE)
BRIF
CIAE
100 MeV p Beijing (CN)
Operational
Future
Offline RIB (operational)
Legend:
p+ High energy
p+ Low energy
e→
Gas catcher
Heavy ion
Reactor
20
LERIB
iThemba LABS
70 MeV p Cape Town (ZA)

## Slide 21: SPES at INFN-LNL
SPES
INFN-LNL
40 MeV p
Legnaro (IT)
Operational
Future
Offline RIB (operational)
Legend:
p+ High energy
p+ Low energy
e→
Gas catcher
Heavy ion
Reactor
Contributions
Invited (Mon 3:30 PM): T. Marchi – SPES facilty talk and commissioning
21

## Slide 22
70 MeV cyclotron IBA up to 750 µA available
ISOL facility takes 40 MeV 200 µA
Targets used: SiC, TiC
Ion sources: FEBIAD and Surface+laser ion source
Commissioned at end of 2024
SPES at INFN-LNL
E. Fagotti et al. DOI: 10.18429/JACoW-HIAT2025-MOB01
T. Marchi et al. DOI: 10.1088/1742-6596/1643/1/012036
J. Esposito et al. DOI: 10.3390/molecules24010020
28Al measured during commissioning

## Slide 23: ISOL RAON at IRIS/IBS
ISOL RAON
IBS
70 MeV p
Daejeon (KR)
Operational
Future
Offline RIB (operational)
Legend:
p+ High energy
p+ Low energy
e→
Gas catcher
Heavy ion
Reactor
Contributions
Invited (Mon 1:00 PM): T. Shin – RAON overview talk
Talk (Fri 9:00 AM): H.-N. Kim – Laser source for ISOL RAON
Poster (Tue 6:00 PM): H.-N. Kim – Laser source for ISOL RAON
Poster (Tue 6:00 PM): T. Shin – RIB operation at ISOL RAON
23

## Slide 24
70 MeV cyclotron IBA up to 750 µA available
Based on the ARIEL/ISAC modular concept
For now 14 µA (1 kW are being used) – to be increased
Targets used: SiC, LaCx,
Ion sources: surface ion source (alkali), laser ion source (Mg)
new: TiC (this year) with FEBIAD, next year ThCx
Mass resolving power from 400 to 600 depending on ion source
Operational since March 2023
ISOL RAON at IRIS/IBS
J. Hee et al. DOI: 10.1016/j.nimb.2023.05.045
W. Hwang et al. DOI: 10.1016/j.nimb.2023.05.059
Institute for Rare Isotope Science | About IBS

## Slide 25: BRIF at CIAE
BRIF
CIAE
100 MeV p Beijing (CN)
Operational
Future
Offline RIB (operational)
Legend:
p+ High energy
p+ Low energy
e→
Gas catcher
Heavy ion
Reactor
25

## Slide 26
100 MeV p+
ISAC like concept (target modules and target)
Modular design in L shape (with p beam diagnostics, target and beam dump modules all in one)
FEBIAD and surface ion source operation
K, Na, Al RIBs produced from CaO, SiC, MgO targets using up to 15 microA
Mass separation up to 20000
Commissioned in 2014
BRIF at CIEA
W. Nan et al. DOI: 10.1016/j.ppnp.2025.104188

## Slide 27: ISOL@MYRRHA at SCK CEN
ISOL@MYRRHA
SCK CEN
100 MeV p
Mol (BE)
Operational
Future
Offline RIB (operational)
Legend:
p+ High energy
p+ Low energy
e→
Gas catcher
Heavy ion
Reactor
ISOL@
Contributions
Talk (Mon 2:20 PM): D. Houngbo– ISOL@MYRRHA facility update
Talk (Wed 9:40 AM): L. Gubbels – Th-based target materials for ISOL@MYRRHA
Talk (Thu 2:00 PM): S. Ramos Garces– Bayesian Optimization Algorithms for ion source tunning
Poster (Tue 6:00 PM): L. Gubbels – Non-actinide materials development at ISOL@MYRRHA
Poster (Tue 6:00 PM): F. Giudubaldi – Day-1 targets for development of Mg and Al beams at ISOL@MYRRHA
27

## Slide 28: ISOL@MYRRHA at SCK CEN
28
ISOL@MYRRHA systems
under advanced prototyping
See talk from D. Houngbo!
Facility within the MYRRHA programme
Modular design the same as ARIEL
100 MeV, < 500 µA
Day-1 targets: SiC, Ti, ThO2, UO2
  Start at low intensity (<20 µA)
Facility designed and licensed aimed at operation of ThCx up to 200 µA (10 kW deposited power)
Ion sources: surface, laser, (FEBIAD)
Building completed to basic design level
ISOL system design completed at conceptual level and most systems already completed basic design stage
Prototyping activities ongoing

## Slide 29: Gas Catcher and Reactor Facilities
TRIGA Reactor
UNI Mainz
n (1.1×1011 n/(cm2 s)
Mainz (DE)
IGISOL
UNI-JYFL
30 MeV p, 14 MeV d,
HI < 130 MeV/u Jyväskylä (FI)
CARIBU
Argonne National Lab
252Cf sf Lemont (US)
Operational
Future
Offline RIB (operational)
Legend:
p+ High energy
p+ Low energy
e→
Gas catcher
Heavy ion
IRIN-PIK reactor
PNPI
n (3×1013 n/(cm2 s)
St. Petersburg (RU)
BISOL-CARIF reactor
CIAE
n (8 × 1014 n/(cm2 s)
Beijing (CN)
Reactor

## Slide 30: CARIBU and IGISOL
IGISOL
UNI-JYFL
30 MeV p, 14 MeV d,
HI < 130 MeV/u Jyväskylä (FI)
CARIBU
Argonne National Lab
252Cf sf Lemont (US)
Operational
Future
Offline RIB (operational)
Legend:
p+ High energy
p+ Low energy
e→
Gas catcher
Heavy ion
Reactor
Contributions
Talk (Wed 11:00 AM): G. Savard – Neutron-rich RIB from gas catchers

## Slide 31
30 MeV protons up to 100 µA, 14 MeV d up to 50 µA
Thin targets 238U (or 232Th) to produce fission products
200 – 500 mbar of He as catcher
Transport times of ~100 ms
Allows refractory elements with ISOL
No ion source as the fragments are still ionized
IGISOL in UNI-JYFL
G. Savard et al. DOI: 10.7566/JPSCP.6.010008
Y. Blumenfeld, et al. DOI: 10.1088/0031-8949/2013/T152/014023
CARIBU in Argonne
D. Gorelov, et al. DOI: 10.1016/j.nimb.2016.02.049
~1 Ci, 252Cf spontaneous fission with a thin degrader
1.2 m x 0.5 m ø chamber filled with gas to stop the fragments
80 mbar of He as catcher
15 to 25 ms of transport times
30 to 50% efficiency at +1 or +2 charge state

## Slide 32: Gas Catcher and Reactor Facilities
TRIGA Reactor
UNI Mainz
n (1.1×1011 n/(cm2 s)
Mainz (DE)
Operational
Future
Offline RIB (operational)
Legend:
p+ High energy
p+ Low energy
e→
Gas catcher
Heavy ion
IRIN-PIK reactor
PNPI
n (3×1013 n/(cm2 s)
St. Petersburg (RU)
BISOL-CARIF reactor
CIAE
n (8 × 1014 n/(cm2 s)
Beijing (CN)
Reactor

## Slide 33
TRIGA at UNI Mainz
J. Grund et al. DOI: 10.1016/j.nima.2020.164013
J. Ketelaer et al. DOI: 10.1016/j.nima.2008.06.023
1440 μg 235U target
Neutron flux: 1.05 ⋅ 1011 cm−2s−1
Aerosol-based gas-jet system, e.g. N2 as carrier gas + CdI2 (BP 742 °C)
Fission fragments are sorbed by the aerosol and carried by the gas
1 s transport time, 60 to 70% transport eff.
Surface ion source breaks the up the aerosols to release the fission fragments

## Slide 34: Offline RIB (operational)
MEDICIS
CERN
1.4 GeV p and
external sources
Geneva (CH)
RISIKO
Mainz UNI
External sources
Mainz (DE)
Operational
Future
Offline RIB (operational)
Legend:
p+ High energy
p+ Low energy
e→
Gas catcher
Heavy ion
Reactor
Worth to mention (future offline RIB facilities):
SMILES from ARRONAX (FR)
RIS2 Lab - University of Manchester (GB)
LIS, Leuven – being restarted (BE)
Contributions
Talk (Fri 9:40 AM): K. Went – PI-LIST developed at RISIKO
Poster (Tue 6:00 PM): K. Went – PI-LIST developed at RISIKO
Poster (Tue 6:00 PM): T.E. Cocolios – Self sputtering of MEDICIS collections
Poster (Tue 6:00 PM): W. Wojtaczka– Revival of the LIS separator in Leuven

## Slide 35
C. Bernerd, T. Stora et al. DOI: 10.18429/JACoW-IPAC25-TUPB047
RISIKO in Mainz UNI
Has separated sources e.g. of 163Ho for ECHo (≈ 1012 atoms/MMC) and 53Mn for PSI (≈ 5 × 1017 atoms total)
Laser ion source and surface ion source, thorughput up to 100 nA
Active development of ion source technologies (e.g. (PI-)LIST ion source for ISOLDE)
Dominik Studer, SANDA General Meeting 2021
unique facility approved for clinical applications (CERN Council decision March 2025), which started in 2017
Work with both locally irradiated sources (ISOLDE) or external ones (reactor/cyclotron activated samples)
(1-several) clinical doses demonstrated for Ac-225, Ra-223, Pb-212, High Molar activity Sm-153, Ba/Cs-128 and also extraction of others
Single collections of up to 1 GBq demonstrated
MEDICIS at CERN
Simulation - FLUKA
Normal mode

## Slide 36
ISOL@MYRRHA offline
ISOLDE offline 1
ISOLDE offline 2
ISAC offline
ARIEL TISA
ALTO Offline
… many others!
“Offline” Non-RIB facilities
Worth mentioning in this talk to pool resources for R&D and technology sharing

## Slide 37
Discussions, content and advice for this talk: Lucia Popescu, Alexander Gottberg, Sebastian Rothe, Simon Stegeman
For sharing material, also: Luca Egoriti, Mia Au, Thierry Stora, Joachim Vollaire, Erwin Siesling, Julien Guillot, Enrique Minaya, Hee-joong Yim, Wonjoo Hwang, Michele Ballan, Pierre Chauveau, Stuart Warren, Donald Houngbo, Tom Day Goodacre
The EMIS XX International Adv. Committee for trust for the 2 invited contributions
Thank you!
For funding my participation in the conference!

## Slide 38
Copyright © SCK CEN
All property rights and copyright are reserved.
This presentation contains data, information and formats for dedicated use only and may not be communicated, copied, reproduced, distributed or cited without the explicit written permission of SCK CEN.
If this explicit written permission has been obtained, please reference the author, followed by ‘by courtesy of SCK CEN’.
Any infringement to this rule is illegal and entitles to claim damages from the infringer, without prejudice to any other right in case of granting a patent or registration in the field of intellectual property.
SCK CEN
Belgian Nuclear Research Centre
Studiecentrum voor Kernenergie
Centre d'Etude de l'Energie Nucléaire
Foundation of Public Utility
Stichting van Openbaar Nut
Fondation d'Utilité Publique
Registered Office:
Avenue Herrmann-Debrouxlaan 40 - 1160 BRUSSELS - Belgium
Research Centres:
Boeretang 200 - 2400 MOL - Belgium