## Slide 1: High-Power Rare-Isotope-Beam Production and Separation at FRIB
Bradley Sherrill Associate Director for Fragment Separation sherrill@frib.msu.edu
20 October 2025

## Slide 2: Outline
Introduction
The Facility for Rare Isotope Beams, FRIB, in context
Overview of FRIB
The Advanced Rare Isotope Separator, ARIS
  High Power Details
Results from First Two Years of Operation
Summary
FRIB Beam Dump after 1 year of operation FY2025

## Slide 3: Congratulations EMIS on a 70th Birthday
Discovery of Isotopes Project
M. Thoennessen frib.msu.edu
The first EMIS conference was held in Harwell Laboratory in England in 1955 – Harwell separated stable isotopes
EMIS-14 was held in Victoria BC in 2002 and chaired by John D’Auria
EMISXX
The program has evolved to focus on rare isotope beam separation, instrumentation, and uses
In 1955 less than 1,000 isotopes were known

## Slide 4: Rare Isotope Beam Production Methods
More primary beam → more rare isotope intensity, more isotopes accessible

## Slide 5: World Landscape of Rare Isotope Beam Facilities
Many of these facilities are represented by talks at EMISXX
The various facilities address similar science, but are complementary by providing unique capabilities
Different production mechanisms can use large cross sections or efficient separation, in addition to high power

## Slide 6: The Facility For Rare Isotope Beams
FRIB is designed for 400 kW beam power
  8 p𝜇A or 5 x 1013 238U /s
  42 p𝜇A or 2.6 x 1014 48Ca /s
Operation at 20 kW now, power ramp-up underway
Range of beam energies provided for experiments
  Fast – 20 to 200 MeV/u
  Stopped – 10 kV
  Reaccelerated – 1.5-10 MeV/u
Started operation in May 2022
  58 experiments completed
Isotope harvesting capability ( collection of otherwise unused isotopes for applications)
  3 experiment completed
Thomas Glasmacher, FRIB Laboratory Director

## Slide 7: Schematic Overview of the FRIB Facility
Superconducting linear accelerator with 3 segments – 46 total cryomodules
Production area and fragment separator with remote access
Stopped beam area with two gas cells and cyclotron stopper
ReA3,6 (up to 10 MeV/u re-accelerator)
Pre-separator
Stopped Beam Area
ReA3,6 up to 6-10 MeV/u
Concepts to add ReA12
15 m underground
Ground level

## Slide 8: Liquid Lithium Charge Stripper
Liquid lithium charge stripper installed in FRIB tunnel
Xe26+ charge state after stripping
T. Kanemura et al., Phys. Rev. Lett. 128 (2022) 212301
Now used for all beams
Needed to achieve design-goal beam energies beyond 200 MeV/u and beam power up to 400 kW
Conventional charge stripping foil can only last seconds under FRIB beam power

## Slide 9: FRIB Power Ramp-up since Start of User Operations Liquid Lithium Charge Stripper Used to Push Heavy Ion Beam Power > 10 kW
Chart: Date [MM/DD/YYYY]
Cumulative LLCS operation hours | 14865.7209 | 14437.7209 | 13717.7209 | 12997.7209 | 12354.7209 | 11610.7209 | 10938.7209 | 10424.0542 | 9910.7209 | 9190.7209 | 8446.7209 | 8350.7209 | 8350.7209 | 7902.1542 | 7229.8209 | 6565.6209 | 5845.6209 | 5132.1709 | 4436.1709 | 4069.5542 | 3565.7042 | 3421.9375 | 3346.7042 | 3223.7375 | 3121.3709 | 3020.1709 | 2548.8042
1 kW
3 kW
5 kW
10 kW
20 kW
20 kW test
Lithium routine operation started
Oct. 2023
Lithium routine
Lithium occasional use
30 kW
Test
10/16/2025
T. Kanamura et al., J. Wei

## Slide 10: High (83% for 238U) Stripping Efficiency with Multiple Charge-state Simultaneous Acceleration
Routinely accelerating up to 5 charge states (for 238U) simultaneously
Multi-charge-state beams tuned to overlap at specified locations
  Target (present)
  Charge stripper (future)
Plan to accelerate multi-charge state beams in Linac Segment 1 (upstream of charge stripper)
In principle LINAC and stripper could operate at 100 kW
Simultaneous acceleration of five charge states of 238U beam in FRIB linac
P. N. Ostroumov, et al., Phys. Rev. Lett. 126, 114801 (2021)
20 kW Uranium – P. N. Ostroumov, et al., Phys. Rev. Acc. and Beams 27, 060101 (2024)

## Slide 11: Rare Isotope Production and Separation
Rare isotopes are separated using the Advance Rare Isotope Separator, ARIS
M. Hausmann et al., NIM B317 (2013), presented at EMIS 2012 (16th EMIS)
Production target is 15 m underground
Experimental facilities are at ground level
Pre-separator
Stopped Beam Area
Bandura et al., NIM A645, Hausmann et al., NIM B317, Portillo et al., NIM B540

## Slide 12: The Advance Rare Isotope Separator, ARIS
Three-stage separation by the use of “wedges”
Special features
  Momentum compression
  Particle identification, PID, of individual atoms
  Designed for operation with 400 kW of primary beam
Remote handling of items in target/wedge area
Atom-by-atom identification of A, Z, q
Modeling with - LISEcute++
Two additional stages of separation for cleanup
Target – carbon disk
“Wedge”
15m
Fragments after target
Fragments after wedge
Fragments at focal plane
Example: 78Ni from 86Kr at 200 MeV/u
Bandura et al., NIM A645, Hausmann et al., NIM B317, Portillo et al., NIM B540

## Slide 13: Target Hall Overview
ARIS “hot cell” target area
Remote handling team lead by M. Larmann
Remotely manipulated components
  Target
  Beam dump
  Wedge module
  Magnets
  Shields
BDS
Target System
Beam Dump System
Wedge System
WIQ1,2,3
SCD1
SCD2
WIQ4,5,7
Cryogenic Transfer Line
Power Supplies and Controls Cables Conduits
Shielding
NCU Connections
Cryo Servicing Platforms
Vertical Preseparator
Vacuum Vessels
Beam from LINAC

## Slide 14: Remote Handling At FRIB
Target and wedge changes are done remotely
Capability to remove all components and inspect them with cameras (see examples from the ARIS beam dump)

## Slide 15: High-power Targetry Devices in Operations
Rotating, single-slice graphite target for rare isotope production
  Absorbs ~ 25% beam power; accommodate small (~ 1 mm diameter) beam size
Static beam dump with shallow beam incident angle
  Absorbs ~ 75% beam power; consideration of radio-activation in water and surroundings
20 kW, 177 MeV/u 238U beam on 2.1 mm thick graphite target rotating at 500 r.p.m.
Single-slice graphite production target
J. Song, et al., HIAT’25, East Lansing, (2025)

## Slide 16: Beam Dump Power Ramp-up Plan
Primary beam
Mini-channel
Water cooling
Rotating drum
Primary beam
Water cooling
1 kW
30 kW
400 kW
20 deg static
6 deg static
Rotatable
10 kW
Mini-channel static
50 kW
S. Miller, et al., HIAT’25, East Lansing, (2025)
T. Kanemura
J. Song
J. Wei
copper-chromium-zirconium (C18150) material

## Slide 17: Static Beam Dump for 10 - 50 kW
Encouraging results from 20 kW operations in FY2025
e-beam test results show operation at 350 C possible
Power is limited based on calculated beam spot size
Observed features on FY2025 dump are understood
6°version-2 beam dump removed from FRIB Sep. 2025
T. Kanemura J. Song
Power limited by beam spot size

## Slide 18: Thermal Simulation of Maximum Beam Power on the Wings
Deformation was observed in the 3D-printed wing of the beam dump
The beam power on the wing was around 1 kW
Based on FY24-25 operation, the max temperature on the 3D-printed Al 6061 wing was around 400 ˚C (Exp 23033)
383C
T. Kanemura J. Song; Simulated by M. Patil

## Slide 19: Beam Dump Image For FY2024 6-degree Dump
Primary beam locations and sizes on the dump for FY2024
Length of the lines are 2σ beam dimension
Agreement with marks on the dump is good → ability to predict beam dump conditions
Analysis by M. Hausmann
A goal is to implement a thermal imaging camera for the dump

## Slide 20: Power Distribution Along ARIS
Approximately 1-5% of the primary beam power is converted to fragments
A typical power distribution for a near-stability fragment (29Mg from 48Ca) is shown

## Slide 21: Ion Optics – ARIS
M. Hausmann, et al., NIM B317 (2013) 349
Optics in dispersive dimension:
Preseparator
C-Bend
Dump
Wedge
DB1
DB1
DB5

## Slide 22: ARIS Feature: Momentum Compression
Preseparator wedge (energy degrader) slows down beam
Wedge shape compresses momentum distribution
  Wedge at dispersive image
  Higher energy particles slowed down more by thicker part of wedge
  Larger resolving power in downstream section maintains achromaticity after 2nd magnetic rigidity separation
Momentum compression improved transmission through downstream beamlines
Target
Achromatic image position
Bandura et al., NIM A645

## Slide 23: ARIS Diagnostics and Particle Identification
DB1
(Pre-Separator Focal Plane)
DB2
DB3
DB4
DB5
(Final
Focal Plane)
Pre-Separator Wedge
Target
PPAC pair*
Not standard
PPAC pair
PPAC pair
PPAC pair
Diamond
Thin Sci
PPAC
Thin
Sci
Thin Sci
PPACS
Sci / Diamond
Pins
TKE
PIN
Thick Sci
Thick Sci
PINs
Tracking
ToF
dE
E
Event-by-Event Identification
M. Smith, D. Kahl, A. Dombos
M. Cortesi, S. DiCarlo
HPGe
Notes: Ok, now back to ARIS, detectors. Salvatore just shared a lot about the ARIS detectors, so I will tell you how we use them.

## Slide 24: ARIS Detectors Allow for Ion-by-Ion Particle Identification
Example of “typical” Particle IDentification, PID, for 238U fragmentation at 177 MeV/u
1.2 mm 12C target; 1 Al mm wedge
TKE measured with a stack of Si-PIN detectors
Purity of high Z beam is acceptable
Gate on
ΔQ = 0
212Rn
Atomic Number (Z)
A/q
hydrogen-like
helium-like

## Slide 25: LISE++ Simulation Code Allows Predictable Operations
LISE++ code maintained at FRIB: covers all aspects of fragment production and separation O. Tarasov, D. Bazin, et al., Nuclear Instruments & Methods B376 and O. Tarasov, et al., NIM B541
Used in beam planning and RIB development at FRIB and elsewhere
Good agreement with experiment, reproduced complicated particle ID and separation for uranium fragmentation
LISE++
Experiment
212Rn
Data 177 MeV/u 238U
Gate on
ΔQ = 0
212Rn
Atomic Number (Z)
A/q
hydrogen-like
helium-like
Notes: We need our tools for fragment separation operation. We rely on LISE simulations (thanks Oleg) which allows us to check on all the needs for a beam delivery, from target to PID and more. You can see here we can get very good agreement, it’s a powerful tool.
Oleg will discuss much more on this in the next talk.

## Slide 26: ARIS Department Supports Secondary Beam Development for Experiments
Primary Beams
18O
22Ne
28Si
36Ar
48Ca
64Zn
70Zn
82Se
124Xe
198Pt
238U
More than 450 Beams Delivered for Experiments as of 10/2025
Beams from 3H to 224Th
58 experiments completed so far
Figure from A. Stolz, M. Smith
Eventually we expect 4,500 isotopes to be made at FRIB
Primary Beams
Observed isotopes
Experiments at FRIB
Stable isotopes
Discovered at FRIB

## Slide 27: Gas Stopping – Beams for Laser Spectroscopy, Mass Measurements and Reacceleration
Provide beams to stopped beam areas and reaccelerated beam areas
User Demands
Stopped Beam Group
  Chandana Sumithrarachchi (group leader), Xiangcheng Chen, Chris Izzo, Nadeesha Gamage, Sierra Rogers
Requests for beams during FRIB PAC3

## Slide 28: Collection of Unused Isotopes - Harvesting
Greg Severin, et al. – White Paper on Harvesting (J. Phys. G 46 (2019) 100501)
Describes opportunities for isotopes collected in parallel to normal operation
  Matched pairs to diagnose and treat disease 64Cu/67Cu and 44Sc/47Sc
  A readily available 52Fe/52mMn generator for oncology, neurophysiology, and diabetes
  Alpha and Auger emitters for therapy
  PET imaging of plants, e.g., 52Fe
  Radioisotope Micro Power Source
  Homeland security
  Special isotopes for tests of Nature’s laws
Contributors: MSU, LLNL, LANL, ANL, Missouri, Alabama, ND, ORNL, BNL, Iowa
Cover: Erin O'Donnell
Available at frib.msu.edu

## Slide 29: Example of Harvesting: 47Ca Collection to Make a 47Sc Generator
Work of K. Domnanich, et al.
47Ca 1 hour collection in Al foils (performed two times) at ARIS DB2 location (at a dispersive image)
Successful 47Sc test labeling with chelators L3 and L3-aga at Univ of Wisconsin
Preclinical SPECT/CT imaging planned
89mm
127mm
20mm
30mm
47Ca beam
Cat+X
47Ca/bulk Al
1st Step: Separate 47Ca from bulk Al
2nd Step: 47Ca/47Sc Generator
47Ca
bulk Al
DGA
47Ca/47Sc
47Ca
47Sc
47Ca yield ~90%
Al foil stack
L3-aga

## Slide 30: Possible Extent of the Nuclear Landscape
Approximately 258 “stable” isotopes are found on Earth
The full nuclear landscape can be estimated using existing nuclear models
Example: Bayesian Analysis of Nuclear Models - Neufcourt et al. Phys. Rev. C101 (2020) 044307
Estimate for Z,N > 8 and Z ≤ 119 is 7708±534 (10% chance of > 10,000)

## Slide 31: Study of Neutron-Rich Calcium Isotopes
Recently 5 (+1) new isotopes have been observed at FRIB using 225 MeV/u 82Se at 20 kW (1 pμA)
63Sc, 65,66Ti, 68V, 71Cr (next slide)
One event for 61Ca was observed (needs confirmation)
Production cross sections were measured
O. Tarasov et al, PRC 112 (2025) 034604
Mass Number
RIKEN: Tarasov, Ahn, et al., Phys. Rev. Lett. 121 (2018)
71Cr

## Slide 32: Observation of 71Cr
With 82Se at 225 MeV/u on an 8 mm C target 2 events of 71Cr, were observed in approximately 40 hours at 550 pnA
3.3 yoctomoles
2 events meet all PID criteria and probability of misidentification is <10-8
71Cr, is interesting because many models have it weakly bound or even unbound – stability is related to N=50 shell closure
S Watters, O Tarasov
Preliminary

## Slide 33: FRIB400 – Upgrade to 400 MeV/u Primary Beam Energy for Uranium
Space in the FRIB tunnel for the needed 11 cryomodules – lends itself to staged implementation
FRIB was designed to allow the opportunity to operate at higher primary beam energy
FRIB500 would provide 400 MeV/u for all beams at 400 kW
The upgrade would consist of 55 SC elliptical cavities (βOPT=0.65, 644 MHz) in 11 cryomodules at 17.5 MV/m
Proposed but not funded

## Slide 34: FRIB400 Reach Toward the Limits
Increase in the FRIB energy will significantly increase the yield of the most exotic isotopes
  Greater than 10x gain
  Better collection efficiency
  Thicker production targets
  Secondary reactions
Red – Current FRIB
Blue – FRIB400
FRIB400 offers the possibility of reaching the drip line up to Z=60 (Z=30 for FRIB)
UNEF0

## Slide 35: Summary
Happy birthday EMIS
Overview of FRIB including ARIS
Isotope separation at FRIB is underway at 20 kW and science results are published (58 experiments conducted so far)
Details shown on the equipment needed for high-power operation
Prospects for further exploration of the nuclear landscape with ARIS and FRIB
  11 new isotopes found so far
Many more isotopes for all of us to be separated before EMISXL

## Slide 36: Acknowledgements
U.S. Department of Energy Office of Science Office of Nuclear Physics, Facility for Rare Isotope Beams; operations under Award Number DE-SC0023633.
US National Science Foundation under Open Quantum Systems grant No. PHY-23-10078
ARIS Department Members – DS. Ahn, M. Hausmann, M. Portillo, O. Tarasov, E. Kwan, M. Smith, A. Dombos, D. Kahl, M. Steiner, K. Fukushima
NSF Grant members - Oleg Tarasov, PhD students Isaiah Richardson, Shane Watters, Holly Matthews, Daniel Kaloyanov, Kenny Haak (graduated)

## Slide 37: Magnets in ARIS High Power Areas
Quadrupole yokes and coils (40 cm dia. aperture)
Model of triplet cryostat
Yoke (warm)
Quadrupole coil
Cryostat wall
Multipole coils
Warm-iron quad cross section
Multipole coils test-assembled around bore tube
40 cm bore tubes with multipoles
T. Xu et al.

## Slide 38: Sophisticated Preseparator Wedge Shape Improves Operation
Linear wedge
  Chromatic distortions
    F1S1.x width wider at edges/larger ΔP/P
Higher order wedge “parabolic-like”
  Smaller chromatic distortions
dispersive image
48Ca + C (8 mm)  44S @ ΔP/P=6%
achromatic image
44S
Neighboring fragment
E23608
44S
achromatic image

## Slide 39: The 71Cr Production Cross Section
71Cr
S. Watters
FRIB200 Limit

## Slide 40: Ion Optical Simulations Match Expectations
Target Dump Wedge DB1
Target Dump Wedge DB1
Preseparator simulated using LISE++
Currents read from control system and envelopes simulated by Monte Carlo tracing of rays
4 quads adjusted by 1 – 10%