## Slide 1
The SPES Facility
first ISOL RIB production
T. Marchi
XX EMIS conference
Whistler, October 20th 2025

## Slide 2: LNL accelerator complex and beamtime
AN2000
Heavy-ion accelerator complex T.A.P.
SPES
CN

## Slide 3: LNL TAP complex and the SPES project – RIB production and post-acceleration
ISOL front-end
LRMS
1+ exp hall
BC + HRMS
CB + MRMS
RFQ
ALPI
EXP HALLS I & II

## Slide 4: The SPES project
Radioisotopes production
Once you have a powerful driver…

## Slide 5: Implementation
Phase 1
Cyclotron
Phase 4
R.I. production
Phase 2
ISOL &
low energy EXPS
Phase 3
Post-acceleration
Phase 5
HRMS
Experiments

## Slide 6: Phase 1 at completion: beam delivered May 2024
SPES-driver
SPES ISOL2
Phase 1
Phase 1 completed.
Cyclotron operational & target station tested.

## Slide 7: Three irradiation runs with 35, 50 and 70 MeV proton beams
Beamline characterization process using IAEA monitor reactions https://www-nds.iaea.org/medical/monitor_reactions.html
natAl(p,x)22/24Na; natNi(p,x)57Ni
Beam
Remeasuring xs for 67Cu production route
68Zn(p,x)67/64Cu && 70Zn(p,x)67/64Cu

## Slide 8: SPES – Phase 2: the ISOL facility and the low-energy exp hall
Phase2
SPES
LERIB
Phase 2 priorities and work plan:
ISOL Machine
  Cooling plants
  Pneumatic plants
  HV plants
  Vacuum plants & Gas Recovery System
  Control systems & MPS
Laser laboratory
  3 dye lasers
  Cooling plants
Low-energy transport and selection beamline
  Beamline elements
  Vacuum plants
  Control system & MPS
  Cooling plants for LRMS
Handling & Temporary Storage Station
  AGV
  Horizontal Handling Machine
  TSS
TASKS
ISOL machine completion & stable beam commissioning
In-beam commissioning of the ISOL machine
LERIB beamlines completion& stable beam commissioning
RIB commissioning on the tape station
AGV & TSS full commissioning
LASER lab. completion & commissioning

## Slide 9
The SPES Target Ion Source
SPES ISOL
Target:
UCx, SiC,...
1013 fiss./s
T ~ 2000oC
3 sources SIS, LIS, PIS
~ 8 kW power
Beam test at iThemba lab. (2014): 66MeV protons, 60 mA on full scale SiC prototype at 1600 oC (FEM sim. Validation)
Former beam tests: ORNL (2007, 2010-2011) SiC, Ucx; ISOLDE(2009) UCx, IPNO (2013) UCx.

## Slide 10: The ISOL machine is completely installed in the ISOL1 bunker

## Slide 11: All service plants are completed and commissioned
50 kV HV platform
Wien Filter cooling
Cooling water & pneumatics distribution

## Slide 12: Controls & MPS are completed and operational
High Current Power Suppliers Control System
Wien Filter Control System: includesautomatic mass scan prcedures
In-house developed control system (100%)
Based on EPICS framework and off-the-shelf Hardware
Compatible with all the LNL accelerators control system
  Allows to exploit LNL-developed AI methods for beam transport
Integrated with the Machine Protection System and the Global Safety System

## Slide 13: Phase 2a: RIB commissioning of the ISOL machine

## Slide 14: Phase 2a: RIB commissioning of the ISOL machine
7 target chambers available and tested for coupling/decoupling on the TIS
2 target chambers fully equipped, ready for beam
Mass markers:
  residual pollution (CO+, N2+)
  gas mix Ne:Ar:Kr:Xe
  natMg; natS/natSn
Preliminary test with stable beam completed

## Slide 15: Phase 2a: RIB commissioning of the ISOL machine
TIS
Phase 2a
Date: 14 Nov 2024
Primary beam energy: 40 MeV
Primary beam current: 100 nA
Target: SiC (standard)
Target temperature: 1600 °C
Ion Source: FEBIAD (plasma)
Extraction Voltage: 30 kV
Vacuum level in the target:
  Oven off: 1.0 10-7 mbar
  Oven on: 4.0 10-7 mbar
W.F. selection: 28 a.m.u.
Stable beam current F.C.2 (A=28) : ̴̴200 nA

## Slide 16: Phase 2a: RIB commissioning of the ISOL machine
TIS
Phase 2a
RIB

## Slide 17: Phase 2a: RIB commissioning of the ISOL machine
TIS
Phase 2a
The beam is about to come…

## Slide 18: Phase 2a: RIB commissioning of the ISOL machine
28Si: 2+→0+
Beam ON
HPGe spectrum in coincidence with beta signal

## Slide 19: First ISOL RIB @ SPES: November 2024

## Slide 20: 𝛾𝛾 coincidence in LaBr3 with 𝛃 coincidence
BEAM ON
BACKGROUND
𝛽+ emitters with beam, no 𝛽+ activity without beam

## Slide 21: Remote Handling of Target-Ion-Sources ready and tested

## Slide 22: Completion of phase2: full LERIB facility
22
May 2024
June 2024
July 2024

## Slide 23: Phase 2 completion: RIB on the tape station
beam
Again on mass 28:
t1/2=2.25 min

## Slide 24: Completion of phase2: full LERIB facility
24
A/q = 29

## Slide 25: Next steps: Phase 3 - ADIGE charge breeder

## Slide 26: 4. Phase 3: RFQ
RFQ assembly completed
Vacuum test passed
Bead pull measurements completed
Tuning completed
RF amplifier tested at 200 kW CW.
Couplers under construction
Main plants completed
Local plants to be installed

## Slide 27: Phase 4

## Slide 28: Phase 5
+
-
+
-
-
+
1 eV
Beam cooler