## Slide 1: Transmission Muon Microscopy and Scanning μSR Microscopy
Yukinori NAGATANI
High Energy Accelerator Research Organization :KEK
Institute of Materials Structure Science :IMSS
16th International Conference on Muon Spin Rotation, Relaxation and Resonance
μSR2025
St. John’s 22/Jul/2025
Supported by MEXT Grant-in-Aid for Scientific Research (S)
Grant-in-Aid for Scientific Research (S) JP24H00028 (2024-2028, PI: Y.N) Transmission Muon Microscopy

## Slide 2: What we can do by Muons
Accelerated μ：Strong Permeability thru Materials
Transmission analysis of thick objects
Positive μ： μSR Spectrum Analysis
Distribution and fluctuation of Magnetic Fields in materials Status of hydrogen, Density of Fermi-surface, …
Negative μ： Characteristic X-ray analysis
Elementary-analysis, Isotope-analysis, Chemical state-analysis
Both +/- μ： Soft/Hard error analysis of IC/LSI
All are applicable to Microscopies!

## Slide 3: Visualization of Volcano by Cosmic-ray Muon (Nagamine)
Applying it to microscopy ➡ Transmission Muon Microscopy
Cosmic-Ray Muon
Mt. Asama
High-energy muons penetrate a mountain (thickness～100m) and visualize internal structure.
Recently, it is applied to Atomic reactors, Pyramids and so on.
Detector

## Slide 4: Our Muon Microscopy Projects at J-PARC
TμM: Transmission Muon Microscopy
Sμ+M: Scanning μSR Microscopy
Sμ-M: Scanning negative Muon Microscopy

## Slide 5: TµM: Transmission Muon Microscopy
It visualizes Electromagnetic Fields in thick specimen
Main Project:

## Slide 6: Our Aims by Visualizing Ele/Mag-field
Our modern civilization is constructed on Electromagnetism. Computer / Semiconductor / Communication dev. / EV / Rader / …
Power Devices: Power / RF Tr, Capacitor, Magnet, Battery, Piezo, … Making them higher voltage / higher speed / higher efficiency contributes to industrial benefits and SDGs of our society.
Visualization of EM-field in devices makes them higher performance. eg.：Specifying field concentration design of relaxation → Higher voltage dev.
Mitochondria: Energy by mem-Potential. Brain / Nerves system: Thinking by network of action potential
Visualization of EM-field in bulk object is quite important subject in wide fields including industry and life science.
Ultrasonic Medical Dev.
←
→
neuron
Axon fiber

## Slide 7: Muon can visualize EM-fields in objects
Muon is charged particle ➡ Sensitivity both E and B field
The highest material permeability by acceleration
Mass production by accelerator
High resolution and high sensitivity of EM fields by beam-cooling
Magnification of Image / Visualization of EM field by TEM tech.
High-resolutional Image-detection by Direct CMOS Sensors for TEM
Combining accelerator technology and electron microscopy one allows us it!

## Slide 8: Demonstration : Visualization of Ele- and Mag- fields in Air
Transparent image thorough magnetic field in air
Kapton win
vac
air
2kG φ20mm
2kG 相当
2kG
Image processing
５ｍｍ
note）Inside of the magnet (cyan part) is calculated by an interpolation
Electric Field in Air is also visualized by μ!
±15kV
Magnetic field made by a magnet is reconstructed as projected-field by the muon imaging

## Slide 9: Image of acc-gen muon beam array

## Slide 10: Image of acc-gen muon beam array with Magnet

## Slide 11: Image of acc-gen muon beam array with Magnet flipped

## Slide 12: Reconstructed Magnetic Field in Air by μ-Beam
2kG
5mm
note）
Inside of the magnet (cyan part) is calculated by an interpolation

## Slide 13: Transmission Electron Microscopy (TEM)
200 kV cryo-TEM
Observable Thickness | ～200 nm | ～１ µm | ～３µm
1 MV HV-TEM @ NIPS
3 MV HV-TEM @ Osaka U.
World Highest
It visualizes EM-field by highest resolution:
Methods： Lorentz Microscopy, Electron Holography (Tonomura), Phase-Contrast TEM (Nagayama)
Targets： Transistor (Rau), Mag-field among atoms (Shibata), Membrane potential of liposomes (Sigworth), …
Specimen should be Ultra-thin （depending on beam energy）

## Slide 14: Penetration-capability of e and μ
Muon
Electron
Ionization Loss
Ionization Loss
Bremsstrahlung Loss
Bremsstrahlung Loss
TEM
HV-TEM
TµM
Relative Energy Loss in Material（log）
More breaking
More penetrating
Kinetic Energy（log）
Electron’s mass scale
Muon’s mass scale
More breaking
More penetrating
Cosmic-ray muon imaging for mountains, pyramids,
atomic-reactors, ….

## Slide 15: Concept of Transmission Muon Microscopy (TμM)
By employing accelerated muons instead of electrons in TEM, Electric- and Magnetic-fields in thick object are visualized.
Comparing with present methods
 | Mag-field | Ele-field | Penetration Power | Versatility of specimen
muon (TμM) | 〇 | 〇 | 〇 10μｍ～cm | Widely acceptable
electron (TEM) | 〇 | 〇 | × 100s nｍ～a fewμm | should be Ultra-thin
Neutron | 〇 | × | 〇 a few cm | Widely acceptable except for B, Gd, Cd, ….
Circular polarized X-ray | △indirect | × | △ 10μm | should has X-ray magnetic circular dichroism.
Optical Kerr scope | △indirect | △indirect | transparent or surface | Limited to transparent magnetic or nonlinear optical materials.
Ca-Imaging fluorescence microscope | × | △indirect | transparent life-tissue | Ca density measurement in life.

## Slide 16: Recent Topics : HV-TEMs are realized by RF-Accelerators
Recently, linear accelerators are applied into HV-TEMs.
NIPS 500kV
Linac TEM
by Y.N. grp.
[PRL123(15)2019]
Osaka U. 3MV
RF-Gun TEM
by J. Yang
[Microscopy, 291-295 (2018)]
Sub-nanometer resolution achieved even using a linear accelerator!
Now, it is the time to apply TEM technology to Accelerator World
Notes: Recently smaller high-voltage TEMs by employing linear accelerator using microwave to accelerate beams, instead of using DC accelerators, are being developed.
Even for using microwave for acceleration, sub nano meter resolution is realized.

## Slide 17
The 5MeV TμM under construction at J-PARC
Muon Beam Cooling
It converts low-luminance beam into high-luminance one.
５MeV Muon Cyclotron
・It gives penetration-capability. ・AVF-type, Flat-top RF accel.
・ΔＥ／Ｅ～10-5 (goal) ・Time to accel. <１μsec
Superconducting Object Lens focuses accelerated μ-beam
Lorentz / Phase-contrast optics to visualize EM-fields
CMOS Image Sensor for TEM is employed
In situ specimen holder for Power-device / Life
Notes: 研究計画では、透過ミュオン顕微起用を開発し、各種の可視化実験を行います。
装置は超低速ミュオン発生装置、ミュオン再加速装置のサイクロトロン、ミュオン顕微鏡光学系の本体、画像センサ、試料ホルダより構成されます。
超低速ミュオン発生装置の１段目はレーザー装置も含めて安定稼働状態にあり、本研究で２段目、３段目と順次段数を増やし、より高輝度なミュオンビームを生成し、分解能と電磁場への感度を順次向上させます。
最終段はフェムト秒レーザーとし、ミュオンの極短パルスビームを得ます。
加速に用いるミュオンサイクロトロンはすでに開発がほぼ完了しており、Ｊ－ＰＡＲＣに設置ずみです。
顕微鏡光学系は、日本電子ＪＥＯＬより現物とともにＫＥＫに技術供与された超伝導対物レンズ、電磁場を可視化する光学系、カメラ、試料ホルダより構成されます。カメラは電顕用の直接検出型ＣＭＯＳ画像センサを用います。我々は既にＣＭＯＳ画像センサによるミュオンビーム像の直接検出に成功しております。

## Slide 18: The need for beam cooling
Beam cooling converts a low-luminance beam into a high-luminance beam that can be focused into a very small spot!
While beam by a fuzzy source can only be blurry focused,
Source
Image
Lens
Lens
Source
Image
Lens
Lens
cooled beam can be focused into a small spot!
Muon beam generated by Accelerator
Light by Flashlight
Laser Beam
Muon beam
like a Laser beam
● Diffusible
● Incoherent
●Focusable
●Coherent
Low luminance
High luminance
Cooling
High current, but

## Slide 19: Essence of the Beam Cooling
Momentum distribution is cleared by stopping.
Volume in phase space (emittance) is shrunken down. = Beam-Cooling
Iteration of this process can cool the beam down much more.
1) Focus
2) Stop
3) Extract and
4)Re-accelerate
Condenser Lens
Target
Beam Input
Cooled Beam Output

## Slide 20: Single- / Multi- step Muon-Beam Cooling
Surface
muon
beam
Surface
muon
beam
Surface
muon
beam
Surface
muon
beam
Mu
Mu
Our Current System
1mm focusable Ultraslow Muon Beam
GND
GND
100μJ Lyman-α＋355nm Laser
100μJ Lyman-α
+ 355nm Laser
1mJ femto-sec
pulse IR Laser
500μJ femto-sec pulse IR Laser
10μJ femto-sec pulse IR Laser
Target
SiO2-AG
1st target
SiO2-AG
2nd target
Mesoporous
SiO2 foil
3rd target
Mesoporous
SiO2 foil
4th target
Mesoporous SiO2 foil
0cm
10cm
20cm
＋30kV Extraction
3kV
3kV
3kV
30kV
D=50mm
D=1mm
D=30μm
D=1μm
30nm focusable
pico-sec pulsed Ultraslow
Muon Beam
SOA Lens System
Single-step
Multi-step
Transmission ～ 10% Luminance ×108
Ultrashort pulse
Mu: bound state among μ+ and e-
μ:Dissociation
μ
μ

## Slide 21: Concrete Design of the multistep cooler
表面
ミュオンビーム
Surface
muon
beam
Mu
GND
100μJ Lyman-α
+ 355nm
1mJ NIR femto-sec pulse Laser
The 1st stage
The 2nd
2kV
28kV
D=1mm
D=30μm
D=1μm
30nm-focusable
pico-sec pulsed muon beam (30kV)
The 1st stage consists of the SiO2-AG target and Half-cylinder cooler.
The 2nd～4th stages consist of a SiO2 mesoporous film and Immersion/Einzel lenses.
Half-cylinder D=80mm
⊗
2kV
2kV
28kV Accel.
The 3rd
The 4th
2kV
47mm
33mm
30mm
40mm
30mm
Total Length ～180mm

## Slide 22: Cyclotron constructed in U1B area of J-PARC
Ultraslow Muon Beam Line
Muon Cyclotron
RF Co-ax
RF Amplifier
PS for RF-Amp
Coil PS
Indicators
RF Controller
Servers
EM-Stop Button
Vacuum Pumps

## Slide 23: Inside of the 5MeV Muon Cyclotron
Beam-pipe
Inflector
Beam Extraction
injects muon beam from back into circular orbit
RF Co-ax
Conventional Acceleration
Flat-top Acceleration
ΔE/E～10-5
about 70-turns in 1μsec
5MeV Muon-beam
1F-Dee
1F-Dee
Flat-top 3F-Dee
Notes: ミュオン顕微鏡に用いるミュオンサイクロトロンは概ね完成し、Ｊ－ＰＡＲＣに設置されております。装置はセクタ磁石、２本の基本波Ｄｅｅ空洞と、１本のフラットトップＤｅｅ空洞より構成され、中心のインフレクタから入射されたビームは、６０回周回で5MeVまで加速され、取り出されます。基本波に加え3倍波を加えたフラットトップ加速で、10のマイナス5乗台の安定度を得て、ナノメートル分解能を可能にします。

## Slide 24: 5MeV TµM：Cyclotron + Main Column of TμM
5MeV Acceleration in 1µsec, stability ΔE/E~10-5, vertical microscope column
Camera
5MeV Muon Beam
Specimen
Height～3m
５MeV Muon Cyclotron
Condenser Lens
Q-magnet Triplet
Condenser Lens Q-magnet Doublet
Superconducting
Object Lens
135-deg Bend Magnet
Notes: This is side view of the cyclotron and the transmission muon microscope.
We developed a new 5MeV cyclotron to accelerate the muon beam.
To reduce a chromatic aberration, a flat top RF acceleration is employed.
We use superconductor object lens, which is developed by Isolde Dietrich, and is transferred from JEOL to KEK.

## Slide 25: R&D of Lenses for TµM
Normal Conductor Lens
Superconducting Object Lens
Superconducting Coil with persistent current SW
Meissner Shield
for field convergence
Developed by I. Dietrich
Transfer from JEOL to KEK
Chart: Z-Position / mm
| 0 | 5 | 10 | 15 | 0 | -5 | -10 | -15 | -20 | -25 | -30 | -35 | -40 | -45 | -50 | -50 | -55 | -60 | -65 | -70 | -75 | 0
External Current | -47938.7 | -44707.0972 | -45752.1542 | -40102.0903 | -32319.3264 | -47908.1486 | -46032.8222 | -41439.5431 | -31703.8347 | -24479.9292 | -18724.475 | -11616.4458 | -2603.3 | -170.4875 | 19.7625 | -231.8972 | -615.4806 | -964.3486 | -965.2736 | -1184.2222 | -1237.9181 | -1170.4903 | -47934.8417
Persistent Current | -47930.9847 | -45798.5986 | -39595.2222 | -27784.2139 | -47932.6819 | -45539.9958 | -38664.3486 | -30976.3208 | -24097.7347 | -17533.1444 | -11576.0208 | -1394.3778 | -118.9514 | 22.6931 | -174.1903 | -705.1278 | -985.7958 | -987.8014 | -987.6472 | -1197.3375 | -1231.5917 | -1165.5514 | -47931.4472
Magnetic field is guided to be focused by Meissner shields rather than pole-piece / yoke.
5MeV TμM becomes 3m Height,
40MeV TµM becomes 9m Length.
Notes: This is an object lens for 300keV transmission muon microscope. Normal conductor lens is used.
The next is the currently constructing 5MV lens.
The superconductor lenses should be required for over 5MeV muon microscopy.

## Slide 26: Visualization of Electromagnetic Fields
Lorentz Method
Zernike Method
TµM can visualize electromagnetic field in a bulk specimen.
The 3D distribution is also obtained by Computed Tomography.
visualizes distribution of beam deflection:
visualizes electrostatic potentials:
Notes: What we can see by muon microscopy?
It is enough to use optical microscopies,
if we want to see a structure of the macroscopic specimen simply.
One of the important merits of transmission muon microscopy is visualization of electric and magnetic field in macroscopic bulk object.
The transmission muon microscopy can import almost of all methods developed for transmission electron microscopies,
including a Lorentz method and a Zernike phase contrast method.
These methods can visualize distribution of electromagnetic field in the specimen.
The Lorentz method visualizes distribution of transversal bending force in the specimen.
The muon beam is partially deflected by the force distribution.
By inserting the object aperture into the back focal plane,
the deflection patten in the specimen arises on the camera screen.
This is principle of the well-known Lorentz method.
The next is the Zernike phase contrast method. It can visualize distribution of electrostatic field in specimen as a contrast image on the camera screen.
It can see distribution of action potentials, whose voltage is 10mV to 100mV in neurons.

## Slide 27
Visualization of Elec-Potential by Phase-Contrast
Phase-shift is converted into Contrast
Phase Shift: θ ＝ (e/h) ΔV×Passing-Time
Projection Lens
Specimen
Muon beam
Object Lens
Zernike Phase Plate
Muon beam
Carbon foil
t～10nm
Center hole
φ～1μm
Beam spot
…No Contrast
Insertion of the Zernike Phase Plate
Phase Plate
.
Sensitivity：25mV/μm thickness ➡It can visualize the electric potentials of Mitochondria and Neurons （～100mV）
Notes: 真空中をミュオン波動関数が進むのに比べ、物質中の電気ポテンシャル中を通過すると、物質に入るときには減速、出るときには加速され、位相差が生じます。その位相差は背景との電位差と通過時間に比例します。
この様な波動関数を通常の結像法で検出しても位相は検出できません。
しかし、後方焦点面に炭素薄膜に中心穴を開けた位相板を挿入すると、位相シフトがコントラストに変換され、可視化できるようになります。

## Slide 28: Test of muon imaging by CMOS Image Sensor
Sensor size 35.9×23.9mm
Pixels 8256×5504、
Unit-pixel size 43μm× 43μm
10mm
Setup and Result
Horse plastic models
μ
CMOS Sensor
CMOS Image Sensors for TEM are too expensive for test (>$150k).
We have tested imaging-capability of commercial digital camera ($3k) Nikon Z7II.

## Slide 29: Expected Resolutions
A prototype microscope for Proof-of-Concept :
Max specimen thickness: ～ 10 μm
Spatial resolution: ～ several 10s nm
Exposure-time: ～ 1day for (0. 5K)2 pixels image with 8bit depth
Phase 1: 5MeV TμM at U-Line
Phase 2: 40MeV TμM at H-Line collaborated with the Muon g-2/EDM exp.
A practical microscope for industrial and scientific applications:
Max specimen thickness: ～ 1 mm
Spatial resolution: ～ a few nm (Goal)
Exposure-time: ～ 40 min for (1K)2 pixels image with 8bit depth ～ 1 day for (1K)3 voxels CT

## Slide 30: Electric field in High Voltage Transistor (AIST)
By finding points of electric field concentration and break-down, we can develop higher voltage devices.
➡ down-sizing, energy-saving ➡ Efficient EV, Power-Grids ➡ SDGs。
By pico-seconds Stroboscopic imaging, RF fields are also visualized ➡Speed up the communication network, Higher performance Rader, …
AIST Power Electric Group developed 14kV SiC MOS FET. （Highest commercial device is 3.3kV）
Simulated Electric Field Distribution

## Slide 31
Ceramic Condenser（MLCC）
Higher dielectric strength in unit volume is essential for market competition. E= (C/2)×V2
TμM visualizes the field concentration and break-down phenomena. ➡ It helps to develop higher performance condensers.
Motor, transformer, generator → EV, Power Grid,
Piezo, ultrasonic devices → Medical、 Non-destructive inspection.
2017 MLCC Market Shares, World：￥8,617 oku ≃ ＄80B
For High Performance Electric Devices
Murata
TaiyoYuden
Ohters
Ref: J-Chip User Kai 2018

## Slide 32
A cell contains thousands of mitochondria.
They form tubular network structures throughout the cytoplasm, which constantly divide and fuse.
These mitochondrial dynamics are related to energy metabolism, and abnormalities are involved in disease.
Present methods can not observe correlation among dynamics and function (mem-potentials).
Meas. of all Mitochondrial Membrane Potentials
Cryo-TμM measures the local membrane potential distribution of all mitochondria within a cell.
➡ A breakthrough in cell biology
https://www.biophys.jp/highschool/A-31.html
Division
Fusion
Image by Optical Microscopy
Notes: 細胞内小器官のミトコンドリアは、その膜電位を基盤として細胞のエネルギー生産を司りますが、 単離したミトコンドリアはTEMで十分に観察可能な大きさです。 ヒト精子の実際のTEM像を示しますが、位相差像の長波長成分には膜電位を反映したコントラストが含まれています。
本研究では、位相差コントラスト形成理論を下にした画像解析手法を構築し、電顕にもミュオン顕微鏡にも使える膜電位の定量測定法を確立します。
同一ミトコンドリア試料の観察で、TEMとミュオン顕微鏡の測定の連続性を証明します。
この応用として、ミュオン顕微鏡で細胞内のミトコンドリア群の全体の膜電位の網羅的な測定を行います。
細胞内で、ミトコンドリアの個数はときに数千個に及び、細胞質全体に管状の網様構造を形成し、絶えず分裂と融合を繰り返していますが、
このミトコンドリアダイナミクスの詳細な機序や、細胞にとっての生理学的な意味や目的も不明です。
クライオミュオン顕微鏡で細胞をCT撮影し、細胞内の全ミトコンドリアの膜電位を網羅測定します。
これによりミトコンドリアの形態と膜電位の関係を明らかにし、これらの細胞生理の謎を解く基盤データを与えます。

## Slide 33: Functional Visualization of Neurons by TµM
Visualization of living neurons/networks.
Live cells/organs in an environmental cell. in bio-liquid at room temp and pressure with windows.
Electric pulse stimulation is synchronized with the muon pulse.
Timing delayed Δt is scanned.
The neuron are cultured on the electric microscope grid.
Freezing rapidly with liquid ethane just after an electric pulse stimulation to a neuron..)
TµM with cryo-holder and stage.
3D measurement by the tomography of phase contrast.
Stroboscopic movie of action-potential propagation in living neurons in environmental cell
3D Tomography of action-potential in neurons frozen just after an electrical stimulation
Notes: What is scientifically interesting?
We have 2 plans,
one is an environmental cell for living neurons,
We prepare an environment in the cell where neurons or a nervous or brain tissue are living and are working by keeping normal pressure, normal temperature, biological liquid environment, and so on.
The environmental cell has vacuum window for passing the muon beam. The transmission muon microscopy can observes such a thick environmental cell.
By applying electric stimulation pulse to the nervous tissue synchronized with the muon pulse, we can take stroboscopic images of electric works of the nervous tissue.
By scanning delta t between stimulation pulse and muon pulse, we obtain 2 dimensional movie of the electric fields in the neural networks.
So we can see the propagation of neural excitation in high resolution.
Another is taking a 3-dimensional snap shot of the neural network.
First an electric stimulation pulse is applied into the tissue.
After waiting a suitable time ~ several milliseconds, the tissue is rapidly frozen by using liquid ethane.
By the rapid freezing, the distribution of the electric field is also frozen, because electric field is given by distributions of ions
and the ion-distributions are also frozen.
The computed tomography of the frozen specimen given the 3-dimensional snapshot of electric field in the neural network.

## Slide 34: EM-fields Imaging for Macroscopic Object
Distribution of beam-deflection in large object is visualized by Talbot-Law like system, without beam-cooling and reacceleration.
High-energy, high-current and low-luminance beam is directly employed.
Object of 10cm scale is visualized, while resolution is limited ～ 100 μm.
Incoherent
Muon Beam
Lau Slit
Talbot Slit
Specimen
Image
on screen
Image of the Lau-slit
is projected on it.
Partially
deflected
beam
Lens
Lens
Lens
Lattice-like multi-slits
distribution of deflections
Notes: At the initial stage of the development, the quality of the beam may be not so good.
Even for incoherent muon beam, we develop this new method to visualize the electromagnetic field in specimen.
This is a kind of modification of the Talbot-Lau interferometer which is often used in X-ray imaging and X-ray microscopy.
We prepare two overlapped transfer-doublets.
At the first plane, a multi slit of lattice pattern is inserted, as a kind of Lau lattice.
The lattice pattern is projected onto the 3rd plane, namely back focal plane.
At the back focal plane, inverted pattern of the multi slit is inserted, as a kind of analyzer lattice of the Talbot-Lau interferometer.
If the specimen on the second plane has no deflection, beam is obscured by the Talbot-slit, and dos not reach to camera screen.
If there is a pattern of deflection in the specimen, the pattern arises on the camera screen.
This is very similar to the Talbot-Lau interferometer which can visualize small deflection and differential phase distribution.
This method employs transfer-doublets instead of the Talbot effect.

## Slide 35: For High Performance Accelerator (TITech Hayashizaki)
Particle Accelerator uses strong RF field in resonant cavity.
Higher RF field makes higher performance accelerator （～100MV/m）, Electric break-down of high RF field limits the highest acceleration.
Physics of the electric break-down in high RF field is unknown.
Visualization of RF break-down and transitional phenomena helps us to develop ultra-high performance accelerators.

## Slide 36: For High Performance Propulsion System in Aerospace
Ion engine / Hall thruster： generate plasma-jet by electricity.
Rail-gun：An acceleration system by Lorentz force.
There arises Complex interactions among EM-, RF- fields, ions and electrons. ➡ Measurement of 4D EM field helps up to make them more efficient and more thrust.
At high velocity（～7km/sec）, velocity skin effect limits the highest velocity. Current concentration ➡ plasma generation ➡ dissipation➡ velocity limit.
Muon visualizes the Lorentz force directly!
4D visualization of velocity skin effect makes design of higher velocity Rail-gun.
Ref: Wikipedia: The velocity skin effect in railgun.
Ref: Yamamoto Lab. Kyushu Univ.
Ref:Tukizaki, ISAS
Ref:Nakanishi, Tohoku Univ.
Wave
Gude
3 Grids
Neutralizer
RF-amp
DC Block
DC Block
Anode
Cathode
OSC
gas isolator
Xe-tank
flow m.
Discharge
Chamber

## Slide 37: Sµ+M: Scanning μSR Microscopy
Nano-resolutional 3D mapping of μSR spectroscopy in specimens
The 2nd Project:

## Slide 38: Sμ+M : Scanning μSR Microscopy
and μSR-spectra are detected point by point.
μ＋
decay positron
as an application of pico-sec pulsed 30nm-focused polarized μ-beam
Specimen is Scanned by focused μ+ beams,
Depth-scan by energy-scan and 2D-scan allow us 3D-Imaging in 30nm-resolution.
Long established μSR method is upgraded into 3D Volumatic Microscopy.
Notes: Our aim of the muon microscopy is
functional visualization of macroscopic object in nanometer resolution
by combining the strong penetration power of the accelerated muon beam and
high resolution obtained by fine emittance of the ultraslow muon beam.
This combination is realized by synergy with the muon g-2/EMD experiment.
Muon microscopies are categorized into two types, namely,
a transmission muon microscopy and a scanning muon microscopy.
This talk mainly focuses on the transmission muon microscopy,
while the whole of the project contains development of
not only the transmission muon microscopy
but also the scanning muon microscopy.

## Slide 39: Problem of Depolarization by the simple USM
Surface μ beam
100% polarized
( μ⇑)
Mu
Laser
Mu target
|μ⇑ e⇑ 〉 has no time evolution.
|μ e 〉 whose muon-spin rotates in Mu Hyperfine frequency (f=4.4633GHz)
Muon-polarization is reduced into 1/2 by the step, if no care. For the 4-step cooler：depolarizations make the muon-polarization into 1/16.
Start-timing of spin-rotation of |μ⇑ e⇓ 〉 is the formation of Mu≃μ-injection timing to the target
By synchronizing the μ-injection timing, μSR of Mu becomes Coherent rotation!
⇑
⇓
Electrons in target are unpolarized (50% e⇑ and 50% e⇓)
Status of the generated Mu consist of |μ⇑ e⇑ 〉and |μ⇑ e⇓ 〉.
⇑
⇓
Hint for Solution

## Slide 40: Zero-field μSR of Mu in SiO2-crystal / -Aerogel and Vac.
The sharp peak (f=4.4962GHz) means that μ-spin rotation of Mu in SiO2 can be coherent.
It allows us synchronization of |μ e 〉 during ΔT= 190nsec at SiO2-AG and Vacuum.
⇑
⇓
⇑
⇓
Hyperfine Interaction 19, 939–944, (1984)
[Dehn 2021:Phys. Rev. Res. 3, 013029]
fSiO2-AG = 4.3927 GHz
|fSiO2-AG / fvac - 1| = 3×10-4, ➡Q～3000.

## Slide 41: Polarization-maintained Multistep μ-cooling
表面
ミュオンビーム
Surface
muon
beam
Mu
GND
The 1st tgt
The 2nd tgt
The 3rd tgt
The 4th tge
2kV
2kV
2kV
30kV
D=50mm
D=1mm
D=30μm
D=1μm
30nm-focasable, Pico-sec,
½-polarized USM beam
μ-spin rotation in Mu (f=4.46GHz)
μ
⇑
⇓
μ
ｔ
The Laser pulses (and 1st extraction) are synchronized with the μ-spin rotation of Mu.
➡ The μ-spin rotations in Mu at the 2nd, 3rd, and 4th targets become coherent.
➡ Final polarization of 30nm-fosacable beam becomes ½.
femto-sec Laser
femto-sec Laser
femto-sec Laser

## Slide 42: Synchronized Laser Irradiation System
表面
ミュオンビーム
Surface
Muon Beam
Mu
GND
1st tgt
2kV
2kV
2kV
30kV
D=50mm
D=1mm
D=30μm
D=1μm
Single-shot / multi-shots
of pico-sec-pulsed beam
MS Cooler
NIR femto-sec
pulsed Laser
Ly-α + 355nm
mirror
mirror
mirror
mirror
mirror
mirror
mirror
mirror
mirror
mirror
mirror
mirror
4th tgt
2nd tgt
mirror
mirror
mirror
mirror
1 nsec, １shot
160f sec 1shot
100ns after
100 nsec delaying path
(446-times of 4.46GHz)
L= (N×6.67cm) Mirror Resonator
L=6.67cm (4.46GHz) Reflector Pair
100 nsec delaying path
(446-times of 4.46GHz)
3rd tgt
pulse-compressed
extraction
just after 355nm shot
The laser path length is always set to an integer multiple of 6.72 cm (4.46GHz).

## Slide 43: Team Members
Laser Devices： Yu Ohishi（KEK、Lyman-α Devices）、
Shinki Nakamura（Ibaraki U.、Yb:YAG Laser）
Cyclotron and Beamlines：
Junichi Ohnishi（Riken、Cyclotron）、 Takayuki Yamazaki（KEK、Beamline Develop.）、
Akira Goto（Riken/KEK、Cyclotron）
Superconducting Lens： Kenicih Sasaki
（KEK Cryo-G、SC-Magnets）
Power Devices：
Hiroshi Sato（AIST、MOSFET）
Life Sciences：
N. Usuda, M. Fukazawa (Fujita Med. U, Brain),
K. Jokura, K. Kameya (Shinshu U. Med.), K. Muratra (NIPS, TEM), T. Senda (KEK, TEM/X-ray)
Optics：
Y. Arai (Terabase)
Direction： Y.N（KEK、Fusion of Microscopies and Accelerators）
Beamline Management：
K. Shimomura （KEK）

## Slide 44: Summary
Acknowledgements
This research is supported by MEXT Grant-in-Aid for Scientific Research (S) JP24H00028, PI: Y.N “Transmission muon microscopy for visualizing electromagnetic fields inside of power-devices and life”.
TμM visualizes Electromagnetic fields in bulk specimen: This capability is widely applicable to sciences and engineering fields, including power-devices and life.
Sµ+M works as 3D-Scanning μSR Microscopy: The long-established μSR is upgraded to a nano-resolution 3-dim microscope.
TμM Kick-off Workshop 29-30/Aug/2024 J-Parc
Notes: We introduce collaboration members and partners.
In KEK, not only muon group, but also the muon g-2 EDM experiment collaboration, accelerator facility, and cryogenic group are collaborating.
RIKEN and Tokyo institute of technology are also members.
I summarize this talk.
g-2/EDM & Muon Microscope have strong synergy.
TµM clarifies how our brain works, by functional imaging of macroscopic neural systems in nanometer resolution.
Visualization of electromagnetic fields in bulk object is widely applicable to material science and engineering fields.

## Slide 45: Work of the Method
No Bends in specimen
Bends in Upper Half specimen
Bends in Lower Half specimen
There arises
Image of
distribution
of the bends
Lorentz-like and Talbot-Lau-like
Lau Slit
Talbot Slit
Specimen
Image
on screen
Image of the Lau-slit
is projected on it.
Lens
Lens
Lens
Lattice-like multi-slits
distribution of deflections
Incoherent
Muon Beam

## Slide 46: Ultra-short pulsed USM-beam Compressor
Harmonic-like distributed potential for extraction is applied by pulse.
Surface μ
Surface μ
Laser
Mesh electrodes for distributed extraction voltages.
Target Stack
Each muon arrives
at the same time.
Side view
Top view
Voltage
Time
Laser
USM
★
focus
Voltage divider registors
パルス HV
Harmonic-like potential
GND
Acceleration
GND

## Slide 47: Beam Compression Ratio
Angular dispersion (room temp) ～ √(0.03eV/3kV) ～ 3mrad
Due to emittance conservation. Compression＝Angular-dispersion/Convergence-angle
1st step：Large Diam（50mm）beam should be focused into as possible as large-convergence angle into next target
➡ Half-cylinder type optics based on Pierce-type e-gun.
μ injection
Mu
Laser for
Mu-dissociation
Mu-gen Tgt
Angular-dispersion
Convergence-angle

## Slide 48: 1st step: Half-cylinder Muon Cooler
Laser
Laser
Surface Muon
Surface Muon
Distributed
Wires
Printed circuit board
Cutaway-model seen from the Laser incident direction
⊗
Laser
40mm
1st Target : SiO2-AG
1st Target : SiO2-AG
Distributed electrodes form 1/r potential distribution.
It converges muons dissociated by straight laser-beam by large-converging angle.
2nd Target
2nd Target
femto-sec
IR Laser
Cutaway-model parallel to the laser-beam

## Slide 49: The cooler is “KAMABOKO” in Japanese
Kamaboko, often referred to as 'fish cake' in English, is a traditional Japanese food made primarily from pureed fish.
1st Target : SiO2-AG
Vacuum with electric-field for beam convergence
Printed circuit board
USM Beam
Lyman-α/355nm
femto-sec
Laser
Surface Muon Beam

## Slide 50: Design of 1/30 shrinking optical system
Acceleration Immersion Lens
HV=3kV
Deceleration Einzel Lens
HV=3kV
Mu Target (Mesoporous SiO2 membrane)
Next Mu Target

## Slide 51: Diffusion in the thin target
t=0nsec
t=200ns
t=100ns
t=50ns
t=10ns
Target Depth / nm
Muon Density (Rate/nm)
Diffusions of Mu in mesoporous silica are evaluated t=100nm, ρ=1.1g/cm3, D=1.6×10-4cm2/sec＝16 nm2/nsec.
SRIM Simulation
➡ Diffusion Equation Analysis
➡
Back Evaporation
Mu-distribution : f(t,x), Eq: df/dt=D△f, BC: f(t, surface) =0, f(0,x)={SRIM-Result}.
Front Evaporation
➡
2keV muon stopping

## Slide 52: Mu-Evaporation from the target
Muoniums are evaporated
～60% from back plane and ～30% from front plane.
Time / nsec
Outgoing Muonium Flux
Time / nsec
Total Evaporated Muoniums
from Back plane
from Front plane
from Back plane
from Front plane
Rate for passing thorough additional 3steps ～ >10%.
Mu-Flux : F=-D∇fsurface
Total Ratio : R(T) =∫0T dt f(t, surface)
The 3 steps-cooler improves ×108 Luminance for US-Muon beam.

## Slide 53: Sµ-M: Scanning negative-muon Microscopy
2D/3D mapping of elements/isotopes
in μm-resolution
The 3rd Project:

## Slide 54
Scanning negative Muon Microscopy: Sμ-M
Specimen is scanned by focused μ- beam,
2D/3D mapping of elements, isotopes and chemical situations.
High sensitivity for light elements ➡ Applicable to Life consisting from C, N, O.
and detect characteristic X-ray
induced by negative muon.
X-ray

## Slide 55
Muonic X-ray energy is 200-times of ordinary one, because muon’s orbit in atom is 1/200 of electron’s.
Almost all elements are analyzable, including He, Li and C,N,O.
High efficiency
Several X-ray photons are always emitted by a single muon.
Efficiency is more than 10000-times of EDX/EDS.
No damage of specimen even for analyzing light elements like C/N/O.
Isotope-identification
X-ray depends on nucleus status, because muon orbits very close to the nucleus.
Chemical property analysis
X-rays depends on valence, bonding state and electron density.
Benefits of negative muon induced X-ray

## Slide 56
(1) Focus
(2) Stop
(3) Extract
Lens
Target
(4) Re-accel
Using μCF reaction for (2) stopping and (3)extracting [Nagamine]。
Low energy muons are emitted after μCF reaction.
Fusion Fuels
Fusion
～few keV
Beam Cooling of negative muon
Beam Input
Cooled Beam Output

## Slide 57
Muon Catalyzed Fusion (μCF) is applied to the beam-cooling. Captured muon into atom is dissociated with low energy ～10keV after μCF .
Accelerator muon is captured by solid H2 with mm-thickness. pμ is converted into dμ, and dμ diffuses in mm-range by Ramsauer–Townsend effect.
μCF on thin DT-layer on solid H2 dissociates the muon. The muon is transported into center by E-field.
Muon beam is extracted, is cooled frictionally, and is focused on specimen.
Generation of Focused neg. Muon Beam.

## Slide 58
Negative Muon Collector

## Slide 59
Use of Ramsauer Townsend Effect
Solid H2 Layer : 1mm : 99.9% H2 + 0.1% T2, Solid DT Layer : 1μm : 70% D2 + 30% T2.
Injected μ- stops at Solid H2 Layer ➡ pμ is formed.
Isotope exchange: pμ ＋ t → tμ ＋ p tμ obtains kinetic energy around E～40eV.
Thermally tμ relaxes into sub meV. At the way, its scattering cross section becomes almost zero at E～1eV by Ramsauer Townsend effect.
Finally, tμ diffuses in sub mm range.

## Slide 60
Negative Muon Collector

## Slide 61: Simulation of Muon Collector
半径
ミュオン密度
Distance from Center of Muon Collector
Density of Muons
η0 : Initial Beam Input as Gaussian

## Slide 62: Simulation of Muon Collector
半径
ミュオン密度
Distance from Center of Muon Collector
Density of Muons
η1 : Distribution after 1-time of μCF reaction

## Slide 63: Simulation of Muon Collector
半径
ミュオン密度
Distance from Center of Muon Collector
Density of Muons
η2 : Distribution after 2-times of μCF reactions

## Slide 64: Simulation of Muon Collector
半径
ミュオン密度
Distance from Center of Muon Collector
Density of Muons
η3 : Distribution after 3-times of μCF reactions