## Slide 1: Exploiting and Developing Time Integral and Differential RF methods: An RF-µSR study of the 2-Norbornyl Radical in Norbornene
Stephen Cottrell and Sean Giblin
(Data measured on EMU at ISIS)

## Slide 2: Overview
Work originally motivated by the question …
‘Can we use a 90º RF pulse to characterise muoniated radicals?’
(following the example of NMR/EPR spectroscopists)
By ‘characterise’ …
    Determine parameters such as muon isotropic hyperfine coupling, Aiso, dipolar anisotropy, D, nuclear hyperfine parameters, An, etc.
To get an answer, we needed a test system …
Norbornene chosen because radicals already (very well) studied with Spin Rotation (TF) and Avoided Level Crossing (ALC) techniques.

## Slide 3: Radio-Frequency (RF) µSR

## Slide 4: RF-µSR? Resonance?
Scan either field or RF frequency, vRF
When RF frequency, matches transition a resonance is observed
The RF field was generated by a few turns of ~0.5mm Cu wire wrapped around the sample, tuned and matched at 170.5 MHz
A couple ways of doing the experiments …
Breit-Rabi energy level diagram for a simple muon-electron system

## Slide 5: Swept field RF-µSR:
RF Sequence:
Plotted for B0 = 50 * B1
Polythene, µ+, ~16.6 MHz
RF Sequence:
Orange: RF Off
Blue: RF On
On resonance:
Field, B0
Scan B0 to map out resonance

## Slide 6: Swept field RF-µSR:
Slowly formed radicals
Final state determination
Manipulating state populations

## Slide 7: Pulsed RF-µSR:
RF Sequence:
Plotted for B0 = 50 * B1
Polythene, µ+, ~16.6 MHz
RF
Free precession
On resonance:
Time RF pulse to tip spin pol. by 90°
Measure free precession in x-y plane (Transverse)
Assume νRF is ‘at resonance’

## Slide 8: Pulsed RF-µSR:
RF Decoupling (‘NMR style’)
Spin evolution in RF field
Extend ISIS frequency response
Start to exploit pulse bandwidth to multiplex information in a free precession signal – FT-NMR  FT-RFµSR

## Slide 9: Why use Norbornene as our example?

## Slide 10: Norbornene
Mu addition across double bond; Muoniated radicals well characterised (TF and ALC studies – Riccò et al; Roduner et al)
‘Exo’ and ‘Endo’ isomers depend on geometry; ‘Exo’ has nice T-dep for Aiso and D.
Plastic phase above ~129K. Averaging of D, but not completely! RF line sensitive to D, but not too broad!

## Slide 11: Analysing the data
Numerical simulations of the response of the muon polarisation to RF fields in these systems was carried out using Quantum, developed by James Lord (Physica B, 374, 2006, 472)
Heff = <HZeeman + HHF>avg, where HHF includes isotropic Aiso, and axial dipolar, Dµ‖, couplings
Polycrystalline sample (pressed into a bag)
Data fitting to obtain hyperfine parameters, etc, carried out using Mantid (mantidproject.org). In this case we’re using Quantum as a fit function
Dµ‖ for Aiso = 419 MHz

## Slide 12: Resonances for ‘Exo’ adduct
Cleaner signal for high field transition - used in these experiments
For Exo adduct in Norbornene, ν12 resonances expected at ~500G and ~2000G @ 170.5MHz

## Slide 13: Swept Field RF Experiments ‘Exo’ isomer in Norbornene

## Slide 14
+ sweep static field to map out resonance line

## Slide 15: T-dep for RF ν12 line (νRF = 170.5 MHz)
250K
200K
150K
Lines broaden and develop a powder structure as molecular motion is frozen out cooling through plastic phase
Quantum model fits to the data are shown

## Slide 16: Comparison of RF data for Aiso
Starting with earlier TF results …
(taken from Riccò et al, J. Chem. Phys. 86 4198 (1987))
Adding values from RF data measured on cooling …
Now add values from RF data measured on warming …
Good agreement – no scatter or hysteresis in RF results

## Slide 17: Comparison of RF data for Dµ‖
Starting with earlier ALC results …
(taken from Roduner et al, Ber. Bunsenges. Phys. Chem. 93 1194 (1989))
Adding values from RF data measured on cooling …
Now add values from RF data measured on warming …
Good agreement on magnitude, but RF and ALC suggest opposite sign for Dµ‖ (to investigate!)

## Slide 18: Signal in the brittle phase (<~129K)
RF signal disappears in brittle phase (as for TF/ALC)
Radicals are still formed – seen in repolarisation data
Lines are likely very broad – suggested by simulations
Dµ‖ for Aiso = 419 MHz

## Slide 19: Pulsed RF Experiments Studying the ‘Exo’ isomer with a 90° pulse

## Slide 20
+ FT of free precession signal

## Slide 21: Why Pulsed RF?
Efficiency – use a short, broadband RF pulse to multiplex information in free precession signal – standard for NMR.
Measure relaxation parameters (e.g. T2) in free precession signal.
Easier to ‘find’ resonances.
May be challenging to multiplex signals 100MHz+ apart (?) but could access proton splittings (a few MHz apart), for example.
Pulsed RF-µSR (ISIS)
νRF = 79.32MHz
60ns 90° pulse
(conditions as in McKenzie et al, J. Phys Chem B 117 13614 2013)
Simulated Bz line, split by proton HFCCs

## Slide 22: Setting up the 90° pulse
Determine resonance (swept field experiment).
Measure with a long RF pulse at resonance.
Precession frequency about RF field, B1, gives us the time required for a 90° rotation.
Frequency ~0.23 MHz, so 1/4 period is ~1µs.

## Slide 23: Free precession signals - Aiso
Now add values of Aiso determined from pulsed RF data …
(fit frequency  Hyperfine coupling)
250K
188K
Two temperatures explored so far:
λ = 1.47(7) µs-1
λ = 2.54(4) µs-1

## Slide 24: Free precession signals - Relaxation
Previous linewidths for polycrystalline data for the ‘exo’ radical circled.
250K
188K
Two temperatures explored:
λ = 1.47(7) µs-1
λ = 2.54(4) µs-1

## Slide 25: Line shape - Dµ‖
250K
188K
Experimental data, asymmetric line … a shoulder appears on the high frequency edge, particularly at 188 K.
Simulations show similar for Dµ‖ ~1 MHz.
Consistent with expected value for Dµ‖, but still positive.
FFT:

## Slide 26: Conclusions

## Slide 27
Swept Field RF study provides another view to compare to previous TF Spin Rotation and ALC studies of the 2-Norbornyl radical.
Consider RF techniques alongside other methods to get a complete microscopic picture of a system, but resilient to slowly formed states.
90° Pulsed RF techniques can access hyperfine parameters and relaxation rates, though experiments aren’t easy!
Just as in NMR/EPR, broadband pulsed techniques promise benefits: a gain in efficiency and the possibility of ‘clever’ pulse sequences.
However, significant technical challenges remain for this method to become routine, e.g. the need for reliable high-power/frequency RF pulses.
Instrument design at pulsed sources needs to catch-up in capability, e.g. resolution (~170 MHz instead of <10 MHz!), solid angle coverage (for spin rotated muons), etc. Likely to come at ISIS with Endeavour instruments.