## Slide 1: ISIS Muon Facility Report
Adrian Hillier, ISIS Muon Group
MUSR2025 St John’s Canada
July 2025

## Slide 2
New ISIS Director
Notes: This year we are celebrating 40 years of ISIS operation. Forty years characterised by scientific excellence, technical innovation and leadership. 40 years that includes 35,000 proposals to use the facility; 80,000 instrument days delivered; 60,000 user visits from 40 countries; and over 15,000 publications.
ISIS is a world-leading asset for UK science and has the potential to continue to be, well into the future.

## Slide 3: Over Forty Years ago – Muons @ISIS

## Slide 4: 40 years since the inception of muons
14 November 1984 – first meeting to discuss the concept of muons at ISIS
2.5 years later first muons

## Slide 5: The ISIS Muon Facility
EC Muons
Fixed Momentum Muons ~27MeV/c
Positive muons
Longitudinal fields upto 5 T
Transverse fields upto 600+ G (pulse width limited)
Temperature range 30mK – 2000K
Laser excitation
Pulsed techniques e.g. RF, EF, Light, ac susceptibility
RIKEN-RAL
Variable Momentum Muons ~15 – 120 MeV/c
Positive or negative muons
Longitudinal fields up to 0.4 T
Transverse fields up to 600+ G (pulse width limited)
Temperature range 300mK – 500K
Pressure
Elemental Analysis
Ports for long term experiments
e.g. proton charge radius experiment
MuX/MEIS

## Slide 6: ISIS Muon Instrument Suite
Instrument | Detectors | Rate (MEv/h) [Double pulse]
ARGUS | 192 | 50 [100]
EMU | 96 | 150
HiFi | 64 | 80
MuSR | 64 | 70
MuX/MEIS
Surface muons
Surface and decay muons
Also, on the ISIS RIKEN-RAL beamlines:
Negative muon elemental analysis – MuX
Effects of Muons on electronics - MEIS
FAMU muonic hydrogen experiment – Port 1
Muon development beamline – Port 3

## Slide 7: Breadth of Science

## Slide 8: Recent Developments

## Slide 9: ISIS Proton Pulse Compression
Frequency response with and without pulse compression – MuSR Cycle 23/5
Improving the performance of the muon spectrometers by optimising the proton beam
Shorter pulses give a better frequency response
Rotating phase space in the final stages of the proton acceleration reduces the pulse width (time)

## Slide 10: RIKEN-RAL Beamlines
Now fully Transitioned to ISIS ownership (2023)
£3.5M Refurbishment Program Complete
Instrument developments on both EC and RIKEN muons give a coherent facility
Celebrate the continuing collaboration with RIKEN

## Slide 11: RIKEN Solenoid replacement
Still the original solenoid
Showing signs of age
Solenoid Ordered
Simple automated control
Cryogen-free
Operating costs greatly reduced
  Pays for itself within 2 years
  Massive reduction CO2 emissions

## Slide 12: Draft phasing
Endeavour Programme Management: project phasing
  Implementation Review Meeting 6th Sept 2023

## Slide 13: Super-MuSR
Detector and instrument improvements
  Use full muon flux and maximise information per muon
  New transverse magnet and cruciform with flypast tube
  Better zero-field (correcting quadrupolar terms)
Beamline improvements
  Pulse slicer reducing muon pulse length to ~10ns
  Spin rotators allowing higher transverse field experiments

## Slide 14: Super-MuSR
Spectrometer
Detector R&D completed, and manufacture started in June 2025.
Spectrometer magnet design completed and now in procurement and manufacture
Spectrometer framework final design progressing well.
Pulse Slicer
Design completed, components in manufacture and assembly due to be completed in June 2025.
Testing of the pulse slicer and pulse slicer power supply is underway.
Spin Rotators in caliboration with PSI
In manufacture, with some components already delivered to site.
High voltage testing to begin in July 2025.
The project is progressing very well, with the beamline components now in manufacture and testing and new data acquisition software being tested on HIFI and MUSR.

## Slide 15: Digital Muons
Power Signal Processing: options from peak-finders to Machine Learning.
Event Formation Unit
Event Filtering
Flexibly select the events that are important for analysis. Filter on parameters such as sample temperature or laser status.
Data Analysis & Retention
Creation of .nxs files and archiving
Lots of particles arrive at the detector
Signals are streamed directly to a broker
NI DAQ 121
2024: SCD Ada Lovelace Centre
Notes: "The design of this pipeline is strongly influenced on the ESS streaming based data acquisition architecture, which was a collaborative project between the ESS DMSC and ISIS."
worth highlighting
that fact that the core of the architecture is the same as what was done for the ESS and
b) the fact that we are using off the shelf, standard, open source technologies wherever possible.
A large benefit is using the skills ISIS has from the ESS collaboration and taking advantage of standard/off the shelf software solutions where possible
Contact Dan Nixon / Dan Kirk

## Slide 16: Digital Muon enables
Sweeping parameters
Event driven
Data Filtering
Multi-hit rejection
Swept TF field on HiFi
  From 4G to 95 G
No dephasing!

## Slide 17: Optimising Muon Measurements of Small Samples
Sample
(EMU data)
Test by measuring characteristic F-µ-F signal in a 4x4mm piece of PTFE suspended in beam
For suspended samples:
less than ~10mg of sample reqd.
for clear, undistorted spectra.
At least an order of magnitude mass reduction compared typical sample mounting.
Successful in the Dilution Fridge

## Slide 18
Composition from
Muon life time
Cl Kα
Cl Kβ
Cl Lα
Cl Lβ
Cl Lβ
Cl Lα
Cl Mα
Cl Mβ
Li Kα?
LiCl
Li: 2.083(15) µs
Cl: 0.548(1) µs
T. Suzuki et al, Phys. Rev. C 35, 2212 (1987)
µ- @ 70 MeV/c

## Slide 19: Muography MeV/c Dependence – 10 min (decay µ+)
27 MeV/c
32 MeV/c
37 MeV/c
42 MeV/c
Scintillator and Camera
Sample
Muon Beam
Images from Tom Ashton UCL

## Slide 20: Alkaline Battery (70 MeV/c µ−)
Zinc anode
(7.14 g cm3)
MnO2 cathode
(5.03 g cm3)
SS cell casing
(≈ 8.00 g cm3)
AA
AAA
AAAA
Images from Tom Ashton UCL

## Slide 21: Future Developments

## Slide 22: Muon target optimisation
Currently 45°, 10mm path
Previous simulations
New geometries
μ+, π+, and π- collected perpendicular to the proton beam axis, simulated in Bungau et al. 2014
Simulations show that a target more parallel to the proton beam increases surface muon yield (Bungau 2014, Berg 2016)
Interaction length of ISIS target less than beam diameter – opposite limit to PSI
X-shaped targets with same interaction length increase surface muon yield >50% while maintaining decay muon yield
Working to improve simulations of these targets and the coupling with the beamline transport
Bungau 2014 Berg 2016

## Slide 23: Muon Future Plans: Proposed instruments
MuX
NuEMU
Chimera
Fully developed instrument for elemental analysis x100+ in rate
High data rate
Improved frequency response
Small samples
Enhanced Laser facility
State-of-the-art instrument to replace a 30+ year old spectrometer
Optimised for µ- and µ+ with variable muon momentum

## Slide 24: New Instrument MuX
Instrument dedicated to elemental analysis studies.
Currently in the review process for Endeavour phase 3
Solve the Data Rate and Sensitivity Problem:
  Aiming for two orders + magnitude in rate
  Improved detector coverage with high segmentation
Enhanced sample automation
  Automatic sample changer
How to analysis all this data!
  Easier data analysis c.f. XRF methods (EVA)
  Machine Learning

## Slide 25: ISIS-II: the successor to ISIS
The UK‘s next-generation neutron and muon source
  ISIS‘s scientific leadership with (more) modern technologies
2030s
2040s
ISIS-II at RAL

## Slide 26
Greenfield facility
Three types of pulse compression ring are under consideration
  Accumulator Ring (AR) – like SNS
  Rapid Cycling Synchrotron (RCS) – like ISIS and J-PARC
  Fixed-Field Alternating-gradient accelerator (FFA) – novel concept
1.2 GeV energy has been chosen as a good working point
  AR will require a full-energy 1.2 GeV linac
  RCS and FFA will require a ~500 MeV linac and will then accelerate the beam to 1.2 GeV
Overall source power could be up to 2.4 MW, dependent on target technology
  Rotating targets required to reach high powers, but have not yet been proven – ESS and SNS plan to use them
  Fixed targets have been proven to be reliable, but power on any one target would be limited to ~500 kW
Upgrade to existing ISIS facility
180 MeV linac injection into the present ISIS RCS
  Overall source power limited to ~500 kW
  Remains reliant on ageing equipment and infrastructure
Accelerator and target options
Performing an evaluation of the environmental impact of the lifetime of ISIS-II based on Life Cycle Assessment.

## Slide 27: Muon target: Comparing two options
Simultaneously accelerates both H+ and H- in LINAC
H+ used for muon generation, H- to synchrotron
Tailor the time structure for our purposes (by changing H+ injection)
Flux will be moderate
Familiarity, reliable, low cost
At least 10X improvement in muon flux
  significant upgrade on TD-μSR
  future LE-μSR source
  other muon applications
TS1
TS2
... Likely option

## Slide 28: Important dates
Muon Advanced School
Next long shutdown
Planned 2027
likely to be 9 months
allows for larger accelerator projects
MEBT, Linac high power amp, TS2 Cryo control
allows for installation of Super-MuSR and RIKEN Solenoid
Muon target water, Muon target shielding

## Slide 29
James Lord
Peter Baker
Adrian Hillier
Steve Cottrell
Mark Telling
Adam Berlie
Francis Pratt
Koji Yokoyama
John Wilkinson
Rhea Stewart
Sayani Biswas
Alex Louat

## Slide 31: nuEMU: Beamline extension
Current beam spot very large in horizontal direction due to dispersion from the kicker
Additional magnets in nuEMU enable
  Canceling the dispersion
  More focused beam (current 27 mm → 10 mm)
  10x improvement for small samples
Pulse slicer for 10 ns pulse width
  Unlocks new materials which can be studied
SuperMuSR beamline
nuEMU
EMU
0

## Slide 32: CHIMERA
Improved data quality
  New detector array matched to the beamline
  Improved Solid angle coverage
  Digital muons
Smaller Samples
  Smaller beam spot by a new slit package
Open access design for novel SE
  Large aperture magnets
  High homogeneity magnet fields