## Slide 1
Status of the
Moderator Test Station at ORNL
E. B. Iverson
Oak Ridge National Laboratory
25 February 2025

## Slide 2
Outline
Moderator Test Station project
Moderator Test Station concept
General description
Target Development
Analyzer Development
Science Case highlights
Operational Plan
Moderator Test Station
First Target Station
Second Target Station
Notes: In building the MDF at SNS, we do not have to focus on flux as much as we would on a stand-alone facility:
  SNS doesn't need another beamline - this is for source technology demonstration - dedicated, single-use optimization
  A small source would never begin to compete on flux; just don't worry about it
  Prototypical nature is more important than flux anyway

## Slide 3
ORNL Moderator Test Station Project
ORNL is developing the Moderator Test Station as an Accelerator Improvement Project, as specific class of DOE project in which funding is taken completely from a single year’s operating budget, so there is a hard cap to the total project cost, but it is all committed from the beginning
Funded for 9M$, with initial contingency >20%
Conceptual Design Review completed 1 April 2024
Preliminary Design Review completed 11 February 2025; report forthcoming
Final Design Review anticipated around May 2026
Installation expected to begin February 2027
Commissioning expected to begin November 2027
Notes: With the SNS front-end copy that makes up the BTF, we get “forced” into a different source configuration than we might choose if we started from scratch. This changes our optimization process, which at least for exploration purposes offers the chance at significantly different features and gains.

## Slide 4
ORNL Moderator Test Station Concept
MTS concept developed to take advantage of the SNS Beam Test Facility and optimize a neutron source to the sole purpose of testing moderator systems and materials, while enabling any moderator testing we ever had trouble performing
SNS RFQ test station (the BTF)
  2.5 MeV negative hydrogen ions, up to 50 mA peak, up to 60 Hz, up to 1 ms; all fixed
Use a LEBT-style proton chopper; choose from 0.5 to 10+ µs proton pulse
Add a target; 3E10 n/s at 75 W from p(7Li,n), low primary energy, large beam spot
Provide a large volume space for test moderator
  Can't do 10 cm high by 16 cm diameter elsewhere, or reflector-filters, or long tubes, or ...
  Wing configuration is prototypic and allows small view of high brightness configurations
Provide for rigorous reproducibility in moderator positioning and orientation
Optimize the facility solely for moderator characterization
Notes: With the SNS front-end copy that makes up the BTF, we get “forced” into a different source configuration than we might choose if we started from scratch. This changes our optimization process, which at least for exploration purposes offers the chance at significantly different features and gains.

## Slide 5
MTS Overview: Layout at extended BTF
Current Beam Test Facility
FODO Extension to BTF
New Bending Magnets and Quads to deliver beam
Relocated BTF Beamstop
Walking access to BTF FODO during MTS operation
MTS Shielding monolith

## Slide 6
MTS and Proton Beamline Extension
Target and
Shielding Block
Proton Beamline
Neutron Beamline
Copper Analyzer
Mica Analyzer
Area
Detector
Area
Detector
Area
Detector
Beam Stop
Not Shown

## Slide 7
MTS Shielding, Moderator, and Neutron Beamline
5 cm steel
5 cm borated polyethylene
1.2 m polyethylene
10 cm lead
1 cm boron carbide
n
p-
from
BTF

## Slide 8
MTS Shielding, Moderator, and Neutron Beamline
5 cm steel
1.2 m polyethylene
10 cm lead
1 cm boron carbide
n
Removable cryostat including neutron beamline, moderator services, and shielding, on tracks for reproducible positioning

## Slide 9
MTS Cryostat
n
Removable cryostat in withdrawn position allowing direct access to test moderator

## Slide 10
MTS Typical Moderator Characterization
Energy spectrum; <0.1 meV to >10 eV
  Simple time-of-flight measurement, both low-efficiency and high-efficiency in-beam detectors, possibly eventually including single-pulse spectral measurements
  Flight path length of ~2.5 m or greater required, short pulse required
  Key Performance Parameter: 1E4 n/ster/eV/(Ws) at 2 W required, 6E4 and 75 objective
Energy-dependent brightness across moderator; 1 meV to 1 eV
  Pinhole collimation with area detector
Energy-dependent emission time distribution; 0.3 meV to 3 eV
  Time-focused crystal analyzers; 0.3 meV to ~3 eV requires two separate analyzer arms, but also makes it practical to check resolution effects
  Flight path lengths of ~6 m total, short pulse required
  1-5 Angstrom required, 0.3 to 18 Angstrom objective

## Slide 11
MTS Target Concept Development
Encapsulated target allows handling in air
Layers are applied using physical vapor deposition
Collaborative effort with Energy Storage and Conversion group at ORNL

## Slide 12
MTS Target Barrier Layer Testing
Lithium reacts with aluminum substrate, barrier required
Copper is a suitable substrate material used in similar applications
Copper exhibits poor adhesion when deposited directly on aluminum
Thin (0.1 µm) chromium layer promotes adhesion
Surface finish of substrate affects adhesion
Test planning underway to evaluate thermal properties of multilayer target
Paralyne or LiPO to protect from oxidation during installation
Courtesy: Katie Browning
Al plate
100 nm Cr Adhesion layer
1 um of Cu
20 um of Li

## Slide 13
MTS Target Cooling

## Slide 14
MTS Target Testing at BTF Planned for June
Confirm that low energy elastic scattering at design angle does not impact target performance
Gather insight to target performance
Test temperature diagnostic setup
Validate target thermal analysis

## Slide 15
MTS Analyzer Arrays
Mica Permanent frame
Mica will be cooled to 80 K
Asymmetric Crystal (Copper) Analyzer Array
Symmetric Crystal (Mica) Analyzer Array

## Slide 16
MTS Mica Analyzer
Mica procured from three vendors
Natural phlogopite
Compared to fluorophlogopite, phlogopite has significantly larger mosaic and reflectivity
SPI Supplies
Mica size: 240 mm x 50 mm
Asheville Mica Energy Solutions
Mica size: 242 mm x
(varies from 102mm to 127mm)
USA Mica
Mica size: 240 mm x 240 mm

## Slide 17
MTS Copper Analyzer
Discussion with ILL Optics Group for production of high mosaic copper
Anticipate 50 mm by 50 mm by 2 mm 221 oriented copper with 2 degree mosaic
Photos from Institut Laue-Langevin

## Slide 18
MTS Science Case
Hydrogen moderators on FTS don’t scale well, losing 20% of the benefit of higher power per MW on proton beam power – we don’t know yet whether this is due to flow maldistribution, entrained gas, stagnation zones, orthohydrogen, or .…
  Varying the design of FTS moderators IN FTS to study is slow, difficult, and high-risk
  A test bed will let us try different things quickly, varying one thing at a time, to diagnose
STS plans leverage high-brightness advanced parahydrogen moderator designs
  Validating these designs will let us push boundaries a little harder, and know just how well we have to catalyze the hydrogen system to support the desired performance
New Moderator Development
  Intermediate temperature moderators like liquid ammonia or ethane might be a better fit to instruments on the current water moderator, or new instruments in a three-source future
  Directionally-enhanced moderators demonstrated to increase brightness into a guide by factors, more efficiently using the neutrons we produce
  Pelletized moderators offer access to colder materials with higher hydrogen density, better serving high resolution long-wavelength instruments
Notes: In building the MDF at SNS, we do not have to focus on flux as much as we would on a stand-alone facility:
  SNS doesn't need another beamline - this is for source technology demonstration - dedicated, single-use optimization
  A small source would never begin to compete on flux; just don't worry about it
  Prototypical nature is more important than flux anyway

## Slide 19
MTS Operational Plans
The MTS will operate for as much as 20 – 25 weeks per year, typically in one- or two-week periods, for system development and moderator testing
The MTS Science Case (ORNL/TM-2024/3583) outlines twelve different moderator concepts and an array of new materials for testing once operational – we will have ample tests to fill the time
Operation of the MTS will require the beam from the BTF. We do not anticipate operating “both” at the same time, but we do anticipate having access to either while the other is running
Running MTS will typically involve much more production level beam than BTF usually uses for accelerator physics and operations studies – 60 Hz continuous operation for several days at a time, totaling as much as 20 to 25 weeks per year
There will be local control, but most accelerator control will be from the Central Control Room
Local and CCR control for the neutron beamline and gas handling system

## Slide 20
MTS Radiation Safety
Shielding analysis performed on CAD geometry converted to MCNP using GEOUNED and GeomWriter
The current shielding layout limits dose rates outside the fence to less than 2 mrem/hour except for some streaming around the in-beam detector, which will be blocked by the beamstop (not included in this particular calculation)
Dose rates near the neutron beamline and the proton beamline will approach 10 mrem/hour, well within guidelines for the posted radiation area, but will generally not be accessed during operation
BTF FODO line will be under 2 mrem/hour

## Slide 21
Summary
The SNS Moderator Test Station will permit characterization of high-brightness parahydrogen cylinder and tube moderators in prototypical wing configuration, supporting FTS improvements, the STS concept, and new moderator development
Along the way we'll develop a capability to explore and characterize advanced moderator configurations that exceeds any facility currently available
Targeted optimization will let us improve the measurement time to characterize a moderator at LENS with two orders of magnitude lower primary source intensity (and even lower shielding requirements)
Improved characterization concepts will let us do so over a larger energy range, with more certain and better understood instrument characteristics