## Slide 1
February 26, 2025
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada
TRIUMF IH-DTL

## Slide 2: Current Status of Neutron Beams in Canada
Similar story globally - major research reactors closed e.g. BER-II, JEEP and Orphée
Canada and global community need new (affordable) pathways for neutron production
Neutron Gap
  National Research Universal (NRU) reactor shut down in 2018
  Canada is facing a neutron gap
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada Laxdal Feb. 26, 2025
Notes: Why is there a neutron gap?
Who is affected?
What is available?
Highlight the fact that this is a problem, worldwide
What is there a demand for?

## Slide 3: Accelerator Based Neutron Sources
p/d on Be/Li
e- on heavy metal
Spallation sources
3
Cost (M$)
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada Laxdal Feb. 26, 2025

## Slide 4: Design Considerations
Beryllium target (despite toxicity) is favoured over Lithium in moderate beam power regime
For protons on Be choose E<13MeV to avoid tritium production
Yield (and accelerator costs) increase with energy - 10 MeV is a reasonable balance between cost and performance
Average beam power limited by target technology Pbeam ~ < 10-20 kW
Neutron peak brightness enhanced by pulsing proton beam (proton pulse length 0.25-2.5ms @ 200 - 20Hz and 5% duty factor)
4
Neutron yield for Protons on Beryllium
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada Laxdal Feb. 26, 2025

## Slide 5
PC-CANS is a proposal for a high intensity pulsed neutron source at the University of Windsor (Ontario, Canada)
Neutrons for Science (cold and thermal)
Neutrons for BNCT (epithermal)
Protons for 18F for PET
PC-CANS (Prototype Canadian CANS)
Station | Energy (MeV) | Iave (µA) | DF (%) | Pave (kW) | Ipeak (mA) | Ppeak (kW)
Neutron | 10 | 200 | 5 | 2 | 4 | 40
18F | 10 | 100 | 5 | 1 | 2 | 20
BNCT | 10 | 200 | 5 | 2 | 4 | 40
Stage 2 totals | 10 | 500 | 5 | 5 | 10 | 100
Stage 3 totals | 10 | 1000 | 5 | 10 | 20 | 200
45 keV
Proton Source
LEBT
RFQ
5%
MEBT
3 MeV
DTL
5%
HEBT
PET
TMR
BNCT
10 MeV
pulse rate 20-200Hz
[1] PC-CANS CDR, TRIUMF internal document, R. Laxdal editor, (2022)
[2] R. Laxdal, Journal of Neutron Research 2399-117, (2021).
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada Laxdal Feb. 26, 2025

## Slide 6: Staged PC-CANS Performance – evolving target capabilities
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada Laxdal Feb. 26, 2025
Stage 1 – shared (Iave / Ipeak =200A/4mA – 2kW)
Stage 2 – dedicated (Iave / Ipeak =500A/10mA – 5kW)
Stage 3 – upgrade (Iave / Ipeak =1mA/20mA – 10kW)

## Slide 7: Overview of Prototype Canadian CANS (PC-CANS)
Design Parameter | Value
Proton Energy | 10 MeV
Duty Cycle | 5%
Total Peak Current | 20 mA
45 keV
Proton Source
LEBT
RFQ
5%
MEBT
3 MeV
DTL
5%
HEBT
PET
TMR
BNCT
Neutron Sciences
(Cold Neutrons)
1 (20) mA,10 kW
1x106 (2x107) n/cm2/s
BNCT
(Epithermal Neutrons)
1 mA, 10 kW
0.5x109 n/cm2/s
F-18 for PET
0.1 mA, 1 kW
10 MeV
7
Design Parameter | Value
Proton Energy | 10 MeV
Duty Cycle | 5%
Total Peak Current | 20 mA
45 keV
Proton Source
LEBT
RFQ
5%
MEBT
3 MeV
DTL
5%
HEBT
PET
TMR
BNCT
Neutron Sciences
(Cold Neutrons)
1 (20) mA,10 kW
1x106 (2x107) n/cm2/s
BNCT
(Epithermal Neutrons)
1 mA, 10 kW
0.5x109 n/cm2/s
F-18 for PET
0.1 mA, 1 kW
10 MeV
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada Laxdal Feb. 26, 2025
Notes: 10 MeV proton linear accelerator (RFQ+DTL) and multiple target stations.
Peak beam intensity required is 10 mA with duty factor of up to 5% (0.5 mA average).
A pulsed switchyard in the high energy beam transport (HEBT) to distribute the beam to each of the three end stations simultaneously.

## Slide 8: Linac studies
8
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada Laxdal Feb. 26, 2025

## Slide 9: Base Parameters
Typically to reduce costs we choose the highest rf frequency that can satisfy the beam dynamics
There are many high intensity proton linacs in the regime from 300-400MHz
Based on these projects we choose an rf frequency of 352.2MHz as the baseline with an RFQ energy of 3 MeV
Project | Freq (MHz) | I_peak (mA)
CERN Linac 4 | 352 | 70
ESS | 352 | 70
SNS | 402.5 | 60
J-Parc | 324 | 60
FAIR p-linac | 325 | 70
CPHS (CANS) | 325 | 50
CSNS | 324 | 40
9
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada Laxdal Feb. 26, 2025

## Slide 10: RFQ variants:
Parameters | 176.1 MHz RFQ | 352.2 MHz RFQ
Beam species | H+ | H+
Injection energy (MeV) | 0.045 | 0.045
Output energy (MeV) | 3 | 3
Resonant frequency (MHz) | 176.1 | 352.2
Peak beam current (mA) | 20 | 20
Inter-vane voltage (kV) | 130 | 78.3
Cavity length (m) | 3.6 | 3.2
minimum aperture a (cm) | 0.38 | 0.19
Ratio rv/r0 | 0.85 | 0.85
Maximum surface field (MV/m) | 26.1 (1.8 Kp) | 34.0 (1.8 Kp)
Input ɛt (n,rms)(cm.mrad) | 0.025 | 0.025
Output ɛt (n,rms)(cm.mrad) | 0.029 | 0.026
Output ɛl (n,rms)( MeV-deg (352)) | 0.238 | 0.135
Transmission (%) | 99.2% | 99 %
Number of cells | 181 | 326
RF power loss (peak kW) - est | 396 | 369
Two variants considered each giving 99% transmission for 20mA beam current from 45 keV to 3MeV as simulated in PARMTEQ:
Each optimized for same Kilpatrick and minimized length
176 MHz
  Subharmonic of DTL frequency
  RF structure – typically 4-rod
  Increased longitudinal emittance
352 MHz
  DTL frequency
  RF structure – typically 4-vane
  Shorter with improved output emittance
DTL studies preformed assuming 352MHz RFQ

## Slide 11
DTL variants:
Alvarez:
Typical structure for high intensity proton acceleration
TM010 mode with  between gaps
Transverse focusing by quad magnets in drift tubes
Longitudinal focusing with rf phase at -25 degrees
H-mode:
TE11 (IH) or TE21 (CH) mode with /2 between gaps
Choice of beam dynamics
Negative synchronous phase
  Periodic Transverse focusing by quad magnets between accelerating tanks
  Longitudinal focusing with rf phase at -25 degrees
KONUS dynamics
  Periodic Transverse focusing by quad magnets between accelerating tanks
  Longitudinal focusing with rf phase at -25 degrees
Alternate phase focusing (APF)
  Transverse and Longitudinal focusing with varying rf phase along the length

## Slide 12: DTL Study
Parameter | Variant 1 | Variant2 | Variant3 | Variant4 | Variant5
Type | Alvarez | Alvarez | CH-KONUS | CH-DTL | CH-APF
Tanks | 1 | 1 | 2 | 3 | 1
Drift tubes | 25 | 25 | 12,15 | 13,10,14 | 46
Eo (MV/m) | 3.4 | 3.4 | 6.6 | 5 | 6.7
Synch. Phase s | -30 | -30 | 0, -60, 0 | -28, -27, -28 | varying
Each variant is Modeled in LANA and PARMILA
Establish 100% transmission with good quality
Calculate emittance growth for RMS and 99% contours
Estimate longitudinal and transverse acceptance
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada Laxdal Feb. 26, 2025

## Slide 13: Alvarez
Adopt PMQs in every second drift tube in FODO lattice
  Strong transverse focusing
Longitudinal focusing with -30 deg synchronous phase
Two variants considered
  Variant 1 – no MEBT but with adjustable quadrupoles in first four drift tubes for transverse matching to the FODO
  Variant 2 – 4Q MEBT with buncher
Variant 1, L=2.6m
Variant 2, L=3.4m
Parameter | Value
Drift tubes | 26
Eo | 3.4 MV/m
Transverse Focusing | F-0-D-0 ±64T/m
Longitudinal focusing | s=-30 degrees
Beam current | 20mA
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada Laxdal Feb. 26, 2025

## Slide 14: CH Structures
Five variants considered:
  Variant 3: 0-degree synch phase (KONUS) beam dynamics – triplets
    E0=6.6MV/m – two tanks
  Variant 4 – negative synch phase beam dynamics – triplets
    E0=5 MV/m - three tanks
  Variant 5 - Alternate phase focusing (APF)
    E0=6.7 MV/m – one tank
G. Clemente, PhD thesis, Frankfurt
Variant 3 - KONUS
Variant 4 – neg. synch phase
Variant 5
The accelerating sections are typically short with quadrupole triplets (or doublets) in between accelerating sections for periodic transverse focusing
Variant 5 - APF
Length= 2.61
Length= 3.5
Length= 3.12

## Slide 15: Summary plot – emittance growth 99%
All variants give reasonable results with 100% transmission in all cases
Alvarez with MEBT (Variant 2), KONUS (Variant 3) have the smallest longitudinal emittance growth.
The smallest transverse emittance growth is with the Alvarez with MEBT (Variant 2)
The largest transverse growth is from the APF (Variant 5)
The longitudinal and transverse acceptance is largest for Variant 2 (Alvarez with MEBT)
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada Laxdal Feb. 26, 2025
https://accelconf.web.cern.ch/linac2022/papers/fr1aa05.pdf

## Slide 16
3.4MV/m Alvarez
Length = 6680mm
6.7 MV/m CH-KONUS
Length = 6680mm
5 MV/m CH s = -27
Length = 7627mm
Summary
Final choice will come down to cost and performance as well as ease of operation and robustness of design
16
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada Laxdal Feb. 26, 2025
Accelerator Session Thursday – Mina Abbaslou TRIUMF
Design Considerations for a Proton Linac for a Compact Accelerator Based Neutron Source for Canada

## Slide 17: High Energy Beam Transport (HEBT)
HEBT designed to deliver protons to all end stations simultaneously
Pulsed deflection kicker deflects selected bunches periodically
Deflected beam is separated from the undeflected beam followed by a DC septum magnet to further separate the beam
Rise and fall time depends on the Linac pulse frequency – for 200Hz separation between macro bunches is 4.7ms
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada Laxdal Feb. 26, 2025

## Slide 18: TMR and End stations
18
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada Laxdal Feb. 26, 2025

## Slide 19: Multi-user capability
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada Laxdal Feb. 26, 2025

## Slide 20: Target
Beryllium is used to generate neutrons through p,n reaction
Layered target technology with thickness chosen to reduce heating in Beryllium layer
A sandwich material is proposed to promote hydrogen diffusion (V or Pd) to reduce degradation through blisterning
Staging – Pave = 2kW -> 5kW -> 10kW
V.V Subbotina et al, NIMA, Vol 1008, Aug. 2021

## Slide 21: Moderator - Reflector
TMR studies have been completed considering a few geometries and different materials
  PC-CANS two tube geometry
  0.7mm Be target
  Polyethylene core R=8 cm
Studies
  cold moderator volume and material – cold methane vs mesitylene
  Reflector material – graphite vs lead vs Be and impact on neutron time structure and energy profile
External shielding
45 cm HDPE
5 cm BPE
6 cm Lead

## Slide 22: Neutron yield
 | Cold neutron tube (2cm Mesitylene – 20K) |  | 
 | Cold neutron flux | Thermal neutron flux | Epi-thermal/fast flux
 | n/cm2/mC | n/cm2/mC | n/cm2/mC
R=1m a = [0,5deg] | 4.2 E+06 | 4.5 E+06 | 4.5 E+07
R=2m a= [0,5deg] | 1.1 E+06 | 8.5 E+05 | 1.1 E+07
 | Thermal Neutron Tube |  | 
 | Cold neutron flux | Thermal neutron flux | Epi-thermal/fast flux
 | n/cm2/mC | n/cm2/mC | n/cm2/mC
R=1m a = [0,5deg] | 1.1 E+06 | 1.2 E+07 | 6.8 E+07
R=2m a = [0,5deg] | 2.2 E+05 | 2.7 E+06 | 1.6 E+07
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada Laxdal Feb. 26, 2025

## Slide 23: Time structure
Macro cycle defines the proton pulse length
  20-200Hz rep rates are typical -> corresponds to 2.5 – 0.25 msec pulse at 5% duty factor
Thermalized neutron production is delayed with respect to protons on target
Fill and decay times depend on TMR details – time constants and yield determined for Be, graphite, lead reflector
Example: DF=20%, Tproton=5ms, Rate=40Hz, =5ms

## Slide 24: Small Angle Neutron Scattering (SANS) performance
Assume proton pulse width of 2msec and rep rate of 25Hz – 5% duty factor
Coll (m) | Sample to detector (m) | Diam of S1 (mm) | Diam of S2 (mm) |  band (A) | Qmin (1/A) | Qmax (1/A) | Flux at sample (n/cm2/mC) | Flux (20mA) (n/cm2/s)
1 | 1 | 20 | 10 | 2 – 10.0 | 0.019 | 1.44 | 5.60E+04 | 1.12E+06
2 | 2 | 20 | 10 | 2 – 9.5 | 0.01 | 0.77 | 3.10E+04 | 6.2E+05
4 | 4 | 20 | 10 | 2 – 8.3 | 0.0057 | 0.39 | 7.70E+03 | 1.54E+05
6 | 6 | 20 | 10 | 2 – 7.4 | 0.0042 | 0.26 | 3.40E+03 | 6.8E+04
10 | 10 | 20 | 10 | 2 – 6.5 | 0.0029 | 0.16 | 1.20E+03 | 2.4E+04
Chart: SANS Yield
| 1.9E-2 | 0.01 | 5.7000000000000002E-3 | 4.1999999999999997E-3 | 2.8999999999999998E-3
Stage 1 | 224000 | 124000 | 30800 | 13600 | 4800
Stage 2 | 560000 | 310000 | 77000 | 34000 | 12000
Stage 3 | 1120000 | 620000 | 154000 | 68000 | 24000
LOQ ISIS | 200000
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada Laxdal Feb. 26, 2025

## Slide 25: BNCT Station
iBNCT simulation
IAEA - Clinical treatments require a epithermal neutron flux of ~1 E09 n/s/cm2
PC-CANS yield is expected to be 0.5 E09 at Stage 3 – within 50% of clinical flux certainly sufficient for BNCT development even in Stage 1
Be target with MgF2 moderator
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada Laxdal Feb. 26, 2025

## Slide 26: Expected Performance
26
Applications |  | Iave/Ipeak (mA) |  |  | 
 |  | PC-CANS1 0.1/2 | PC-CANS1 0.2/4 | PC-CANS2 0.5/10 | PC-CANS3 1/20
Neutron Science | Cold (a) (n/cm2/s) | - | 2.2x105/ 4.4x106 | 5.5x105/ 1.1x107 | 1.1x106/ 2.2x107
 | Thermal (a) (n/cm2/s) | - | 5.4x105/ 1.1x107 | 1.4x106/ 2.7x107 | 2.7x106/ 5.4x107
 | SANS (d) (n/cm2/s) | - | 3.1x104 | 7.7x104 | 1.5x105
BNCT | Epithermal (b) (n/cm2/s) | - | 1x108 | 2.5x108 | 5.0x108
PET | 18F (GBq) (c) | 240 |  |  | 
Yield at 2m from target
Yield from MgF2
Saturated yield
Assuming =2-8.3 A, Qmin=0.006 A-1
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada Laxdal Feb. 26, 2025

## Slide 27: Present status
Conceptual design released in support of proposal
Plan is to prepare a detailed technical proposal for a future funding opportunity
Linac studies including further analysis, RF design, detailed costing are continuing
27
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada Laxdal Feb. 26, 2025

## Slide 28: Acknowledgments
Dalini Maharaj (Julich)
Sana Tabbassum (Purdue)
Mina Abbaslou (TRIUMF/UVic)
Marco Marchetto (TRIUMF)
Zahra Yamani (CNL)
Vinicius Anghel (CNL)
Ronald Rogge (CNL)
Helmut Fritsche (CNL)
Daniel Banks (TVB Associates)
Zin Tun (TVB Associates)
Alexander Gottberg (TRIUMF/UVic)
Oliver Kester (TRIUMF/UVic)
Drew Marquardt (UWindsor)
Philipp Kolb (TRIUMF)
This work is supported by NFRF-E Grant Number NFRFE-2018-00183

## Slide 29: Thank you Merci
Follow us @TRIUMFLab
www.triumf.ca

## Slide 30: DTL – length – rf power
The tank (rf) length is directly related to the chosen gradient while the linac length is impacted by the number of external focusing sections required.
Total power is reduced for lower gradients but may require additional triplets in the CH variants.
Choice of the gradient will come from a cost optimization of structure and rf power.

## Slide 31: Longitudinal acceptance
Longitudinal acceptance is estimated by looking at the fractional emittance growth for sequentially increasing input emittances
Variant 2
Alvarez
Variant 3 CH-KONUS
1x
2x
3x
4x
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada Laxdal Feb. 26, 2025

## Slide 32: Transverse acceptance
Transverse acceptance is estimated by looking at the transmission for sequentially increasing input emittances
PC-CANS - Conceptual Design of a Compact Accelerator Based Neutron Source for Canada Laxdal Feb. 26, 2025