## Slide 1: The CoolGal target: core of the Phase 0 NEPIR (NEutron and Proton IRradiation) facility
Dr. Elizabeth Musacchio-González, Ing. Alberto Monetti, Ing. Alberto Campagnolo,
Dr. Jeffery Wyss, Dr. Pierfrancesco Mastinu, Dr. Luca Silvestrin

## Slide 2: INFN- National Institute for Nuclear Physics
4 National laboratories
20 Divisions
3 National Centers and School
1 International Consortia
6 Associated groups
INFN facilities

## Slide 3: INFN- National Institute for Nuclear Physics
4 National laboratories
20 Divisions
3 National Centers and School
1 International Consortia
6 Associated groups
National Laboratories of Legnaro
INFN facilities

## Slide 4: LNL-INFN – National Laboratories of Legnaro
CN
TANDEM
AN
SPES CYCLOTRON
ACCELERATOR COMPLEX
ALPI
6 MV Van de Graaff electrostatic
2 MV electrostatic
(micro beam)
14 MV
Linear with superconducting cavities
35-70 MeV

## Slide 5: Neutron sources @ LNL-INFN
Neutron Sources
Lithium target
@ CN accelerator
Neutrons
@ SPES (P70)
Inverse reactions
@ Tandem accelerator
Maxwell-Boltzmann-like spectrum
Quasi-monoenergetic neutrons

## Slide 6: Neutron sources @ LNL-INFN
Neutron Sources
Lithium target
@ CN accelerator
Neutrons
@ SPES (P70)
Inverse reactions
@ Tandem accelerator
This talk

## Slide 7: Neutrons @ SPES facility
Neutrons @ SPES
NEPIR-0
NEPIR-1
White neutron spectrum (CoolGal)
Quasi Mono-energetic Neutron (QMN)
Atmospheric Neutron Emulator (ANEM)
The facility has been partially funded by the MIUR within the PRIN (2022JCS2CN) project and the SPARE (Space Radiation Shielding) project.
NEutron and Proton IRradiation facility
(multidisciplinary project)
Fast neutron irradiation facility
NEPIR
ISOL 1
ISOL 2
Main machine parameters | 
Type | Cyclotron with 4 sectors, resistive magnet
Particles | Protons (H–)
Energy | 35 - 70 MeV
Maximum current intensity | 750 µA
Extraction | Double
Maximum magnetic field | 1.6 T (Bo = 1 T)

## Slide 8: Neutrons @ SPES facility
Shielding performance
Production of quality nuclear data
Radiation damage in electronics
Bio-medical
Radiation instrumentation
Neutrons @ SPES
NEPIR-0
NEPIR-1
White neutron spectrum (CoolGal)
Quasi Mono-energetic Neutron (QMN)
Atmospheric Neutron Emulator (ANEM)
The facility has been partially funded by the MIUR within the PRIN (2022JCS2CN) project and the SPARE (Space Radiation Shielding) project.
NEutron and Proton IRradiation facility
(multidisciplinary project)
Study the neutron-induced radiation effects in electronics for Space, Avionics, HEP, and Information Technology.
Oncology with direct fast neutrons;
Exposure to secondary neutrons at hadron therapy facilities;
Space health.
Benchmark experiments of innovative materials for hadron therapy facilities and for space colonization.
Manufacturers/users of instrumentation;
Dosimeters (energy response and calibration);
Development of novel neutron detection systems.
Cross-sections of neutron production and neutron driven reactions for basic science and for nuclear physics applications.
NEPIR Applications
Fast neutron irradiation facility

## Slide 9: Neutrons @ SPES facility
Shielding performance
Production of quality nuclear data
Radiation damage in electronics
Bio-medical
Radiation instrumentation
Neutrons @ SPES
NEPIR-0
NEPIR-1
White neutron spectrum (CoolGal)
Quasi Mono-energetic Neutron (QMN)
Atmospheric Neutron Emulator (ANEM)
The facility has been partially funded by the MIUR within the PRIN (2022JCS2CN) project and the SPARE (Space Radiation Shielding) project.
NEutron and Proton IRradiation facility
(multidisciplinary project)
Study the neutron-induced radiation effects in electronics for Space, Avionics, HEP, and Information Technology.
Oncology with direct fast neutrons;
Exposure to secondary neutrons at hadron therapy facilities;
Space health.
Benchmark experiments of innovative materials for hadron therapy facilities and for space colonization.
Manufacturers/users of instrumentation;
Dosimeters (energy response and calibration);
Development of novel neutron detection systems.
Cross-sections of neutron production and neutron driven reactions for basic science and for nuclear physics applications.
NEPIR Applications
Fast neutron irradiation facility

## Slide 10: Neutrons @ SPES facility
Neutrons @ SPES
NEPIR-0
NEPIR-1
White neutron spectrum (CoolGal)
Quasi Mono-energetic Neutron (QMN)
Atmospheric Neutron Emulator (ANEM)
NEPIR
ISOL 1
ISOL 2

## Slide 11: Quasi mono-energetic neutrons (QMN)
Thin lithium and beryllium targets (1-4 mm thick).
Controllable neutron energy peak in the 35-70 MeV energy range.
The protons that pass through the thin targets are deflected by a bending magnet and guided to a heavily shielded beam dump.
Neutron spectrum for Li (4.7 mm)
Neutron spectrum for Be (4 mm)
Angular dependence at Eproton = 70 MeV
Kamata S., Itoga T., Unno Y., Baba M. (CYRIC ANNUAL REPORT 2005)
Journal of the Korean Physical Society, Vol. 59, No. 2, August 2011, pp. 1676-1680
NEPIR-1
Cross-section data for basic science
Radiation instrum. (detectors & dosimeters)
Shielding-benchmark experiments
QMN applications
Accelerators in research & medicine
Electronics industry
The “good” truly mono-energetic neutrons are produced mainly in the direction of the proton beam.

## Slide 12: Neutrons @ SPES facility
Neutrons @ SPES
NEPIR-0
NEPIR-1
White neutron spectrum (CoolGal)
Quasi Mono-energetic Neutron (QMN)
Atmospheric Neutron Emulator (ANEM)
NEPIR
ISOL 1
ISOL 2

## Slide 13: Atmospheric Neutron Emulator (ANEM)
NEPIR-1
A coaxial rotating Be sector and W disk intercept the off-axis proton beam; a stainless-steel rotating drum houses a helicoidal water cooling circuit.
An intense source of fast neutrons (E > 1 MeV) with a continuous energy distribution.
Atmospheric-like energy distribution in the 1-65 MeV energy range, found at flight-altitudes and at sea-level.
Designed to handle 2.1 kW (30 μA @ 70 MeV). The maximum 10 μA proton current is set by radioprotection constraints, A < 1 Bq/g.
ANEM applications
Study radiation damage effects of atmospheric neutrons on material, in particular electronic devices and systems at sea level, but also at flight altitudes (avionics) where the neutron flux is 300–450 times higher.
Thickness
W: 5 mm (beam stopping)
Be: 24 mm

## Slide 14: Neutrons @ SPES facility
Neutrons @ SPES
NEPIR-0
NEPIR-1
White neutron spectrum (CoolGal)
Quasi Mono-energetic Neutron (QMN)
Atmospheric Neutron Emulator (ANEM)
NEPIR
ISOL 1
ISOL 2

## Slide 15: CoolGal
A simplified Phase-0 fast neutron irradiation facility, still attractive for academic and electronics industrial users.
Based on a thick proton stopping Be target, that produces a continuous energy neutron beam.
The Be is immersed in a static bath of a liquid metal Galinstan (eutectic alloy of gallium, indium and tin).
Due to radioprotection constraints, the 70 MeV proton current is limited to 1 μA.
NEPIR-0
Havar window
Too complicated for low power target
First prototype without Galinstan
High power target
2 kW - 54 kW

## Slide 16: CoolGal
The target consists of:
The beryllium target (30 mm thick).
A separation window to divide the vacuum of the target from that of the accelerator, thus preventing contamination of the line.
Aluminum chamber containing the target and the cooling system.
Target compression springs for thermal dissipation.
The target diagnostics system.
NEPIR-0
Cooling channels
Compression springs
Aluminum chamber
Be
Window
protons
Cooling channels
Be target
Compression springs
Window
Windows
Be target
Diagnostic system
Material & thickness
Thickness
Temperature
Cooling system
Neutron spectrum
Simulations
Coolant & Power dissipated

## Slide 17: CoolGal
NEPIR-0
Material request
Low density (low Z)
High thermal conductivity
Limited residual radioactivity
Resistance to radiation damage
Cost & availability on the market
Gas impermeability
Low thermal expansion coefficient
Titanium alloy grade 5
Aluminum alloy 6061
Havar
Titanium alloy grade 9
0.03 mm
0.1 mm
0.05 mm
0.03 mm
Window
protons

## Slide 18: CoolGal
NEPIR-0
Material request
Low density (low Z)
High thermal conductivity
Limited residual radioactivity
Resistance to radiation damage
Cost & availability on the market
Gas impermeability
Low thermal expansion coefficient
Titanium alloy grade 5
Aluminum alloy 6061
Havar
Titanium alloy grade 9
0.03 mm
0.1 mm
0.05 mm
0.03 mm
I = 10 A
Maximum temperature at the center of the window
Window
I = 1 A
protons
Havar
0.1 mm
Havar Window
Radius [mm]
Radius [mm]
Temperature [°C]
Temperature [°C]

## Slide 19: CoolGal
NEPIR-0
Window
Material request
Low density (low Z)
High thermal conductivity
Limited residual radioactivity
Resistance to radiation damage
Cost & availability on the market
Gas impermeability
Low thermal expansion coefficient
Titanium alloy grade 5
Aluminum alloy 6061
Havar
Titanium alloy grade 9
Maximum dpa
Activity (100d irrad. 1 μA - 35 MeV)
Temperature (1μA – 35MeV)
Dose at 1m (100d irrad. 1 μA - 35 MeV)
0.03 mm
0.1 mm
0.05 mm
0.03 mm
protons
Aluminum
Havar
Titanium
Temperature (10μA – 35MeV)
Radial distance [mm]
Radial distance [mm]
Time[days]
Time[days]
Aluminum Titanium Havar
Material
Activyty [Bq]

## Slide 20: CoolGal
Beryllium target
NEPIR-0
I = 10 A
I = 1 A
protons
Maximum temperature on the upper surface; Change in slope at the point where the Bragg peak occurs.
Be Target (70 W)
1 A & 70 MeV
(70 W)
Tmax =35°C
Axis[mm]
Axis[mm]
Temperature [°C]
Temperature [°C]

## Slide 21: CoolGal
Diagnostic system
NEPIR-0
crack
Without crack
Crack of 5 mm
Crack of 10 mm
Crack of 14 mm
Crack of 16 mm
Crack of 20 mm
protons
P = 700 W
The crack made on the target under consideration is a lateral fissure, 0.5 mm thick, with increasing length.
Without crack
Temperature along the z axis
Temperature on the upper surface of the target (along y axis)

## Slide 22: CoolGal
Diagnostic system
NEPIR-0
Temperature along the circumference at different z heights
Hole for thermocouples
Without crack
Crack of 5 mm
Crack of 10 mm
Crack of 20 mm
z = 2.5 mm
z = 13 mm
z = 27 mm
3 thermocouples at z = 13 mm from the base;
Temperature monitoring of the target
3 thermocouples at z = 27 mm from the base;
3 thermocouples in the shoulder (2.5 mm).
Thermocouple junction
Connection transition
Through thermocouple
Angle [°]
Angle [°]
Angle [°]

## Slide 23: CoolGal
Cooling system
NEPIR-0
Designed to dissipate a power of 700 W with a water flow rate of about 200 l/h, resulting in a maximum temperature increase of 55°C at the point of contact with the beryllium target.
Natural convection
Pdiss = 20 W
Compress air
Pdiss=70-150 W
Water
I = 0.1-0.3 μA
I = 1-2 μA
Pdiss > 150 W
I > 2 μA
Liquid metal
Pdiss > 1400 W
I > 20 μA
1° channel
Pdiss = 377 W
2° channel
Pdiss = 322 W

## Slide 24: CoolGal
Thickness change
30 mm 26 mm
Neutron spectrum
NEPIR-0
All protons are stopped at the Be, increasing the probability of blistering.
Neutron spectrum (new target)
Neutron spectrum (new target)
7% less neutrons but with En < 3 MeV

## Slide 25: CoolGal
Thickness change
30 mm 26 mm
Neutron spectrum
NEPIR-0
All protons are stopped at the Be, increasing the probability of blistering.
Neutron spectrum (new target)
Expected neutron energy spectra (in the forward direction, with a 3° semi-angle, at 1 m) with 26 mm Be target and 0.1 mm aluminum window
≈ 106 n/cm2/s
Pseudo-monocromatic neutrons

## Slide 26: Final layout of the CoolGal target
Aluminum chamber containing the Be target (26 mm thickness) with the aluminum window.
The target is electrically isolated from the surrounding elements.
Directly measure the number of protons deposited and the actual alignment of the target measuring the current on target.
Passive collimation system that, under nominal conditions, should not measure any beam current.
Manual valve to safely close the target after irradiation and a flange with a chain for quick detachment of the system after irradiation.
Active collimator
(suppressed)
Passive collimator
(suppressed)
Target chamber
(suppressed)
Vacuum valve
(acc. side)
Chain for quick detachment
Manual valve
(target side)

## Slide 27: Conclusions
Needs Ep = 35 - 70 MeV and I = 0.1 - 10 µA.
(probable measurement at ISOL2 bunker of SPES facility).
The Neutron and Proton Iradiation (NEPIR) facility was presented, and the applications of the facility were discussed.
Phases 0 and 1 were explained, emphasizing the main characteristics of the QMN, ANEM and CoolGal beam.
The CoolGal target was presented in more detail since it is the core of the Phase 0 of NEPIR. In particular, thermo-structural analysis of the main components was discussed, and the expected neutron spectrum was shown.
The target system is composed of thick beryllium block pressed to a water-cooled aluminum vacuum chamber. The target vacuum is enclosed by using a thin window, such as aluminum or titanium, to exclude Beryllium contamination of the overall beam pipe.
We will gather data and experience in view of a potential prototype (high power target) with Galinstan.
The first CoolGal target is under production
and will be delivered and tested within this year
Offline test
To validate the thermal and structural simulations (window, Be and cooling system).
Online test
Test and verification of the Target’s Mechanical & Diagnostic System Measure the neutron spectrum  Activation foils  Calibrated scintillator detector
Near future developments

## Slide 28: Thank you for your attention!

## Slide 30: More spectra comparison
0.88 (12%)

## Slide 31: Comparison old and new prototype
1 A & 70 MeV
(70 W)
Tmax =28°C
10 A & 70 MeV
(700 W)
Tmax =100°C
protons
1 A & 70 MeV
(70 W)
Tmax =35°C
10 A & 70 MeV
(700 W)
Tmax =165°C

## Slide 32: Deposition at the window

## Slide 33: Selective Production of Exotic Species (SPES)
Main machine parameters | 
Type | Cyclotron with 4 sectors, resistive magnet
Particles | Protons (H–)
Maximum energy | 70 MeV
Maximum current intensity | 700 µA
Extraction | Double
Maximum magnetic field | 1.6 T (Bo = 1 T)
Selective
Production of
Exotic
Species
Proton Beam
Radioactive Beam
Cyclotron
Target chamber
Target
SPES bunker

## Slide 34: Thermo analysis all target– 700 W, 10 μA, 4 MPa

## Slide 35: Galinstan advantages & disadvantages
NEPIR-0
Galinstan (GaInSn) is a non-toxic liquid metal, a eutectic alloy of gallium (Ga), indium (In), and tin (Sn)
Pro:
To cool down the havar window;
To ensure a good thermal contact and heat transfer to the cladding for conduction;
To keep the debris of beryllium if/when blistering occurs;
Allow thermal dilatation of the beryllium;
Thanks to natural convection, distribute the heat on the whole surface of the cladding.
Cons:
Cost;
Corrosive material, study the effect with the materials in contact;
More complicated geometry with an external vessel;
Becomes radioactive.
GaInSn droplets and corrosion areas after test
For nickel-alloy and stainless-steel samples, no obvious differences between the control & test specimen were observed
visually or at high magnification.
Duration test of 2000 h except for A2 500 h instead.
25°C
100°C
200°C
Aluminum
Copper
Pre-test photos
After-test photos
“The Effect of Static Liquid Galinstan on Common Metals and on-Metals at Temperatures up to 200 °C” Philip Geddis, et.al. Canadian Journal of Chemistry; 5 August 2020; https://doi.org/10.1139/cjc-2020-0227
In the case of beryllium ,it is reported that the corrosion to gallium is good to 500°C, limited at 600°C, and poor at 800°C. Indium and thallium are very likely less corrosive than gallium.
“Corrosion of Beryllium” P. D. Miller and W. K. Boydj ; DMIC Report 242, 11 December 1967
Experimental test
Galinstan on:
Havar;
Titanium (alternative window);
Gold (copper block coating);
Steel;
Chromium;
and finally, also on beryllium.
Proved too complicated, with no significant advantages
First prototype without Galinstan
Notes: The top row for
each metal shows the sample before cleaning, and the lower row shows the sample afterwards.
are shown in (A)
AL1100 (B) CDA122.
Smaller images are from after testing. Exposure at 25 °C is shown in A1, B1, and C1. Exposure at 100 °C is shown in A2, B2, and C2.
Exposure at 200 °C is shown in A3, B3, and C3.
is shown due to severe degradation of the 2000 h sample.