## Slide 1: RIKEN Accelerator-Driven Compact Neutron Systems, RANS Project
Yoshie OTAKE yotake@riken.jp
Neutron Beam Technology Team, RAP、RIKEN Team leader,
T-RANS、President Technology Research Association for Neutron Next Generation System
President of Japanese Society of Neutron Science, JSNS,
Chief Technical Advisor, Rans Veiw
RANS-RIKEN Accelerator-driven compact Neutron Systems-
26 Feb.2025, UCANS11, Vancouver, Invited talk

## Slide 2: RIKEN COMPACT NEUTRON SYSTEMS: RANS-I,-II,-III & m
検出器
Under dev.
RANS-III in trailer !
In operation, RANS, RANS-II, and RANS-μ(* on-site)
Up-grade of moderator-reflector system 2020-2021
7MeV proton
Be target 100μA Pulse
2.49MeV proton
Li target 100μA Pulse
Salt-meter:
252Cf source
PGAA (Ge+BGO)
T.Kobayashi, M.Mizuta, T.Takanashi, T.Fukuchi, Y.Wakabayashi, Y.Okuno, S.Imajo, H.Kusano, A.Muneem, T.Takamura, T.Hashiguchi, Yujiro IKEDA (Special Advisor) ,

## Slide 3: Cooperation, collaboration International, domestic, academia, industry.
Hokkaido Univ. HUNS
50 anniv.(2023)
Tohoku Univ.
Ibaraki U.
J-PARC, JRR3
Kanazawa Univ.
Tokyo City Univ.
Nihon Univ.
Nagoya
Univ.
NUANS
Waseda Univ.
Tottori Univ.
Kyoto
Univ.
KUANS
Osaka
Univ.
Tokyo Univ.
Akita Univ.
Xi’an Jiaotong
University
Every year, Ph.D students study at RANS since 2014.
Ph.D from XJTU
NIMS
AIST AISTANS
Companies: more than 20
Iron and steel companies, Highway, Railway,
and so on….
HBS, Hi-CANS, Cooperation
Joint WS JCNS-RIKEN, every year, since2017
Researchers exchange- Dr.Paul Zakalek, 2022 Dr.S.Ikeda 2023, ? 2024 .
CANS project at CEA
RANS
Spain, DIPC, etc. at Basque
April 2024 RANS, RANS-II experiments for 1 month

## Slide 4
RIKEN RANS Objectives: Compact neutron systems neutrons, anytime, anywhere
Neutron Source development
RANS, RANS-II, RAS-III
(Accelerator-based)
RANS-μ (RI)
+ Moderator, reflector, shielding
Instruments design, analytical methods should be
based on strong demand from the society
R&D
The development purpose
in order to respond to the needs! New needs
and to realize the non-destructive test instruments of neutron on-site
On-site:
Manufacturing sites, infrastructure sites, research sites, space

## Slide 5: Some crtical needs from industrial applications on-site use
Non-destructive test: transmission imaging for such a large area as 10cm2 with *100μm resolution
  Corrosion visualization
  bonding interface and joints of multi-materials
Material development engineering diffraction towards high strength-formability for weight reduction
  volume fraction evaluation
  texture evolution estimation
  SANS, PGAA, as well
Thin-film like hydrogen between dissimilar metals (water, adhesives, rust) and rust between metals and coatings

## Slide 6: The most critical need is non-destructive diagnostic system for infrastructure: To meet needs： preventive maintenance
USA I-70 Concrete bridge collapse
Dec. 2005 , 45 years after the construction Pennsylvania. Rebar corrosion because of ant freezing agent
Canada Collapse of a Portion of de la Concorde Overpass
Sept, 2006, 35 years after construction, Montreal
Initial construction failure
From：Pittsburg Post-Gazette
出典：落橋に関する委員会報告書
Message from Dr. Banthia to Japanese researchers:
The novel non-destructive test methods such as x-ray, electromagnetic induction method, elastic wave method.出典：六郷ら、カナダのデラコンコルド跨道橋の崩落事故に学ぶ、コンクリート工学,2008.12
From Mr. R.Ooishi (Institute Public Work)
Taiwan bridge collapse1 Oct. 2019）
Salt damage->bridges collapse
Initial construction failure
Vigili del Fuoco/AFP
Italy ・Moradi bridge collapse
（14 Aug.2018. ）Salt damage
Notes: A number of severe and unpredictable bridge falls have so far occurred around the world.. Preventive maintenance, rather than the conventional after-the-fact maintenance that is carried out after cracks and other external damage have already started to occur, can extend service life. Non-destructive observation of the inside is essential for preventive maintenance, and expectations are high for neutrons.

## Slide 7: Research Projects with Space as the Place 1. water resources exploration: Moon, Mars 2. neutron lifetime: lunar orbit together with RANS team (collaboration from 2020-)
Dr. Teruaki Enoto (Kyoto Univ. RIKEN)

## Slide 8: Compact neutron systems neutrons, anytime, anywhere
Development objective:
Research and development in response to needs
Needs: we focus on.
  Manufacturing sites: human resources development, materials development, non-destructive testing
    Neutron scattering instruments:<- Proof and examples of what CANS can do.
      Engineering diffraction,
      SANS,
      imaging,
      PGAA, NAA
  Infrastructure sites: preventive maintenance Conversion from after-the-fact maintenance to preventive maintenance. Conventionally, only preventing accidents before they happen
    Fast neutron scattering imaging and PGAA: RANS-III (transportable)
    PGAA on-site, of ultra-compact detection system with Cf source with reflector system: RANS-μ

## Slide 9: Major parameters of RANS
1.Proton 7MeV 100 μA (max. av.) Daily use
  ７MeV、100μA、Rf power supply.: 350kW(peak) duty 1.3%,Electric power peak 40kVA, Cooling water：75L/min ,pulse width (30～200μs)repetition frequency～20～180Hz RF power 425MHz, Injection energy0.030-3.5MeV
2.compact and low cost
proton linac: in our case less than <2億円=2*10^8 yen=2 million US$
shielding design Multilayer shielding of target station
Be (p,n)reaction: Be (Dr. Y.Yamagata)
7MeV 100 μA 700W
Pulse condition
10-180μs pulse width
20-180Hz repetition rate
  Neutron max total flux ~1012/sec
Choose them under the condition 1.3 %duty, 100μA
2012 7MeV proton linac was installed (Accsys co.)
2013 Operation starts with fast and thermal neutron

## Slide 10: Major parameters of RANS-II
1.Proton 2,49MeV 100 μA (max. av.) 200MHz
2.compact and low cost
Easy to operate, and robust
Li (p,n)reaction: Li target (covered with CrN)
2.5 MeV 100 μA 250W
Pulse condition
  pulse width 10μs~ * ms
  repetition rate *Hz~2000Hz
  Neutron max total flux ~1011/sec
under the condition 3.3 %duty, 100μA
2.5 MeV Proton linac plan discussion with Prof.N.Hayashizaki of TITECH
2015 Prof.Hayashizaki, Time Co., RIKEN design discussion
2019 Neutron generation
T.Kobayashi, S.Ikeda N.Hayashizaki, Okamura TIME Co.
Both the accelerator and target are robust and easy to operate stably.
MIRROTRON CANS
RANS2.1 model

## Slide 11
Typical Neutron Spectra for p-Be and p-Li with respective proton energy of 7 MeV and 2.5 MeV
Neutron Energy
Spectrum 1.5m from target ( Target station exit)
Moderator thickness
Neutron flux
Neutron Energy
Without Moderator
・Thermal moderator: PE
・Cold moderator: Mesitylene
・Reflector: Graphite, and PE
・Without moderator ,
・or thermal moderator(PE)
・Reflector: PE
Without
PE
Moderator

## Slide 12
1840
1875
3030
1250
400
Graphite Reflector
Refrigerator
Be Target
Plug
Cold moderator
Beam extractor
PE
PE
Pb Shield
RANS cold neutron moderator system with a plug
Proton beam
Graphite
30
15
15
150
28
Mesitylene
Aluminum
Air
Polyethylene
Ti
PEEK insulator
Be
proton
Yujiro IKEDA, Teshigawara
Notes: The conceptual structure of the RANS target station is shown in Fig with major components of the neutron source, e.g., Be neutron production target, moderator, reflector and radiation shield. The plug system is also depicted where the plug with cryogenic moderator is moved horizontally along rails placed on a support structure into the place at the central target location.
Fig. b gives a layout of the expanded TMR configuration, where the mesitylene moderator with PE pre-moderator are directly coupled with the Be target. All in detailed geometries of those components are modeled in the simulation.

## Slide 13
RANS, RANS-II neutron Scattering experiments
Imaging experiments special resolution, 0.5mm, 0.2mm, Non-destructive test
Engineering Diffraction, iron steel, austenite phase fraction, texture, residual stress
PGNAA, Prompt gamma-ray Neutron Activation Analysis, elemental analysis
SANS with Ibaraki Univ. (Small Angle Neutron Scattering) nano, sub-mic.
Fast neutron transmission imaging for thick samples
Fast neutron scattered imaging from the surface, infrastructure degradation visualization
Phase contrast imaging with Tohoku Univ. Prof. A. Momose
Polarized neutron experiment for fundamental physics, with Nishina-center, Tohoku Univ. Kyushu- Univ.
Neutron γ-ray irradiation application:
  Food: space application (Prof.M.Hatsuda et al)
  Neutron detectors using solar cells (Dr.Okuno, et al)
  others

## Slide 14: Realized with RANS: What can be done with CANS CANS applications from RANS and RANS-II results.

## Slide 15: Visualization of bonding interface and joints of multi-material structural materials
Aluminum
Steel
rivet connection
Rivet and adhesive connection
Aluminum
Steel
RANS imaging
rivet
Visualization of air hole, thinner part
Dr.A.Taketani, Dr.Naito (NIMS), and Takahashi ( Kobe steel) by ISMA project
NEDO/ISMA project with NIMS and AISTANS
To evaluate the bonding interface and joints of multi-material structural materials.
Quantitative observation of water penetration into the bonding interface was achieved. We have also obtained a technique for observing the state of the bonding area regardless of the bonding material.
Visualization of moisture penetration of bonding
Higher resolution, FNTD
Dr.Saito, Dr. Abdul Muneem (25th)

## Slide 16: RANS up-grade 2: Towards stress measurement RANS: engineering diffraction
volume fraction evaluation
texture evolution estimation
H.Suzuki, P.Xu, Y.Ikeda, C.Iwamoto

## Slide 17
＜Engineering diffraction RANS＞
for quantitative evaluation (Iron and steel industrial use)
For lower background, shielding
Institute steel and iron Japan Research Group activity ₍2014-2016₎,
Nippon Steel & Sumitomo Metal Co. JFE-Steel, Kobe steel, Daido steel
Y. Ikeda et al.: “Prospect for application of compact accelerator-based neutron source to neutron engineering diffraction”, Nucl. Instr. Meth. A 833(2016)pp61-67

## Slide 18: Volume fraction estimation with RANS engineering diffraction
retained austenite evaluation
Highly accurate agreement with measurements at the large facility (J-PARC) (only 1% or less difference)-
> Compact source has high potential to use on-site
9mm×10mm×9.5mm
Controlled samples produced
Y.Ikeda et al, Tetsu to Hagane vol.104, No.3 (2018) pp.18-24
J-PARC Takumi: 13.9％
Austenite：13.1%
TR2 full angle(300min,
current32μA)
→BCC peaks
→FCC peaks
The result of measurement during uniaxial rotation (30 min) for round robin sample is consistent with J-PARC measurement

## Slide 19: Realization of high resolution in a small size: Pulses are not shortened.
proton
sample
(A) Decoupled collimator system
(B)de-convolution analytical method
Deconvolution of delayed neutron components.
-> diffraction components-> peak fit
Neutron intensity doubled, and sharpness increased by 30%.
Stress measurement of around 130MPa can be measured.
Stresses can now be measured up to 130 MPa for practically relevant steel materials in RANS.
Notes: One of the recent results. Now at RANS, stress measurement of around 130MPa can be measured. The key technology which enable this stress measurement are two, one is decoupled collimator system, another
Stress measurement is made possible by two breakthrough developments One is the Decoupled Collimator system and the other as a data analysis method. Deconfovution The introduction of the De-convolution method as a data analysis method has enabled only the stress-related components to be extracted .Decoupled Collimator allows The black dots in the diagram on the right show the data obtained by narrowing the pulse width without reducing the peak intensity.

## Slide 20
Ib-SANS(Small Angle Neutron Scattering), Ibaraki Univ. Prof.S.Koizumi

## Slide 21
150mm
150mm
1
2
3
4
5
6
7
8
9
2
3
4
5
6
7
8
9
10mm
10mm
5mm
5mm
To have much lower q, Mesh Type Multi-pinhole （9x9）
Ib-SANS,Ibaraki Univ. Prof.S.Koizumi
Multi-pin-hole system has succeeded at RANS
Multi-pinhole
Mode-rator
Sample
2-Detector
Length 207cm
Vacuum

## Slide 22
Counting Efficiency： 1/1000 → 1/40
Converging Beam Device: Multi-pinholes （5x5） & (9x9)
発明名称：「中性子光学素子及び中性子源」 、出願番号：特願2017-140192
@ RIKEN RANS

## Slide 23
l = 10–1 A
Wave number q (A-1)
Intensity (cm-1)
Red circles by ib-SANS (1 hr)
Black line by iMATERIA (0.2 hr)
(2) Low-angle
Detector
(1) Small-angle
Detector
10
1
10-1
10-2
102
1
0.007
Small Angle Neutron Scattering experiment with RANS
Ib-SANS on SDS micelle solution with a cold source (before up-grade)
Developed by Prof.S.Koizumi, Ibaraki University
Differential Scattering Cross Section

## Slide 24: RANS-II: two function (Stational CANS)
Power | Neutron Yield @target | TMR shielding size | Distance from TM | Neutrons @ sample position | Acce. Duty
RANS 7MeV 700W | 1012 n s-1 | Volume：~ 8m3 weight～23ton | 1.5m | *105 n cm-2 s-1 | RANS 1.3% (RF Duty cycle)
 |  |  | 5m | *104 n cm-2s-1 Diffraction, ToF Imaging, | 
RANS-II 2.49MeV 250W | *1011 n s-1 | V~1m3 W~ 3.5ton | 0.5m | *104~105 n cm-2 s-1 | RANS-II 3% (RF Duty cycle)
 |  |  | 1.5m | *104 n cm-2 s-1 Diffraction etc. | 
・Standard Model of stational compact neutron system
・Accelerator- development: 2.49 MeV proton RFQ linac: Tokyo Inst.Tech.
・Li-Target: Sanki co. ( with QST,放医研)
・Proto-type of transportable compact neutron systems, same neutrons as RANS-III: All the development of detection tech. development

## Slide 25: Nondestructive test on site use need two ways; Stational system on floor, and transportable compact system
Neutron
Lower radiation level during operation
Easy to operate, and easy and safe for maintenance
Good S/N measurements for quantitative analysis ( No powerful source, but proper technology for compact source including shielding design, pulse structure, etc. )
As few as possible of activation products
RANS-II MODEL
Ｘ-ray, Electron,
SEM, TEM,EBSD
On-site non-destructive test
Transportable type
On-site non-destructive test
Floor-standing type
RANS-μ
Neutron Salt-meter
RANS-III MODEL
Notes: For on-site use, for example, the floor-standing type is intended to be used in the same way as electron microscopes and X-ray CT systems, while the transportable type is intended for outdoor use at bridge sites.
For this purpose. There are such requirements as 1….

## Slide 26
RANS challenge
to meet the needs for such non-destructive test with neutrons!
RIKEN Accelerator-driven compact Neutron Sources RANS
15m
5m
70cm
RANS: Research with neutron scattering at the institutes, universities, etc.
RANS-II: MODEL of non-destructive test instrument with neutrons on-site.
-> Hungarian case: PHOTO (from Prof. Dr. F.Mezei)
Now at RIKEN, Ex. Neutron CT instrument development is performing
RANS-III: Transportable neutron system out-side
RANS-μ: Neutron salt meter with bridge inspection vehicle
It will be appeared in 2023 with T-RANS activities
4m

## Slide 27: For the infrastructure preventive maintenance RANS-III: research and development RANS-μ: on-site use and up-grade development
USA I-70 Concrete bridge collapse
Dec. 2005 , 45 years after the construction Pennsylvania. Rebar corrosion because of ant freezing agent
Canada Collapse of a Portion of de la Concorde Overpass
Sept, 2006, 35 years after construction, Montreal
Initial construction failure
From：Pittsburg Post-Gazette
出典：落橋に関する委員会報告書
Message from Dr. Banthia to Japanese researchers:
The novel non-destructive test methods such as x-ray, electromagnetic induction method, elastic wave method.出典：六郷ら、カナダのデラコンコルド跨道橋の崩落事故に学ぶ、コンクリート工学,2008.12
From Mr. R.Ooishi (Institute Public Work)
Taiwan bridge collapse1 Oct. 2019）
Salt damage->bridges collapse
-> Salt density measurement
Degradation
-> Visualization of the water, air hole
Vigili del Fuoco/AFP
Italy ・Moradi bridge collapse
（14 Aug.2018. ）Salt damage
Notes: A number of severe and unpredictable bridge falls have so far occurred around the world.. Preventive maintenance, rather than the conventional after-the-fact maintenance that is carried out after cracks and other external damage have already started to occur, can extend service life. Non-destructive observation of the inside is essential for preventive maintenance, and expectations are high for neutrons.

## Slide 28
放射性同位元素等の規制に関する法律 第１０条 および 関連規定（平成１７年７月改定）Japanese regulation 4MeV>linac
  橋梁等の非破壊検査に用いる直線加速器で４メガ電子ボルト以上のエネルギーを有する放射線を発生しないものは、放射線発生装置の使用の場所の変更を都度許可を得る必要がなく届出で足りることとする。（ただし、設備については、事前に原子力規制委員会原子力規制庁の届け出許可が必要。）
  実行線量：（3か月で1.3mSv)
  労働安全衛生法令による管理区域
  人事院規則による管理区域
RANS:III: 2.49 MeV, Li target
Proton: the same energy, current
with RANS-II
・ECR ion source：Permanent magnet
・Frequency of proton linac 500MHz
RANS-III Transportable CANS (Compact Accelerator-driven Neutron system)
Japanese radiaton regulation: Using the linac, particle energy is smaller than 4MeV, accelerator-driven quantum beam can be used for non-destructive test for bridges (Act on Prevention of Radiation Hazards due to Radioisotopes, etc)
Dr T.Kobayashi 25th

## Slide 29: ECR ion source, proton linac for RANS-III
２.Proton 2,49MeV 100 μA (max. av.) 500MHz
Background: Already working on vibration, stable operation, etc. with RANS-II.
The centerpiece of further advancement! Downsizing and weight reduction of the RANS-II ion source and acceleration cavity!
１.ECR ion source development
：Neodymium magnet used
←No cooling required
Plasma chamber
with permanent magnet
Dr. Shota IKEDA
T.Kobayashi, SYujiro IKEDA, M. Okamura
Three-body copper construction: compact, lightweight, vibration-resistant screw-on only

## Slide 30
 | RANS-Ⅱ RFQ | RANS-Ⅲ RFQ
Resonant frequency [MHz] | 200 | 500
Input beam energy [keV] | 35[keV] | 30[keV]
Output beam energy [MeV] | 2.49[MeV] | 2.49[MeV]
Peak beam current [mA] | ≦10.45 | ≦10.2
MAX Duty cycle [%] | 3.3 | 3.0
Average beam current [µA] | 100 | 100
Power loss [kW, 80%Q] | 192 | 275
Unloaded Q | 11750 | 8730
Cavity length [mm] | 2555 | 2370
Cavity diameter [mm] | ~540 | ~300
Cavity weight [t] | 3 | 0.7
2370 mm
300 mm
330 mm
2, Optimized cavity parameter
Cavity parameter of
RANS-Ⅱ RFQ and RANS-Ⅲ RFQ
RANS-III.Proton 2.49MeV 100 μA (max. av.) 500MHz
Dr.Shota Ikeda, Prof.N.Hayashizaki,
Dr. Okamura, Dr.T.Kobayashi
200MHz-> 500MHz
Higher RF frequency for lighter and smaller acceleration cavities
Width
54㎝(RANS-II)⇒33㎝( RANS-III)

## Slide 31: Acceleration test: success in-door RANS-III
500MHz proton accelerator.
Ion source + acceleration (500MHz) Successful indoor acceleration
Dr. Shota IKEDA
T.Kobayashi, SYujiro IKEDA, M. Okamura
Performed accelerated testing at low radiation doses.E < 2.5 MeV in a room without radiation controlled area designation,

## Slide 32: RANS-III Recent development
Proton Acc system and target shielding system are installed in the trailer.
2.49 MeV proton acceleration test is running.
In 2025, neutron experiment will start in new building
2.49 MeV proton Li (p,n) the same as RANS-II
Proton Accelerator +Magnet
Target + Shielding system

## Slide 33: RANS-III non-destructive measurement technology is under development based on high demand from the society
Deterioration Visualization Method
Depth [cm]
Dl density
[kg/m3]
0 surface）
5
10
5
Distribution of salt
cable-stayed bridge anchorage deterioration （High way companies）
Fast neutron scattering ToF imaging method
NEXCO中日本との共同研究
Visualization of floor slab deterioration, sheath grout unfilled areas
1H
ガンマ線エネルギー (keV)
ガンマ線強度
56Fe
28Si
28Si
35Cl
35Cl
35Cl
27Al
1165keV
1951keV
1959keV
6111keV
Concrete internal elemental analysis of PGNAA
40Ca
High sensitibitiy for Cl
Salt damage
Prevention of rupture accidents due to internal steel corrosion caused by salt damage → measurement of internal salt concentration
PGNAA method

## Slide 34: Fast neutron scattering (back scattering) time of flight imaging method to meet the needs for the visualization of the floor slab deteorisation
Fast neutron is inserted
→Select the timing, and the energy according to the materials to be visualized
→water, or air hole (gap) in the second layer
Get 2D non-destructive imaging under the first layer

## Slide 35
Fast neutron scattering imaging with time of flight method (New Tech.) (Back scattering imaging technology)
Fast neutron is inserted（100keV~*MeV) injected
→Select the timing, and the energy according to the materials to be visualized
→water, or air hole (gap) in the second layer
Get 2D non-destructive imaging under the first layer
detector
reflected
Water, airgap, rebar, etc.
detector
reflected
Timing to detect
50μs<t<1ms
Energy to detect
E<150 meV
Back scattered imaging
=Scattered imaging
Simulation study to optimize the energy and the timing for the vilialisation at the surface

## Slide 36
Neutrons increase 4~8 times
Void, decrease 20~40%
Healthy condition
Timing(TOF), energy, intensity ratio
-> Non-destructive inspection inside concrete degradation
Degradation：water
N
concrete void
Back scattered neutron imaging method: Results
Enin>fast neutron

## Slide 37
Asphart
Concrete
RC floor slab
RC floor slab
300
単位: mm
中性子ビーム
Steel bar
75
70
60
70
1
2
3
4
Dry sedimentation(30mm)
300 0 -300
300 0 -300
y(mm)
y(mm)
1.2 1.1 1 0.9
150
0
-150
1.2 1.1 1 0.9
x(mm)
Beam spot
損傷部
ratio
ratio
Water (5mm)
Comparison between the fast and slow detection timing enables to distinguish the water+ degradation from other degradation
Detection timing
100＜t<600μs
RANS-II Visualization of degradation: sedimentation
degradation
degradation
N -beam
N –beam spot
Water
Moisture degradation
Dry degradation
Water + degradation
Water
Moisture degradation
Dry degradation
Water + degradation
Negative peak
= Water+ degradation
Detection timing
40＜t<100μs
Positive peak
= Water+ degradation
Fast Neutron Beam
N
Detector

## Slide 38
中性子検出器
To prevent bridge collapse accident: corrosion Visualization of stagnant water at the suspension bridge cable anchorage ⇒RANS-II experiment
NEXCONaka nihon：Collaboration
Photo of Meiko-Higashi oohashi：名港東大橋
Dr T.Fukuchi 25th

## Slide 39: Development of new detection techniques: from scattering cross sections of neutrons with energies from 500 KeV to 1 MeV
Fast neutrons are scattered.
H of the water, and the corrosion decelerate the neutrons
-> can be detected with ToF tech.
JENDL 4.0
To detect 1% water (hydrogen) inside iron with a diameter of 10 cm or more.
100 KeV to 1 MeV

## Slide 40: Visualization of water at the suspension bridge cable anchorage ⇒RANS-II experiments towards RANS-III
Neutron beam injected from the end of Anchorage.
Thin water detected by backscattered neutrons
Depth of the inside water: 10㎜、3㎜、1㎜
Volum: 100％、50％ 33％
Detector
Neutron
Anchorage

## Slide 41: Visualization of water at the suspension bridge cable anchorage ⇒RANS-II experiments towards RANS-III
Neutron beam injected aside of the cable ancholrage reason from road level is considered.

## Slide 42
Neutron Application Facility North building
Neutron irradiation experiments indoors under the same conditions as outdoors.
Neutron experiments RANS-III: Need the new building Required to obtain a radiation permit for outdoor use

## Slide 43: Urgent Non-destructive test with neutrons：RANS-μ（Ready to use）and RANS-III
1H
ガンマ線エネルギー (keV)
ガンマ線強度
56Fe
28Si
28Si
35Cl
35Cl
35Cl
27Al
1165keV
1951keV
1959keV
6111keV
Elemental analysis insice concrete
40Ca
High sensitivity for Cl.
計測結果概念図
depth[cm]
Cl density [kg/m3]
0 （surface）
5
10
5
Distribution Cl
Neutron Salt-meter： Salt distribution according to the depth until 7cm: for preventive maintenance
Salt density:
Detection limit, 1.0Kg/m3 3cm
土砂化
入射ビーム
アスファルト
コンクリート
散乱中性子
Floor slab degradation
乾燥土砂化
滞水土砂化
Visualization of degradation
Wet sedimentation
Indicated by the increase of scattered neutron
dry sedimentation
Chart: 土砂化厚さ [mm]
| 10 | 40 | 60
滞水している土砂化 | 3.7907 | 6.6289 | 10.86
乾燥している土砂化 | -3.9878 | -7.4942
Sedimentation criteria
On-site use

## Slide 44: RIKEN's RANS Project Challenges for Social Implementation of Compact Neutron Systems
Toward Practical Application of RANS-III in Outdoor Use
development and practical application of RANS-μ (RANS-micro, not “mu”),
commercialization of RANS-μ RANS-VIEW (sponsorship UCANS),
development of legislation and social implementation for the use of compact neutron systems in bridges for the approach to the Ministry of Land, Infrastructure, Transport and Tourism (MLIT) and for the spread of the use of compact neutron sources on-site

## Slide 45
Minimum Cl detection should be 1.0±0.2 kg/m3 at 7cm depth from the concrete surface
・Non-destructive measurement
Urgent issue: Salt damage
RANS-m Neutron salt meter： Non-destructive measurement of salt density distribution near the steel
Cf &
Reflector and
Shield
Concrete
g ray
Steel bar
(corrosion)
Cl measurement by RANS-m
Neutron distribution in the concrete
3～7cm
Ge γ-detector
Neutron
Objectives: Salt density non-destructive detection
Salt above 1.2 kg/m3 initiates steel corrosion.
Steel corrosion progresses to the point of rupture, causing the bridge to collapse.
To prevent the bridge collapse and for preventive maintenance
45
Dr.Y.Wakabayashi 27th

## Slide 46: RANS－μ is now listed in the catalog of the Ministry of Land, Infrastructure, Transport, and Tourism on 31 March 2023
RANS VIEW, the company established April 2023 based on the T-RANS (Technological Associate for neutron next generation system) and RIKEN
The content is updated annually by T-RANS.

## Slide 47: T-RANS and Rans View Corporation
Establishment of T-RANS Technology Research Association for Neutron Next Generation System Licensed by MILT (September 1, 2020) :
18 Companies+2 Academia (2025)
Corporate philosophy：Standardization of neutron non-destructive inspection technology.
・MILT Catalog Update
・RANS-µ Certified Metrologist
・Standardized walk-in price release (price standardization)
Establishment of Rans View Corporation (April 3, 2023)
Measurement services using non-destructive testing technology
Research and development, sales and rental of non-destructive testing equipment
Consulting using non-destructive testing technology
Numerical analysis and software development associated with non-destructive testing technology

## Slide 48
RIKEN Accelerator-driven compact Neutron sourcesRANS,RANS2, 3, μ
Compact Neutron
RANS：15m, 25ton MeV～meV
Anytime, anywhere
RANS-III
Non-destructive visualization
Visualization of the bonding interface and joints of multi-material, corrosion and its related water movement of the painted steel
PGAA Salt detection of concrete
Element analysis on site
Diffractometer volume fraction, texture evaluation, stress
Non-destructive inspection; infrastructure
retained austenite fraction measurement
Texture evolution
In the pavement： back-scattered imaging
JAXA Satellite 1
Salt distribution
Visualization of water movement of the concrete
Ib-SANS, Ibaraki Univ.
Phase contrast, Tohoku Univ.
Towards stress measurement, 130 M Pa
RANS-II：~5m
E=800keV～meV

## Slide 49: Thank you for your kind attention!!!