## Slide 1: The High-Brilliance Neutron Source Project
Paul Zakalek, JCNS
HEREON
TUM
IKP
ZEA
JCNS
CEA

## Slide 2
Accelerator Based Neutron Sources
From CANS* to HiCANS**
0.01 kW | 0.1 kW | 1 kW | 10 kW | 100 kW
0.001-0.01 mA | 0.01-1 mA | 0.5-5 mA | 1-20 mA | 50-100 mA
~1011 n/s | ~1012 n/s | ~1013 n/s | ~1014 n/s | ~1015 n/s
10 Mio EUR 500 Mio EUR
Running CANS facilities:
LENS, Indiana University (USA)
HUNS, Hokaido University (Japan)
RANS, RIKEN (Japan)
NUANS, Nagoya University (Japan)
CPHS, Tsinghua University (China)
IREN, JINR Dubna (Russia)
(*Compact Accelerator based Neutron Source , ** High-Current Accelerator based Neutron Source)
HiCANS projects:
HBS, JCNS (Germany)
ICONE, CEA LLB (France)
ARGITU, ESS Bilbao (Spain)
SARAF, SOREQ (Israel)
Notes: 2

## Slide 3
Every beam port serves only 1 Instrument
Optimize neutron source spectrum
Several target stations
Optimize pulse structure (length, rep. rate)
Optimize geometry
Integrate neutron optics with beam port
Optimize thermal spectrum
Small shielding
Neutron guide around cold source
Chopper at <2 m from target
High current linear accelerator
100 mA, 70 MeV pulsed proton beam
Variable frequency
Project rationale
HBS, a High-Current Accelerator-driven Neutron Source (HiCANS)

## Slide 4: HBS Technical Design Report
https://go.fzj.de/hbs-tdr
Project Published summer 2023
Notes: We published a TDR about the accelerator with our partners at IAP Frankfurt, who are accelerator experts. We worked on the target station and the moderators, the instrumentation with the contribution of many external experts and the TDR about infrastructure and sustainability. If anyone is interested, I would highly recommend the summery of all volumes.

## Slide 5
Efficient and sustainable neutron production
https://doi.org/10.1016/j.ppnp.2025.104163
Notes: On the left hand side, you see the primary neutron spectra of all three processes. You can see, that the spectrum for a HiCANS is around 3 orders lower than for spallation and fission. But the spectrum is also much softer, you have much less high energy neutrons and also the mean energy is lower than for the other processes.
Due to this soft energy spectrum it is thus possible to built quite small target stations in comparision to reactors and especially to spallation sources. They are therefore much cheaper, reducing the cost of a facility significantly. The inner Target-moderator-structure is due to the lower energies and fluxes also very compact allowing a very efficient chain of neutron production, moderation and extraction. HiCANS are therefore efficient and sustainable neutron sources.
HiCANS, are competitive to other sources, as seen on the right side. The average extractable brightness is similar ot higher than ISIS or PSI and the peak brightness is above PSI, HZB and can be similar to LLB and MLZ.

## Slide 6
Every beam port serves only 1 Instrument
Optimize neutron source spectrum
Several target stations
Optimize pulse structure (length, rep. rate)
Optimize geometry
Integrate neutron optics with beam port
Optimize thermal spectrum
Small shielding
Neutron guide around cold source
Chopper at <2 m from target
High current linear accelerator
100 mA, 70 MeV pulsed proton beam
Variable frequency
Project rationale
HBS, a High-Current Accelerator-driven Neutron Source (HiCANS)
https://go.fzj.de/hbs-tdr

## Slide 7
COSY Facility
2.7 GeV proton 2.1 GeV deuteron
Big Karl
45 MeV proton 76 MeV deuteron
~ 10 nA
~ 1 nA
Free pulse structure
Large experimental space
Flight paths of up to 7 m
~ 10 nA
JULIC Neutron Platform

## Slide 8
Experimental Platform at Big Karl @ COSY
HBS Target-Moderator-Reflector Unit
HEREON
TUM
IKP
ZEA
JCNS
CEA
Reflectometry
Imaging
Detector tests
Moderator tests
Notes: Wedge shaped target within moderator
Cold “finger moderator”
Direct coupled neutron optics

## Slide 9
- Time-of-Flight (ToF) imaging proof of concept at 1m to source successful.
- High signal to noise despite proximity to target.
- Using an event counting detector, images with good counting statistics at ~250um resolution in tenth of minutes already possible.
- Due to short distance to source, energy resolution is low but sufficient for e.g. hydrogen quantification or general qualitative isotopic analysis via ToF.
115 mm
Radiograph of a Cactus
(not normalized atten.)
Epithermal Neutron Radiograph
Thermal Neutron Radiograph
115 mm
115 mm
Contribution from:
Adrian Lasko (TUM) Alexander Wolfertz (TUM)
Richi Kumar (HEREON)
Imaging measurements with ~30 neutrons/cm2/s
HBS Imaging Test Highlights (MLZ imaging group)

## Slide 10: HBS – Phase I
First stage of HBS
Facility parameters
  First stage of accelerator: 20 MeV
  1 target station
  20 kW average power
  Neutron yield of 1014 n/s
  5 Instruments: Reflectometer, diffractometer, SANS, imaging, PGNAA
Application for national prioritization of RIS
  106 M€ Investment
  6 M€ Anual operation cost
Notes: We published a TDR about the accelerator with our partners at IAP Frankfurt, who are accelerator experts. We worked on the target station and the moderators, the instrumentation with the contribution of many external experts and the TDR about infrastructure and sustainability. If anyone is interested, I would highly recommend the summery of all volumes.

## Slide 11
HBS – Phase I
COSY Facility shutdown 2024
Large available space ~ 25 x 30 m2
Controlled area with sufficient shielding
Can house HBS Phase I facility

## Slide 12
HBS – Phase I
Average power: 40 kW
Proton energy: 20 MeV
Duty cycle: 2% to 4%
Proton pulse current: up to 100 mA
Accelerator
Neutron yield: ~ 5*1013 n/s
Frequencies: 24 - 96 Hz
Typ. neutron pulse length: 0.2 ms (96 Hz),
1.2 ms (24 Hz)
Thermal moderator: H2O
Cold moderators: H2, CH4
Target station for 5 instruments

## Slide 13
Instrumentation
HBS – Phase I
Technical Data:
Moderator: H2
d-spacing range: 0.005 Å-1 < Q < 1 Å-1
Wavelength band: 2.5 Å < λ < 20 Å
Flux at sample: 8.5·105 n/(cm²s)
Length: < 18 m
Detector coverage: 1 m²
Technical Data:
Moderator: H2 moderator
Wavelength band: 2 – 15 Å
Q range: 0.001 – 1 Å
Resolution: 10% – 15%
Flux at sample: 5·105 n/(cm²s)
Length: 13 m
Poster for all instruments

## Slide 14
HiCANS Projects in Europe
ARGITU
ICONE
HBS
HBS (JCNS)
Expertise: Target & Moderators, Instrumentation
Available components: Target Station, Ta Target
ICONE (LLB)
Expertise: Target, Instrumentation
Available components: Instruments (HERMES), Be Target
ARGITU (ESS Bilbao)
Expertise: Target, Accelerator
Available components: Ion source, 3 MeV RFQ, Building
Joint forces between JCNS, LLB, ESS Bilbao
Complete facility

## Slide 15
HiCANS Neutron Platform at ESS Bilbao

## Slide 16
HiCANS Neutron Platform at ESS Bilbao

## Slide 17
HiCANS Neutron Platform at ESS Bilbao
HBS-I
20
100
0,4 - 2
24 - 96
2 - 4
20 - 40
~3E+13
HBS-II
70
100
0,16 – 0,67
24, 96
1,6
100
~E+15

## Slide 18
TDR Finished
HBS
2023
2024
2025
202X
2026
JULIC Neutron Platform
HiCANS Neutron Platform Setup at ESS Bilbao
National Roadmap Application
Decision on National Roadmap
202X+5
HBS-I Construction
203X
HBS-II Upgrade
Funding for HBS-I

## Slide 19
HBS Vision
A healthy landscape
of large and small
neutron sources
complementing
each other
The Landscape 2000
Thank you for your attention.