## Slide 1: The French ICONE Instruments Suite
Alain MENELLE in replacement of Xavier Fabrèges
Alexis Chennevière, Arnaud Desmedt Nicolas Pichoff (ICONE project leader)
Laboratoire Léon Brillouin Iramis
CEA Saclay, France CEA Saclay, France

## Slide 2: What is the ICONE French project ?
A project to provide France with a national neutron scattering user facility for the next 50 years
Able to do similar experiments than what was done on the Orphée reactor (shutdown end of 2019)
Able to do any type of neutron scattering experiment
Able to provide an experimental capacity of about 300 experiments per year open to users
Able to train and prepare the French community for the use of ESS with the best possible efficiency
Reach these goals within a limited budget
Do it without the construction of a new nuclear reactor
Do it with available technologies in France
ICONE
Innovative COmpact NEutron facility

## Slide 3: The ICONE HiCANS project
Technical solution proposed
Not a reactor : build an accelerator based neutron source
Limited budget : use a low energy accelerator (25 MeV for low cost, low activation)
Orphée performances : Be target and high peak current (80 mA), compact design
Capacity of 300 experiments/year : 2 targets, 5/6 instruments per target, 200 beam days / year
Thermal (water) and cold liquid H2 moderators
https://icone-neutron.fr

## Slide 4: TMR assembly geometry
protons
neutrons
Illumination over 45°
Cold cell insert
Insertion / extraction from the « back »
è No interference with the guide / chopper system

## Slide 5: Within a European momentum
ARGITU@Bilbao
High Brillant Source HBS@Julich
ICONE@Saclay
Proton: 32mA, 31.5MeV
Single proton pulse
1 target
3 instruments
Brilliance@2.2Å: ~5.1011 n/cm2/s/Å/sr
~15M€
Proton: 80mA, 25MeV
Multiplexed proton beam
2 targets
10-12 instruments
Brilliance@2.2Å: ~1012 n/cm2/s/Å/sr
~150M€
Proton: 100mA, 70MeV
3 targets
23 instruments
Brilliance@2.2Å: ~1013 n/cm2/s/Å/sr
~500M€
LLB, JCNS, ESS-B agreement on HiCANS development

## Slide 6: Scientific case supporting the project
Be able to address societal challenges
Health
  Medicine vectorization studied by SANS
  New drugs characterization by diffraction
Energy
  Fuel cells operations improvement by life imaging
  Better diffusion in batteries with quasi-elastic scattering
  Hydrogen storage with neutron diffraction
  High Tc superconductors with inelastic scattering
  Improved metallurgy with strain scanner and texture determination
Information technology
  Development and understanding of new quantum materials
Climate
  Studies of clathrates stability by diffraction and inelastic scattering

## Slide 7: The Icone instrument suite
Provide users with all necessary neutrons scattering techniques
Diffraction (high resolution / high flux, powder and single crystal)
SANS (multipurpose) and VSANS
Reflectivity
Technological diffractometer (Texture, strain scanner)
Inelastic spectrometer (direct or indirect geometry)
Quasi-elastic spectrometers
Imaging : complementary to SANS
PGAA : elemental analysis technique
Test beam line for technical developments

## Slide 8: Flux available
A comparison to known and future neutron sources
Roughly speaking
ICONE will be between Orphée and PSI
(*) Recent improvement in moderator design to provide a bispectral distribution of flux at ICONE
(peak flux for pulsed sources)

## Slide 9: PRESTO our first powder diffractometer
Low cost powder diffractometer with re-use of 7C2 detector
Large 3He position sensitive multitube detector (256 tubes, diam. 1.25 cm, length 50 cm, 30 bars)
Position resolution improved by adding more Mesytec electronics in order to provide some SANS capabilities
1st chopper as close as possible to the target to be able to adapt resolution
7C2 Detector

## Slide 10: PRESTO detailed parameters
Instrument | PRESTO
𝜆min | 0.6 Å
𝜆max | 6 Å
Δ𝜆 | 2 Å
𝛿𝜆/𝜆 min | 1 %
𝛿𝜆/𝜆 max | 10 %
Sample size | 10x20 mm (WxH)
distance | 30 m
frequence | 50 Hz
Pulse width | 400 μs
duty cycle | 2 %
Δ𝜆 | 3.3 Å
𝛿𝜆/𝜆 min | 0.9 %
𝛿𝜆/𝜆 max | 8.8 %
Moderator : 20x50 mm (WxH)
Cold spectrum centered at 60 K (~2.6 A)
Detector
  133°x26° angular coverage
  256 tubes, 128 pixels
400 µs @ 40 Hz (HR)
Flux: 1.4x107 n/s/cm2 at sample
Incident divergency : +- 0.5°
- Sample volume : 2 cm3

## Slide 11: PRESTO calculated performances
Same resolution and 70 times faster than G41 on Orphée
G4.1
PRESTO
λ (Å)
1.8 2.17 2.54 2.91 3.27 3.63
Na2Ca3Al2F14 spectra, measured on G41 and calculated on PRESTO. Both spectra show similar resolution. PRESTO spectrum has been divided by 70 for proper resolution comparison.

## Slide 12: SAMBA : a SANS instrument
Requirements :
    Q range = 0.002 to 0.6 Å-1
    Smaller than 20 m
    0.1 < dQ/Q < 0.5
Reference apparatus :
    PAXY (Orphée, LLB)
    SAM (ILL)
    SANS_LLB (SINQ, PSI)
A. Chennevière@LLB

## Slide 13: HERMES the horizontal reflectometer
Total length: 10 m, High-flux target. 10 nm Ni thin film deposited on Si substrate
2.17 x 106 n/s/cm2
Side view
2° x 0.08°
20 mn measurement
BG = 5%
1.00 x 107 n/s/cm2
Top view
Sample / det. distance = 2 m
Orphée reference design
On ICONE
Convergence criteria

## Slide 14: INEDIT : direct geometry inelastic spectrometer
PSC
SC0
SC1
SC2
115°
Choppers cascade
𝝀1
𝝀4
115° x 30°
337 tubes
Sample to detector : 2.5 m
Moderator to sample: 40 m
Resolution
Wavelength range
Anti-overlap
50 Hz
WFM 200 Hz
40 m

## Slide 15: INEDIT : resolution and Q range
On the detector
(Q,E) accessible
σ3A = 0.40 meV FWHM
σ4A = 0.24 meV FWHM
σ5A = 0.13 meV FWHM
Fit by pseudo-voigt
Lorentzian: reference
Gaussian: instrument
Suited for diffusion coefficient measurements (soft mater)

## Slide 16: FANTASTIC : spectrometer in indirect geometry
sample
20x10 mm
Shielding between sector (cross-talk)
    30 movable analyzors
    120 ° horizontal coverage
    1.0 < kf < 2.4
  60 tubes of 3He at 15 bars
  0.75" x 22" (from 5C1)
2𝜃ana = 50°
2.8 A
2𝜃ana = 120°
5.8 A
Incident white beam
HR target at 50 Hz
Sample
BIFROST like

## Slide 17: FANTASTIC : resolution and Q range
(Q,E) accessible
30 counts/sec expected
σinst = 0.4 meV
Phonons and magnons measurements (hard matter)

## Slide 18: Possible layout for ICONE Phase 1 2032
40m
20m
PRESTO
FANTASTIC
SAMBA
HERMES
IMAGING
TEST
GUIDE HALL
9° between guides
Target casemate
Target monolith

## Slide 19: Thank you

## Slide 20: SPARE1
Detailed specifications of ICONE
SOURCES requirements | High Flux | High Resolution
Energy p+ [MeV] | 25 | 
Peak Intensity p+ [mA] | 80 | 
Pulse Duration [ms] (Rate [Hz]) | 0.8(50) - 2(20) | 0.2 (100) - 0.4(50)
Duty Cycle | 4% | 2%
Average Flow p+ [/s] | ~2 1016 | ~1016
Average Flow nfast [/s] | ~4 1014 | ~2 1014
Average Flow nu [/s/cm2/sr] | ~4 1010 | ~2 1010
Neutron beam ports | 5+2 | 5+2
nu : useful neutrons (<100 meV i.e. >0.9 Å)
Pulse
Time
High resolution pulse
High flux pulse
Flexible pulse rate and duration

## Slide 21: SPARE2
ICONE current possible layout

## Slide 22: SPARE3
Estimate the lambda dependance of the thermal and cold spectra
NOTA : at JNP, Mariano mesured this (on the JCNS moderators PE Vs pH2) Beware, there was a m=1.5 guide between the moderators and the detector

## Slide 23: SPARE4 : Target
Various type of Be plates
Tested 100h at 3MeV >25kW