## Slide 1: Beyond the BeEST: SALER
Andrew Marino
Colorado School of Mines
Electroweak Interactions Group
BeEST Collaboration Meeting 2025
FRIB
Notes: Slide numbers are helpful
Reference Keith and Caitlyn's talks

## Slide 2: Background Status Current Work: Taking beam this year!
Andrew Marino
BeEST Collaboration 2025
Beyond the BeEST

## Slide 3
Nuclear Recoil Spectroscopy with Short-Lived Radioisotopes
Andrew Marino
BeEST Collaboration 2025
Beyond the BeEST
BeEST: Excellent demonstration of nuclear recoil spectroscopy with STJs
Implantation into room temperature STJs limits applications to long-lived isotopes, T1/2 ⪆ 10 days
SALER: Bringing a cryostat to a rare isotope beam allows isotopes with T1/2 ⪆ 100 ms
SALER couples cold STJs directly
to the ReA3 beamline at FRIB
7Be: T1/2 ≈ 53 days
19Ne (simulated): T1/2 ≈ 17 seconds
Notes: Precision beta decay sensitive to new physics via things like beta-nu correlations, but doing traditional beta spectroscopy at this level is difficult due to the precision required
Recoil spectroscopy is still sensitive to these physics, but is typically very hard to do because the low energies involved typically require slower sensors which limit the possible rate
For example, if you wanted to look at the decay of 11C for a determination of V_ud, you would have a recoil endpoint of less than 100 eV!
New quantum sensors now exist that allow access to these low energies with fantastic resolution and maximum rate: superconducting tunnel junctions
The BeEST experiment is pioneering the use of STJs for "long-lived" (53 day halflife) isotopes as Spencer just told us about, but to do these new experiments require looking at things with much shorter half-lives
To that end, the SALER experiment will run STJs coupled directly to a rare isotope beam at FRIB
Read less of text: will also save time
STJs aren't new, this is a new application
Possibly need to delete some stuff from here because I don't plan to discuss it
Words can be said instead of printed
Recoil spectroscopy is hard because of <reasons> and interesting because of <reasons>, and we can potentially do it
Precision beta decay is sensitive to TeV-scale physics via
CKM unitarity (Vud)
Angular correlations (exotic S, T)
But e+- spectroscopy challenging
Recoil spectroscopy sensitive to both, but typically inaccessible because of energy (<keV) and statistics/rate (<0.1%)
Quantum sensors with great resolution and speed new opportunities @RIB

## Slide 4
Nuclear Recoil Spectroscopy with Short-Lived Radioisotopes
Precision beta decay is sensitive to TeV-scale physics, but e+/- spectroscopy challenging
Angular correlations are accessible through average momentum sharing with the nucleus
Many other possibilities with exotic isotopes!
Talk to me, Kyle, or Leendert later if you have ideas
Andrew Marino
BeEST Collaboration 2025
Beyond the BeEST
Notes: Precision beta decay sensitive to new physics via things like beta-nu correlations, but doing traditional beta spectroscopy at this level is difficult due to the precision required
Recoil spectroscopy is still sensitive to these physics, but is typically very hard to do because the low energies involved typically require slower sensors which limit the possible rate
For example, if you wanted to look at the decay of 11C for a determination of V_ud, you would have a recoil endpoint of less than 100 eV!
New quantum sensors now exist that allow access to these low energies with fantastic resolution and maximum rate: superconducting tunnel junctions
The BeEST experiment is pioneering the use of STJs for "long-lived" (53 day halflife) isotopes as Spencer just told us about, but to do these new experiments require looking at things with much shorter half-lives
To that end, the SALER experiment will run STJs coupled directly to a rare isotope beam at FRIB
Read less of text: will also save time
STJs aren't new, this is a new application
Possibly need to delete some stuff from here because I don't plan to discuss it
Words can be said instead of printed
Recoil spectroscopy is hard because of <reasons> and interesting because of <reasons>, and we can potentially do it
Precision beta decay is sensitive to TeV-scale physics via
CKM unitarity (Vud)
Angular correlations (exotic S, T)
But e+- spectroscopy challenging
Recoil spectroscopy sensitive to both, but typically inaccessible because of energy (<keV) and statistics/rate (<0.1%)
Quantum sensors with great resolution and speed new opportunities @RIB

## Slide 5: Background Status Current Work
Andrew Marino
BeEST Collaboration 2025
Beyond the BeEST

## Slide 6: SALER@FRIB
Andrew Marino
BeEST Collaboration 2025
Beyond the BeEST
Notes: STAR Cryoelectronics adiabatic demagnetization refrigerator (ADR)
XIA 128-channel low-noise preamplifier
< 0.8 pA/√Hz
⇒ Up to 128 superconducting tunnel junction (STJ) sensors on-line at FRIB
262 nm pulsed UV calibration laser (4.73 eV)
X-ray tube for fluorescence (≤15 keV)

## Slide 7: ADR Performance
Magnetic cycle: Base temperature 38 mK!
Hold time: > 3 days
Andrew Marino
BeEST Collaboration 2025
Beyond the BeEST
Notes: After assembly, we cooled down the fridge
It took roughly 18 hours to go from room temperature down to operation
The stages are named based on their analogues in a dil fridge, so the actual numbers are not quite as claimed:
  50K actually reaches 33K, other stages reach 2.8-3K depending on coupling to pulse tube
Then performed a number of magnetic cycles, which leave the 50K and 4K stage unchanged and send the 1K and 50 mK to 0.42 K and 38 mK respectively
Swap axes on magnetic cycle plot

## Slide 8: STJs at FRIB
Andrew Marino
BeEST Collaboration 2025
Beyond the BeEST
Notes: SALER supports up to:
128 shared-ground STJs
64 separate-ground STJs
ADR equipped with cold finger to minimize ion beam dispersion
1 Amp STJ magnet
Mu-metal magnetic shielding

## Slide 9: Laser commissioning
Andrew Marino
BeEST Collaboration 2025
Beyond the BeEST

## Slide 10: Resolution: March 2025
Andrew Marino
BeEST Collaboration 2025
Beyond the BeEST
Evenly spaced peaks at 4.73 eV
~80% of STJs could resolve peaks
Resolution 2-4 eV FWHM

## Slide 11: Background Status Current Work
Andrew Marino
BeEST Collaboration 2025
Beyond the BeEST

## Slide 12: Laser integration
Andrew Marino
BeEST Collaboration 2025
Beyond the BeEST
Custom nanostructure thin films, 100-200 nm thick
Simulations show ~104x reduction in IR transmission
>50% transmission of UV laser
50 K
4 K
0.1 K
Laser
Ion beam
Similar prior work*
*Shiki et al., https://iopscience.iop.org/article/10.1143/JJAP.47.3682/pdf

## Slide 13: Magnetic shielding
Andrew Marino
BeEST Collaboration 2025
Beyond the BeEST
Hole open:
High leakage current,
Many Fiske modes
Hole covered:
Almost no leakage current,
Suppressed Fiske modes

## Slide 14
Andrew Marino
BeEST Collaboration 2025
Beyond the BeEST
Proof of concept at Mines
Magnetic shutter
No shutter
Shutter adjacent
Ansys simulations courtesy of Grace Wagner
STJs
STJs
Field direction

## Slide 15: X-ray tube
Andrew Marino
BeEST Collaboration 2025
Beyond the BeEST
Enables calibration with high-energy fluorescence lines
Allows use of lower-resolution STJs
LLNL X-ray tube, Ta STJ
277 eV
392 eV
525 eV
705 eV

## Slide 16: Conclusion and outlook
ADR/STJ commissioning complete as of March
Final laser, x-ray tube, and shielding in progress but not required for beam
Stable beam commissioning planned for late 2025!
Radioactive beam planned for 2026
Andrew Marino
BeEST Collaboration 2025
Beyond the BeEST

## Slide 18
Superconducting Tunnel Junction (STJ) Quantum Sensing
Two superconducting electrodes separated by a thin insulating tunnel barrier
meV "bandgap" 1 eV resolution
Up to 10 kBq/detector!
Recoil
50 mm
Andrew Marino
BeEST Collaboration 2025
Beyond the BeEST
Notes: This is mostly a status update talk, but I would be remiss if I didn't describe quickly what STJs are and why they're so great
They consist of 2 superconducting electrodes separated by a thin insulating tunnel barrier and operate similar to a semiconductor detector
The electrodes are held at a roughly 100 uV bias and deposited energy (such as a nuclear recoil) break the superconducting ground state analogous to moving electrons from a valence -> conduction band in a semiconductor with a gap 1000x smaller: typically millielectronvolts
The liberated electrons tunnel back and forth across the barrier and can be read out as a current proportional to deposited energy
Quick rise/recombination times allow for rates of up to 10 kBq/pixel, and these are easily scalable into arrays
Too busy, too many words
Remove first bullet and probably second
"imagine a semiconductor detector with 1000x smaller gap"
Pick one of diagram-style figures to pick and photo
Connor would probably remove bottom left and bottom right
Maybe blow up photo of whole array amd focus on what is important for this project: specific properties relevant to FRIB: fast detector with eV scale resolution of nuclear recoil from RIB which nobody else can do in an array