## Slide 1
Optomechanical sensing
D. Moore, Yale
BeEST Collaboration Meeting, TRIUMF
2025/05/15
David Moore
Yale University

## Slide 2
Photographs of trapped nano/micro particles at Yale:
Levitated nanoparticles
D. Moore, Yale
Nano- to micro-sized dielectric masses can be optically trapped with ~100 mW of laser power
Levitated masses are isolated both electrically and thermally
Reaching “standard quantum limit”, where the measurement itself provides the dominant noise
  Force sensitivities at the zN level and acceleration sensitivities near a nano-g
Highly focused tweezers (~0.1 – 1𝜇m):
Levitation trap
(~1 – 30 𝜇m):
~1 fg – 1 pg
~1 pg – 30 ng
Particle mass
fg
pg
ng
Force sensitivity [N/]
Accel. sensitivity [g/]
10-21
10-20
10-19
10-8
10-7
10-6
Force and acceleration sensitivity vs particle mass:

## Slide 3
Nuclear decays in mechanical sensors
D. Moore, Yale
Auger e-
x-rays
EC decay
decay
10 m sphere
10 MeV/c = 5x10-21Ns
100 nm sphere
10 keV/c = 5x10-24 Ns
Particle trajectory (quantum harmonic oscillator):
Magrini et al., Nature 595, 373 (2021)
Tebbenjohanns et al., Nature 595, 378 (2021)
See, e.g.:
Example force measurements for nuclear decay:
Levitated sensors are now reaching sufficient sensitivity to detect the miniscule forces imparted by single sub-atomic particles
  For weak decays, allows the momentum of each neutrino to be reconstructed on an event-by-event basis
D. Carney, K. Leach, and DCM, “Searches for massive neutrinos with mechanical quantum sensors,” PRX Quantum 4, 010315 (2023) arXiv:2207.05883
J. Wang et al., “Mechanical detection of nuclear decays,” Phys. Rev. Lett. 133, 023602 (2024), arXiv:2402.13257

## Slide 4
Nuclear decays in mechanical sensors
D. Moore, Yale
Magrini et al., Nature 595, 373 (2021)
Tebbenjohanns et al., Nature 595, 378 (2021)
See, e.g.:
Auger e-
x-rays
EC decay
decay
10 m sphere
10 MeV/c = 5x10-21Ns
100 nm sphere
10 keV/c = 5x10-24 Ns
D. Carney, K. Leach, and DCM, “Searches for massive neutrinos with mechanical quantum sensors,” PRX Quantum 4, 010315 (2023) arXiv:2207.05883
Example force measurements for nuclear decay:
J. Wang et al., “Mechanical detection of nuclear decays,” Phys. Rev. Lett. 133, 023602 (2024), arXiv:2402.13257
Levitated sensors are now reaching sufficient sensitivity to detect the miniscule forces imparted by single sub-atomic particles
  For weak decays, allows the momentum of each neutrino to be reconstructed on an event-by-event basis
Particle trajectory (quantum harmonic oscillator):

## Slide 5
Complementarity to energy measurements
D. Moore, Yale
Compared to energy resolving measurements such as those in BeEST, directly measuring the momentum of the recoil has some differences/complementarity:
  Momentum transfer is independent of daughter mass M, so signals do not decrease for heavy isotopes (i.e., E = p2/2M, while p unchanged)
    E.g., could look for 765 keV from 207Bi with good SNR, tagged on delayed gamma (while in an energy resolving detector, the 1.4 eV NR would be more challenging)
  Atomic de-excitations (Augers, x-rays) tend to be less important since they are at lower momentum:
    E.g. for 37Ar, 3 keV Auger has 50 keV/c momentum (compared to 813 keV momentum ) but can deposit much higher energy than the NR
  Detection of vector momentum of recoil allows emitters to also be used (given sufficiently accurate detection of energy and direction)
  Multiple coincident signals with recoil can minimize backgrounds (charge change, detection of secondary particle, possibly scintillation)

## Slide 6
Nanoparticle arrays for sterile
D. Moore, Yale
Arrays of radioisotope loaded nanoparticles can search for steriles following similar strategy to BeEST
  Possibility to probe many orders of magnitude beyond best existing limits
  These are naïve projections and time will tell what the most challenging backgrounds, systematics are
Projected sterile sensitivity vs livetime:
1 sphere month
10 sphere years
1000 sphere years
PRX Q 4, 010315 (2023) arXiv:2207.05883
Detector concept:
Nanosphere array
Scintillator + SiPM arrays

## Slide 7
Example electron capture decay (37Ar):
Example decay (32P):
Experimental signature
D. Moore, Yale
If a keV – MeV mass sterile 𝜈 mixes with the light 𝜈, then expect small fraction of decays to emit a heavy 𝜈
Momentum difference between heavy and light state is largest for non-relativistic neutrinos, i.e.,
= 750 keV
PRX Quantum 4, 010315 (2023)

## Slide 8
Proof of principle ( decays)
D. Moore, Yale
As a proof-of-principle, we have detected single 𝛼 decays with >m sized spheres
  Momentum is ~200 MeV/c (compared to 0.1-1 MeV/c for typical )
Have demonstrated loading of small quantities of 212Pb into trapped microspheres
Rn-220 decay chain:
Schematic of loading scheme:
220Rn
216Po+
Drift in E-field
212Pb
~100 nm
T1/2 = 56 s
T1/2 = 0.14 s
T1/2 = 10.6 h
3 m diameter SiO2 sphere
J. Wang et al, PRL133, 023602 (2024), arXiv:2402.13257
Jiaxiang Wang

## Slide 9
Detection of single nuclear decays (charge)
Can detect single nuclear decays through the change in net charge of the particle
Example of measured charge changes vs. time:
decays
Auto-discharge
PRL133, 023602 (2024), arXiv:2402.13257

## Slide 10
Detection of single nuclear decays (recoil)
Reconstruct recoil of the entire particle correlated with the decay time
Recoil coincident with charge change:
Signal to noise = 13
PRL133, 023602 (2024), arXiv:2402.13257
Zoom to decay time:

## Slide 11
Resolution vs. pulse amplitude:
Rn-220 decay chain:
fg mass spheres
D. Moore, Yale
In parallel, have reached required sensitivity to detect neutrinos with high signal-to-noise with ~150 nm diameter spheres
Resolution now reaching <3x of Standard Quantum Limit (SQL)
S/N>10 for 208Tl
Calibrated response, 5 fg particle (4 MeV/c):
Yu-Han Tseng
Tom Penny

## Slide 12
Microsphere trap has been upgraded with high power laser (100 W) to allow up to ~10 x 10 arrays
Similar technology to tweezer arrays for neutral atom quantum computing
  Real time control over trap positions
Ben Siegel
Microsphere arrays
D. Moore, Yale
7x7 array of spheres (~1 mbar):
~500 m
Simplified schematic:
100 m
Rearrangement example (10 m spheres @ ~1 mbar):
Played at 8x speed
Siegel et al. PRA 111, 033514 (2025)

## Slide 13
Summary
Optomechanical sensors can directly measure the missing momentum in weak decays
While similar in concept to energy resolving measurements in the BeEST, there are some complementary features of the optomechanics approach
Technology is still under development, but hope to do our first searches e.g. with 90Y in the coming year or two
May provide a path to isotopes and branching ratios that BeEST is not sensitive to
D. Moore, Yale

## Slide 14
Light 𝜈
D. Moore, Yale
A fixed solid source localizing nuclei at atomic distances cannot produce 𝜈 with sufficiently well defined momenta:
Relevance of Heisenberg Uncertainty also recently pointed out for PTOLEMY (C𝜈B):
Example of requirements on state preparation and measurement:
5 nm graphene flake in ground state of 100 Hz trap
Squeezed by 20 dB
Flake COM
𝜈
See, e.g., Cheipesh et al., PRD 104, 116004 (2021)
Apponi et al. (PTOLEMY), arXiv:2203.11228 (2022)
Delocalizing COM of solid nanoparticle could allow required state-preparation
Substantially beyond current state-of-the-art in quantum optomechanics
Reaching a projective measurement of light 𝜈 masses would require measurements deep in the quantum regime
Projective measurement of sphere momentum:
Projective measurement of
Prob. =