## Slide 1
Auger electron loss simulation for the BeEST experiment
Vancouver, Canada
BeEST collaboration meeting 2025

## Slide 2: Table of content
Motivations
Elastic and inelastic scattering approximations
Simulation and results
Conclusions and perspectives

## Slide 3: Motivations
Auger electrons energy loss: very poor knowledge!
Limiting factor for the sterile neutrinos sensitivity!
*I. Kim et al., Phys. Rev. D 111, 5 (2025)
Fit of the experimental recoil spectrum

## Slide 4: What happens inside the detector?
Ta
Auger electron
7Be
Tr
Te ≈ 55 eV
Elastic scattering
Inelastic scattering
Free electron
Collective electrons
Creation of a plasmon
Creation of a secondary electron
Ta
Ta
Ta
Ta
Ta
Ta
Ta
Ta
Ta
ΔTe ≈ 0
ΔTe ≠ 0
How can any of these very low energy electrons escape the detector?

## Slide 5: What happens inside the detector?
Secondary electrons with very low energy:
  Big mean free path
  Increased probability of escape!
Need for a precise simulation to constrain the energy loss!

## Slide 6: Elastic scattering of electrons
Al
Valid down to 10 eV!
Calculated with the ELastic Scattering of Electrons and Positrons by Atoms, positive ions and molecules (ELSEPA) code!
*F. Salvat et al., Computer Physics Communications 165, 2 (2005)

## Slide 7: Inelastic scattering of electrons
Dielectric formalism: (Precise down to few eVs)
Energy Loss Function (ELF) --> cannot be obtained with theoretical calculations
Penn (1987) proposed a method to extrapolate ELF(0, ω) to the (q, ω) plane
With ELF(0, ω) is calculated from the very abundant experimental optical data
*E.D. Palik, Handbook of Optical Constants of Solids (1985)
Diff cross section:

## Slide 8: Electron scattering simulation
G4Microelec package:
Elastic scattering (1.1 eV -> 500 keV): ELSEPA cross-sections
Inelastic scattering (1.1 eV -> 10 keV): Dielectric formalism
Includes several materials: Al, C, Al2O3, Cu, Ge, Si, …
*Q. Gibaru et al., NIM B 487 (2021)
Our extension of G4Microelec:
Elastic scattering (1.1 eV -> 10 MeV): ELSEPA cross-sections
Inelastic scattering (1.1 eV -> 10 MeV): Dielectric formalism
Additional material: Ta
Electron energy loss simulations for the BeEST and SALER experiments

## Slide 9: Simulation geometry
Al
Al
Ta
Ta
Obtained with SRIM
7Be @ 25 keV
Generate 55 eV electrons
Calculate deposited energy inside the STJ

## Slide 10: Electron scattering energy escape
The shape can be used to fit the experimental data!
The amplitude is not yet trustworthy due to unprecise cross-sections below 10 eV!
Energy deposition inside the STJ
Primary electrons energy: 55 eV

## Slide 11: Elastic scattering involvement
without elastic scattering
With elastic scattering
0.1% of events with energy escape
1.5% of events with energy escape

## Slide 12: Low energy secondary electrons
With secondaries
Without secondaries
0.1% of events with energy escape
0.02% of events with energy escape
80% of the energy escape is caused by the low energy secondaries!

## Slide 13: Conclusions and perspectives
The simulation for the electron energy loss can produce the shape of the Auger electrons energy escape tail despite the present limitations
The current status of the simulation can already be used to improve the fit of the experimental recoil spectrum of the BeEST experiment
The elastic cross-sections below 10 eV can be calculated and added to the simulation later on
The electron energy loss simulation can be used as well for the shake off tails

## Slide 15: Inelastic scattering of electrons
Mermin dielectric function:
: Lindhard dielectric function
Fit of ELF(0, ω) with the Merimin function

## Slide 16: Inelastic scattering of electrons
Q-expansion of the optical ELF
Mermin dielectric functions are used to fit the optical ELF(0, ω)
-> Extrapolate ELF (q, ω)

## Slide 17: Elastic scattering cross-section
For Tantalum