## Slide 1: Overview of the ISOLDE Facility and of the EPIC Project
J. Vollaire, M. Calviani , R. Catherall, T. Giles, G. Neyens
6th Radiate Collaboration Meeting
9-13 December - Triumf, Vancouver (Canada)

## Slide 2: Outline
The ISOLDE facility (focusing on targets)
The EPIC project
  New beam dumps
  Possible new irradiation facility
Conclusions

## Slide 3: ISOLDE in CERN accelerator chain
New injector for protons
Long Shutdown ongoing (LS2)
LHC Injector Upgrade Project (LIU). No proton beam to ISOLDE in 2019
Connection of a new Linac

## Slide 4: ISOLDE infrastructure
CERN Meyrin site
ISOLDE is located on the Meyrin site
Facility located on both sides of the boarder
ISOLDE at the PS Booster since 1992
1000 isotopes available already (of 3000 known) (60 keV – 10 MeV/u)
  70 different elements
  10 different permanent experimental set-ups (and new ones coming)
ISOLDE is CERN
Radioactive Ion Beam
Facility
Capitalize on 50 years of experience with production of RIBs

## Slide 5: The ISOLDE facility
“Hot” Laboratories (target lifecycle)
Target area (shielded) with two stations
Two mass separators (GPS and HRS)
Low energy beam lines (60 keV)
Post-Accelerator: EBIS source and Linac with NC and SC structures (HIE ISOLDE)
Three High Energy beam lines

## Slide 6: ISOLDE RIB production principle

## Slide 7: The PS Booster (proton driver)
The PS Booster (will) receive 160 MeV H- from the Linac4 (charge exchange at injection)
Acceleration and extraction at 2 GeV (after LS2) except for ISOLDE (1.4 GeV only). PS Booster cycle 1.2 s.
Transfer line to ISOLDE (~100 m):
  NORM beams used for solid targets (4 bunches with 4E1013 protons max in total and a bunch separation of 572 ns)
  STAGISO (staggered) beams for liquid targets (3 bunches with maximum of 1E1013 and a 16 µs bunch spacing)
  Averaged current limited to 2 µA (1.25x1013 pps) due to the actual beam dump design and radiation protection issues (air activation)
  Transfer line magnets and power supplies not compatible with 2 GeV
In 2018: 1020 protons have been distributed to the two target stations

## Slide 8: Target Stations
PS Booster
protons
RIB
Dump
HRS side: MEDICIS irradiation point
GPS side target station
Fraction of the beam only interacts in the target material.
Protons are “lost” in the beam dump or used for target irradiation (HRS side)
Irradiated targets used for medical isotopes production (MEDICIS)

## Slide 9: ISOLDE target assembly & coupling
Target base
Target Container + transfer line
Surface/Laser ion source
Target material
Gas
injection
Oven
(mass marker)
Heating:
Line & target
Water connectors
FE view
FRONT END
(target station)
Plasma ion
source

## Slide 10: Target Production (2018)
Total targets assembled end of 2018 : 49
Delivered to ISOLDE: 29 (replaced after 1 to two weeks)
Delivered to MEDICIS: 10 + 2 in December
Used for development: 8 (16%)
10 different materials
Mostly carbides and metal foils
Most popular: uranium carbide
7 different ion sources
LIST and negative ion source back in action
Courtesy of S. Rothe

## Slide 11: Target Handling and waste disposal
Remote handling capabilities:
  Three industrial robots (made radiations hard) for targets handling
  A rail conveyor system going from the HRS irradiation point (MEDICIS) to the laboratory area (accessible during beam operation)
Shielded storage (inside the target area and in the laboratory)
A shielded hot cell (being commissioned):
  Dedicated mainly to targets dismantling and UCx re-oxidation (for waste disposal) but scope of use could be extended (15 cm lead equivalent)
A “hot-laboratory” with the technical and procedural (close RP support) requirements for handling of radioactive materials:
  Dedicated to target lifecycle and CERN-MEDICIS infrastructure
  Civil engineering for the hot-laboratory extension will start in 2020 (nano-laboratory for actinide target production and shielded storage area)

## Slide 12: Target Handling and Storage
Storage (target area)
GPS and HRS robots (target area)
RCS and robot
RCS chicane toward
the laboratory
Hot Cell (back)

## Slide 13: Target disposal (actinide)
Oxidation
Cementation for
UxOy-C powder
Conditioning
Dismantling
(not started)
Target Storage
Target material
Micro UCx after oxidation (U3O8) at 350°C under 10% O2
Uranium carbide pellets
d=14 mm
Thickness 1.5 mm
Thermal analysis
Microstructural analysis
Work in progress (tests on non-irradiated UCX)
Courtesy of N.-T. Vuong

## Slide 14: The EPIC project
Exploiting the Potential of ISOLDE at CERN, ISOLDE input in view of the definition of European Strategy for Particle Physics
The proposal identifies several ways to increase ISOLDE capabilities and capacities:
  Take advantage of LHC Injector Upgrades (LIU)
    Increase of p-intensity with the new Linac
    Increase of PS-BOOSTER p-energy (1.4 to 2 GeV)
  Allow parallel beam operation with (a) new target station(s)
  Higher quality beams for improved RIB beam purification
  Upgrade the REX-ISOLDE post-accelerator (NC and SC sections)
  Implement a new compact storage ring to store RIBs
  Build a new experimental hall to host new experiments
Discussed in the coming slides

## Slide 15: Energy and intensity upgrade
Energy upgrade: electro-magnets in the transfer line can’t cope with the 2 GeV protons. Modifications (higher magnetic rigidity) or relocations of dipoles being studied
Intensity Upgrade: Higher beam power on the targets and on the beam dumps (absorbing the majority of the beam)
  Coupled FLUKA/thermo-mechanical analyses are showing that the dumps operate at their limit in terms of temperature and mechanical stresses with the actual beam parameters (2 A – 1.4 GeV beam). Exclude any increase
560 ℃ steady state for HRS assuming ~3-5 W/m2K HTC
Dump material:
Iron Blocks
Unknown thermal contact

## Slide 16: Beam dumps (visual inspection)
Signs of corrosion and condensation on the visible face (accessible from target area)
  Dump material not up to date with best practices in the field
Unknown condition (neither access nor monitoring)
Proposal:
  Study the implementation of PSB type cores (CuCrZr water cooled)
  Improve shielding and limit backscattering of secondary particles (to limit activation)
  Include maintenance and failure scenario in design
Molten material?
2 GeV core (PS Booster)

## Slide 17: New dumps implementation
Beam dump HRS
Measured artificial radioactivity (above “Clearance Limits”) with Na-22 and Mn-54 dominating. Sample taken about 4 m from the HRS dump (2 m from shielding)
Need to remove the soil above the target area
Careful planning and proper radiation protection

## Slide 18: New target station(s) (brainstorming)
FLUKA Simulation: Ch. Duchemin
ISOLDE Target #1
UC2 3.5 g/cm3
19.6 cm length
0.7 cm radius
ISOLDE Target #2
UC2 7.0 g/cm3
10.0 cm length
2.5 cm radius
25 cm
Proposal: M. Lozano
Two FE solution:
Optimize use of bem
Low/High density
Long/Thick targets
Integration and maintenance challenging
New FE solution:
Surface building
FE removal from the top
New separator
Proposal: S. Marzari

## Slide 19: Irradiation facility at ISOLDE
Detailed model of the target and target area implemented in FLUKA
Using “standardized” quantities for comparison of different radiation fields (dose, 1 MeV neutron equivalent, high energy hadron equivalent)
Normalization to 5x1019 protons (in 2018 ~1x1020 protons equally shared between GPS and HRS). All quantities scale to the number of protons delivered (intensity, irradiation time…)
Comparison of 1.4 GeV/2.0 GeV protons and 3.5/1.3 g/cm3 UCx
FLUKA model

## Slide 20: Fluence mapping (1.4 GeV – 3.5 g/cm3 UCX)
All particles
Neutrons
Protons
1 MeV neutrons eq.
Heavy Hadrons eq.
ISOLDE 2021 parameters:
@1m from the target:
~ 4-5x1017 HH along beam
~ 8-9x1014 HH 90°
~ 2-3x1017 1_MeV_n along beam
~ 4-5x1015 1_MeV_n_eq 90°

## Slide 21: Fluence mapping (2.0 GeV – 1.3 g/cm3 UCX)
All particles
Neutrons
Protons
1 MeV neutrons eq.
Heavy Hadrons eq.
ISOLDE 2 GeV low density:
@1m from the target:
~ 1-2x1018 HH along beam
~ 5-6x1014 HH 90°
~ 6-7x1017 1_MeV_n along beam
~ 2-3x1015 1_MeV_n_eq 90°

## Slide 22: Dose (deposited energy)

## Slide 23: Dose Profiles
Beam axis profile
Lateral profile
~100 MGy/year @ 1 m forward direction
Several hundreds of kGy laterally (Front End)
Higher energy increases dose in the forward direction relatively more than laterally (good for Front End considering that a good dump design can ensure a safe beam absorption)
Going to “thinner” targets, use of the area before the beam dump even more interesting

## Slide 24: Conclusions
ISOLDE will not benefit from injector upgrades taking place during the long shutdown at CERN
Studies are being launched in order to define the necessary actions to allow ISOLDE to receive the 2 GeV proton beam from the PS Booster and higher beam intensity (beneficial for some exotic beams)
Important to understand the degradation of target performances and cause of failure considering higher energy/intensity (more systematic post-irradiation analysis). Radiation Hardening of Front Ends.
The modification of the beam dump is a good opportunity to foresee an irradiation station (only a small fraction of the beam interacts inside the target). ~100 MGy a few 1017 1 MeV neutrons equivalent per year expected.
Long terms development of ISOLDE with new target stations, better beam purification schemes, an upgrade of the post-accelerator and the extension of the experimental hall are being studied in the context of the EPIC project.

## Slide 25
THANK YOU FOR YOUR ATTENTION

## Slide 26: Radiation hardness tests
Courtesy of J. Cruikshank
Materials used for the Front End and targets placed behind the GPS beam dump window
  EDPM Ethylenee Propylene Diene (EPDM) O-ring seals (compressed and not compressed during irradiation)
  Kapton (commonly used insulator in radiation environment)
  PEEK samples (High Voltage Insulator for the Front Ends)
Samples placed during the 2018 run (to be analyzed)

## Slide 27: 1 MeV neutrons equivalent Front End