## Slide 1: The Formation of Radiolysis Products during Isotope Harvesting with a Flowing Water Target
Katharina A. Domnanich, E. Paige Abel, Colton Kalman, Wes Walker, Todd Barnhart, Jonathan Engle, Greg Severin

## Slide 2: Introduction I
Water radiolysis
  Only molecular species have sufficient lifetimes to accumulate
  Only molecular products long enough life times to accumulate
Reference: S. Le Caer (2011)

## Slide 3: Introduction II
Primary radiolytic yield
  Escape yield, G value [molecules/100eV]
    Type of radiation, Linear Energy Transfer, pH of solution
  Knowledge about the behavior of H2O2, H2 and O2 to ensure adequate conditions for isotope harvesting
 | G value [molecules/100 eV]
H2O2 | 0.74
H2 | 0.63
O2 | 0.073
Reference: Pastina et al (1999), Wasselin-Trupin et al (2002), Elliot et al (1993), Meesungnoen et al (2005)

## Slide 4: Experimental Setup I
Irradiation at the University of Wisconsin – Madison
Removal of radiolysis products from our system
  Decomposition of H2O2 by catalytic converter (KLC)
tirr: 190 min
4 run segments
Int.: 1 - 33 μA
LET: 12.6 keV/μm
H2O2 H2O + ½ O2
Pd, Zr, Ce

## Slide 5: Experimental Setup II
H2
D2
D1
KLC
Tank
He
water samples
p+

## Slide 6: Formation of H2O2
Escape yield-based H2O2
  Formation based on G value and destruction by KLC
  2.5 – 8 times lower [H2O2] measured
  Long-term irradiations
  H2O2 + e-aq  OH- + HO·
  H2O2 + HO·/H·  H2O + HO2·/HO·
  HO· + HO·  H2O2
  HO2· + HO2·  H2O2 + O2
  Formation
  Steady State
  Destruction
Reference: Pastina et al (1999), Le Caer (2011), Iwamatsu et al (2018), Meesungnoen et al (2005)

## Slide 7: Interaction of Spurs
Our harvesting system
  Tank with 36 L H2O
  Small volume of beam spot (~0.7 mL)
  Low beam currents
0.01 – 5 μA:
p+
H2O
p+
p+

## Slide 8: Interaction of Spurs
Our harvesting system
  Tank with 36 L H2O
  Small volume of beam spot (~0.7 mL)
  Higher beam currents
10 – 35 μA:
p+
H2O
p+
p+
p+
p+
p+

## Slide 9: Beam current-based H2O2 calculation
Reference: Meesungnoen et al (2005)
  Decreased G(H2O2) at higher beam currents  overlapping spurs
  Literature: declining G(H2O2) with increased ionization densities

## Slide 10: Formation of O2
  Two dissolved O2 sensors
  Escape yield-based diss. O2
  Formation with G value
  Deareation from water by He
  Additional O2 input by KLC
KLC H2O2  H2O + ½ O2
H2O
Sensor 1
Sensor 2

## Slide 11: Formation of O2
  Two dissolved O2 sensors
    Intra-track formation
    HO2· + HO·/ HO2·  O2 + H2O/H2O2
    Intra-track decay
    O2 + e-aq/H·  O2- + O2·-
  Agreement with measured diss. O2 (D1)
  10-times lower G(O2)  less O2 track interactions
  Virtually no O2 data on long term irradiations
KLC H2O2  H2O + ½ O2
H2O
Sensor 1
Sensor 2
Reference: Burns et al (1981), Meesungnoen et al (2005)

## Slide 12: Indirect measurement of [H2O2] with diss. O2
  No on-line determination of H2O2 in water
  difference of diss. O2 sensor readings
  H2O2 in system water
  Verification of beam current-based H2O2 calculation
Δ(Sensor 2 – Sensor 1) = H2O2 converted by KLC

## Slide 13: Formation of H2
  Escape yield-predicted %H2 2-times higher than measured %H2
    Formation with G value
    Transfer into headspace and transport to H2 sensor by He
  Formation e-aq + e-aq + 2 H2O  H2 + 2 OH- e-aq + H· + H2O  H2 + OH-
  Allen cycle
    Presence of HO· and H· radicals
    Only sustainable at LET ≤ 20 keV/μm
    HO· + H2  H2O + H·
    H· + H2O2  H2O + HO·
  Mutual annihilation of H2O2 and H2 can be assumed

## Slide 14: Formation of H2
    Fitted H2 calculation
      Assumes const. G(H2) of 0.34
      Transfer into headspace and transport to H2 sensor by He
      Assumed that decreased G(H2) accounts for the H2 decay within Allen-cycle

## Slide 15: Acknowledgements
The isotope harvesting gang
  Greg Severin
  Paige Abel
  Hannah Clause
  Scott Essenmacher
  Colton Kalman
  Chloe Kleinfeldt
  Samridhi Satisja
  Chirag Vyas
  Wesley Walker
  Funding
  Michigan State University
  U.S. Department of Energy (DOE-FOA-0001588)