## Slide 1
Experience of the TITAN’s MR-TOF-MS at ISAC and its potential capabilities at ARIEL
Samuel Ayet San Andres
Instituto de Fisica Corpyscular – CSIC - UV
for the FRS Ion Catcher Collaboration
(MR)-TOF-MS
Genealogy
MR-TOF-MS Performance
Isomers

## Slide 2
Enables high performance
Fast  access to very short-lived ions (T1/2 ~ ms)
Sensitive, broadband, non-scanning  efficient, access to rare ions
H. Wollnik et al., Int. J. Mass Spectrom. Ion Processes 96 (1990) 267
Injection trap
Detector
Analyzer
Applications
Diagnostics measurements: monitor production, separation and low-energy beam preparation of exotic nuclei
Direct mass measurements of exotic nuclei
High-resolution mass/isomer separator
C. Scheidenberger et al., Hyperfine Interact. 132 (2001) 531
W.R. Plaß et al., NIM B 266 (2008) 4560, T. Dickel et al., PLB 744 (2015) 137
W.R. Plaß et al., Int. J. Mass Spectrom. 394 (2013) 134
To achieve high mass resolving power and accuracy:
Multiple-reflection time-of-flight mass spectrometer (MR-TOF-MS)
...
Detector
Injection trap
Time-of-flight Mass Spectrometry

## Slide 3: Genealogy of MR-TOF-MS built @ JLU Giessen
MR-TOF-MS Isobar separator
for the TITAN facility (TRIUMF)
MR-TOF-MS at FRS Ion Catcher (GSI)
1.2 m
0.8 m
Inlet
Mobile MR-TOF-MS for analytical mass spectrometry (JLU)
Ion-optical identical scaled down versions
Development platform:
Retrapping
Software
Electronics
…
Dickel et al. NIM B 317 (2013)
T. Dickel et al., NIM A 777 (2015) 172
C. Jesch et al., Hyperfine Interact. 235 (2015) 97
Notes: MR-TOF-MS around the world.
Show what it can do…

## Slide 4
First operation steps…
Installation and first beamtimes:
- MR-TOF-MS @ Platform 20.03.2017
- First Vacuum 25.03.2017
- Offline Commissioning 27.04.2017
- OLIS Beamtime 03.05.2017
- 1st RIB (Titanium) 11.05.2017
- 2nd RIB (Gallium) 18.06.2017

## Slide 5: MR-TOF-MS @ TITAN
TOF analyzer
MPET:
mass measurement
via determination of cyclotron frequency
MR-TOF MS:
remove isobaric contaminants and mass measurements via time-of-flight
J. Dilling et al., NIMB 204 (2003) 492, C. Jesch et al., Hyperfine Interact. 235 (2015) 97
TRIUMF’s Ion Trap for Atomic and Nuclear Science
High-precision mass measurements
In-trap decay spectroscopy
RFQ: accumulate, cool and bunch
MCP
RF
Injection and
Retrapping
Trap
RF
Accumulation
Trap
EBIT: Charge State Breeding
Cooler Trap:
Cooling of HCIs

## Slide 6: Performance of MR-TOF-MS: Mass resolving power and accuracy
I. Mardor et al., PRC 103, 034319 (2021)
MRP of almost 1,000,000 at total TOF of ~23 ms (~900T)
Mass accuracy down to
- 485 events collected
- Dm = 2.6 keV - Dm/m = 4.0×10-8
We need:
Faster measurement
Higher precision
Higher sensitivity
Higher rate capability
M. P. Reiter et al., NIM A 1018 (2021) 165823
All species 250k below 9ms!
TITAN’s MR-TOF-MS
Notes: The vicinity of the N=Z line is of special interest in nuclear structure physics, in nuclear astrophysics and for the basic understanding of nuclear forces and symmetries in nuclei.
Physics Goals:
rp-process
Nuclear structure (isospin symmetry, Wigner energy, pn interaction)
Nuclei in this region have rapidly-changing, varying shapes

## Slide 7: Performance of MR-TOF-MS: Rate capabilities
M.P. Reiter et al. NIM B 463 (2020) 431-436.
Improved diagnostics
 Improved beam tuning
 Higher sensitivity
E. Leistenschneider et al., PRL 120 (2018) 062503
Non scanning & higher efficiency
Higher sensitivity
We need:
Faster measurement
Higher precision
Higher sensitivity
Higher rate capability
Two neutrons more exotic!

## Slide 8: Performance of MR-TOF-MS: Rate capabilities
U
z
Injection Trap
Entrance Reflector
Exit Reflector
Detector
Stage 1: Injection
Stage 2: TOF Separation
Stage 3: Re-Trapping
T. Dickel, et al. J. Am. Soc. Mass Spectrom. 28 (2017) 1079.
T. Dickel et al., IJMS 412 (2017) 1-7
Beck at al., PRL 127(2021)112501
We need:
Faster measurement
Higher precision
Higher sensitivity
Higher rate capability
Novel method: Mass-selective retrapping  Operate MR-TOF as its own pre-separator
Enable at least two neutrons more exotic!

## Slide 9
Requirements for system for
isomere search:
  Fast: ~ms
  Sensitive: non-scanning
  High mass resolving power: >>105
  High dynamic range: > 10:1
Atlas of nuclear isomers – second edition
S. Garg et al., At. Data Nucl. Data Tables 150 (2023) 101546
Established mass
spectrometry methods
(e.g., Penning traps and
storage rings)
g-spectroscopy
MR-TOF-MS
Why a new method to measure isomers?

## Slide 10: Discovery of isomeric states
  97Ag
C. Hornung et al., PLB 802 (2020) 135200
W. S. Porter et al, PRC Letter 105 (2022) L041301
FRS Ion Catcher
Fe isomer
TITAN@TRIUMF
First isomer discovery with an
MR-TOF-MS

## Slide 11
MCP
Detector
Ion mirror 1
Ion mirror 2
N = 345 turns
MCP
Detector
Ion mirror 1
Ion mirror 2
High-resolution example
  e.g. separation of ground and isomeric states
    At EX ~ 1.5 MeV
Discovery of isomeric states
Discovery of isomeric states
Tailoring Isomeric-Clean Beams for Experiments Downstream

## Slide 12
Trap depth 4.5 V
High-resolution example
  Set to a tRT=7719.26 µs fully isolates 127nIn from 127g+mIn
MCP
Detector
Ion mirror 1
Ion mirror 2
N = 345 turns
MCP
Detector
Ion mirror 1
Ion mirror 2
N = 345 turns
Tailoring Isomeric-Clean Beams for Experiments Downstream

## Slide 13
MCP
Detector
Ion mirror 1
Ion mirror 2
N = 345 turns
MCP
Detector
Ion mirror 1
Ion mirror 2
N = 345 turns
Trap depth 4.5 V
High-resolution example
  Set to a tRT=7719.26 µs fully isolates 127nIn from 127g+mIn
Isomeric pure beams for
downstream experiments!
Ongoing project with GSI and TRIUMF to design an “Isomer Beam Line”
  Enable dedicated, background free, decay spectroscopy of isomeric states (@GRIFFIN?)
Tailoring Isomeric-Clean Beams for Experiments Downstream

## Slide 14
Thanks!
TITAN @ TRIUMF
MR-TOF-MS Students and Post-docs:
2016
2017
2018 - 2019
2024
2021
IONAS @ JLU Giessen

## Slide 15: Backup Slides

## Slide 16: Mass measurements with the JLU MR-TOF-MS
T. Dickel et al., PLB 744 (2015) 137
S. Ayet et al., PRC 99 (2019) 064313
I. Miskun et al., EPJA 55 (2019)148
S. Ayet et al., EPJA 56 (2020) 143
C. Hornung et al., PLB 802 (2020) 135200
A. Spataru et al., BJOP 48 (2021) 535
I. Mardor et al., PRC 103 (2021) 034319
A. Mollaebrahimi et al., PLB 839 (2023) 137833
E. Leistenschneider et al., PRL 120 (2018) 062503
M. P. Reiter et al., PRC 98 (2018) 024310
M. P. Reiter et al., PRC 101 (2020)
E. Leistenschneider at al., PRL 126 (2021) 042501
S. Beck et al., PRL 127 (2021)
I. Mukul et al., PRC 103 (2021)
C. Izzo et al., PRC 103 (2021)
S. F. Paul et al., PRC 104 (2021)
W. S. Porter et al., PRC 105 (2022)
R. Silwal et al., PLB 833 (2022)
W. S. Porter et al., PRC 106 (2022)
A. Jacobs et al., NPA 1033 (2023)
E. M. Lykiardopoulou et al., PRC 107 (2023)