## Slide 1
ARIEL Facility Overview
Luca Egoriti
ARIEL target station co-lead (integrator)
On behalf of:
Alexander Gottberg, ARIEL program leader
2026-04-20

## Slide 2
TRIUMF accelerators
Muons for
material science
500 MeV – 400 μA
P+ Cyclotron
PIF
STF
T1
T2
82Sr medical production
30 MeV – 10 mA
e- LINAC
120 MeV – 10 nA
Electronics irradiations
Proton FLASH
Ocular melanoma treatments (-2019)
ITW
ITE
TR: 13
TR: 30-1
TR: 30-2
TR: 24
Medical isotopes
AETE
ISOL
(ARIEL)
225Ac et al. production
IPF
Neutron Irradiations
NIF
Radioactive Ion Beams
~10 user facilities
Nuclear & atomic physics
Material science
ISAC I and II halls
ISOL
(ISAC)
User facilities
ISAC ISOL targets (since 2000s)
ARIEL ISOL targets (from ~2025)
Cyclotron & beamlines (since ~1975)
E-linac and beamline (since ~2013)
RIB lines
APTW
BL1A
BL2A
BL2C

## Slide 3
ARIEL Scope
ARIEL Ultimate Objectives:
Two new radioisotope production target stations 50 kW protons and 100 kW electrons
Multi-user operation up to three simultaneous isotope beams (9000 RIB hours) delivered to the existing experimental facilities
More efficient post acceleration electron beam ion source - charge state breeder, radiofrequency quadrupole, Nier-spectrometer and unique 1/20,000 resolution high-resolution mass separator.
Medical Isotopes production in proton target station beam dump and transfer to medical isotope research

## Slide 4
Tripling TRIUMF‘s Radioisotope Science Program
Advanced Radioisotope Laboratory (ARIEL)
ARIEL-I (2012 - 2014) e-linac, beam tunnel, target building
ARIEL-II (2017 - 2028) target stations, shielding, hot cells, RIB distribution
CANREB (2014 - 2019) charge state breeding and purification for post-acceleration in ISAC II
Therapeutic Isotopes (2020 - 2028) production and processing of medical isotopes at ARIEL proton target station
$200 million investment by federal and 6 provincial governments; supported by 21 universities across Canada, about 700 FTE years total effort.

## Slide 5
ARIEL facility description

## Slide 7
ARIEL e-linac
300 keV
10 MeV
30 MeV
NORTH
To “Driver tunnel”
E = 30 MeV (upgradable to 50 MeV); Current up to 10 mA; Power up to 100 kW
Early science enabled: AETE material developments, FLASH studies on mice, DarkLight
Status: Commissioned up to 10 kW (beam dump rating)
CTS
[1] Egoriti, L. et al., Material development towards a solid 100 kW electron-gamma converter for TRIUMF-ARIEL https://doi.org/10.1016/j.nimb.2019.05.031
[2] Esplen, N., et al., Dosimetric characterization of a novel UHDR megavoltage X-ray source for FLASH radiobiological experiments. Sci Rep 14, 822 (2024). https://doi.org/10.1038/s41598-023-50412-w
[3] Ford, N. et al., Respiratory-gated micro-computed tomography imaging to measure radiation-induced lung injuries in mice following ultra-high dose-rate and conventional dose-rate radiation therapy, J. Med. Imag. 12(1) 014002 (30 January 2025) 10.1117/1.JMI.12.1.014002
FLASH
DarkLight

## Slide 9
Driver beam line tunnel
AETE
APTW
BL4N Vault region
BL4N Proton Cave region
BL4N Pharoah’s tomb region
EHBT dogleg region
BL4N & EHBT
Straight Tunnel section
BL4N & EHBT
North Tunnel bend section
NORTH
One proton & one electron beam line, for transport, spaced by ~1 meter
Status: beam line & services (cables, piping) installation in progress

## Slide 11
Target hall: Irradiation Stations (APTW and AETE)
[µSv/h]
P+ beam on APTW at 100 µA
~2.5m tall
Steel “plugs”
~2m tall
Steel + Concrete
APTW target
AETE target

## Slide 12
Target Hall
Driver tunnel
Target Hall
APTW station
AETE station
Cap shielding
Hot Cell
Spent target vault
Tunnel access maze
Module storage
Status: Target stations constructed, modules and services being assembled

## Slide 14
Low-energy beam transport and manipulation
Mass separation, charge breeding, bunching of two RIBs in parallel
Status: constructed, commissioned at low RIB intensity

## Slide 15
ARIEL Program Timeline
ARIEL-I
CANREB
ARIEL-II: Proton & Electron Stations
Therapeutic Isotopes
Today
2012
2014
2016
2018
2020
2022
2024
2026
Target Building construction, beam tunnel, e-linac
charge state breeding and purification for post-acceleration in ISAC II
Target Station Installation
AETE Integration & Commissioning
APTW Integration & Commissioning
Beam Line Installations
Integration
& Commissioning
2028
Operations Ramp Up
2030
E-linac Upgrades
CANREB Upgrades
RIB Target Laboratories & Spend Targets Storage Vault
Beam Ramp Up
First Beam
Med. Isotopes to Users
Three Beam Capability
Concept & Design
Shielding Component Installation
CANREB CFI Closeout
ARIEL-I CFI Closeout
Regular User Operation

## Slide 16
ARIEL RIB Rampup

## Slide 17: ISAC operation without LS26
ISAC operation from June to December, generating about 3200 RIB hours per year available to experiments
Chart: 
| 6 month operation | 6 month operation | 6 month operation | 6 month operation |  |  | 6 month operation |  |  | 6 month operation |  |  | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
ITE/ITW | 3200 | 3200 | 3200 | 3200 | 3200 | 3200
APTW | 0 | 0 | 0
AETE | 0 | 0 | 0
total RIB hours | 3200 | 3200 | 3200 | 3200 | 3200 | 3200
accumulative, 6 month operation | 3200 | 3200 | 3200 | 3840 | 4480 | 5120 | 5760 | 6400 | 7040 | 7680 | 8320 | 8960 | 9600 | 10240 | 10880 | 11520 | 12160 | 12800 | 13440 | 14080 | 14720 | 15360 | 16000 | 16640 | 17280 | 17920 | 18560 | 19200

## Slide 18: LS26 – Comparison with ISAC Generated RIB alone
Chart: RIB Hours in Different Scenarios
| 6 month operation | 2026 SD, ISAC only |  | 6 month operation | 2026 SD, ISAC only |  | 6 month operation | 2026 SD, ISAC only |  | 6 month operation | 2026 SD, ISAC only |  | 6 month operation | 2026 SD, ISAC only |  | 6 month operation | 2026 SD, ISAC only |  | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
ITE/ITW | 3200 | 3200 | 3200 | 0 | 0 | 3200 | 4400 | 3200 | 4400 | 3200 | 4400 | 3200 | 4400
APTW | 0 | 0 | 0 | 0 | 0 | 0 | 0
AETE | 0 | 0 | 0 | 0 | 0 | 0 | 0
total RIB hours | 3200 | 3200 | 3200 | 0 | 0 | 3200 | 4400 | 3200 | 4400 | 3200 | 4400 | 3200 | 4400
accumulative, 6 month operation | 3200 | 3200 | 3200 | 3840 | 4480 | 5120 | 5760 | 6400 | 7040 | 7680 | 8320 | 8960 | 9600 | 10240 | 10880 | 11520 | 12160 | 12800 | 13440 | 14080 | 14720 | 15360 | 16000 | 16640 | 17280 | 17920 | 18560 | 19200
Comments:
LS26 and ARIEL project acceleration.
ISAC moves back to 8 months operation, generating about 4400 RIB hours per year available to experiments
Impact:
Shutdown overhead fraction reduced.
Resource competition with ARIEL greatly reduced
Break-even point in accumulated RIB hours reached 2028-2029
Chart: RIB Hours in Different Scenarios
| 6 month operation | 2026 SD, ISAC only |  | 6 month operation | 2026 SD, ISAC only |  | 6 month operation | 2026 SD, ISAC only |  | 6 month operation | 2026 SD, ISAC only |  | 6 month operation | 2026 SD, ISAC only |  | 6 month operation | 2026 SD, ISAC only |  | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
ITE/ITW | 3200 | 3200 | 3200 | 0 | 0 | 3200 | 4400 | 3200 | 4400 | 3200 | 4400 | 3200 | 4400
APTW | 0 | 0 | 0 | 0 | 0 | 0 | 0
AETE | 0 | 0 | 0 | 0 | 0 | 0 | 0
total RIB hours | 3200 | 3200 | 3200 | 0 | 0 | 3200 | 4400 | 3200 | 4400 | 3200 | 4400 | 3200 | 4400
accumulative, 6 month operation | 3200 | 3200 | 3200 | 3840 | 4480 | 5120 | 5760 | 6400 | 7040 | 7680 | 8320 | 8960 | 9600 | 10240 | 10880 | 11520 | 12160 | 12800 | 13440 | 14080 | 14720 | 15360 | 16000 | 16640 | 17280 | 17920 | 18560 | 19200
accumulative, ISAC only | 3200 | 3200 | 3200 | 3200 | 3200 | 3200 | 3200 | 3200 | 4080 | 4960 | 5840 | 6720 | 7600 | 8480 | 9360 | 10240 | 11120 | 12000 | 12880 | 13760 | 14640 | 15520 | 16400 | 17280 | 18160 | 19040 | 19920 | 20800

## Slide 19: LS26 – Factoring in Additional RIB Hours from ARIEL
Chart: RIB Hours in Different Scenarios
| 6 month operation | 2026 SD, ISAC only | 2026 SD, incl ARIEL | 6 month operation | 2026 SD, ISAC only | 2026 SD, incl ARIEL | 6 month operation | 2026 SD, ISAC only | 2026 SD, incl ARIEL | 6 month operation | 2026 SD, ISAC only | 2026 SD, incl ARIEL | 6 month operation | 2026 SD, ISAC only | 2026 SD, incl ARIEL | 6 month operation | 2026 SD, ISAC only | 2026 SD, incl ARIEL | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
ITE/ITW | 3200 | 3200 | 3200 | 3200 | 0 | 0 | 3200 | 4400 | 4400 | 3200 | 4400 | 4400 | 3200 | 4400 | 4400 | 3200 | 4400 | 4400
APTW | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 330 | 660 | 660 | 990
AETE | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 330 | 660 | 660
total RIB hours | 3200 | 3200 | 3200 | 3200 | 0 | 0 | 3200 | 4400 | 4730 | 3200 | 4400 | 5390 | 3200 | 4400 | 5720 | 3200 | 4400 | 6050
accumulative, 6 month operation | 3200 | 3200 | 3200 | 3840 | 4480 | 5120 | 5760 | 6400 | 7040 | 7680 | 8320 | 8960 | 9600 | 10240 | 10880 | 11520 | 12160 | 12800 | 13440 | 14080 | 14720 | 15360 | 16000 | 16640 | 17280 | 17920 | 18560 | 19200
accumulative, ISAC only | 3200 | 3200 | 3200 | 3200 | 3200 | 3200 | 3200 | 3200 | 4080 | 4960 | 5840 | 6720 | 7600 | 8480 | 9360 | 10240 | 11120 | 12000 | 12880 | 13760 | 14640 | 15520 | 16400 | 17280 | 18160 | 19040 | 19920 | 20800
Chart: RIB Hours in Different Scenarios
| 6 month operation | 2026 SD, ISAC only | 2026 SD, incl ARIEL | 6 month operation | 2026 SD, ISAC only | 2026 SD, incl ARIEL | 6 month operation | 2026 SD, ISAC only | 2026 SD, incl ARIEL | 6 month operation | 2026 SD, ISAC only | 2026 SD, incl ARIEL | 6 month operation | 2026 SD, ISAC only | 2026 SD, incl ARIEL | 6 month operation | 2026 SD, ISAC only | 2026 SD, incl ARIEL | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
ITE/ITW | 3200 | 3200 | 3200 | 3200 | 0 | 0 | 3200 | 4400 | 4400 | 3200 | 4400 | 4400 | 3200 | 4400 | 4400 | 3200 | 4400 | 4400
APTW | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 330 | 660 | 660 | 990
AETE | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 330 | 660 | 660
total RIB hours | 3200 | 3200 | 3200 | 3200 | 0 | 0 | 3200 | 4400 | 4730 | 3200 | 4400 | 5390 | 3200 | 4400 | 5720 | 3200 | 4400 | 6050
accumulative, 6 month operation | 3200 | 3200 | 3200 | 3840 | 4480 | 5120 | 5760 | 6400 | 7040 | 7680 | 8320 | 8960 | 9600 | 10240 | 10880 | 11520 | 12160 | 12800 | 13440 | 14080 | 14720 | 15360 | 16000 | 16640 | 17280 | 17920 | 18560 | 19200
accumulative, incl. ARIEL | 3200 | 3200 | 3200 | 3200 | 3200 | 3200 | 3200 | 3200 | 4146 | 5092 | 6038 | 6984 | 7930 | 9008 | 10086 | 11164 | 12242 | 13320 | 14464 | 15608 | 16752 | 17896 | 19040 | 20250 | 21460 | 22670 | 23880 | 25090
accumulative, ISAC only | 3200 | 3200 | 3200 | 3200 | 3200 | 3200 | 3200 | 3200 | 4080 | 4960 | 5840 | 6720 | 7600 | 8480 | 9360 | 10240 | 11120 | 12000 | 12880 | 13760 | 14640 | 15520 | 16400 | 17280 | 18160 | 19040 | 19920 | 20800
Comments:
LS26 and ARIEL project acceleration.
ISAC moves back to 8 months operation, generating about 4400 RIB hours per year available to experiments.
ARIEL gradually ramping up to 2-3 targets per year per station in 2030
Impact:
Shutdown overhead fraction reduced
Resource competition with ARIEL greatly reduced and site-wide services less loaded from ARIEL
Break-even point in accumulated RIB hours reached earlier.

## Slide 20
ISAC vs ARIEL schedules and complexity
Three weeks irradiation
One day of cooldown
Remote vacuum disconnection
Move target to spent target vault
Move new target to irradiation station
Remote vacuum connection
Few hours pump-down
Three weeks irradiation
Approx. two days without beam on one station
Three weeks irradiation
One week cooldown
Hands-on service disconnection
Move module to Hot Cell
Remote target exchange in Hot Cell
Move module to irradiation station
Hands-on service connection
Few days pump-down
Three weeks irradiation
Three weeks without beam on one station
ISAC
ARIEL
ITW
ITE
ISAC
RIBs
APTW
AETE
ARIEL includes several systems different from ISAC, given the more aggressive constraints and RIB-hours requested from the project.
 ARIEL ramp-up will take time and include lots of learning

## Slide 21: Ramp-Up Considerations
Technical
Learning to operate several new systems to support ARIEL RIB production and delivery
Resources
The full 5YP proposal was foreseeing a personnel ramp-up. Current scenario is resource flat
Hence, project, technical ramp-up and operational resources will compete
Full operational resources will need to be requested and wait for FYP 2030-2035
Skills
ARIEL commissioning and ISAC operation will require the same experienced operators, beam delivery and target experts, etc
Regulatory
ARIEL will be rolled into TRIUMF’s class IB license, before starting commissioning. Safety package is being prepared for regulators
 Schedule: Installation in 2026, commissioning in 2027, beam delivery in 2028, 5000 hours of RIB in 2029

## Slide 22: ARIEL commissioning/operations in 2027-2029: “day-1” and beyond
Targets
APTW: SiC, Ta, UCx. Low power, with surface ion source
AETE: UCx, surface ion source
Facility configuration 2027
First beams have to be surface ionized, low energy.
No RILIS, no post acceleration, no CANREB, no parallel beams for beam delivery from ARIEL in 2027
Ramp Up:
AETE: 100 W – 1 kW in 2027 (commissioning), exceeding 1 kW in 2028, towards 10 kW in 2029
APTW: 1-5 kW In 2027 (commissioning), towards full power in 2028
RILIS, CANREB, post-acceleration possible
Experiments:
What experiments fit into these constraints?
For 2030 onwards…what are your ideal RIB parameters?
More of the same, three times as much?
Getting more exotic? Increased purity vs intensity, molecular beams, novel T&IS, etc.
What else?

## Slide 23: Technical Electron Beam Power ramp-up considerations
Simulated temperature profile in an AETE target with a 25 kW electron beam power
The current world-record for e-induced RIB production is 500 W (ALTO).
At 1 kW and for the small target, the power temperature homogeneity manageable
The more we increase beam power, the steeper temperature gradients are across the target, mostly in the beam direction
Moreover, UCx material properties are not well known, and this uncertainty makes the simulation more uncertain
    Sundeep Gosh’s PhD thesis is aimed at measuring UCx material properties

## Slide 24
Yields &
Experiment Planning

## Slide 25
ISOL targets for RIB production
500 MeV – 100 μA
P+ Cyclotron
Extraction electrode
HV ~60 kV
Target
T=2000 °C
Ionizer
Radioactive
Ion
Beam
Low energy experiments
High energy experiments
Post-accelerator
Mass separator
Neutrals
Ions
Isobars only
Post-accelerated
18 m
20 cm
[pps]
Medium E: RFQ + DTL
  0.117 MeV/u to 1.8 MeV/u
High E: SC linac
  6 MeV/u up to 16 MeV/u

## Slide 26
TRIUMF accelerators
Muons for
material science
500 MeV – 400 μA
P+ Cyclotron
PIF
STF
T1
T2
82Sr medical production
30 MeV – 10 mA
e- LINAC
120 MeV – 10 nA
Electronics irradiations
Proton FLASH
Ocular melanoma treatments (-2019)
ITW
ITE
TR: 13
TR: 30-1
TR: 30-2
CP: 42
TR: 24
Medical isotopes
AETE
ISOL
(ARIEL)
225Ac et al. production
IPF
Neutron Irradiations
NIF
Radioactive Ion Beams
~10 user facilities
Nuclear & atomic physics
Material science
ISAC I and II halls
ISOL
(ISAC)
User facilities
ISAC ISOL targets (since 2000s)
ARIEL ISOL targets (from ~2025)
Cyclotron & beamlines (since ~1975)
E-linac and beamline (since ~2013)
RIB lines
APTW
BL1A
BL2A
BL2C
Future AETE
γ
e-
Converter
Target
γ
e-
Converter
Target
Current ISAC Future APTW

## Slide 27: AETE Projected Yields
AETE day-1 target
In-target production (FLUKA)
Extrapolated efficiency (from historical efficiencies)
 | AETE day-1, 1kW (FLUKA) | Extrapolated yields
150Cs | 2.42E+04 | 5.93E+00
130Cd | 5.90E+05 | 7.25E+00
135Sn | 7.15E+05 | 6.41E+03

## Slide 28: AETE / APTW in-target production:
AETE day-1 target vs APTW nominal
AETE / APTW in-target production (FLUKA)
 | AETE day-1, 1kW (FLUKA) | APTW nominal, 10 kW (FLUKA) | AETE/APTW
85Ga | 8.08E+03 | 3.58E+07 | 2.3E-04
150Cs | 2.42E+04 | 8.65E+05 | 2.8E-02
150Ba | 2.42E+06 | 3.19E+07 | 7.6E-02
130Cd | 5.90E+05 | 8.80E+06 | 6.7E-02
135Sn | 7.15E+05 | 1.49E+07 | 4.8E-02
AETE in-target production (FLUKA)
AETE/APTW (contaminant)
<5E-07 (85Rb)
<2E-06 (150Eu)
<2E-06 (150Eu)
< 5E-07 (130Cs)
6.9E-06 (135Cs)

## Slide 29: Questions and discussion points
What experiments fit into the constraints of “day-1” RIBs from ARIEL?
More of the same, three times as much?
Getting more exotic? Novel target and ion sources, molecular beams, increased purity vs intensity, etc.
What else?

## Slide 30
Backup

## Slide 31
ARIEL target station concept
And comparison to the ISAC facility
“Driver” beam
  ARIEL: Two simultaneous, one 500 MeV proton, one 50 MeV electron beams
  ISAC: One 500 MeV proton beam
Target station operation
  ARIEL: Two simultaneous
  ISAC: Two, one irradiation at a time
Medical irradiation station
And several other “small” improvements

## Slide 32
Compact, modular shielding approach – similar to ISAC
[µSv/h]
P+ beam on APTW at 100 µA
~2.5m tall
Steel “plugs”
~2m tall
Steel + Concrete
APTW target
AETE target

## Slide 33
ISAC target lifetime and sequence
Service connections
Front end
+
Target
Shielding
ISAC
Irradiation station
ISAC
Hot Cell
Front end
+
Target
Shielding
Three weeks irradiation
One week cooldown
Hands-on service disconnection
Move module to Hot Cell
Remote target exchange in Hot Cell
Move module to irradiation station
Hands-on service connection
Few days pump-down
Three weeks irradiation
Approx. two-three weeks without beam on one station
Vacuum volume
ITW
ITE
ISAC
RIB

## Slide 34
ARIEL target lifetime and sequence
Service connections
Front end
+
Shielding
ARIEL
Irradiation station
Three weeks irradiation
One day of cooldown
Remote vacuum disconnection
Move target to spent target vault
Move new target to irradiation station
Remote vacuum connection
Few hours pump-down
Three weeks irradiation
Approx. two days without beam on one station
Vacuum volume
Spent target vault
Target
Target
(New) Target
Target hall

## Slide 35
ISAC vs ARIEL target exchange
Three weeks irradiation
One day of cooldown
Remote vacuum disconnection
Move target to spent target vault
Move new target to irradiation station
Remote vacuum connection
Few hours pump-down
Three weeks irradiation
Approx. two days without beam on one station
Three weeks irradiation
One week cooldown
Hands-on service disconnection
Move module to Hot Cell
Remote target exchange in Hot Cell
Move module to irradiation station
Hands-on service connection
Few days pump-down
Three weeks irradiation
Approx. two-three weeks without beam on one station
ISAC
ARIEL
ITW
ITE
ISAC
RIBs
APTW
AETE

## Slide 36
ISAC vs ARIEL target module – services
Service connections
Front end
+
Target
Shielding
Vacuum volume
All services routed within tall vacuum volume
All services routed in GN2
Service connections
Front end
+
Shielding
Vacuum volume
Target

## Slide 37
Medical facility for 225Ac production
Medical system in orange made up of:
  Medical module: 0.5 m x 1 m x 3 m tall, where the “rabbit” irradiation position is
  Transfer line: steel, 3” ID tube passing through the facility, with embedded sections
  Send/receive station: inside the hot cell, shielded
  Pneumatically actuated by a blower system
  Runs parasitically, with independent schedule from the main (ISOL) target timeline
Rabbit and medical target material
  Target is positioned inside the rabbit in thin, encapsulated Inconel “pucks”
  These “pucks” are produced with same method used for IPF, at the end of BL1A
  Water cooled through remote actuation mechanism
  Target material is sent for processing to users (e.g. TRIUMF Life Science Department)
  Rabbit (aluminum, steel and bronze) is either reused or disposed of alongside high-activity waste
Medical rabbit
Medical module
Transfer line
Send/receive station
Med. target material

## Slide 38
ARIEL org chart

## Slide 39
Target vessel capabilities
Target Ion Source Front End
ISOLDE-style, high-power target vessel
Improved DC current delivery
  Increasing temperature
  Thicker target heaters to reduce likelihood of breaking
  Bigger diameters possible
  Compatible with beam rastering (rotating)
Mass markers for offline/pre-delivery tuning
Gas injection
  For plasma ion source (FEBIAD)
  To support radioactive molecule production
All-metal sealing solution is possible
Feet for landing
P+ beam window
3D printed cup
Back plate
Ion source
Target
Mass markers conductors
Gas injection
Gate valve

## Slide 40: Technical Electron Beam Power ramp-up considerations
FLUKA power deposition showing bad homogeneity
Simulated temperature profile in an AETE target with a 25 kW electron beam power
The current world-record for e-induced RIB production is 500 W.
At 1 kW and for the small target, the power temperature homogeneity manageable
The more we increase beam power, the steeper temperature gradients are across the target, mostly in the beam direction
Moreover, UCx material properties are not well known, and this uncertainty makes the simulation more uncertain
  Sundeep Gosh’s PhD thesis is aimed at shining light on UCx material properties using “CHI stand”

## Slide 41: Origin of the Areas of Poor Isotope Release
Experimental LE Isotope Rates at ISAC since 2000 [1/s]

## Slide 42: AETE day-1 target
Diameter ~2 cm as APTW targets
Length ~6 cm, vertical
Volume ~ 16 cm3
UCx density: 3.5 g/cm3
Converter geometry: nominal for higher powers too
Top view of a cross section of an AETE, day-1 target (from FLUKA)
Nominal
Day-1

## Slide 43: AETE “nominal” target
Diameter ~3.6 cm as APTW targets
Length ~6 cm, vertical
Volume ~32 cm3
UCx density: 3.5 g/cm3
Converter geometry: nominal
Top view of a cross section of an AETE, long-term target (from FLUKA)
Nominal
Day-1

## Slide 44
Target vessel capabilities
Target Ion Source Front End
ISOLDE-style, high-power target vessel
Improved DC current delivery
  Increasing temperature
  Thicker target heaters to reduce likelihood of breaking
  Bigger diameters possible
  Compatible with beam rastering (rotating)
Mass markers for offline/pre-delivery tuning
Gas injection
  For plasma ion source (FEBIAD)
  To support radioactive molecule production
All-metal sealing solution is possible
Feet for landing
P+ beam window
3D printed cup
Back plate
Ion source
Target
Mass markers conductors
Gas injection
Gate valve

## Slide 45
Target vessel capabilities
ISOLDE-style, high-power target vessel
Improved DC current delivery
  Increasing temperature
  Thicker target heaters to reduce likelihood of breaking
  Bigger diameters possible
  Compatible with beam rastering (rotating)
Mass markers for offline/pre-delivery tuning
Gas injection
  For plasma ion source (FEBIAD)
  To support radioactive molecule production
All-metal sealing solution is possible
Feet for landing
Electron-to-photon
converter
3D printed cup
3d printed
Back plate
Ion source
Target
Mass markers conductors
Gas injection
Gate valve

## Slide 46
ARIEL will triple TRIUMF’s radioisotope beam science

## Slide 47: Status of ARIEL
Nominal driver beam parameters achieved, commissioning in progress.
Target ion source system fully prototyped, tested without beam and in fabrication
Target hall shielding 92% design completed, 70% installation completed
Hot cell (largest single capital invest) installation completed
200 m of RIB distribution line installed and commissioned
HRS 1/13,0000 mass resolution achieved
Radioactive isotopes from ISAC injected into CANREB, charge-state boosted and post-accelerated in ISAC II, issues with EBIS being addressed.
Nominal electron beam
BL4N vault installation
Target shielding installation
RIB transport system
ARIEL hot cell
Target system prototype
ARIEL HRS
Target module design completion

## Slide 48
2025
2027
153 days
Jan 1 - Aug 1
100%
173 days
Jan 1 - Aug 31
90%
174 days
Aug 1 - Apr 1
153 days
Dec 1 - Jul 1
522 days
Jan 1 - Dec 31
261 days
Jan 1 - Dec 31
175 days
Dec 31 - Sep 1
88 days
Sep 1 - Dec 31
303 days
Jan 1 - Mar 1
197 days
Mar 1 - Dec 1
64 days
Dec 1 - Feb 28
522 days
Jan 1 - Dec 31
23 days
Dec 1 - Dec 31
67 days
Jul 1 - Oct 1
250 days
Jun 30 - Jun 15
250 days
Jan 1 - Dec 16
152 days
Sep 1 - Mar 31
Aug 1
ARIEL - Milestones
ARIEL-II: Proton & Electron Stations
Therapeutic Isotopes
Fixed Shielding
Infrastructure
Target Hall Services
Proton Station Modules
Electron Station Modules
Driver Beam Lines
Medical Module & Target
Controls
ARIEL Operations
Ramp up
Today
2025
2026
2027
Construction
Design/Mfr/Assemble
Design/Manufacture/Assembly/Install
Design/Procure
Assembly & Test
Install
Design/Procure
Assembly & Test
Install
Design/Manufacture/Assembly/Install
Install
Controls, MPS and Safety Systems installed
Apr 1
Last system ready for Gate 4A
Dec 1, 2027
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Assy & Test
Design, Manufacture
Testing & Commissioning
Delay
APTW Install
AETE Install
Ready to start module assembly
Mar 1
Modules ready to install
Sep 1
BL4N and electron line installed
Dec 31
Ready to start module assembly
Dec 31
Modules ready to install
Dec 1
Fixed Shielding Construction Complete
Proton Station ready to receive modules
June 1
Electron Station ready to receive modules
Sep 1
Gate 3 Complete
Dec 1, 2025
Resource ramp-up in 2025 lower than planned + extended running period
Design/Procure/Assembly /Install

## Slide 49
Electrons versus Protons

## Slide 50: Projecting ARIEL AETE Yields
FLUKA ISAC in-target isotope production rates from UCx [1/s]
FLUKA AETE in-target isotope production rates from UCx [1/s]
scaled to 10 kW electron beam power
scaled to 10 kW proton beam power
Isotope production ratio AETE vs ISAC per kW

## Slide 51: ARIEL Targetry Systems
module storage
spent target storage
protons
electrons
AETE
APTW
drivers beam tunnel
RIB
RIB
ASTM
Hot cell facilities
Remote-controlled crane
2000 t of steel and concrete components
Modular RH high-power infrastructure
Symbiotic medical target in APTW beam dump

## Slide 52: Electron-Driven ISOL Challenges
e-
Target
Converter
γ
Ion source
e- 30 MeV, 100 kW
Separator
magnet
A
++
++
A
A
++
A
++
A
++
A
++
A
++
A
++
A
++
++++
A
A
++
++
A
A
++
e- LINAC
γ
60 kV Target and ion source
2000 oC
Radioactive ion beams
→ Thin target or change of orientation
→ ISAC target geometry not viable for AETE.
→ ISAC isotope extraction efficiencies not directly applicable to ARIEL AETE, but best assumption available…

## Slide 53: Hub for Training and R&D
High-power ISOL targets
ARIEL is a platform for student projects across all disciplines (engineering, math, physics, graphics design, chemistry) and all levels (high school students, 30+ coop students, 8+ master students, 10+ PhD students, post-docs)
Example: The joint University of Victoria /TRIUMF accelerator research program
2 joint faculty positions,
NSERC grant for student support in accelerator physics since 2011
  6 PhD, 4 MSc (6 international)
  So far 1 PhD and 4 MSc theses finished
One lecture taught by the adjunct faculty each year
Research topics:
  Beam physics and instrumentation (R. Baartman, T. Planche, O. Kester)​
  Superconducting RF (R. Laxdal, T. Junginger)​
  Ion Sources and Targets (A. Gottberg, O. Kester) ​
Dust in Accelerators
Target Materials
RIB Ion Sources
Material Radiation Damage
More efficient SRF Cavities

## Slide 54
TRIUMF expanded RIB program (ARIEL)
Three radioisotope production target stations
  2 x 50 kW protons and 1 x 100 kW electrons
Multi-user operation
  Up to three simultaneous radioisotope beams
  Up to 9000 RIB hours
More efficient post acceleration
  Buncher + Charge state breeder + Nier-spectrometer
  Δm/m up to 1/20,000 high resolution separation
Medical Isotopes
  Production of 225Ac in ARIEL proton target station
Development ongoing while ARIEL is being built
  RIB: nanomaterials, converters, ion sources
  Medical RIBs: 149,155Tb, 225Ac extraction
  Infrastructure: rad hard seals, irradiation damage in materials

## Slide 55: ARIEL Targetry: Green-Field ISOL Technology
ISAC inspired:
Module, crane, hot-cell-based handling paradigm
Compact shielding with radiation hard components at beam level and sensitive equipment on top of shielding
Externally inspired:
Hermetic target unit
Flexible and efficient direct target exchange
New:
GGy – level radiation hard technology
Consistent remote repair and decommissioning
Reduced material activation
Superior power management
Improved HV design and reliability
Prototype tests completed

## Slide 58: Mass Distribution in p+238U Reaction at Various Energies
50 MeV
500 MeV

## Slide 59: Mass Distribution in p+238U Reaction at Various Energies
50 MeV
500 MeV
1000 MeV

## Slide 60: Mass Distribution in p+238U Reaction at Various Energies
50 MeV
500 MeV
1000 MeV
1400 MeV

## Slide 61: Mass Distribution in p+238U Reaction at Various Energies
50 MeV
500 MeV
1000 MeV
1400 MeV
2000 MeV