## Slide 1: Accelerator technology R&D at TRIUMF
Oliver Kester
Director, Accelerator Division
TRIUMF-CNRS IRL workshop April 23, 2026

## Slide 2
  The TRIUMF accelerator complex and the future - ARIEL
  Accelerator science at TRIUMF
    Beam physics, secondary particle production and SRF/RF
  Areas of accelerator and associated technologies in the IRL
    Superconducting RF
    ISOL: Rare isotope production with electron beams and laser ionisation
    ECR Ion Sources
    MRTOF and Penning trap (TITAN)
Outline

## Slide 3
TRIUMF is Canada’s Particle Accelerator Centre, which essentially leads most of the Canadian activities in accelerator sciences.
We have more than five decades of experience in building a rich particle accelerator infra-structure that enables cutting-edge research while growing accelerator expertise.

## Slide 4
ARIEL will have two high power driver accelerators the 520 MeV cyclotron and the ARIEL SC electron linac.
It will triple present rare isotope capabilities of the Isotope Separator and Accelerators (ISAC) by adding
  a 50kW proton target station
  a 100kW electron target station
  Unique beam preparation and transport system (CANadian Rare isotope facility with Electron Beam ion source - CANREB)
ARIEL is the only rare isotope facility that can and will provide three RIB beams simultaneously to experiments.
ARIEL: ISAC×3

## Slide 5: To establish and operate ARIEL
R&D required on:
  Target materials and production
  Offline target operation on a test stand – TISA
  Resonant laser ion sources
  Remote handling: Target decay storage vault, hot cells, target hall shielding, remote controlled crane
  Machine protection system: Driver accelerators and electron and proton beam transport lines in the same tunnel
  SRF linac technologies
  Automatic beam tuning, digital twins
Target hall shielding
TISA

## Slide 6: Accelerator science at TRIUMF

## Slide 7: ACC Division physics and technology activities
  Areas of activities:
  Operation, refurbishment and upgrade of the TRIUMF accelerator complex
  Capacity increase via design and construction of new accelerator systems (ARIEL, CANREB, THz radiation)
  Domestic and international accelerator projects
   Accelerator research and development
  based on three pillars of excellence in
  beam physics
  secondary particle production
  SRF/RF technologies and research

## Slide 8: Beam Physics
Beam Physics does focus internally on cyclotrons and linacs and externally on ring accelerators / colliders:
Beam physics studies of the ARIEL e-linac for THz radiation and DarkLight. Recirculation ring and Energy Recovery Linac operation mode. Rastering of 100 kW e-beam on the ARIEL electron convertor target.
Commissioning protons (BL4N), simultaneous electron&proton operation. Increasing the beam current in the cyclotron (500 mA capability, 400 mA daily operation) and overcome issues of high current beam extraction into three beam lines.
RIBs from ARIEL  towards regular ARIEL HRS operation at a resolution oft 20,000.
Dust in accelerators – new hot topic in the accelerator community.  UFO analysis in LHC and dust migration in SC linacs. Investigating the charging mechanism of dust and migration in the ARIEL electron linac (Aveen Mahon, Ph.D. student Uvic)
Collaboration with CERN on LHC: Beam-Beam Long Range and compensation methods
Test of Wire Compensators for LHC Run 3 around IP1 and IP5

## Slide 9: Automatic beam tuning activities
Transmission
MCAT – TRANSOPTR model of the real machine continuously synchronized (O. Shelbaya, scientist)
Bayesian Optimization for Ion Steering (BOIS): Optimizes corrective steerers to maximize beam current on a Faraday cup (O. Hassan, Ph.D. UVic).
Decoupled Machine Coupled ACC tuning (MCAT) and beam orbit correction using Bayesian Optimization (BO).
Easier parameter space to optimize and influence of quadrupole hysteresis is reduced.  limits server requirements Much faster convergence of the orbit correction!
In the future this approach will be extended to the ion sources at TRIUMF (M.Sc. A. Katrusiak, UVic).

## Slide 10: Targets and Ion Sources Research Examples
Converter targets
R&D on high power electron convertor target for ARIEL
e-
Target
Converter
γ
Ion source
→ ISAC isotope extraction efficiencies not directly applicable to ARIEL AETE, but best assumption …
→ Thin target or change of orientation
→ ISAC target geometry not viable for AETE.
  ARIEL proton & electron targets and target assemblies have been prototyped, optimized and built.
Proton-to-neutron convertor to explore fission fragment production

## Slide 11: Targets & Ion Sources research examples
Irradiation damage studies – example: PEEK  tensile and fracture properties
Student-led research & development projects continue in the fields of
  Novel target materials for intense radioisotope release  synthesis of highly porous microstructures, post-irradiation examinations and target material thermal conductivity  Development of TiC material ongoing
  Material irradiation damage for accelerator and nuclear applications  Radiation damage studies
  Example: Canadian Nuclear Labs (CNL) collaboration: Temp. control stage, material irradiation and characterization  ongoing studies on Al and Cu alloys for beam intercepting elements, and PEEK seals for ARIEL targets
  Applications of accelerators and high-power targets for neutron and medical isotopes production
  Ionization schemes and laser ionization efficiency  at the ARIEL laser ion source systems
Helium bubbles, ISAC irradiated Al6061

## Slide 12
SRF science and technology (2001-present)
Development towards the ISAC-II Superconducting linac motivated SRF development and infrastructure at TRIUMF
Cavity design, cryomodule design and assembly, fundamental SRF studies are now core competencies at TRIUMF
SRF activities focus on operation of the SRF linacs, external collaborations (HI-Lumi) and student led research in fundamental science and technology
ISAC-II Cryomodule

## Slide 13: SRF Accelerators at TRIUMF
40MV ISAC-II SRF heavy ion linac @ 106MHz - operational since 2006
30MV ARIEL SRF 10mA electron linac @ 1.3GHz – first beam 2014

## Slide 14
`-SRF’ Facility for SRF material characterization
Helmholtz coil
New beamline extension installed at -NMR facility for SRF materials characterization
`-SRF’ - Unique facility in the world for depth profiling materials in parallel magnetic fields up to 200mT – SRF regime – critical field of Nb
First results published in Nature Scientific Reports show Meissner screening in two samples as a function of applied field:
Clear difference in screening profile between the two samples
Clear breakdown of Meissner screening with applied field
Baseline
Doped
https://doi.org/10.1063/5.0137368
https://www.nature.com/articles/s41598-024-71724-5

## Slide 15: Areas of accelerator and associated technologies in the IRL

## Slide 16: Plasma Processing
ARIEL clone cavity
Moving He plasma from cell to cell
Plasma processing is a surface cleaning method used in SRF to reduce the negative impact of field emission that lowers the useful accelerating gradient
  The cleaning method can be deployed with the cavity installed in the linac
Development for ARIEL – Off-line studies demonstrating readiness for electron linac deployment (Will Stokes – UVic MSc)
Development for ISAC-II – test cavity prepared for collaborative study at IJCLab – Will Stokes to travel to IJCLab in July to work with Camille Cheney (PhD IJCLab) to optimize processing of an ISAC-II quarter wave resonator based on Spiral2 QWR processing
Cell: 7
6
5
4
3
2
1
Gas evolution cell by cell during processing
ISAC-II Cavity copper model
Spiral2 QWR

## Slide 17: SRF heat treatment study (TRIUMF/IJCLab)
TRIUMF’s coaxial cavity program has revealed reduced BCS resistance for high frequency mode after mid-T heat treatment but with higher residual resistance
Concerned about growth of lossy carbides during heat treatment
Sample heat treatment study with IJCLab
  Student visit - Chahinez Boutilaa (IJCLab) - paper/talk SRF2025
  IJCLab/TRIUMF collaborative investigation of carbide formation as a function of temperature on niobium samples
  X-ray Photoelectron Spectroscopy (IJCLab) and TOF-SIMS (Western U.)
Study determined the temperature regime for carbide growth
TRIUMF Rf induction oven
Carbide formation vs temperature
No carbide
Carbide growth
Carbide diffusion
2K – mid-T bake – 1166MHz
TRIUMF coaxial cavities
Notes: XPS=X-ray photo-emission spectroscopy, TOF-SIMS=time of flight secondary ion mass spectroscopy

## Slide 18: ARIEL Electron Target station
Photofission production from electron beam like at ALTO  we are using 30 MeV electrons but e-linac will be build out to its design energy of 50 MeV
Can provide competitive yield of many neutron rich species with relatively low isobaric contamination with respect to proton induced spallation.
High beam power requires converter technology

## Slide 19: Technical solution for high electron Beam Power
The current world-record for e-induced RIB production is 500 W (ALTO). We will go towards 100 kW.
At 1 kW and for the small target, the power temperature homogeneity manageable  the more we increase beam power, the steeper temperature gradients are across the target, mostly in the beam direction
UCx material properties are not well known, and this uncertainty makes the simulation more uncertain  online tests required
ISOLDE-style, high-power target vessel
Convertor integrated in the beam window

## Slide 20
ARIEL RILIS p+
~2031
muon spin rotation
Irradiation p+, n
isotope production
ultra cold neutrons
meson hall
480 MeV, 100 μA p+
e- LINAC
30 MeV, 10 mA
ITW
ITE
AETE
ISOL
(ARIEL)
ISOL
(ISAC)
user facilities
ISAC ISOL targets (since ~ 2000)
ARIEL ISOL targets (from ~2026)
cyclotron & beamlines (since ~1975)
e-linac and beamline (since ~2014)
RIB lines
APTW
BL1A
BL2A, 100 μA p+
BL2C
BL4N, 100 μA p+
experimental hall (ISAC I)
radioactive ion beams (RIB)
~10 user facilities
nuclear & atomic physics
material sciences
experimental hall (ISAC I)
TRIUMF RILIS
ARIEL RILIS e-
~2027
2 accelerated beam
3 laser ion source systems in the ARIEL era

## Slide 21
3 laser ion source systems – ARIEL era
Ionization schemes for 45 elements used online (2026)
ionization schemes for 9 elements ready to go online (2026)
6ea ALIS p+ station tuneable lasers under construction
6ea ALIS e- station tuneable lasers (FY2031)
ALIS p+ and e- laser beam transport under construction
ALIS laser cleanroom commissioning Q3 2026
most complex component “4-plate birefringent filters” developed (BSc/MSc student), build of 12ea in Q2/Q3 2026
TRIUMF TiSa laserintra-cavity,
birefringent filter assembly characterization (2026)
students (Alexia Landry / Lucie Savajols)

## Slide 22: TRIUMF Charge State breeders
drift tubes
solenoid
ion beam
electron beam
anode
electron collector
electron repeller
barrier electrode
1+
n+
CANREB EBIS (similar to the TITAN EBIT): 6T superconducting magnet in a Helmholtz coil set-up  Allows radial optical access to the electron beam. Running at Ultra High Vacuum!
separation
of rest gas ions
singly
charged
ions
n+ ions
solenoid
coils
Magnetic field confinement
RF injection
TRIUMF Charge State Booster (CSB): A 14.5 GHz PHOENIX Electron Cyclotron Resonance Ion Source (ECRIS) from PANTECHNIK  running at 10-8 mbar (world record), still significant rest gas ion background

## Slide 23: Current research on TRIUMF ECRIS devices
Increase of charge breeding efficiency by implementing
  two-frequency heating technique that provides two resonance zones
  frequency tuning technique to find optimize RF matching (scanning the microwave frequency)  Bayesian Optimization
Improving the beam properties by optimizing the extraction system
  Simulations with the code IGUN©
  Benchmarking with emittance measurements using beam tomography (quadrupole scans)

## Slide 24: TITAN + IJCLab: Ion Traps for Mass & Exotic Decays
Multi-Reflection Time-Of-Flight Mass Separator / Spectrometer:
Ions bounce between electrostatic mirrors to temporally separate by m/q
Typical R ≈ 500k
In-situ beam purification  dynamic range 104-8 & yields ≥0.006 pps
Benefits RIB development
Collaboration via w/ Dave Lunney

## Slide 25
TRIUMF operates a rich array of particle accelerators for both hadrons and electrons  requires expertise in Target and Ion Source, Beam Physics and SRF and a healthy R&D program and collaboration
The future ARIEL facility is the only rare isotope facility that will provide three RIB beams simultaneously to experiments.
The infrastructure and know-how provides opportunities for international collaboration, like in NPAT!
Summary

## Slide 26: Thank you, Merci
www.triumf.ca

## Slide 27
Backup slides

## Slide 28: Core Competencies of the Accelerator Division
Operation of a sophisticated accelerator facilities with simultaneous delivery of multiple beams
Particle sources: H--sources, Heavy ion sources, charge state breeder (ECR and EBIS), electron guns
Beam physics: Simulation codes, beam tuning applications, physics of space charge dominated ion and electron beams, collider beam physics
Beam transport systems: Electrostatic and magnetic beam line systems, high resolution mass separators
Target technology and ISOL systems: High power RIB targets, target ion sources (SIS, FEBIAD, LIS), in-target beam purification technologies (IG-LIS, cold transfer line, proton-to-neutron converter), nuclear spin polarization, muon production targets, high-power targetry, material radiation damage
Remote handling: Hot cell technology, robotics, irradiated target and radioisotope handling, manipulation of activated and contaminated parts, cyclotron services, radioactive waste management
Accelerators: Linacs (heavy ions and electrons) normal and superconducting, cyclotrons (H-), synchrotrons, FFA, accelerator design
Accelerator systems: RF (low level and power RF, SRF, cavity development), cryomodules, vacuum (including UHV), cryogenic systems, power converter technologies, high and low intensity beam diagnostics (ions and electrons), machine protection
Accelerator Application: Medical isotope production, irradiation (material, therapy, electronics,…)
Education: Seminars, lectures, lab research projects and thesis research

## Slide 29: Link to TRIUMF 20-year vision: Accelerator Science and Facilities
Isotope Valley
With ISAC+ARIEL+IAMI we will greatly expand our capabilities, and establish TRIUMF as a leading global center for isotope research.
Isotopes for physical science
Isotopes for life science
Isotopes to cure Canadians
Canadian Hub
We are Canada’s centre of excellence in accelerator-related science and technology.
We centralize knowledge, and diffuse it through training, counsel, and collaborations.
With our always evolving expertise we remain a leader in Canada’s transformation to a knowledge based economy.
Big Science — Big Tech
International collaborations are key to contribute to the most significant discoveries, attract talents, and maintain cutting-edge expertise.
We support international projects by leveraging our core knowledge and engaging Canadian industry.
We build on our strengths to serve science and invent life-changing technologies.
https://beamphys.triumf.ca/~tplanche/20-year-vision-acc.pdf

## Slide 30: TRIUMF accelerator complex
Primary beam driver:
Cyclotron, 500 MeV, H-
Produces rare isotopes, neutrons and muons!
Isotope Separator and Accelerator facility - ISAC
Isotope Separator Online (ISOL) facility ISAC-I: Normal conducting-linac, 0.15-1.5 MeV/u
ISAC-II: Superconducting-linac, 5-15 MeV/u
Advanced Rare Isotope Laboratory - ARIEL Superconducting electron linac
30 MeV, 10 mA, cw
4 Cyclotrons for medical isotope production
(with a TR24 to be commissioned in the Institute for advanced Medical Isotope – IAMI)
500 MeV
Cyclotron
ISAC-II
High energy
ISAC-I
Low and
medium
energy
ARIEL
Cyclotrons
for medical
Isotope
production

## Slide 31
High Resolution Spectrometer
Two 90-degree dipole design
Electrostatic Multi-pole corrector between dipoles
M/M=1/16000 resolution tune demonstrated with high transmission
Latest commissioning results
Emittance at exit slit before multipole correction
Emittance at exit slit after multipole correction
Collaboration on the DESIR-HRS

## Slide 32
SRF: RF Dipole Cryomodule Project at TRIUMF
TRIUMF will produce four crab cavity cryomodules for the Hi-Lumi project at CERN by July 2028
Eight crab cavities fabricated through a US collaboration
32

## Slide 33: THz radiation project
650 MHz e-Gun
1.3 GHz SRF Cavities
Transport
to ARIEL
THz chicane
septum
beam dump
Photo-gun
TRIUMF, as part of a pan-Canadian collaboration (including TRIUMF and CLS), will receive CFI funding to develop a THz light source within the ARIEL e-linac hall.
Addition of a new photo-gun to produce short, high brightness, low emittance, beam bunches, and a bunch compression chicane.
A partial recirculation arc and septum will be used to install the chicane off the main linac beamline.
Additional funds are being sought to complete the recirculation ring for either Energy Recovery or Energy doubling for DarkLight for instance.

## Slide 34: Example domestic: PC-CANS
TRIUMF is collaborating with the University of Windsor and the Canadian neutron scattering community towards an accelerator-based neutron facility Collaboration has conceptualized a stageable prototype CANS facility, PC-CANS, based on linac technology.
PC-CANS will allow competitive rates for neutron science, while simultaneously producing F18 for PET and neutrons for a dedicated BNCT research and development facility.
The PC-CANS prototype would be the first CANS in Canada and the first for BNCT in North America.
The project will augment and solidify TRIUMF core competence in linac and target systems and the proton accelerator technology is well aligned with applications