## Slide 1: Interactions of Particles through Bulk Matter: THE Fundamental of Radiation Detectors
Dr. Marcello Pavan
TRIUMF
GRIDS 2026

## Slide 2: Overview
What is a Detector?
Energy Loss of Heavy Charged Particles
Electron/Positron Energy Loss
Photon Energy Loss
Particle “showers”
Cherenkov radiation
Summary and Further Reading

## Slide 3: References
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
W.R. Leo, Techniques for Nuclear and Particle Physics Experiments (Springer-Verlag)
Fernow, Richard, Introduction to experimental particle physics (Cambridge University Press; ISBN 0-521-37940-7)
Grupen, Claus & Shwartz, Bori, Particle Detectors (Cambridge Monographs; ISBN 978-0-521-18795-4)
Viehhauser, George & Weidberg, Tony, Detectors in Particle Physics – A Modern Introduction (https://archive.org/details/oapen-20.500.12657-88075/mode/2up)

## Slide 4: What does a (modern) Particle Detector DO exactly?
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
Basically one thing:
  Generate and then register a pulse of ionization
  Generate a flash of light
    But then that light must be converted to a pulse of ionization before its registered

## Slide 5: Particle Detector functions
simply detect (or not!) passage of a particle into a larger detector volume or array
  i.e. neutral particles won’t “trigger” system
Measure time-of-flight between two parts of detector  measure speed
  Can be used to identify particles
Localize charge to infer passage of particle at a certain point
  Track trajectory through many layers
Measure energy loss and total energy deposit
  Can be used for Particle Identification
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
Notes: Chernenkov radiation has a threshold

## Slide 6: Examples of Particle Detectors – “light-based”
Passage of ionizing radiation excites atoms to release light
Scintillators (Darren Grant June 4)
  Light output depends on energy deposition
  No inherent directionality to light
  Solid or liquid material
Cherenkov Detectors
  Light output depends on energy and speed of charged particle
  Light “cone” highly directional
Ultimately, light must be converted to electrical pulse to be “registered”.
DAQ & Electronics (Ben Smith June 8)
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary

## Slide 7: Examples of Particle Detectors – Ionization based
Semiconductor-based detectors (Serge Charlebois June 3):
  For precise position localization
  Good timing accuracy
  Expensive
Gas-based detectors (Scott Menary June 2):
  Position localization
  Energy measurements
  Can be deployed over large areas
Crystal-based detectors (Garnsworthy, Vachon, Diamond)
  Very dense, can stop particles in short distances
  Generally excellent energy resolution
  Weak position resolution, decent timing
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary

## Slide 8: Energy Loss interactions crucial to detector design choices
Modern detectors, especially in particle physics, are a complex mix of subdetectors with multiple functions
  Designing these systems half science, half art, half engineering
  The performance of these complex systems dictate what can and cannot be detected, and what can and cannot be discovered (or inferred)
  They really are foundational to modern subatomic physics
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary

## Slide 9: Therefore, important to understand basics of particle interactions with bulk materials, especially EM energy loss
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary

## Slide 10: Which particles CAN we detect directly?
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary

## Slide 11: Which other particles CAN we detect directly?
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
+ charged stable or long-lived nuclei (4He++, 16O+, etc)

## Slide 12: Which particles CAN we detect semi-directly? i.e we can detect the scattered particle and infer the incident one
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary

## Slide 13: ALL other particles can be “detected” only indirectly through the decay products that we can detect.
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
Aside: this is one of THE key challenges for identification of short-lived particles…
i.e we detect the daughter products and infer the parent

## Slide 14: Particle interactions and Fundamental forces
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
Particle must interact somehow with the detector in order to be “seen”
  Gravity will be ignored as irrelevant
Ultimately, either the particle or interaction products must interact electromagnetically in order to be detected electronically

## Slide 15: Relativistic Kinematics notation we will need…
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
These show up all over the derivation of charged-particle energy loss we are about to explore.
Velocity:
Energy:
Momentum:
Taking c=1, m=m0:

## Slide 16: QM reigns: Interactions are probabilistic
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
The interaction probability p depends on:
  Density of medium r
  Thickness of medium d
    Define “areal density” S= d*r
    Units [mass/area], Usually [g/cm2]
  Interaction “cross-section” s
    units [area], usually “barn”
    1 barn = 10-28 m2 = 100 fm2
    Depends on specific interaction (strong, weak, EM), energy, etc
So, the interaction rate R …
  R = I *s *S, where I=Nincident/(unit time)
Define:
  r = medium density
  d = medium thickness
  S = medium surface area
  N2 = # particles in medium volume
  s = “cross section” probability of incident particle on medium particle
  N1 = # incident particles
Notes: Cross section is interaction probability per unit area

## Slide 17: The Mean Free Path: l
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
The mean distance between successive interactions:
Derivation: Calculate the probability that a particle doesn’t interact
after having traversed a length x in the medium of area density S
  Interaction probability per unit distance
    w = p/d = σ (S/d)
  Interaction probability between x et x+dx
    w dx = σ (S/d) dx
  Probability to not have an interaction between x and x+dx
    P(x+dx) = P(x) (1- w dx)
      Expanding: P(x) + P’(x)dx = P(x) – P(x) w dx
    Therefore P’(x) = -wP(x)
    P(x) = e-wx
Define thus,
Notes: Substitute P(x) = exp(-w x) into the integral

## Slide 18: Energy Loss by Heavy Charged Particles
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
“Heavy” means all charged particles heavier than electrons (positrons)
At low energy (keV to MeV)
  Energy loss dominated by EM interactions with atomic electrons
    Size of an atom ~10-10 m
    Size of a nucleus ~10-14 m ~ 10fm
  Interaction transfers part of the energy of the incident particles into kinetic energy of the atom that will either get excited (electrons move to higher orbitals) or ionized (electrons break free)
    The physics behind this is the same in both cases, just differences in the amount of energy transferred
The interaction cross section can be very small (~10-21 m2) but the high atomic density (NA= 6 *1023 g-1) of most materials can result in significant energy loss
  10 MeV protons lose all their energy in 0.25mm of copper (on average)

## Slide 19: “Classical” derivation of Energy Loss
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
Let’s dispense with all the quantum mechanically mumbo jumbo to gain some intuition…
  An incident charged particle with charge z1e creates an electric field at the position of a particle 2 in the medium.
  The incident particle is at a transverse distance b (impact parameter) from the medium particle
  By symmetry the net force on 2 is transverse to the trajectory of 1.
  If v1 is small, we can ignore the magnetic field.

## Slide 20: “Classical” calculation of momentum/energy transfer
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary

n.b. the energy loss is dominated by the interactions with atomic electrons, not the nuclei (mnucleus >> me).
1/b2v12 => energy loss is dominated by close collisions and slow particles.
The force F by the electric field is F = q
  So the momentum transfer Dp is:
  Thus the energy transfer per interaction DE is:

## Slide 21: Now integrate over all atomic electron interactions…
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
In a vertical slice of the cylinder at right, there are
atomic electrons.
Integrating over all the interactions ne*DE we get the energy loss per unit length,
Doing the integral, and using ne = r(NA/A) Z and the vacuum permittivity e0, we get:

## Slide 22: “Classical” derivation of Energy Loss, final result
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
The ln(bmax/bmin) term diverges for either
bmax  ∞ or bmin  0
∴ introduce physically realistic limits
If projectile mass >> me, then DEmax,e = 2mev2 , consequently:
Minimum energy transfer must be enough to ionize an atomic electron So DEmin,e = I (ionization constant), consequently:
bmin bmax

## Slide 23: “Classical” derivation of Energy Loss, final result
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
Redoing the integration with the new ”realistic” limits bmax , bmin , we get our final result
bmin bmax
Where re is the “classical electron radius”
1/v2 decrease at low energies
Slower ln(v2) at high energies
Depends on (incident charge)2

## Slide 24: “Classical” derivation of Energy Loss, final result
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
1/v2 decrease at low energies
Slower ln(v2) at high energies
Depends on (incident charge)2

## Slide 25: Result of better Quantum Mechanical calculation
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
Our semi-classical derivation was:
Hans Bethe and Felix Bloch did the QM calculation (famous Bethe-Bloch formula) and got: where d is a charge density correction, and Wmax = max (DE) for a collision for large M

## Slide 26: Bethe-Bloch formula: new features
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
The ionization constant (I) groups together the global properties of atoms
  Measured experimentally for different materials
  Parameterized as a function of the number of electrons (Z)
The charge density (δ) correction is due to:
  the electric field of the incident particle polarizing the atoms close to its trajectory thus reduces the impact of the electric field of the further away electrons (like a screening effect) which consequently reduces the energy loss i.e. δ >0
  The effect becomes larger if the energy of the incident particle increases (longer range electric field) or the density of material increases

## Slide 27: Bethe-Bloch formula in action
Particles with larger charge lose energy faster
Heavier materials do not stop particles as well, BUT density makes it up
Energy loss is inversely proportional to the velocity squared (v2)
Relativistic rise due to the relativistic deformation of the Coulomb field, which makes bmax larger)
“Minimum ionization”
dE/dx 2 MeV/(g/cm2). at
Fermi Plateau:
Screening of the Coulomb field by atomic electrons for large b.
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary

## Slide 28: Material Properties vis a vis Energy Loss
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
.

## Slide 29: Energy loss in the real world
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
Different particles traversing gaseous chamber in the ALICE detector at the CERN LHC

## Slide 30: Range of stopped heavy charged particles in thick media
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
“thick” meaning thick enough to stop all the particles
As particle in a medium loses energy, the amount of dE/dx changes.
  Starting from above the minimum ionizing energy, dE/dx first decreases, until 𝜷𝜸~𝟑
  Then it increases due to dE/dx rise.
  Eventually particle loses all of its energy and stops.
Can calculate the average range R from:

## Slide 31: Range scaling relations
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
Doing the range integral yields average range R: where h is a universal function
This demonstrates the scaling law, e.g. comparing protons to alpha particles:
  At a given energy, lighter particles go deeper, linearly
  Particles with larger charge go shallower, quadratically

## Slide 32: Fluctuations in Energy Loss
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
The aforementioned discussion was about the average energy loss (and range)
But, energy loss is a statistical process. The number of ionizations varies depending on particle trajectory.
  One expects a roughly Gaussian distribution for large #s of collisions
  However, sometimes a “head on” collision with an atomic electron can occur, where the electron ejects with substantial energy (maybe even exiting material).
  These electrons are called d-rays, resulting in a long Landau tail at large energy transfer

## Slide 33: Energy Loss by Electrons and Positrons
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
Bethe-Bloch assumes M >> me
  When M= me , even a single interaction with an atomic electron can change the incoming particle energy substantially
  Moreover, the positron also can annihilate with an atomic electron
So we get a different dE/dx for e- and e+
  Electron Moller scattering
  Positron Bhabba scattering

## Slide 34: Energy Loss by Electrons and Positrons
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary

## Slide 35: Bremsstrahlung energy loss for Electrons and Positrons
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
Charged particles emit EM radiation when accelerated in an electric field.
e.g. a particle slowing down due to dE/dx in the electric field of a nucleus
  For photons of wave-number k, bremsstrahlung cross section is:
Scales as 1/(mass of incoming particle)2
[m()/m(e)]2 40,000
The cross-section drops off with increasing photon energy as 1/k
Heavy elements are more efficient at producing brems.
Because of 1/M2 dependence, really only matters for electrons/positrons in most scenarios

## Slide 36: Electron and Positron Bremsstrahlung
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
Charged particles emit EM radiation when accelerated in an electric field.
e.g. a particle slowing down due to dE/dx in the electric field of a nucleus
For photons of wave-number k, bremsstrahlung cross section is:
Scales as 1/(mass of incoming particle)2
[m()/m(e)]2 40,000
Cross-section falls as
1/k with increasing g energy
Heavy elements are more efficient at producing brems.
Because of 1/M2 dependence, really only matters for electrons/positrons in most scenarios

## Slide 37: Bremsstrahlung energy loss, part deux…
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
Energy loss due to bremsstrahlung is:
where
and
Energy loss increases with increasing Eincoming
  Radiation energy losses dominate above Ecrit
  Lower Ecrit for higher Z media. (e.g. lead, tungsten,..)

## Slide 38: Radiation length: LR (or X0)
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
We can rewrite bremsstrahlung energy loss as:
where,
Solving the simple ODE, one gets:
X0 is the radiation length, where on average the incoming particle energy is reduced by a factor 1/e due to bremsstrahlung

## Slide 39: Material Properties vis a vis Energy Loss
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
.

## Slide 40: Photon Interactions
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
Photons interact with matter in 4 basic ways (here ordered by increasing photon energy):
  Photoelectric effect: photon absorbed by atomic electron, which is then ejected
  Rayleigh scattering: photon scatters coherently off all the electrons in an atom
  Compton Scattering: photon scatters incoherently off a single atomic electron
  Pair production: For Eg>2me, photon converts into an electron-positron pair
n.b. Photon interactions are important as eventually even high-energy particles end up producing photons.
(foreshadowing…)
Also, photons are either absorbed (disappear) or scattered by a large angle, largely keeping its energy
  So one usually refers to photon attenuation rather than energy loss

## Slide 41: Rayleigh and Photo-electric effects
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
Rayleigh dominated by very low wavelengths: sR ~ 1/l4 (why the sky is blue)
In the Photoelectric effect, an atomic electron is freed after absorbing a photon Te = k - Ebind
  where Ebind is the binding energy of the electron (which depends on the orbital layer: k,l,m)
  This process (γ+e  e) is not possible for a free electron since it violates momentum conservation
If Eγ > BK-shell, the cross section is dominated (80%) absorption in the innermost layer k as the proximity to the nucleus allows easier absorption of the recoil energy

## Slide 42: Atomic relaxation after P.E. effect
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
General trend of p.e. cross section is sp.e. ~ Z5/Eg-7/2
i.e. dominates at low energies in heavy materials, like lead
Low energy cross sections complicated by electron shell structure
  Cross section jumps way up at each shell
Shell edges
After the electron is ejected, another atomic electron from a higher orbital (say L) can “drop down” into the hole (say K), resulting in either:
  a new emitted X-ray photon with energy BK – BL
  or a second “kicked out” (Auger) electron when BK – BL > BL

## Slide 43: Compton Scattering
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
Photon scatters off a (quasi-)free electron
Eg >> Bi i=K,L,M, etc
Angular distribution (Klein-Nishima)
  At low energy, angular distribution is symmetric
  At high energies, it peaks near 00
The total cross section is:

## Slide 44: Pair Production
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
For Eg > 2me ~ 1.2 MeV, photon can convert into a e+/e- pair in the field of a nucleus (or an electron)
  The nucleus supplies the other photon to conserve momentum
    Recoil energy of nucleus is very low <1 MeV
Dominates photon interactions at high energies
At low energies, cross section rises with Eg
But above ~ 1GeV, it becomes ~constant due to a screening effect and only depends on the medium

## Slide 45: Electromagnetic Showers
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
So we’ve seen that:
  electrons can interact to produce photons (bremsstrahulung), and
  photons can interact to produce electrons (pair production, Compton, etc)
these interactions happening in combination result in an electromagnetic shower
  Particularly important at high energies
  Rigorous calculation only by Monte Carlo simulation
Starting with a photon E0, after a distance:
  X0: create e+/e- pair each with E0/2
  2 X0: Bremsstrahlung yields 4 particles (e+,e-, g, g)
  N X0: after each step X0 get twice as many particles, each with ½ the energy E(N)=E0/2N
  Shower development stops when E(N)=Ecrit, or Nmax = ln(E0/Ecr)/ln(2)

## Slide 46: Hadronic Showers
Strong interactions between hadrons (pions, protons, neutrons) and nuclei in medium also can lead to showers.
  Strong interaction cross sections MUCH less than EM, but at high energies in dense media, it becomes important
Shower initiated by the secondary hadrons produced by the primary incident hadron
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
  Longitudinal development characterized by nuclear absorption length lnucl
    lnucl >> X0 so detectors have to be much thicker than for EM showers
  Secondary hadrons have high transverse momentum, so shower width is wider
Fluctuations are large (due to lower interaction probability), so energy measurements using hadronic showers are less precise than for electrons and gs

## Slide 47: Shower Calorimeters at CMS and ATLAS (CERN)
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
1m
5m
Silicon tracker
EM calorimeter
hadronic calorimeter

## Slide 48: Cherenkov Radiation
Emitted when a charged particle passes through a dielectric (polarizable) medium with vparticle > clight/n, where n=refractive index
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary
  Particle polarizes the molecules in the medium
  Molecules de-exciting emit EM radiation isotropically in the rest frame
  Locus of each outgoing wavefront outruns the previous wavefront
    This results in a “shock front” at an angle qch to the trajectory
Exact form of emission angle:
  At threshold qch =0, which implies
  i.e. particles heavier than mth will not emit light
   particle discriminator

## Slide 49: Differential Cherenkov detector
bmin determined by threshold 1/n
bmax determined by:
  Physical aperture
  Total internal reflection angle in light guide
e.g using diamond (n=2.42) as radiator, we have bmin =0.413 and bmin ~ 0.454
Db/b ~ 0.10 resolution
Best differential counters can achieve
Db/b ~ 10-7 resolution for particle discrimination
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary

## Slide 50: RICH imaging Cherenkov detector
Ring Imaging Cherenkov uses position sensitive light detectors to image the Cherenkov light cone patterns
  use to determine type of particle, its speed, and its direction
  e.g. basis of the huge underground neutrino detectors at Kamiokande, Japan
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary

## Slide 51: Still Awake?
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary

## Slide 52: Summary
Reviewed the fundamental electromagnetic interactions at the basis of all particle detectors
  Ionization by charged particles (heavy, and electrons)
  Radiation by accelerating charged particles
The physical dependencies of these interactions are essential for detector design and performance
The “art” and “engineering” comes in the clever use of these mechanisms and in their optimization to achieve a specific goal.
i.e. it is worth your while to internalize these principles and mechanisms as you pursue experimental subatomic physics
Basics
Energy Loss
e-/e+
Photons
Showers
Cherenkov
Summary

## Slide 53
Thank you for your attention
Merci
Follow us @TRIUMFLab
www.triumf.ca