## Slide 1: New TRIUMF facility: ARIEL
Oliver Kester
Director, Accelerator Division
for the ARIEL team
KEK / TRIUMF Symposium September 28, 2025

## Slide 2
The Advanced Rare IsotopE Laboratory (ARIEL) is the world’s most powerful Isotope Separation OnLine (ISOL) complex.
It will triple the present rare isotope capabilities of the Isotope and ACcelerator facility (ISAC).
ARIEL is the only rare isotope facility that will provide three RIB beams simultaneously to experiments.
ARIEL: ISAC×3

## Slide 3
TRIUMF campus
ARIEL - TRIUMF’s flagship project
Simultaneous RIB production from 3 targets
  50 kW existing ISAC proton target
  50kW new ARIEL proton target
  100kW new ARIEL electron target
Multi-user capability with more and new isotopes for
  Nuclear Structure and Dynamics
  Nuclear Astrophysics
  Fundamental Symmetries
  Materials Science
  Life Sciences
Unique beam preparation and transport system (CANadian Rare isotope facility with Electron Beam ion source - CANREB)
  High resolution separator
  Beam preparation with RFQ cooler buncher and EBIS

## Slide 4
Development of ARIEL – the ARIEL project
ARIEL-I (2012 - 2014) e-Linac, beam tunnel, target building
ARIEL-II (2017 - 2028) target stations, shielding, hot cells, RIB distribution
CANREB (2014 - 2019) charge state breeding and purification for post-acceleration in ISAC II
Therapeutic Isotopes (2020 - 2028) production and processing of medical isotopes at ARIEL proton target station
$200 million investment by federal and provincial governments; supported by 21 universities across Canada, about 700 FTE years total effort

## Slide 5
ARIEL
500 MeV – 400 μA
P+ Cyclotron
30 MeV – 10 mA
e-Linac
AETE
ARIEL
(ISOL)
ARIEL ISOL targets (from 2027)
Cyclotron & beamlines (since ~1975)
E-linac and beamline (since ~2013)
RIB lines
APTW

## Slide 6: ARIEL – superconducting electron-Linac
e-gun
cryo-module 2
10 kW beam dump
cryo-module 1
e-Gun delivers max. 10 mA at 300 keV beam
The injector cryomodule (1) accelerates to 5-10 MeV
The accelerator cryomodule (2) is equipped with two cavities and reaches max. 30 MeV.

## Slide 7: e-Linac updates
10 kW demonstration @ 30 MeV : September 2021
Reliability efforts
  3-days of continuous beam delivery in March 2025
Currently e-Linac shutdown
  Next step, in 2027: commissioning the beamline in the ARIEL tunnel

## Slide 8
Upcoming:
Build and install a new photo-gun capable of producing high-charge electron bunches.
Construct a laser lab to host the laser system.
Design, build and install a magnetic compressor to shorten the electron bunches (wavelength >> bunch length)
Milestones:
Succeeded to secure a CFI grant in 2023.​
A series of demonstration experiments were conducted since 2024 to learn the THz-oriented e-Linac operation and to develop the THz instrumentation.
First e-Linac-THz paper published 2026 in Canadian Journal of Physics [1].​
e-Linac : Terahertz (THz) test facility project
[1] V.A. Verzilov, et. Al. 2026. First observation of coherent THz radiation at TRIUMF electron accelerator. Canadian Journal of Physics. 104: 1-9.
Will increase the availability of beam from the e-linac for ARIEL operation!

## Slide 9
ARIEL
500 MeV – 400 μA
P+ Cyclotron
30 MeV – 10 mA
e-LINAC
AETE
ARIEL
(ISOL)
ARIEL ISOL targets (from 2027)
Cyclotron & beamlines (since ~1975)
E-linac and beamline (since ~2013)
RIB lines
APTW

## Slide 10
Requires the target hall infrastructure for both stations (shielding, target building infrastructure, gas handling, HV infrastructure, vacuum systems)
Target and RIB modules and beam dumps including the medical target and transfer system
Beam line 4 North (BL4N) and the electron beam line and the integration, testing and commissioning of all systems
Required for the ramp up in operation :
  Spent target decay storage vault
  Target production infrastructure (laboratories)
  Offline target acceptance stand – TISA
  HV infrastructure for APTW
  e-Linac upgrade to full performance
  CANREB operation (EBIS, RFCB and HRS)
module storage
spent target storage
protons
electrons
AETE
APTW
drivers beam tunnel
RIB
RIB
Remote-controlled crane
2000t of steel and concrete
Hot cell facilities consisting of maintenance cell and target disposal cell
TISA
Target Hall
Completion of the ARIEL project

## Slide 11
AETE
APTW
BL4N Vault region
BL4N Proton Cave region
BL4N Pharoah’s tomb region
EHBT dogleg region
BL4N & EHBT
Straight Tunnel section
BL4N & EHBT
North Tunnel bend section
Tunnel Overview
NORTH
EHBT (Electron Beam Transport) delivers an electron beam from the e-Linac to the AETE Target Station
BL4N (Beam Line 4 North) delivers a proton beam from the Cyclotron to the APTW Target Station

## Slide 12
BL4N Overview

## Slide 13: Shielding Design Structure
Level 4b: Removable Cap Shielding
Level 4a: Fixed Cap Shielding
Level 3: Service Space
Level 2-4, 2-5, 2-6: Upper Canyon
Level 2-1, 2-2, 2-3: Lower Canyon
Level 1: Below Station
8.1m
The Target Pit Shielding  ensure the access to the hall while beam operation, provide all services (cooling water, ventilation, compressed air etc.)
It consists of 9 layers of fixed shielding and removable cap shielding.
Notes: The entire shielding construction had to be split into layers to allow for all the components to be built and placed

## Slide 14: Target Hall Shielding Progress
Level 1 Complete 2020
beam
Concrete poured for all levels combined: ~ 595 m3 or ~ 1430 metric tons

## Slide 15: Target Hall Shielding Progress
Finally, Summer 2025 level 9 completed!
Installation work in the target hall started.
Layer 9 Complete

## Slide 16: Target Hall installations
ARIEL Module Mounting System
With module mounting system installation complete, ARIEL is now ready* to receive modules!
Module mounting system is the module interface with the ARIEL canyon and provide a smooth, level landing surface  Allows for repeatable positioning of modules and seals the secondary gas volume
HV chase provides supply lines for high voltage, high current (target heating) and cooling water.
High voltage chase

## Slide 17: ARIEL module assembly in ISAC-I
Assembly of the modules requires assembly of the shielding and of the related beam line element
Target module, RIB modules  support structure
ARIEL Module assembly frame
ARIEL Module test frame
ARIEL Module storage frame

## Slide 18: Module assembly jungle

## Slide 19: ARIEL target modules
No Services in Vacuum
HV Services (HVFT)
Ground Services
(GSI)
2m
1.2m
Driver Beams IN
Proton on APTW
Electron on AETE
RIB Beam OUT
Tested to 75 kV

## Slide 20: ARIEL target module front end (FE) Remote Handling (RH) tests
The ARIEL FE has around 120 RH maintenance operation possible, 6 times more than the ISAC FE  ARIEL hot cell
Exchange of every services possible (hoses, connectors, pistons, limit switches)
Exchange of the Extraction electrode, swap from an AETE configuration to an APTW configuration

## Slide 21: Status of Beam Delivery Systems - CANREB
Completed:
250 m of RIB beam distribution lines
CANREB HRS with world-record mass resolving power
ARIEL yield station
Ongoing:
Address remaining issues with CANREB EBIS (e-gun test stand) and CANREB RFQ
HRS HV enclosure to be assembled
RIB modules  module assembly

## Slide 22
ARIEL Science Workshop, 20-23 April 2026
Nuclear Physics - Nuclear Astrophysics - Fundamental Interactions
Around 135 international participants.
Nuclear-physics focused workshop was the first in a series of ARIEL Science Workshops.
Series of invited presentations, panel discussions on ten nuclear physics research topics.
Strong endorsement of the existing research programs at ISAC and the plans to strengthen and expand these with ARIEL beams.
A clear message that post-accelerated RIBs are needed and have been a problem in the past.
There is a large demand for a ramp up to the 9000 RIB hours RIB operation ARIEL will be able to provide in the futre.
A consensus on new ideas emerged for nuclear structure and astrophysics to perform dedicated campaigns of study around the peaks of photo-fission production (Ga, Sn and Ba etc).
Radioactive molecules at ARIEL show significant promise and excitement for impactful science.
Suggestions for TRIUMF to host an active time-projection chamber and a solenoid-based transfer reaction detector were put forward.

## Slide 23
ARIEL Progress in Long Shutdown 2026 is significant
towards the completion of ARIEL

## Slide 24: Thank you Merci

## Slide 25: Additional slides

## Slide 26: TRIUMF accelerator complex
Primary beam driver:
Cyclotron, 500 MeV, H-
Produces rare isotopes, neutrons and muons!
Providing beam for:
Isotope Separator and Accelerator facility – ISAC (ISOL facility) ISAC-I: Normal conducting-linac, 0.15-1.5 MeV/u
ISAC-II: Superconducting-linac, 5-15 MeV/u
And the
Advanced Rare Isotope Laboratory - ARIEL
4 Cyclotrons for medical isotope production
(with a TR24 to be commissioned in the Institute for advanced Medical Isotope – IAMI)
500 MeV
Cyclotron
ISAC-II
High energy
ISAC-I
Low and
medium
energy
ARIEL
Cyclotrons
for medical
Isotope
production

## Slide 27: ARIEL ORG CHART